## Slide 1
Lean Six Sigma Black Belt Training
Featuring Examples from SigmaXL v.8

## Slide 2: 1.0 Define Phase

## Slide 3: 1.1 Overview of Six Sigma

## Slide 4: Black Belt Training: Define Phase
1.1 Six Sigma Overview
1.1.1 What is Six Sigma
1.1.2 Six Sigma History
1.1.3 Six Sigma Approach Y = f(x)
1.1.4 Six Sigma Methodology
1.1.5 Roles and Responsibilities
1.2 Six Sigma Fundamentals
1.2.1 Defining a Process
1.2.2 VOC and CTQs
1.2.3 QFD
1.2.4 Cost of Poor Quality (COPQ)
1.2.5 Pareto Analysis (80 : 20 rule)
1.3 Lean Six Sigma Projects
1.3.1 Six Sigma Metrics
1.3.2 Business Case and Charter
1.3.3 Project Team Selection
1.3.4 Project Risk Management
1.3.5 Project Planning
1.4 Lean Fundamentals
1.4.1 Lean and Six Sigma
1.4.2 History of Lean
1.4.3 The Seven Deadly Muda
1.4.4 Five-S (5S)

## Slide 5: 1.1.1 What is Six Sigma

## Slide 6: What is Six Sigma?
What is “sigma”?
  In statistics, sigma (s) refers to “standard deviation,” which is a measure of variation.
  You will come to learn that variation is the enemy of any quality process. We need to understand, manage, and minimize process variation.
What is “Six Sigma”?
  Six Sigma is an aspiration or goal of process performance.
  A Six Sigma “goal” is for a process average to operate approximately 6s away from customer’s high and low specification limits.
Notes: Most people think of Six Sigma as a disciplined, data-driven approach to eliminating defects and solving business problems.
If you break down the two words, “Six Sigma,” they really describe a measure of quality that strives for near perfection.
Sigma and standard deviation are the same thing, a measure of variation.
Variation is the enemy of quality; it makes it much more difficult to meet a customer’s expectation for a product or service.
The aspiration is to limit the variation to such a degree that 6 “sigmas” (or standard deviations) above or below your mean will fall within the limits that are acceptable to customers.

## Slide 7: What is Six Sigma?
A process whose average is about 6s away from the customer’s high and low specification limits has abundant room to “float” before approaching the customer’s specification limits.
A Six Sigma process only yields 3.4 defects for every million opportunities! In other words, 99.9997% of the products are defect-free!
Notes: The more variation that can be reduced in the process (by narrowing the distribution), the more easily the customer’s expectations can be met.
A Six Sigma process will yield only 3.4 defects for every million opportunities, but some processes require more quality and some require less.
It is important to note that a Six Sigma level of quality does not come without cost, so one must consider what level of quality is needed or acceptable and how much can be spent on resources to remove the variation.

## Slide 8: What is Six Sigma: Sigma Level
Sigma level measures how many “sigma” there are between your process average and the nearest customer specification.
Let us assume that your customers upper and lower specifications limits (USL & LSL) were narrower than the width of your process spread.
The USL & LSL below stay about 1 standard deviation away from the process average. Therefore, this process operates at 1 sigma.
Notes: On the previous page, the LSL and USL were at 6 standard deviations from the mean. Would that process be more or less forgiving than the one that is pictured?
This process is much less forgiving. It is a 1 sigma process because the USL and LSL are only 1 standard deviations from the mean.
The area under the blue curve to the left of the LSL and to the right of the USL represents process defects.

## Slide 9: What is Six Sigma: Sigma Level
A process operating at 1 sigma has a defect rate of approximately 70%.
          This means that the process will generate defect-free products only 30% of the time.
What about processes with more than 1 sigma level?
A higher sigma level means a lower defect rate.
Let us take a look at the defect rates of processes at different sigma levels.
Notes: A 1 sigma process will generate defects 70% of the time, so for every 3 units that are good, there are 7 defective.
A 1 sigma process is not desirable anywhere. What are the implications of such a process? High customer claims, high process waste, lost reputation…any others?

## Slide 10: What is Six Sigma: Sigma Level
This table shows each sigma level’s corresponding defect rate and DPMO (defects per million opportunities).
The higher the sigma level, the lower the defective rate and DPMO.
How does this translate into things you might easily relate to?
Notes: The table on this page shows how dramatically the quality can improve when moving from a 1 sigma process, to 2 sigma, to 3, and so on.
On the next page we will look at how this concept applies to some everyday applications.

## Slide 11: What is Six Sigma: Sigma Level
Let us take a look at processes operating at 3 sigma.
3 sigma processes have a defect rate of approximately 7%. What would happen if processes operated at 3 sigma?
  Virtually no modern computer would function*.
  10,800,000 health care claims would be mishandled each year.
  18,900 US savings bonds would be lost every month.
  54,000 checks would be lost each night by a single large bank.
  4,050 invoices would be sent out incorrectly each month by a modest-sized telecommunications company.
  540,000 erroneous call details would be recorded each day from a regional telecommunications company.
  270 million erroneous credit card transactions would be recorded each year in the United States.
(*http://www.qualityamerica.com)
Notes: Can you imagine what a 3 sigma process would look like in the tech industry, in health care, in banking?
Can you apply this concept to a process that you relate to?

## Slide 12: What is Six Sigma: Sigma Level
What if processes operated with 1% defect rate?
  20,000 lost articles of mail per hour*.
  Unsafe drinking water almost 15 minutes per day.
  5,000 incorrect surgical operations per week.
  Short or long landings at most major airports each day.
  200,000 wrong drug prescriptions each year.
  No electricity for almost 7 hours per month.
Even at 1% defect rate, some processes would be unacceptable to you and many others.
So what is Six Sigma?
  Sigma level is the measure!
  Six is the goal!
(* Implementing Six Sigma – Forest W. Breyfogle III)
Notes: Even with a 1% defect rate, these processes would be nowhere near acceptable.
Would you drink the water in a community where the local water treatment facility operates at a 1% defect rate?
Would you go to a surgeon with a 1% defect rate?
So to recap where we started: Sigma level is the measure of quality level, and Six Sigma is the goal to aspire to.

## Slide 13: What is Six Sigma: The Methodology
Six Sigma itself is the goal, not the method.
In order to achieve Six Sigma, you need to improve your process performance by:
  Minimizing the process variation so that your process has enough room to fluctuate within customer’s spec limits
  Shifting your process average so that it is centered between your customer’s spec limits.
Accomplishing these two process improvements (along with stabilization and control), you can achieve Six Sigma.
DMAIC is the systematic methodology prescribed to achieve Six Sigma.
Notes: While Six Sigma is often associated with the methodology, it is actually the goal.
To achieve the goal, process performance must be achieved by reducing the variation and/or shifting the process average.
By doing this, the process is more capable of meeting the specification limits that are set by the customer.
Stabilization and control refer to the ability to maintain the process improvements or level of quality over time.
The methodology that should be used to achieve the goal is called DMAIC.

## Slide 14: What is Six Sigma: The Methodology
DMAIC is a systematic and rigorous methodology that can be applied to any process in order to achieve Six Sigma.
It consists of 5 phases of a project:
  Define
  Measure
  Analyze
  Improve
  Control.
You will be heavily exposed to many concepts, tools, and examples of the DMAIC methodology through this training.
You will be capable of applying the DMAIC methodology to improve the performance of any process at the completion of the curriculum.
Notes: DMAIC is the path to Six Sigma. It is a disciplined, rigorous, data-driven approach that can be applied to any process.
The phases are DEFINE, MEASURE, IMPROVE, ANALYZE, and CONTROL.
The goal of this training is to teach you how to apply DMAIC and leverage the many concepts and tools within it.

## Slide 15: 1.1.2 Six Sigma History

## Slide 16: Six Sigma History
Polaroid
Notes: Six Sigma was originally developed by Motorola in 1986, but really became popular when Jack Welch at GE made it the focus of his business strategy. Since the late 90s, it has become widely used across many industries. Maybe you have heard of a few of these?
While the term “Lean” was coined in the 1990s, the methodology is mainly based on the concepts of the Toyota Production System, which was developed by Taiichi Ohno, Shigeo Shingo, and Eiji Toyoda at Toyota between 1948 and 1975.

## Slide 17: Six Sigma History
The “Six Sigma” terminology was originally adopted by Bill Smith at Motorola in the late 1980s as a quality management methodology.
As the “Father of Six Sigma,” Bill forged the path for Six Sigma through Motorola’s CEO Bob Galvin who strongly supported Bill’s passion and efforts.
Starting from the late 1980s, Motorola extensively applied Six Sigma as a process management discipline throughout the company, leveraging Motorola University.
In 1988, Motorola was recognized with the prestigious Malcolm Baldrige National Quality Award for its achievements in quality improvement.
Notes: Bill Smith originally approached Bob Galvin with what he referred to as the “theory of latent defect.”
The core principle of the theory is that variation in manufacturing processes is the main driver for defects, and eliminating variation will help eliminate defects. In turn, it will eliminate the wastes associated with defects, saving money and increasing customer satisfaction.
The threshold agreed to by Motorola was 3.4 defects per million opportunities…does it sound familiar?

## Slide 18: Six Sigma History
Six Sigma has been widely adopted by companies as an efficient way of improving the business performance since General Electric implemented the methodology under the leadership of Jack Welch in the 1990s.
As GE connected Six Sigma results to its executive compensation and published the financial benefits of Six Sigma implementation in their annual report, Six Sigma became a highly sought-after discipline of quality.
Notes: In the 1990s, Six Sigma became widely popular after it was implemented at GE under the leadership of Jack Welch.
Companies across many industries followed suit. In some cases GE taught companies how to deploy the methodology, and in many cases experts from GE and other pioneer companies were heavily recruited to companies that were new to methodology.

## Slide 19: Six Sigma History
Most Six Sigma programs cover the aspects, tools, and topics of Lean or Lean Manufacturing.
The two work hand in hand, benefitting each other.
  Six Sigma focuses on minimizing process variability, shifting the process average, and delivering within customer’s specification limits.
  Lean focuses on eliminating waste and increasing efficiency.
Lean and its popularity began to form and gain significant traction in the mid 1960s with the Toyota initiative “TPS” or Toyota Production System.
The concepts and methodology of Lean, however, were fundamentally applied much earlier by both Ford and Boeing in the early 1900s.
Notes: The DMAIC methodology is essentially an ordered collection of concepts and tools that were not unique to Six Sigma. The concepts and tools are leveraged in a way that leads down a problem solving path.
Another methodology that is complementary to Six Sigma is Lean or Lean Manufacturing.
While Six Sigma focuses on process variability, Lean focuses on eliminating waste and improving process flow and efficiency.
Although the concepts have been applied all the way back in the early 1900s by Ford and Boeing, they were made popular by Toyota in the 1960s with what was originally known as the “just-in-time production system,” and became known as the Toyota Production System.

## Slide 20: Six Sigma History
Despite the criticism and immaturity of Six Sigma in many aspects, its history continues to be written with every company and organization striving to improve its business performance.
Polaroid
Notes: The track record for many of these companies, after implementing Six Sigma, speaks for itself.

## Slide 21: 1.1.3 Six Sigma Approach

## Slide 22: Six Sigma Approach: Y = f(x)
The Six Sigma approach to problem solving uses a transfer function.
A transfer function is a mathematical expression of the relationship between the inputs and outputs of a system.
Y = f(x) is the relational transfer function that is used by all Six Sigma practitioners.
It is absolutely critical that you understand and embrace this concept.

## Slide 23: Six Sigma Approach: Y = f(x)
“Y” refers to the measure or output of a process.
  Y is usually your primary metric
  Y is the measure of process performance that you are trying to improve.
f(x) means “function of x.”
  x’s are factors or inputs that affect the Y
Combined, the Y = f(x) statement reads “Y is a function of x.”
In simple terms: “My process performance is dependent on certain x’s.”
The objective in a Six Sigma project is to identify the critical x’s that have the most influence on the output (Y) and adjust them so that the Y improves.
Notes: You might have been introduced to the transfer function in middle school algebra, but it means so much more than symbolizing an algebraic equation.
It is important to keep in mind this concept throughout the DMAIC process. The system (or process) outputs (Y’s) are a function of the inputs (x’s).

## Slide 24: Six Sigma Approach: Y = f(x)
Let us look at a simple example of a pizza delivery company that desires to meet customer expectations of on-time delivery.
  Measure = on-time pizza deliveries
    Y = percent of on-time deliveries
  f(x) would be the x’s or factors that heavily influence timely deliveries
    x1: might be traffic
    x2: might be the number of deliveries per driver dispatch
    x3: might be the accuracy of directions provided to the driver
    x4: might be the reliability of the delivery vehicle
    etc.
The statement Y = f(x) in this example will refer to the proven x’s determined through the steps of a Six Sigma project.
Notes: Most would agree that an important requirement of pizza delivery is to be fast or “on-time.” In this example, let us consider factors that might cause variation in Y (percent of on-time deliveries).
In the DMAIC process, the goal is to determine which inputs (x’s) are the main drivers for the variation in Y.

## Slide 25: Six Sigma Approach: Y = f(x)
With this approach, all potential x’s are evaluated throughout the DMAIC methodology.
The x’s should be narrowed down until the vital few x’s that significantly influence “on-time pizza deliveries” are identified!
Y=f(x)
X8
X6
X1
X5
X7
X4
X3
X2
Notes: One might think of the DMAIC process as a funnel to narrow down all the possible x’s to the vital few.
Why might it be important to know what the vital few x’s are? To focus improvement where the most impact can be affected through changing the inputs.

## Slide 26: Six Sigma Approach: Y = f(x)
This approach to problem solving will take you through the process of determining all potential x’s that might influence on-time deliveries and then determining through measurements and analysis which x’s do influence on-time deliveries.
Those significant x’s become the ones used in the Y = f(x) equation.
The Y = f(x) equation is a very powerful concept and requires the ability to measure your output and quantify your inputs.
Measuring process inputs and outputs is crucial to effectively determining the significant influences to any process.
Notes: The approach will funnel the possible x’s to the few that do influence Y. The measurement of those x’s and their effect on the Y then become the focus to determine which have the most significant impact.
By determining which have the most impact, resources can be focused on changing those inputs to achieve the desired process output.

## Slide 27: 1.1.4 Six Sigma Methodology

## Slide 28: Six Sigma Methodology
Six Sigma follows a methodology that is conceptually rooted in the principles of a five-phase project.
Each phase has a specific purpose and specific tools and techniques that aid in achieving the phase objectives.
The 5 phases of DMAIC:
  Define
  Measure
  Analyze
  Improve
  Control
Notes: Six Sigma is a data-driven methodology for solving problems, improving, and optimizing business problems.
It has 5 phases, each with a specific and important purpose toward achieving the goal of the project.

## Slide 29: Six Sigma Methodology
Define
Define and quantify the problem and objective
Measure
Baseline process, validate measures, and identify all possible x’s and dependent Y’s
Analyze
Analyze and validate causes identifying critical factors
Improve
Control
Develop solutions
Implement and sustain solutions
Notes: DEFINE – the main goal is to “define” what the project is setting out to do and scope the effort.
MEASURE – To establish a baseline for the process, ensure the measurement system is reliable, and identify all possible root causes for a problem.
ANALYZE – To narrow down all possible root causes to the critical few that are the primary drivers of the problem.
IMPROVE – To develop the improvements for the process.
CONTROL – To implement the fix and a control plan to ensure the improvements are sustained over time.
In terms of the transfer function:
DEFINE – Understand the project Y’s and how to measure them.
MEASURE – Prioritize potential x’s and measure x’s and Y’s.
ANALYZE – Test x-Y relationships and verify/quantify important x’s.
IMPROVE – Implement solutions to improve Y’s and address important x’s.
CONTROL – Monitor important x’s and the Y’s over time.

## Slide 30: Six Sigma Methodology: Define Phase
The goal of the Define phase is to establish a solid foundation and business case for a Six Sigma project.
Define is arguably the most important aspect of any Six Sigma project.
All successful projects start with a current state challenge or problem that can be articulated in a quantifiable manner.
  It is not enough to just know the problem, you must quantify it and also determine the goal.
Once problems and goals are identified and quantified, the rest of the define phase will be about valuation, team, scope, project planning, timeline, stakeholders, Voice Of the Customer (VOC), and Voice Of the Business (VOB).
Notes: DEFINE is a critical phase. It sets the foundation for the project, and if it is not done well and properly thought, it is very easy for a project to go off-track.
All problems start with a quantifiable problem statement – without a baseline and a goal, it is very difficult to keep boundaries around the project. Without knowing how much improvement is needed or desired, it can be very difficult to control the scope of the project.

## Slide 31: Six Sigma Methodology: Define Phase
Define Phase Tools and Deliverables
  Project Charter – Establish the:
      Business Case
      Problem Statement
      Project Objective
      Project Scope
      Project Timeline
      Project Team.
  Stakeholder Assessment
  High-Level Pareto Chart Analysis
  High-Level Process Map
  VOC/VOB and CTQs Identified and Defined
  Financial Assessment
Notes: The project charter is essentially a contract formed between a project team, the champion, and the stakeholders. It defines what the project is going to do, why they are going to do it, when it will be done, and by whom. It includes the business case, problem statement, project objective, scope, timeline, and team.
A stakeholder assessment is done to understand where there are gaps in stakeholder support and develop strategies to overcome them.
High-level Pareto chart and process maps, along with VOC (voice of customer), VOB (voice of business), and CTQs (critical to quality requirements) also help to develop the scope and put some guardrails around the process.

## Slide 32: Six Sigma Methodology: Measure Phase
The goal of the Measure phase is to gather baseline information about the process (process performance, inputs, measurements, customer expectations etc.).
Throughout the Measure phase you will seek to achieve a few important objectives:
  Gather All Possible x's
  Assess Measurement System and Data Collection Requirements
  Validate Assumptions
  Validate Improvement Goals
  Determine COPQ (Cost of Poor Quality)
  Refine Process Understanding
  Determine Process Stability
  Determine Process Capability.
Notes: The MEASURE phase is necessary to establish the baseline performance for the process, determine if the measurement system(s) is (are) reliable. It is also important to determine if the process is stable and how capable the process is of meeting the customer’s specifications.
There are a few important objectives: identify all the possible x’s, plan what data needs to be collected, assess measurement systems for reliability, validate assumptions and improvement goals, determine the Cost of Poor Quality (COPQ), determine if the process is stable and if the process is capable of meeting customer requirements.

## Slide 33: Six Sigma Methodology: Measure Phase
Measure Phase Tools and Deliverables
  Process Maps, SIPOC, Value Stream Maps
  Failure Modes and Effects Analysis (FMEA)
  Cause-and-Effect Diagram
  XY Matrix
  Six Sigma Statistics
    Basic Statistics
    Descriptive Statistics
  Measurement Systems Analysis
    Variable and/or Attribute Gage R&R
    Gage Linearity and Accuracy or Stability
  Basic Control Charts
  Process Capability (Cpk, Ppk) and Sigma Levels
  Data Collection Plan
Notes: There are many powerful tools that will be introduced to you throughout the MEASURE phase.
There are many different types of maps to visualize a process:
A SIPOC or a Value Stream Map
An FMEA (Failure Modes and Effects Analysis) to identify possible process failure modes and prioritize them
Tools to brainstorm possible root causes for defects (Cause and Effect) and prioritize those (XY matrix)
Some basic statistical tools to understand more about your process data (Basic and Descriptive Statistics)
Measurement system analysis tools to establish repeatability, reproducibility, linearity, accuracy, and stability
Basic control charts to assess process stability
Tools to assess and quantify a process’ ability to meet customer specification limits
A data collection plan to ensure that when data is collected, it is done properly.

## Slide 34: Six Sigma Methodology: Analyze Phase
The Analyze phase is all about establishing verified drivers.
In the DMAIC methodology, the Analyze phase uses statistics and higher-order analytics to discover relationships between process performance and process inputs (in other words, what are the root causes or drivers of the improvement effort).
Ultimately, the Analyze phase establishes a reliable hypothesis for improvement solutions.
  Establish the Transfer Function Y = f(x)
  Validate the List of Critical x's and Impacts
  Create a Beta Improvement Plan (e.g., pilot plan).
Notes: The ANALYZE phase is where the potential root causes are narrowed down to the critical root causes.
Statistical tools are used to determine whether or not there are relationships between process performance and the potential root causes.
Where the strong relationships are discovered, these become the foundation for the solution to improve the process.
This is where the transfer function, Y = f(x), is established and the project can establish a hypothesis for improved results.

## Slide 35: Six Sigma Methodology: Analyze Phase
Analyze Phase Tools and Deliverables
  The Analyze phase is about proving and validating critical x’s using the appropriate and necessary analysis techniques. Examples include:
    Hypothesis Testing
      Parametric and Non-Parametric
    Regression
      Simple Linear Regression
      Multiple Linear Regression
  The Analyze phase is also about establishing a set of solution hypotheses to be tested and further validated in the Improve phase.
Notes: There are many tools that are used to prove and validate the critical x’s:
Hypothesis tests such as t-tests, ANOVA, Chi-Square, to name a few
Different types of regression to establish quantitative and predictive relationships between the x’s and Y’s
The tools help to formulate a hypothesis about how much improvement can be expected in the Y, given a change in the x.

## Slide 36: Six Sigma Methodology: Improve Phase
The goal of the Improve phase is. . .you guessed it! "make the improvement." Improve is about designing, testing, and implementing your solution.
To this point you have defined the problem and objective of the project, brainstormed possible x's, analyzed and verified critical x's. Now it's time to make it real!
  Statistically Proven Results from Active Study/Pilot
  Improvement/Implementation Plan
  Updated Stakeholder Assessment
  Revised Business Case with Return on Investment (ROI)
  Risk Assessment/Updated FMEA
  New Process Capability and Sigma.
Notes: Methodologies for the IMPROVE phase include:
Experiments and planned studies
Pilots or tests designed to validate relationships and determine how much change in an input is needed to induce the desired result in the output.
Implementation plan to stimulate thoughts and planning for any necessary communications, training, and preparations to implement the process improvement

## Slide 37: Six Sigma Methodology: Improve Phase
Improve Phase Tools and Deliverables
  Any Appropriate Tool from Previous Phases
  Design of Experiment (DOE)
    Full Factorial
    Fractional Factorial
  Pilot or Planned Study Using:
    Hypothesis Testing
    Valid Measurement Systems
  Implementation Plan

## Slide 38: Six Sigma Methodology: Control Phase
The last of the 5 core phases of the DMAIC methodology is the Control phase.
The goal of the Control phase is to establish automated and managed mechanisms to maintain and sustain your improvement.
A successful control plan also establishes a reaction and mitigation plan as well as an accountability structure.
Notes: The CONTROL phase is a common failure point for projects.
Improvements are made, but gains will only be temporary if the proper controls are not in place.
The purpose of the CONTROL phase is to establish the mechanisms to ensure the process sustains improved performance and a reaction/mitigation plan to activate by a process owner if it does not.

## Slide 39: Six Sigma Methodology: Control Phase
Control Phase Tools and Deliverables
  Statistical Process Control (SPC/Control Charts)
    IMR, XbarS, XbarR, P, NP, U, C etc.
  Control Plan Documents
    Control Plan
    Training Plan
    Communication Plan
    Audit Checklist
  Lean Control Methods
    Poka-Yoke
    Five-S
    Kanban
Notes: Control charts are useful for monitoring process inputs and outputs for stability and quickly identifying when the process goes “out of control.”
Control plans are used to ensure control points are identified and accountability for monitoring them is taken.
A training plan is needed to ensure employees are properly trained to perform process changes.
A communication plan is useful to alert any stakeholders of a change.
Lean tools can be used to “poka-yoke” (mistake proof) a process.
Five-S can be used to organize the workplace and make it more visual.

## Slide 40: Six Sigma Methodology
Define
Goal: Problem Statement, Objective, Business Case, Project Scope, Team
Main Tools: Project Charter, Pareto, Process Maps
Measure
Goal: Brainstorm/Prioritize Possible x’s, Validate measurement, Capability
Tools: Basic Statistics, C & E, XY Matrix, Capability Analysis, MSA, Process Maps, Control Charts
Analyze
Goal: Identify critical x’s
Goal: Lock-in the Improvement
Improve
Control
Tools: Hypotheses Tests (Normal/Non Normal), Regression and Correlation
Goal: Design, Test, and Implement Improvement
Tools: DOE, Implementation/Change/Communication Plan
Tools: Control Plan, Poka-Yoke, SPC, SOPs, Training Plans etc.
Six Sigma DMAIC Roadmap
Notes: This slide provides a high-level view of the DMAIC phases and basic tools. It can be turned into a nice wall-chart or placemat to jog your memory.

## Slide 41: 1.1.5 Roles and Responsibilities

## Slide 42: Roles and Responsibilities
The various roles in a Six Sigma program are commonly referred to as “Belts.”
In addition to Belts, there are also other key roles with specific responsibilities.
Let us explore the different roles and their corresponding responsibilities in a Six Sigma program.
Notes: It is important to know the many roles in Six Sigma to understand where responsibilities lie to execute a project.
Most commonly known are Belts (Black Belt, Green Belt, Master Black Belt, and Yellow Belt).
There are other roles as well, such as Champion, Sponsor, and Stakeholder.

## Slide 43: Roles and Responsibilities
Expert
Novice
Each of the four Six Sigma belts represents a different level of expertise in the field of Six Sigma.
  Six Sigma Master Black Belt (MBB)
  Six Sigma Black Belt (BB)
  Six Sigma Green Belt (GB)
  Six Sigma Yellow Belt (YB)
In addition to Belts, there are other critical and complementary roles:
  Champions
  Sponsors
  Stakeholders
  Subject Matter Experts (SMEs).
Notes: Different Belt levels are associated with differing levels of expertise in Six Sigma, with Master Black Belt being the most highly trained expert, to Yellow belt having very basic knowledge.
There are also other roles that are very important to the success of Six Sigma initiatives, such as Champions, Sponsors, Stakeholders, and Subject Matter Experts.

## Slide 44: Roles and Responsibilities: MBB
The Master Black Belt (MBB) is the most experienced, educated, and capable Six Sigma expert.
A typical MBB has managed dozens of Black Belt level projects.
The MBB can simultaneously lead multiple Six Sigma Belt projects while mentoring and certifying Black Belt and Green Belt candidates.
The MBB typically works with high-level operations directors, senior executives, and business managers to help with assessing and planning business strategies and tactics.
Notes: The MBB is often thought of as a trusted advisor to high-level leaders.
The MBB often guides or coaches Black Belts and Green Belts and ensures the proper and consistent application of Six Sigma across departments.
While an MBB is typically technically savvy with all of the concepts and tools, it is critical that he or she has the skills to communicate in a practical manner with those that are not well-versed in Six Sigma.
Also, the MBB needs to have a strong ability to communicate with and influence leaders at all levels of an organization.

## Slide 45: Roles and Responsibilities: MBB
MBB commonly advises management team on the cost of poor quality of an operation and consults on methods to improve business performance.
Typical Responsibilities of a MBB
  Identifies and defines the portfolio of projects required to support a business strategy
  Establishes scope, goals, timelines, and milestones
  Assigns and marshals resources
  Trains and mentors Green Belts and Black Belts
  Facilitates tollgates or checkpoints for Belt candidates
  Reports-out/updates stakeholders and executives
  Establishes organization’s Six Sigma strategy/roadmap
  Leads the implementation of Six Sigma.
Notes: A MBB often is a trusted advisor to senior leaders in an organization, articulating the cost of poor quality and consulting with them about how to go about improving performance.
A MBB is responsible for defining a project portfolio to solve the businesses problems and drive the strategy.
He or she shapes the work by establishing scope, goals, and timelines.
He or she gathers resources, trains Belts, facilitates tollgates, and reports out to stakeholders and executives.
Finally, the MBB establishes a strategy for Six Sigma implementation and leads the way.

## Slide 46: Roles and Responsibilities: BB
The Black Belt (BB) is the most active and valuable experienced Six Sigma professional among all the Six Sigma Belts.
A typical BB has
  led multiple projects
  trained and mentored various Green Belts candidates
  understood how to define a problem and drive effective solution.
The BB is well rounded in terms of project management, statistical analysis, financial analysis, meeting facilitation, prioritization, and a range of other value-added capabilities, which makes a BB highly valuable asset in the business world.
Notes: The Black Belt is the key to success among all the other Belts.
The role of a Black Belt is to lead multiple projects, train and mentor Green Belts, define a problem, and drive change effectively.
The Black Belt incorporates many skills that are critical to successfully and quickly implementing a process improvement initiative through the DMAIC methodology.

## Slide 47: Roles and Responsibilities: BB
BBs commonly serves as the dedicated resource continuing their line management role while simultaneously achieving a BB certification.
Typical Responsibilities of a BB
  Project Management
    Defines projects, scope, teams etc.
    Marshals resources
    Establishes goals, timelines, and milestones
    Provides reports and/or updates to stakeholders and executives.
Notes: Often Black Belts are dedicated to improvement efforts, but typically pursue certification while simultaneously performing their normal line role.
Responsibilities include project definition, resource gathering, planning, and reporting outs.

## Slide 48: Roles and Responsibilities: BB
Typical Responsibilities of a BB (continued)
  Task Management
    Establishes the team’s Lean Sigma roadmap
    Plans and implements the use of Lean Sigma tools
    Facilitates project meetings
    Does project management of the team’s work
    Manages progress toward objectives.
  Team Management
    Chooses or recommend team members
    Defines ground rules for the project team
    Coaches, mentors, and directs project team
    Coaches other Six Sigma Belts
    Manages the team’s organizational interfaces.
Notes: The BB typically performs the role of a project manager, planning the project, facilitating project meetings, and managing toward objectives.
The BB plays a key role in forming, directing, mentoring, and coaching the team.

## Slide 49: Roles and Responsibilities: GB
The Green Belt (GB) is considered as a less intense version of Six Sigma professional than the Black Belt (BB).
A GB is exposed to all the comprehensive aspects of Six Sigma with less focus on the statistical theories and some other advanced analytical methodologies such as Design of Experiment (DOE).
When it comes to project management, a GB has almost the same responsibilities as a BB.
In general, the GB works on less complicated and challenging business problems than a BB.
Notes: While a Black Belt’s sole business responsibility could be the implementation of projects, Green Belts often implement projects in addition to other job responsibilities. Therefore, the Green Belt typically works on less complicated business problems.
A Green Belt takes direction and coaching from the Black Belt.
While exposed to all the concepts of Six Sigma, the Green Belt does not typically get deep into some of the more advanced statistical tools (at least not without significant direction from an expert Black Belt or Master Black Belt).

## Slide 50: Roles and Responsibilities: GB
Typical Responsibilities of a Green Belt
  Project Management
    Defines the project, scope, team etc.
    Marshals resources
    Sets goals, timelines, and milestones
    Reports-out/updates stakeholders and executives.
  Task Management
    Establishes the team’s Lean Sigma Roadmap
    Plans and implements the use of Lean Sigma tools
    Facilitates project meetings
    Does Project Management of the team’s work
    Manages progress toward objectives.
  Team Management
    Chooses or recommends team members
    Defines ground rules for the project team
    Coaches, mentors, and directs project team
    Coaches other Six Sigma Belts
    Manages the team’s organizational interfaces.
Notes: As you can see, the roles and responsibilities are identical to those of a Black Belt.
The key differences are the level of complexity and the dedication that a Black Belt has toward Six Sigma projects. Again, a Green Belt typically does projects in addition to his or her normal line job responsibilities.

## Slide 51: Roles and Responsibilities: YB
The Yellow Belt (YB) understands the basic objectives and methods of a Six Sigma project.
YB has an elementary understanding about what other Six Sigma Belts (GB, BB, MBB) are doing to help them succeed.
In a Six Sigma project, YB usually serves as a subject matter expert regarding some aspects of the process or project.
Supervisors, managers, directors, and sometimes executives are usually trained at the YB level.
Notes: Yellow Belts have enough understanding of Six Sigma so they can be effective in assisting other Six Sigma Belts to succeed with their projects, usually in the role of subject matter experts.
This level of training is important to have in an environment where Six Sigma projects are prevalent, such as when managing Belts.

## Slide 52: Roles and Responsibilities: YB
Typical Responsibilities of a Yellow Belt
  Helps define process scope and parameters
  Contributes to team selection process
  Assists in information and data collection
  Participates in experiential analysis sessions (FMEA, Process Mapping, Cause and Effect etc.)
  Assists in assessing and developing solutions
  Delivers solution implementations.
Notes: The Yellow Belt serves in a support role for Six Sigma projects.
The Yellow Belt participates in defining projects, assists in data collection, contributes in analysis sessions, and assists in assessing, developing, and implementing solutions.

## Slide 53: Roles and Responsibilities: Champions & Sponsors
Champions and sponsors are those individuals (directors, executives, managers etc.) chartering, funding, or driving the Six Sigma projects that BBs and GBs are conducting.
Champions and sponsors need to have a basic understanding of the concepts, tools, and techniques involved in the DMAIC methodology so that they can provide proper support and direction.
Notes: Champions and Sponsors’ roles are to set direction for projects and ensure that the path is clear for the Belts to succeed: obtain resources and funding, overcome stakeholder issues, and knock down other barriers to progress.

## Slide 54: Roles and Responsibilities: Champions & Sponsors
Champions and sponsors play critical roles in the successful deployment of Six Sigma.
Strong endorsement of Six Sigma from the leadership team is critical for success.
Typical Responsibilities of a Champion/Sponsor
  Maintains a strategic oversight
  Establishes strategy and direction for a portfolio of projects
  Clearly defines success
  Provides resolution for issues such as resources or politics
  Establishes routine tollgates or project reviews
  Clears the path for solution implementation
  Assists in project team formation.
Notes: Strong support from leadership is critical to success, and the Champions and Sponsors are responsible for building that support.
From a project standpoint, it is important for them to be highly engaged in the work.
It is their role to provide oversight and guidance to define success for the project(s).
They resolve issues when necessary, such as resource needs, stakeholder conflicts, or political issues.
They create the routines for tollgate reviews to ensure there are regular checkpoints with the project team.

## Slide 55: Roles and Responsibilities: Stakeholders
Stakeholders are usually the recipients or beneficiaries of the success of a Six Sigma project.
Stakeholders are individuals owning the process, function, or production/service line that a Six Sigma Belt focuses on improving the performance of.
BBs and GBs need to keep strong working relationships with stakeholders because without their support, it would be extremely difficult to make the Six Sigma project a success.
Notes: Generally speaking, a Stakeholder is anyone who has interest in a project; stakeholders are usually the beneficiaries of the process improvement.
A stakeholder can be a person, a group, or an organization that is affected by the project.
A lack of stakeholder support can cause a project to fail, either through active or passive resistance, so it is very important to be aware of how stakeholders feel about the work being done so the team can proactively manage their perceptions and level of support.

## Slide 56: Roles and Responsibilities: SMEs
Subject Matter Experts (SMEs) are commonly known as the experts of the process or subject matter.
Six Sigma Belts should proactively look to key SMEs to round out their working project team.
SMEs play critical roles to the success of a project.
  Based on SMEs’ extensive knowledge about the process, they have the experience to identify which solutions can work and which cannot work.
  SMEs who simply do not speak up can hurt the chances of the process’ success.
  SMEs are also the same people who prefer to keep the status quo. Six Sigma Belts may find many of them unwilling to help implement the changes.
Notes: A Subject Matter Expert is someone who is a known expert in the process or other aspect of the problem.
SMEs’ input is critical to ensure the team is leveraging accurate information when it comes to the process or evaluating data and information.
When selecting a SME, it is important to choose people who are vocal, but who also bring ideas. SMEs that are closed-minded to change may be vocal, but can be a barrier to making the necessary improvements.

## Slide 57: Roles and Responsibilities
Throughout this module we have reviewed the various common roles and corresponding responsibilities in any Six Sigma program:
  Six Sigma Master Black Belt
  Six Sigma Black Belt
  Six Sigma Green Belt
  Six Sigma Yellow Belt
  Champion and Sponsors
  Stakeholders
  Subject Matter Experts (SMEs)
These Six Sigma belts and other roles are designed to deliver value to the business effectively and successfully.
Notes: In review, there are many important roles in Six Sigma.
For a Six Sigma program to be effective, it is important to assign these roles to individuals who are well equipped to carry out the responsibilities.

## Slide 58: 1.2. Six Sigma Fundamentals

## Slide 59: Black Belt Training: Define Phase
1.1 Six Sigma Overview
1.1.1 What is Six Sigma
1.1.2 Six Sigma History
1.1.3 Six Sigma Approach Y = f(x)
1.1.4 Six Sigma Methodology
1.1.5 Roles and Responsibilities
1.2 Six Sigma Fundamentals
1.2.1 Defining a Process
1.2.2 VOC and CTQs
1.2.3 QFD
1.2.4 Cost of Poor Quality (COPQ)
1.2.5 Pareto Analysis (80 : 20 rule)
1.3 Lean Six Sigma Projects
1.3.1 Six Sigma Metrics
1.3.2 Business Case and Charter
1.3.3 Project Team Selection
1.3.4 Project Risk Management
1.3.5 Project Planning
1.4 Lean Fundamentals
1.4.1 Lean and Six Sigma
1.4.2 History of Lean
1.4.3 The Seven Deadly Muda
1.4.4 Five-S (5S)

## Slide 60: 1.2.1 Defining a Process
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 61: 1.2.2 VOC and CTQs

## Slide 62: Voice of the Customer
VOC stands for “Voice of the Customer.”
Voice of the customer is a term used for a data-driven plan to discover customer wants and needs.
VOC is an important component to a successful Six Sigma project.
There are also other “Voices” that need to be heard when conducting projects. The 3 primary forms are:
  VOC: Voice of the Customer
  VOB: Voice of the Business
  VOA: Voice of the Associate.
Notes: VOC is an acronym that means “voice of the customer,” and the term refers to data or information collected from the customers to understand what they want or need.
It is always important to understand the VOC when designing and improving any Six Sigma process.
There are other types of “Voices” that are important as well:
  Voice of the Business (VOB) – what does the business require of a process?
  Voice of the Associate (VOA) or Voice of the Employee – what does the employee require of a process (e.g., safety, simplicity)?

## Slide 63: Gathering VOC
Gathering VOC should be performed methodically.
The two most popular methods of collecting VOC are
  Indirect
  Direct.
1. Indirect data collection for VOC involves passive information exchange:
  Warranty claims
  Customer complaints/compliments
  Service calls
  Sales reports.
2. Indirect methods are less effective, sometimes dated, require heavy interpretation, and are also more difficult to confirm.
Notes: There are several ways to collect VOC, but they can be broken down into two main collection methods: indirect and direct.
Indirect collection of VOC involves passive information exchange, meaning the VOC was not expressly collected for the purposes of the project, but was gathered through byproducts of the process.
Warranty claims, customer complaints, and service calls are effective ways to understand how the customer feels about a product or service.
Since the data was not collected to understand VOC specific to a business or process problem, it is more difficult to sort through and interpret the information that is relevant.

## Slide 64: Gathering VOC
Direct data collection methods for VOC are active and planned customer engagements:
  Conducting interviews
  Conducting customer surveys
  Conducting market research
  Hosting focus groups.
Direct methods are typically more effective for several reasons:
  Less need to interpret meaning
  Researchers can go a little deeper when interacting with customers
  Customers are aware of their participation and will respond better upon follow-up
  Researchers can properly plan engagements (questions, sample size, information collection techniques etc.).
Notes: Direct VOC collection methods are carefully planned, active engagement around the customer to solicit specific information.
Customer interviews, surveys, focus groups, and market research are common methods of direct VOC collection.
There is less interpretation needed for this kind of VOC, and in interactive forms of VOC collection (e.g., focus groups or interviews) there is an opportunity to go deeper into a topic or take a direction that might not have been expected or planned.
There are professional organizations that can perform customer data collection on behalf of a company. They commonly plan carefully by designing the questions, determining the sample size, and consider what technique is most appropriate.
If there is a need to get very specific customer feedback, a survey is appropriate.
However, if the need is more exploratory, interviews or focus groups are more appropriate.

## Slide 65: Gathering VOC
Gathering VOC requires consideration of many factors such as product or services types, customer segments, manufacturing methods or facilities etc.
All this information will influence the sampling strategy.
Consider which factors are important and build a sample size plan around them.
Also, consider response rates and adjust the initial sample strategy to ensure adequate input is received.
Once a sampling plan is in place, collect data via the direct and indirect methods discussed earlier.
After gathering VOC it will be necessary to translate it into something meaningful: CTQs.
Notes: One must consider different factors to ensure the right, representative data is collected:
  Product/service types
  Customer segments
  Manufacturing methods.
The factors above are important because they might indicate different customer needs across customer segments, or perhaps the customers’ feedback may differ by product type or manufacturing method.
Once the VOC has been collected, it must be translated into CTQs (Critical To Quality).

## Slide 66: Critical to Quality: CTQ
CTQ stands for Critical to Quality.
CTQs are translated from VOC or “voice of the customer” feedback.
VOC is often vague, emotional, or simply a generalization about products or services.
CTQs are the quantifiable, measureable, and meaningful translations of VOC.
Organizing VOC helps to identify CTQs.
One effective way to organize VOC is to group or bucket it using an affinity diagram.
Affinity diagrams are ideal for large amounts of soft data resulting from brainstorming sessions or surveys.
Notes: CTQs are generated from the voice of the customer (VOC).
Because VOC is usually vague and emotional, it is important to translate it into something that is applicable to a process.
CTQs are quantifiable, measureable, and meaningful.
To create CTQs, the VOC must be organized first into like groupings. An affinity diagram is a useful tool to do this.

## Slide 67: Affinity Diagram: Building a CTQ Tree
Steps for conducting an Affinity Diagram exercise:
  Step 1: Clearly define the question or focus of the exercise (“Why are associates late for work?”).
  Step 2: Record all participant responses on note cards or sticky notes (this is the sloppy part, record everything!).
  Step 3: Lay out all note cards or post the sticky notes onto a wall.
  Step 4: Look for and identify common themes.
  Step 5: Begin moving the note cards or sticky notes into the themes until all responses are allocated.
  Step 6: Re-evaluate and make adjustments.
Notes: This is an outline of building an affinity diagram (or CTQ tree); it is typically done with a group of people.
The group must agree on what question they are trying to answer, or what the focus is for the VOC.
All of the individual VOC responses are recorded on note cards or sticky notes. (Sticky notes are an easier way to do it).
Lay out all the VOC either on a table or a wall so they can all be seen.
Look for common themes across the VOC.
Move cards around so they are grouped by the common themes.
Re-evaluate and make adjustments.
It is good to do this in a group because people bring different perspectives and might understand and organize VOC differently than a single person would.

## Slide 68: Affinity Diagram: Building a CTQ Tree
Define the question or focus
Record responses on note cards or sticky notes
Display all note cards or sticky notes on a wall if necessary.
Notes: In this example, the focus question is “Why are associates late to work?”
You can see all of the responses randomly distributed across the page.

## Slide 69: Affinity Diagram: Building a CTQ Tree
Look for and identify common themes within the responses.
Notes: Now you see that some common themes are identified (delays at home, delays on the commute, kids/pet related delays, or delays in the building).

## Slide 70: Affinity Diagram: Building a CTQ Tree
Group note cards or sticky notes into themes until all responses are allocated.
Re-evaluate and make final adjustments.
Notes: Now you can see that the individual responses are lined up under each theme. See any that might be misplaced? How about “dog threw up?”
Perhaps “Delays at Home” and “Kid/Pet-Related Delays” do not need to be broken down separately.
These are the kinds of things to consider when evaluating and adjusting.

## Slide 71: CTQ Tree
Example of a generic CTQ tree transposed from a white board to a software package.
Notes: This slide illustrates how the CTQ tree might translate to a software package that would allow one to capture and display it electronically.

## Slide 72: Kano
Another VOC categorization technique is the Kano.
The Kano model was developed by Noriaki Kano in the 1980s.
The Kano model is a graphic tool that further categorizes VOC and CTQs into 3 distinct groups:
  Must Haves
  Performance Attributes
  Delighters.
The Kano helps to identify CTQs that add incrementalvalue vs. those that are simply requirements and having more is not necessarily better.
Notes: In the 1980s, Noriaki Kano developed a VOC categorization technique.
It classifies the VOC/CTQs into three groups: must haves, performance attributes, and delighters.
It is important to understand what CTQs are non-negotiable (must haves). These attributes are taken for granted when they are fulfilled, but result in dissatisfaction when they are not fulfilled. The curve for a must have will drop in satisfaction as you move to left where the need is not fulfilled, but flattens out at a neutral satisfaction level as you move to the right.
A delighter is the opposite of the must have – if it is not fulfilled, the customer will not be dissatisfied, but as it is fulfilled, the customer’s satisfaction increases. These are things the customer did not realize they want or need, until they have experienced them. Eventually, delighters will become expected, turning them into performance attributes or must haves.
Examples:
  How would you classify the steering wheel in a car?
  Low prices at a discount store?
  What about the touch screen on an iPhone (think back to when it came out)?
A performance attribute (or one-dimensional attribute) will increase satisfaction level as the need is fulfilled, and will decrease satisfaction when it is not fulfilled.

## Slide 73: Validating VOC and CTQs
After determining all CTQs, confirm them with the customer.
Confirming can be accomplished by conducting surveys through one or more of the following methods:
  Group sessions
  One-on-one meetings
  Phone interviews
  Electronic means (chat, email, social media etc.)
  Physical mail.
Consider your confirming audience and try to avoid factors that may influence or bias responses such as inconvenience or overly burdensome time commitments.
Notes: Once the process of collecting VOC is complete, and CTQs have been determined, the next step is to validate what has been developed.
Many of the methods through which VOC is collected also serve well for confirming the VOC, such as through group sessions, one-on-one interviews in person or over the phone.
It is important that thought is put into what audience is used to confirm the VOC, ensuring that there is not a potential to bias the results. For example, an overly extensive customer survey might end up getting a rushed response and therefore may not represent the true views of an audience.

## Slide 74: Translating CTQs to Requirements
Lastly, CTQs must be transformed into specifics that can be built upon in a process.
A requirements tree translates CTQs to meaningful and measureable requirements for production processes and products.
Notes: To be able to incorporate a CTQ into the design of a process, the next step is to translate CTQs to process requirements.
In this example, the VOC is probably something like, “Deliver my product when you say you’re going to deliver it,” which obviously can be measured by “on-time delivery.”
One must then consider what aspects of the process contribute to the time that elapses between when the customer places an order and when it is delivered.
The order has to be fulfilled, and the shipment processed and inspected by quality control.
The process then can be assigned specifications for what maximum turn time is required to ensure the process is completed and the order is delivered on time.

## Slide 75: 1.2.3 Quality Function Deployment
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 76: 1.2.4 Cost of Poor Quality

## Slide 77: Cost of Poor Quality
Cost of Poor Quality (COPQ) is the expense incurred due to waste, inefficiencies, and defects.
The COPQ has been proven to range from 5% to 30% of gross sales for most companies.
The COPQ can be staggering when considering process inefficiencies, hidden factories, defective products, rework, scrap, etc.
Understanding COPQ and where to look for it will help uncover process inefficiencies, defects, and hidden factories within your business.
Notes: Cost of Poor Quality (or COPQ) is exactly what it sounds like. It is the cost absorbed when a process operates at anything less than optimal: the cost of waste, resource inefficiency, and defects (e.g., repairs, rework, service calls, scrap, warranty claims, and write-offs).
Experts have estimated COPQ to be 5%–30% of gross sales for most companies. Consider a company that does ~$100 million in sales per week, and has a COPQ of 20%. That means that 1 day out of a 5-day work week is completely devoted to producing scrap!
A thorough understanding of this concept can help uncover lots of opportunities. Consider for instance the hidden factories – do you have procedures for rework, or work-arounds? They might seem “hidden” at first, because they have come to be accepted as the normal process for doing things.
There are many different types of non-value added activities that can drive waste. (Discussed on the next slide.)

## Slide 78: Cost of Poor Quality
There are 7 common forms of waste that are often referred to as the “7 deadly muda.”
Technically, there are more than 7 forms of waste but if you can remember these you will capture over 90% of your waste.
  Defects
  Overproduction
  Over-Processing
  Inventory
  Motion
  Transportation
  Waiting
Notes: Muda is a Japanese word meaning “futility, uselessness, idleness, superfluity, waste, wastage, wastefulness.”
The “7 deadly muda,” as defined by Taiicho Ohno (the Toyota Production System), are:
  Defects
  Overproduction – producing more than what your customers are demanding.
  Over-processing – unnecessary time spent (e.g., relying on inspections instead of designing a process to eliminate problems)
  Inventory – things awaiting further processing or consumption
  Motion – extra, unnecessary movement of employees
  Transportation – unnecessary movement of goods
  Waiting – for an upstream process to delivery, for a machine to finish processing, or for an interrupted worker to get back to work.

## Slide 79: Cost of Poor Quality
The “7 deadly muda” are very important to understand. They are the best way to identify the COPQ.
The presence of any muda causes many other forms of inefficiencies and hidden factories to manifest themselves.
  There are four key categories of costs related to muda:
    Costs Related to Production
    Costs Related to Prevention
    Costs Related to Detection
    Costs Related to Obligation
Notes: As mentioned previously, the seven wastes (or “deadly muda”) are important to understand because they help identify where costs of poor quality exist.
The next few slides will lay how to determine the cost of poor quality related to the seven muda.

## Slide 80: COPQ: Costs Related to Production
Costs related to production are the direct costs of the presence of muda. These forms of COPQ are usually understood and easily observable. They are in fact the “7 deadly muda” themselves.
  Defects
  Overproduction
  Over-Processing
  Inventory
  Motion
  Transportation
  Waiting
Notes: The costs related to production are most evident in a process and are most easily understood and estimated.
Consider:
The cost of a defect itself (i.e., the lost labor and materials)
The cost of overproduction (resources spent producing more of something than what is needed, along with the material cost). This is producing “just-in-case” instead of “just-in-time.” This creates excessive lead times, results in high storage costs, and makes it difficult to detect defects. Over-producing hides problems in production and takes a lot of courage to produce only what is needed (which will uncover where the issues are)
The cost of over-processing (resources spent inspecting and fixing instead of getting right the first time)
The cost of inventory (work in process on the floor is a symptom of over-processing and waiting)
The cost of motion (unnecessary time spent by employees to perform the process; consider motion like bending, stretching, walking, lifting, and reaching)
The cost of transportation (adds no value to the product and even increases risk of damage). This can be a hard cost to overcome if facilities are built in a way that requires transportation from one process to another.
The cost of waiting (usually because material flow is poor, production runs are too long, and distances between work centers are too long).

## Slide 81: COPQ: Costs Related to Prevention
Costs related to the prevention of muda are those associated with trying to reduce or eliminate any of the “7 deadly muda.”
  Costs for error proofing methods or devices
  Costs for process improvement and quality programs
  Costs for training and certifications
  etc.
Any costs directly associated with the prevention of waste and defects should be included in the COPQ calculation.
Notes: The costs related to prevention are those incurred trying to reduce or eliminate any of the 7 deadly muda before they occur.
Consider the cost of any action taken to reduce defects, make process improvements, error-proof processes or devices, implement a quality program, conduct training, and obtain certifications.

## Slide 82: COPQ: Costs Related to Detection
Costs related to the detection of muda are those associated with trying to find or observe any of the “7 deadly muda.”
  Costs for sampling
  Costs for quality control check points
  Costs for inspection costs
  Costs for cycle counts or inventory accuracy inspections
  etc.
Any costs directly associated with the detection of waste and defects should be included in the COPQ calculation.
Notes: The costs of detection are those spent trying to find or observe any of the 7 deadly muda after they occur.
Detection is not as effective as prevention, but sometimes is the only option. It can keep additional costs from being incurred, like continuing to process a defective unit.
Examples include costs of sampling and monitoring, costs of inspecting, costs of inventory checks.

## Slide 83: COPQ: Costs Related to Obligation
Costs related to obligation are those associated with addressing the muda that reaches a customer.
  Repair costs
  Warranty costs
  Replacement costs
  Customer returns and customer service overhead
  etc.
Any costs directly associated with customer obligations should be included in the COPQ calculation.
Notes: The costs related to obligation are those things associated with addressing the muda that reach the customer.
The cost of repair or replacement, the cost of returns, and the cost of handling customer service calls are examples.

## Slide 84: COPQ: Types of Cost
There are two types of costs to be considered when determining COPQ
  Hard Costs
    Tangible costs that can be traced to the income statement
  Soft Costs
    Intangible costs: avoidance, opportunity costs, lost revenue etc.
Calculating the COPQ
  Determine the types of waste that are present in your process
  Estimate the frequency of waste that occurs
  Estimate the cost per event, item, or time frame
  Do the math.
Notes: When determining the costs of poor quality, one must consider both hard costs and soft costs.
Hard costs – costs of resources or materials are good examples
Soft costs
  cost avoidance (the difference between what is actually spent and what could have been spent had no action been taken; think of this as slowing the rate of cost increases)
  opportunity cost (value of lost time that could have been used producing something of value
To estimate the cost of poor quality, there are a few basics steps:
  Find the waste
  Estimate how often the waste occurs
  Estimate the cost per event, per item, or per time frame (whichever is appropriate)
  Multiply the costs.

## Slide 85: 1.2.5 Pareto Charts and Analysis

## Slide 86: Pareto Principle
The Pareto principle is commonly known as the “law of the vital few” or “80:20 rule.”
It means that the majority (approximately 80%) of effects come from a few (approximately 20%) of the causes.
This principle was first introduced in early 1900s and has been applied as a rule of thumb in various areas.
Example of applying the Pareto principle:
  80% of the defects of a process come from 20% of the causes.
  80% of sales come from 20% of customers.
Notes: The Pareto principle is known as the “law of the vital few” or sometimes referred to as the “80:20 rule.”
It is a very powerful tool for scoping process improvement efforts because it tells us what the “few” causes are that drive the majority of the effects (or in many cases defects).
The “few” meaning approximately 20% of the causes, and the majority meaning 80% of the “effects.”
Business-management consultant Joseph M. Juran suggested the principle and named it after Italian economist Vilfredo Pareto, who observed in 1906 that 80% of the land in Italy was owned by 20% of the population; he developed the principle by observing that 20% of the pea pods in his garden contained 80% of the peas.

## Slide 87: Pareto Principle
The Pareto principle helps us to focus on the vital few items that have the most significant impact.
In concept, it also helps us to prioritize potential improvement efforts.
Since this 80:20 rule was originally based upon the works of Wilfried Fritz Pareto (or Vilfredo Pareto), the Pareto principle and references to it should be capitalized because Pareto refers to a person (proper noun).
  Mr. Pareto is also credited for many works associated with the 80:20, some more loosely than others:
    Pareto’s Law
    Pareto efficiency
    Pareto distribution etc.
Notes: Again, the Pareto principle is a powerful tool for narrowing focus, scoping a project, and prioritizing our efforts. It tells us what the vital few items are that have the most significant impact.
Because the rule was named after Wilfried Pareto, we always refer to it as a proper noun, and capitalize the term Pareto.
There are other references to Pareto’s works, so you may hear of people refer to it as Pareto’s Law, Pareto’s efficiency, and Pareto distribution.

## Slide 88: Pareto Charts
A Pareto chart is a chart of descending bars with an ascending cumulative line on the top.
  Sum or Count:
The descending bars on a Pareto chart may be set on a scale that represents the total of all bars or relative to the biggest bucket, depending on the software you are using.
  Percent to Total: A Pareto chart shows the percentage to the total for individual bars.
  Cumulative Percentage: A Pareto chart also shows the cumulative percentage of each additional bar. The data points of all cumulative percentages are connected into an ascending line on the top of all bars.
Notes: So what is a Pareto chart:
It is a chart of descending bars that typically represent a count of effects grouped by the cause.
It also includes a line that represents a cumulative percentage of the total effects for each cause.
Not all software packages display Pareto charts the same way. Some show the percent of total for each individual bar, and others show the cumulative percentage as mentioned previously.

## Slide 89: Pareto Charts
Case study time!
  Next we will use SigmaXL to run Pareto charts on exactly the same data set.
  The following table shows the count of defective products by team.
  Input the tabled data below into your software program and follow the instructions over the next few pages to run Pareto charts in the appropriate software.
Notes: Now we will use a sample data set to create a Pareto chart using your software program.
The first step is to input this data set into your program, and follow instructions over the next few pages.

## Slide 90: Create Pareto Chart in SigmaXL
Steps to generate a Pareto chart using SigmaXL:
  Open the Pareto Chart spreadsheet.
  Highlight both columns of “Count” and “Category.”
  Click SigmaXL → Graphical Tools → Basic Pareto Chart.
  A new window named “Pareto Chart” pops up.
  Click “Next>>.”
  A new window named “Basic Pareto Chart” pops up.
  Select “Category” as the “Pareto Category (X)” and “Count” as the “Optional Numeric Count (Y).
  Click “Finish.”
  The Pareto chart is created in a new tab.
Notes: To create a Pareto chart in SigmaXL, follow the steps listed on this page.

## Slide 91: Create Pareto Chart in SigmaXL
Notes: Here is a pictorial version of the instructions on the previous page.

## Slide 92: Create Pareto Chart in SigmaXL
The Pareto chart at right generated in SigmaXL presents the count of defective products by team.
The bars are descending on a scale with the peak at 25, which is approximately the size of the largest bar.
Compared with Minitab, it is a bit more difficult to ascertain the total number of defective items in the Pareto chart created in SigmaXL.
Notes: In comparison to Minitab, it is a little more difficult to ascertain the total number of defects by the graph. This is because the two axes are not aligned.
Alignment in this case means that the maximum number of defects on the left Y-axis does not align to 100% on the second Y-axis.
Minitab does this automatically, but in Excel it can be manually changed by setting the maximum on the Y-axis to the total number of defects.

## Slide 93: Pareto Analysis
The Pareto analysis is used to identify the root causes by using multiple Pareto charts.
In Pareto analysis, we drill down into the bigger buckets of defects and identify the root causes of defects that contribute heavily to total defects.
This "drill down" approach effectively solves a significant portion of the problem.
Next you will see an example of three-level Pareto analysis.
  The second-level Pareto is a Pareto chart that is a subset of the tallest bar on the first Pareto.
  The third-level Pareto is a subset of the tallest bar of the second-level Pareto.
Notes: The Pareto analysis is the process of using multiple Pareto charts to identify root causes of defects.
In this analysis we drill down by creating secondary or second-level Pareto charts for the tallest bars on the primary or first-level Pareto chart.
The following example will illustrate Pareto analysis taken to three levels.

## Slide 94: Pareto Analysis: First Level
  First-level Pareto
  Shows the count of defective items by team
  Next level will only show the defective items of team 4
Notes: In this first level Pareto, you can see that Team 4 accounts for 50% of the total number of defects.
In the second level Pareto, you will see how Team 4 defects are accounted for.

## Slide 95: Pareto Analysis: Second Level
  Second-level Pareto
  Shows the count of the defective items by section for only team 4
  Next level will only show the defective items of section 3
Notes: This Pareto breaks down by sections only the 22 defects of Team 4.
Section 3 of Team 4 is accounting for 14 (or 64%) of all Team 4’s defects.
In the third level Pareto you will see the breakdown of those 14 defects.

## Slide 96: Pareto Analysis: Third Level
  Third-level Pareto
  Shows the count of defective items by associate for only section 3 of team 4
  Next level will only show the defective items of Dave
Notes: 13 of the 14 defects in Section 3 of Team 4 are accounted for by 1 person – Dave.
Now instead of focusing on all teams to reduce the number of defects, we can focus on a single individual who is contributing with 13 defects out of a total of 44 (30%).

## Slide 97: Pareto Analysis: Conclusion
After drilling down three levels we find that most of the defective products are from Dave who is in Section 3 of Team 4.
Determining what Dave might be doing differently and solving that problem can potentially fix about 30% of the entire defective products (13/44).
Notes: In conclusion, this type of analysis significantly narrowed the focus for reducing defective products.
By focusing on what Dave is doing (or not doing), the defect rate could be improved by as much as 30%.

## Slide 98: 1.3 Six Sigma Projects

## Slide 99: Black Belt Training: Define Phase
1.1 Six Sigma Overview
1.1.1 What is Six Sigma
1.1.2 Six Sigma History
1.1.3 Six Sigma Approach Y = f(x)
1.1.4 Six Sigma Methodology
1.1.5 Roles and Responsibilities
1.2 Six Sigma Fundamentals
1.2.1 Defining a Process
1.2.2 VOC and CTQs
1.2.3 QFD
1.2.4 Cost of Poor Quality (COPQ)
1.2.5 Pareto Analysis (80 : 20 rule)
1.3 Lean Six Sigma Projects
1.3.1 Six Sigma Metrics
1.3.2 Business Case and Charter
1.3.3 Project Team Selection
1.3.4 Project Risk Management
1.3.5 Project Planning
1.4 Lean Fundamentals
1.4.1 Lean and Six Sigma
1.4.2 History of Lean
1.4.3 The Seven Deadly Muda
1.4.4 Five-S (5S)

## Slide 100: 1.3.1 Six Sigma Metrics

## Slide 101: Six Sigma Metrics
There are many Six Sigma metrics and/or measures of performance used by Six Sigma practitioners.
In addition to the ones we will cover here, several others (Sigma level, Cp, Cpk, Pp, Ppk, takt time, cycle time, utilization etc.) will be covered in other modules throughout this training.
The Six Sigma metrics of interest here in the define phase are:
  Defects per Unit (DPU)
  Defects per Million Opportunities (DPMO)
  Yield (Y)
  Rolled Throughput Yield (RTY).
Notes: In this module, we will seek to cover many performance metrics that are commonly used by Six Sigma practitioners.
It is important to identify the right Six Sigma metric that is appropriate for a business situation, so that it helps tell a good story about the problem faced.

## Slide 102: Defects per Unit: DPU
DPU stands for “Defects per Unit“
DPU is the basis for calculating DPMO and RTY, which we will cover in the next few pages.
DPU is found by dividing total defects by total units.
  DPU = D/U
For example, if you have a process step that produces an average of 65 defects for every 598 units, then your DPU = 65/598 = 0.109.
Notes: The calculation is simple: the defects per unit are the total number of defects divided by the total number of units.

## Slide 103: DPMO: Defects per Million Opportunities
DPMO is one of the few important Six Sigma metrics that you should get comfortable with if you are associated with Six Sigma.
In order to understand DPMO it is best if you first understand both the nomenclature and the nuances such as the difference between defect and defective.
Nomenclature
  Defects = D
  Unit = U
  Opportunity to have a defect = O
Notes: DPMO (Defects per Million Opportunities) is one of the most important Six Sigma metrics. It is commonly referred to in context of a Six Sigma process. Remember 3.4 defects per million opportunities?
Take note of the following abbreviations: D = defect, U = unit, O = opportunity.

## Slide 104: DPMO: Defects per Million Opportunities
In order to properly discuss DPMO, we must first explore the differences between "defects" and "defective."
  Defective
    Defective suggests that the value or function of the entire unit or product has been compromised.
    Defective items will always have at least one defect. Typically, however, it takes multiple defects and/or critical defects to cause an item to be defective.
  Defect
    A defect is an error, mistake, flaw, fault, or some type of imperfection that reduces the value of a product or unit.
    A single defect may or may not render the product or unit "defective" depending on the specifications of the customer.
  Summary
    Defect means that part of a unit is bad.
    Defective means that the whole unit is bad.
Notes: To correctly leverage the DPMO metric, it is important to understand the difference between a “defect” and something that is “defective.”
Defective suggests that a unit has been compromised in some way. It has at least 1 defect, but typically has multiple defects or critical defects to cause an item to be defective.
A defect is a single error, mistake, flaw, or any other type of imperfection that reduces the value of a product or unit. A single defect may not render the product or unit defective, depending on how it impacts the functionality for the customer (or customer specifications).
So to differentiate between terms, a defect means that part of a unit is bad, and defective means the whole unit is bad.

## Slide 105: DPMO: Defects per Million Opportunities
Now let us turn our attention to defining "opportunities" so that we can fully understand Defects per Million Opportunities (DPMO).
  Opportunities
    Opportunities are the total number of possible defects.
    Therefore, if a unit has 6 possible defects, then each unit produced is equal to 6 defect opportunities.
    If we produce 100 units, then there are 600 defect opportunities.
Notes: Every possible defect is considered an “opportunity.” If a unit has 6 possible defects, then it has 6 opportunities. 100 units have 600 opportunities (100 units × 6 opportunities/unit).

## Slide 106: DPMO: Defects per Million Opportunities
Calculating Defects per Million Opportunities
The equation is DPMO = (D/(U × O)) × 1,000,000
Example: Let us assume:
    There are 6 defect opportunities per unit
    There are an average of 4 defects every 100 units.
  Opportunities = 6 × 100 = 600
  Defect rate = 4/600
  DPMO = 4/600 × 1,000,000 = 6,667
Notes: This is how to calculate DPMO.
Using the given information (6 opportunities per unit, and an average of 4 defects per 100 unites)
Total opportunities = 6 defect opportunities per unit × 100 units = 600 defect opportunities
Defect rate = 4 defects/600 defect opportunities
DPMO = 6,667 defects per million opportunities

## Slide 107: DPMO: Defects per Million Opportunities
What is the reason or significance of 1,000,000?
Converting defect rates to a per million value becomes necessary when the performance of your process approaches Six Sigma.
When this happens, the number of defects shrinks to virtually nothing. In fact, if you recall from the “What is Six Sigma” module, sigma is 3.4 defects per million opportunities.
By using 1,000,000 opportunities as the barometer we have the resolution in the measurement to count defects all the way up to Six Sigma.
Notes: So why is the “million” in “defects per million” opportunities significant?
Because when a process approaches Six Sigma performance, the number of defects becomes immeasurable across smaller populations. At Six Sigma it is only 3.4 defects per million.
We need the million to have enough resolution to count the defects.

## Slide 108: RTY: Rolled Throughput Yield
Rolled Throughput Yield (RTY) is a process performance measure that provides insight into the cumulative effects of an entire process.
RTY measures the yield for each of several process steps and provides the probability that a unit will come through that process defect-free.
RTY allows us to expose the "hidden factory" by providing visibility into the yield of each process step.
This helps us identify the poorest performing process steps and gives us clues into where to look to find the most impactful process improvement opportunities.
Notes: Rolled Throughput Yield is a measure for the cumulative quality across an entire process.
It measures the yield for each step in a process to determine the probability that a unit will make it through the entire process without a defect.
It can help uncover where we have waste in a process, helping to scope process improvement efforts.

## Slide 109: RTY: Rolled Throughput Yield
Calculating RTY:
RTY is found by multiplying the yields of each process step.
Let us take the 5-step process below and calculate the RTY using the multiplication method mentioned above.
The calculation is: RTY = 0.90 × 0.91 × 0.99 × 0.98 × 0.97 = 0.77
Therefore, RTY = 77%.
Notes: In this example you can see how RTY is calculated.
The yield (or percent of units that get through without a defect) is shown for each step in this 5-step process.
To calculate the RTY, multiply the yield for all 5 steps. In this example 77% of units get through all 5 process steps without a defect.

## Slide 110: RTY: Rolled Throughput Yield
You may have noticed that in order to calculate RTY we must determine the yield for each process step.
Before we get into calculating yield, there are a few abbreviations that need to be declared.
  Abbreviations
    Defects = D
    Unit = U
    Defects per Unit = DPU
    Yield = Y
    e = 2.71828 (mathematical constant)
Notes: In the previous example, the yield for each step was provided. Obviously, one must be able to calculate yield to get to RTY.
Here are a few key terms/abbreviations that are important when calculating yield.

## Slide 111: RTY: Rolled Throughput Yield
Calculating Yield
The yield of a process step is the success rate of that step or the probability that the process step produces no defects.
In order to calculate the yield, we need to know the DPU and then we can apply it to the yield equation below.
Example
  Let us assume a process step has a DPU of 0.109 (65/598)
  Y = 2.718 ^ -0.109 = 0.8967. Rounded, Y = 90%.
Notes: Yield is the success rate for a process step, or probability that it will not produce a defect.
To calculate the yield, use the equation on this slide.
In this example, the DPU (defects per unit) is 0.109 (65 defects/598 units).
Plugging the DPU, and using the mathematical constant for e (2.718), the result is 0.8967, or 90% when rounded.

## Slide 112: RTY: Rolled Throughput Yield
Below is a table using the above process yield data that we used in the earlier RTY calculation.
This table allows us to see the DPU and yield of each step as well as the RTY for the whole process.
Notes: This slide allows us to see a visual, in tabular form, that shows the inputs when calculating DPU and yield for each process step.
On the right of the table you can see the RTY variation through the process steps.
Which steps seem to be opportunities? Notice the yield in steps 1 and 2.

## Slide 113: RTY: Using an Estimate of Yield
Calculating RTY using yield estimation
  It is possible to “estimate” yield by taking the inverse of DPU or simply subtracting DPU from 1.
  Yield Estimation = 1 − DPU
    Yield Estimate for process step 1: 1 − 0.10870 = 0.90
    Yield Estimate for process step 2: 1 − 0.09006 = 0.91
    Yield Estimate for process step 3: 1 − 0.01031 = 0.99
    Yield Estimate for process step 4: 1 − 0.02083 = 0.98
    Yield Estimate for process step 5: 1 − 0.02972 = 0.97
  RTY using the Yield Estimation Method
    RTY = 0.90 × 0.91 × 0.99 × 0.98 × 0.97 = 0.77 = 77%
Notes: Instead of using the equation provided earlier, there is a simpler way to calculate yield.
The maximum DPU is 1, so to get a yield percent just subtract DPU from 1.
As you can see, by calculating the yield this way we get the same result for the RTY calculated earlier (which was 77%).

## Slide 114: 1.3.2 Business Case and Charter

## Slide 115: Business Case and Project Charter
Earlier we stated that DMAIC is a structured and rigorous methodology designed to be repeatedly applied to any process in order to achieve Six Sigma.
We also stated that DMAIC was a methodology that refers to 5 phases of a project.
  Define, Measure, Analyze, Improve, and Control
Given that the premise of the DMAIC methodology is project-based, we must take the necessary steps to define and initiate a project, hence the need for. . .
  Project Charters
Notes: A recap from our overview of Six Sigma. DMAIC is a structured, rigorous methodology that can be applied to any process to achieve Six Sigma.
DMAIC consists of 5 phases: Define, Measure, Analyze, Improve, Control.
The first step in any DMAIC project, beginning in the define phase of course, is to create a project charter. It is what sets direction for a project.

## Slide 116: Project Charter
The purpose of a project charter is to provide vital information about a project in a quick and easy-to-comprehend manner.
Project charters are used to get approval and buy-in for projects and initiatives as well as declaring:
  The scope of work
  Project teams
  Decision authorities
  Project lead
  Success measures
Notes: A project charter is important because it provides information that is core to a project. It is a contract of sorts between project champions, sponsors, stakeholders, and the project team. It is a quick reference to tell the story of what, why, who, when, etc.
To set the right direction for a project, it is critical to define certain guardrails to ensure the project stays on track and is successful. Examples are:
  The scope of work, or boundaries within which the project will operate
  The team that will execute the project and who will lead them
  Who the decision makers are
  What are the measures of success.

## Slide 117: Project Charter
Key Elements of Project Charters
  Title
  Project Lead
  Business Case
  Problem Statement
  Project Objective
  Primary and Secondary Metrics
  Project Scope
  Project Timeline
  Project Constraints
  Project Team
  Stakeholders
  Approvers
  Constraints
  Dependencies
  Risks
Notes: Here you can see an example of a project charter that shows all the key elements in a one-page layout. It is easy to share, easy to read, and is useful for quickly communicating to people who may not be familiar with the project.

## Slide 118: Project Charter: Key Elements
Title
  Projects should have a name, title, or some reference that identifies them.
  Branding can be an important ingredient in the success of a project so be sure your project has a reference name or title.
Leader
  Any projects needs a declared leader or someone who is responsible for project’s execution and success.
  You may hear references to RACI throughout in your Six Sigma journey.
  RACI stands for Responsible, Accountable, Consulted, Informed and identifies the people that play those roles.
  Every project must have declared leaders indicating who is responsible and who is accountable.
Notes: A title may seem like an insignificant piece of the charter, but do not underestimate the power of branding. This is how your project will be known to others, and keeping it top of mind is obviously part of ensuring its success.
The project leader is responsible, and ultimately accountable, for the execution and success of the project.

## Slide 119: Project Charter: Key Elements
Business Case
  A business case is the quantifiable reason why the project is important.
  Business cases help shed light on problems. They explain why a business should care.
  Business cases must be quantified and stated succinctly.
  COPQ is a key method of quantification for any business case.
Notes: A business case clearly articulates why it is necessary to do the project and what is the benefit to the customer, to employees, or to the shareholders.
A problem by itself is not enough to articulate why a project needs to be done. The business case turns the problem into the reason a business should care: what is the cost of the problem, what is the impact to customers, or what is the lost revenue opportunity?
It is important for the business case to be quantifiable. Stakeholders have to know what success looks like.
Cost of poor quality, as described earlier, is a great approach to quantifying the business case.

## Slide 120: Project Charter: Key Elements
Problem Statement and Objective
  A properly written problem statement has an objective statement woven into it.
  There should be no question as to the current state or the goal.
  A gap should be declared, the gap being the difference between the present state and the goal state.
  The project objective should be to close the gap or reduce the gap by some reasonable amount.
  Valuation or COPQ is the monetary value assigned to the gap.
  Lastly, a well-written problem statement refers to a timeline expected to be met.
Notes: A well-written problem statement includes all of the following:
  Declaration of the current state of a problem in terms of a given measure
  A goal for the measure, which establishes a gap from the current state
  An objective that states how much of the gap the project aims to close
  The monetary value of the objective (cost of poor quality)
  Finally, a timeline that the project will meet.

## Slide 121: Project Charter: Problem Statement Examples
Currently, process defect rates are 17% with a goal of 2%. This represents a gap of 15%, costing the business $7.4 million dollars. The goal of this project is to reduce this gap by 50% before Nov 2010 putting process defect rates at 9.5% and saving $3.7MM.
Process cycle time has averaged 64 minutes since Q1 2009. However, production requirements put the cycle time goals at 48 min. This 16-min gap is estimated to cost the business $296,000. The goal of this project is reduce cycle time by 16 min. by Q4 2010 and capture all $296,000 cost savings.
Notes: Here are a couple of example problem statements.
Can you identify the key elements of a problem statement?

## Slide 122: Project Charter: Key Elements
Metrics
  A measure of success is an absolute for any project.
  Metrics give clarity to the purpose of the work.
  Metrics establish how the initiative will be judged.
  Metrics establish a baseline or “starting point.”
  For Six Sigma projects…metrics are mandatory!
Notes: How does one know if a project does what it sets out to do?
It is critical that every project chooses the right metrics to determine success.
The metrics are the center point for the work to ensure that the direction and decisions made through the course of the project are based on data.
The metrics are what stakeholders will judge the success of the project on.

## Slide 123: Project Charter: Key Elements
Primary Metric
  The primary metric is a generic term for a Six Sigma project's most important measure of success. The primary metric is defined by the Black Belt, GB, MBB, or Champion.
  A primary metric is an absolute MUST for any project and it should not be taken lightly. Here are a few characteristics of good primary metrics.
  Primary metrics should be:
    tied to the problem statement
    measureable
    expressed with an equation
    aligned to business objectives
    tracked at the proper frequency (hourly, daily, weekly, monthly etc.)
    expressed pictorially over time with a run chart, time series, or control chart
    validated with an MSA.
Notes: A project can have many metrics, but the primary metric is the most important.
Choosing the primary metric should not be taken lightly. A Six Sigma expert should play a significant role in determining the primary metric to ensure it meets the characteristics of a good one.
The primary metric should be tied to the problem to ensure that what is being measured is a direct indication of whether the problem is being solved or not.
Obviously, the primary metric should be measureable, otherwise it is of no use.
It should be expressible as an equation, meaning that the primary metric, Y, can be expressed as a function of the x’s.
The Y’s should be aligned to business objectives, meaning that the primary metric should be correlated to business results.
The primary metrics should be tracked at the proper frequency; in other words, they should be something that can be tracked frequently enough so that action can be taken quickly when the metric changes.
The primary metrics should always be expressed pictorially over time with a line chart (a run chart, time series, or control chart for example)
And, of course, it is important to validate that the measurement system is reliable.

## Slide 124: Project Charter: Key Elements
The primary metric is the reason for your work.
It is the success indicator.
It is your beacon.
The primary metric is of utmost importance and should be improved, but not at the expense of your secondary metric.
Notes: Do not trade one problem for another. Solutions need to be balanced. Be sure that you do not create an issue somewhere else when you implement a solution to improve your primary metric. That is why secondary metrics are important.

## Slide 125: Project Charter: Key Elements
Secondary Metric
  The secondary metric is the thing you do not want sacrificed on behalf of a primary improvement.
  A secondary metric is one that makes sure problems are not just "changing forms" or "moving around."
  The secondary metric keeps us honest and ensures we are not sacrificing too much for our primary metric.
  If your primary metric is a cost or speed metric, then your secondary metric should probably be some quality measure.
    Example: If you were accountable for saving energy in an office building and your primary metric was energy consumption then you could shut off all the lights and the HVAC system and save tons of energy. . .except that your secondary metrics are probably comfort and functionality of the work environment.
Notes: When you think about your primary metric, think about the really easy and obvious ways to improve the primary metric. Chances are that you can easily improve it by sacrificing something else.

## Slide 126: Project Charter: Key Elements
Elements of a Good Project Charters (continued)
  Scope Statement – defined by high-level process map
  Stakeholders Identified – who is affected by the project
  Approval Authorities Identified – who makes the final call
  Review Committees Defined – who is on the review team
  Risks and Dependencies Highlighted – identify risks and critical path items
  Project Team Declared – declare team members
  Project Timeline Estimated – set high-level timeline expectations.

## Slide 127: 1.3.3 Project Team Selection

## Slide 128: Project Team Selection
Six Sigma project team selection is the cornerstone of a successful Six Sigma project.
Teams and Team Success
  A team is a group of people who share complementary skills and experience.
  A team will be dedicated to consistent objectives.
  Winning teams share similar and coordinated goals.
  Teams often execute common methods or approaches.
  Team members hold each other accountable for achieving shared goals.
Notes: Team selection is obviously not something that is unique to a Six Sigma project. Team selection is important in any kind of project. You want to choose a group of people that complement each other, share similar goals and objectives, and are not afraid to hold each other accountable for achieving the project’s objectives.

## Slide 129: Project Team Selection
What makes a team successful?
  Shared goals
  Commitment
  Leadership
  Respect
  Effective communication
  Autonomy
  Diversity (capabilities, knowledge, skills, experience etc.)
  Adequate resources.
Notes: There should not be any surprises about what makes a team successful. These characteristics are all important for a team to be successful.

## Slide 130: Project Team Selection
Keys to Team Success
  Agreed focus on the goal or the problem at hand
    Focus on problems that have meaning to the business
    Focus on solvable problems within the scope of influence; a successful team does not seek unattainable solutions.
  Team Selection
    Selected teammates have proper skills and knowledge
    Adequately engaged management
    Appropriate support and guidance from their direct leader
  Successful teams use reliable methods
    Follow the prescribed DMAIC methodology
    Manage data, information, and statistical evidence
  Successful teams always have exceeds players
    Winning teams typically
      Have unusually high standards.
      Have greater expectations of themselves and each other.
      Do not settle for average or even above average results.
Notes: Teams should be able to agree on what the focus is. The team members all need to understand how the problem translates to something meaningful for the business. They also should be realistic about what they can and should seek to accomplish.
The people that are selected need to have “skin in the game.” Not only do they need to be knowledgeable and have the needed skills, but they (and their management) need to be motivated to seek the solution.
The team should use the facts and data to lead the way. Be disciplined to follow the DMAIC approach and be aware of when a gut feeling or emotion is driving their behavior.
Of course teams should be built from the top performers whenever possible.

## Slide 131: Project Team Selection
Principles of Team Selection:
  Select team members based on
    Skills required to achieve the objective
    Experience (Subject Matter Expertise)
    Availability and willingness to participate
    Team size (usually 4–8 members)
        Don’t go at it alone!
        Don’t get too many cooks in the kitchen!
    Members’ ability to navigate
      The process
      The company
      The political landscape
  Be sure to consider the inputs of others
    Heed advice
    Seek guidance
Notes: A team member should be selected based on the skills and subject matter expertise. For example, if you are focusing on a process improvement, find a top performing employee that performs the process on a regular basis.
A team member needs to have capacity to participate on a project. This is why it is important to pick people with shared goals. If they have a shared goal, it is likely that they can find the time.
The team size needs to be optimal. Include enough people to generate consensus, but not too many people because they can never reach consensus, and this can paralyze a project.
Be open minded, listen to others, be inclusive

## Slide 132: Project Team Development
All teams experience the following four stages of development. It is helpful to understand these phases so that you can anticipate what your team is going to experience.
The four stages of team development process:
  Forming
  Storming
  Norming
  Performing
Teammates seek something different at each stage:
  In the forming stage they seek inclusion
  In the storming stage they seek direction and guidance
  In the norming stage they seek agreement
  In the performing stage they seek results.
Notes: Teams do not generally develop “chemistry” overnight.
There are typically four stages to team development, which will be discussed over the following pages.

## Slide 133: Project Team Development
Patterns of a team in the Forming stage:
  Roles and responsibilities are unclear
  Process and procedures are ignored
  Scope and parameter setting is loosely attempted
  Discussions are vague and frustrating
  There is a high dependence on leadership for guidance
Patterns of a team in the Storming stage:
  Attempts to skip the research and jump to solutions
  Impatience for some team members regarding lack of progress
  Arguments about decisions and actions of the team
  Team members establish their position
  Subgroups or small teams form
  Power struggles exist and resistance is present
Notes: In the Forming stage:
  People are trying to figure out where they fit in.
  The team is trying to figure out where the social boundaries are with each other.
  They are all trying to “get to know” each other.
In the Storming stage
  After the delay of the forming stage, urgency can set in and they start to seek progress.
  Team members even seek progress by sacrificing the discipline.

## Slide 134: Project Team Development
Patterns of a team in the Norming stage:
  Agreement and consensus start to form
  Roles and responsibilities are accepted
  Team members’ engagement increases
  Social relationships begin to form
  The leader becomes more enabling and shares authority
Patterns of a team in the Performing stage:
  Team is directionally aware and agrees on objectives
  Team is autonomous
  Disagreements are resolved within the team
  Team forms above average expectations of performance
Notes: In the Norming stage:
  The team is settling into place and into roles with responsibilities.
  Once roles are clear, engagement increases with comfort level, and the team starts to form relationships with each other.
In the Performing stage:
  The team is aligned and directed.
  The are autonomous in that they can resolve issues within and stay on the path to progress.
  The team is united to exceed expectations of performance.

## Slide 135: Project Team Development
Well-structured and energized project teams are the essential components of any successful Six Sigma project.
To have better chances of executing the project successfully, you will need to understand and effectively manage the team development process.
Notes: Even with the most perfectly defined project, a well-structured team can be the difference between success and failure.

## Slide 136: 1.3.4 Project Risk Management
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 137: 1.3.5 Project Planning

## Slide 138: What is Project Management?
Project management is the process of defining, planning, organizing, managing, leading, securing, and optimizing the resources to achieve a set of planned goals and objectives.
*Project Management is the application of knowledge, skills, tools, and techniques to project activities in order to meet project requirements.
*This definition was taken from the Glossary of the Project Management Institute, A Guide to the Project Management Body of Knowledge, (PMBOK®Guide) –Fifth Edition, Project Management Institute, Inc., 2008
Notes: Project management involves understanding project needs, planning those needs, and properly allocating resources to achieve the desired results.
The basic steps of project management as we will cover in greater detail later are: initiating the project, planning the project, executing the project, and closing the project.

## Slide 139: What is a Project Plan?
A project plan is a crucial step in project management for achieving a project’s goals.
A project plan is a formal approved document used to guide and execute project tasks.
It provides an overall framework for managing project tasks, schedules, and costs.
A project plan is a coordinating tool and communication device that helps teams, contractors, customers, and organizations define the crucial aspects of a project or program.
Notes: Project planning involves defining clear, distinct tasks and deliverables, and the work needed to complete each task and phase of the project.

## Slide 140: Project Planning Stages
Determine project scope and objectives: Explore opportunities, identify and prioritize needs, consider project solutions.
Plan the project: Identify input and resources requirements such as human resources, materials, software, hardware, and budgets.
Prepare the project proposal: Based on stakeholder feedback, plan the necessary resources, timeline, budget etc.
Implement the project: Implement the project by engaging responsible resources and parties. Ensure execution and compliance of the defined plans.
Evaluate the project: Regularly review progress and results. Measure the project’s effectiveness against quantifiable requirements.
Notes: The 5 key stages of project planning are:
Determining project scope and objectives
Project planning
Project proposal and approval
Project implementation
Project evaluation.

## Slide 141: Planning and Scheduling Objectives
To optimize the use of resources (both human and other resources).
To increase productivity
To achieve desired schedules and deliverables
To establish an approach to minimize long-term maintenance costs
To minimize the chaos and productivity losses resulting from planned production schedules, priority changes, and non-availability of resources.
To assess current needs and future challenges.
Notes: Proper project planning is necessary to coordinate all resources and tasks.

## Slide 142: Project Planning Activities
Statement of work (SOW)
Work breakdown structure (WBS)
Resource estimation plan
Project schedule
Budget or financial plan
Communication plan
Risk management plan
Notes: The essential high-level project activities that apply to all projects are:
statement of work, work breakdown structure, resource estimation, scheduling, budgeting, communication, and risk management.

## Slide 143: Project Planning Activities
Statement of Work (SOW)
Define the scope of the project.
Establish customer expectations.
Identify technical requirements for the project.
Notes: SOWs or statements of work are important “contracts” which outline many critical elements of a project or body of work. SOWs clarify expectations, deliverables, timelines, budgets, and responsibilities.

## Slide 144: Project Planning Activities
Work Breakdown Structure (WBS)
Identify all the tasks that need to be done in order to complete the project.
Structure the tasks into small logical components and subcomponents.
Define each task in detail so that each person responsible understands what is expected of them.
Summarize and report project progress and results.
Notes: A Work Breakdown Structure (WBS) is an important parameter in project planning because projects must inevitably be divided into smaller, more manageable tasks and subtasks.
These breakdowns must be aligned in a logical manner to meet customer defined target dates.
The WBS is required to prepare a project schedule and/or Gantt chart as well as to identify project milestones.

## Slide 145: Project Planning Activities
Resource Estimation Plan
Estimate resources
  Human resources
  Hardware and software
Plan resources
Index | Resources Required | No. Required | By date | Responsibility
1 | RAN access, SSE file transfer, office | 1 | 03 Jan 11 | John
2 | Access to ITS | 1 | 03 Jan 11 | Bob
3 | Software Engineers | 4 | 12 Jan 11 | Dave
4 | Onwing-EgtMargin-V1, RCCMacro-V2, | 1 | 03 Jan 11 | Michael
Notes: The estimation of resource requirements (human, software, hardware, materials etc.) is necessary for each task and is useful for the creation of a project plan.

## Slide 146: Project Planning Activities
Project Schedule
Assign time estimates to each activity in the WBS.
Create each task start and end dates.
Represent schedules as Gantt charts or network diagrams (PERT/CPM) charts.
Identify critical dependencies between tasks.
Notes: Scheduling is critical because without it you will miss deadlines and poorly organize dependent tasks and activities. The result of the lack of scheduling, or of poor scheduling, can be catastrophic to a project.

## Slide 147: Project Planning Activities
Project Schedule – Gantt Chart:
The advantage of a Gantt chart is its ability to display the status of each task/activity at a glance.
Because it is a graphic representation, it is easy to demonstrate the schedule to all the stakeholders.
Notes: A Gantt chart offers visibility to a project plan. It displays many key elements of the project plan in a simple and well organized manner.

## Slide 148: Project Planning Activities
Budget or Financial Plan
Planned expenses
Planned revenues
Budget forecast
Notes: Create a preliminary project budget that outlines the planned expenses and revenues pertaining to the project.
Preliminary budgets are commonly used for project justification and future business forecasts.
Most organizations expect to see some financial analysis regarding the payback of a project. IRR (Internal Rate of Return) and NPV (Net Present Value) are two very common and acceptable financial measures that can be used to justify a project.

## Slide 149: Project Planning Activities
Communication Plan
Establish communication procedures among management, team members, and relevant stakeholders.
Determine the communication schedule.
Define the acceptable modes of communication.
Notes: Effective communication and frequency of communication are vital to any project. Keeping participants, stakeholders, and customers updated with progress and forecasts helps ensure good communication.

## Slide 150: Project Planning Activities
Risk Management Plan
Identify the sources of project risks and estimate the effects of those risks.
Risks might arise from new technology, availability of resources, lack of inputs from customers, business risks etc.
Assess the impact of risk to the customers/stakeholders.
Calculate the probability of risk occurrence based on previous similar projects or industry benchmarks
Initiate mitigation and contingency plans
Review risks on a periodic basis
Notes: Most projects that fail are due to the lack of, or improper, risk management.
Identify sources of risk as early as possible in the project.
Determine the severity and frequency of possible risk occurrences and establish controls or mitigation plans.
Prioritize your energy and resources based on risk severity.

## Slide 151: Project Planning Tools Advantages
    Project planning tools are very useful to organize and communicate project plans, status, and projections.
    They help link tasks and sub-tasks or other work elements to get a whole view of what needs to be accomplished.
    They allow a more objective comparison of alternative solutions and provide consistent coverage of responsibilities.
    They allow for effective scope control and change management.
    They facilitate effective communication with all project participants and stakeholders.
    They help define management reviews.
    They act as an effective monitoring mechanism for the project.
    They establish project baselines for progress reviews and control points.

## Slide 152: Project Planning Tools Disadvantages
    Project planning tools can sometimes take too much time to maintain.
    Data updating and accuracy can be cumbersome.
    Too much documentation can cause version control to be challenging.
    Ineffective use of tools, especially risk management tools or project plans, can bring unwarranted project risks because bad decisions can be made on inaccurate information.
    Understanding of tools and usage of the tools may require training, hence additional costs and time.

## Slide 153: 1.4 Lean Fundamentals

## Slide 154: Black Belt Training: Define Phase
1.1 Six Sigma Overview
1.1.1 What is Six Sigma
1.1.2 Six Sigma History
1.1.3 Six Sigma Approach Y = f(x)
1.1.4 Six Sigma Methodology
1.1.5 Roles and Responsibilities
1.2 Six Sigma Fundamentals
1.2.1 Defining a Process
1.2.2 VOC and CTQs
1.2.3 QFD
1.2.4 Cost of Poor Quality (COPQ)
1.2.5 Pareto Analysis (80 : 20 rule)
1.3 Lean Six Sigma Projects
1.3.1 Six Sigma Metrics
1.3.2 Business Case and Charter
1.3.3 Project Team Selection
1.3.4 Project Risk Management
1.3.5 Project Planning
1.4 Lean Fundamentals
1.4.1 Lean and Six Sigma
1.4.2 History of Lean
1.4.3 The Seven Deadly Muda
1.4.4 Five-S (5S)

## Slide 155: 1.4.1 Lean and Six Sigma

## Slide 156: What is Lean?
A lean enterprise intends to eliminate waste and allow only value to be pulled through its system.
Lean manufacturing is characterized by:
  Identifying and driving value
  Establishing flow and pull systems
  Creating production availability and flexibility
  Zero waste
Waste Elimination
  Waste identification and elimination is critical to any successful lean enterprise.
  Elimination of waste enables flow, drives value, cuts cost, and provides flexible and available production.
Notes: A Lean Enterprise seeks to purge the waste and to only focus on value-adding activity in its system.
A Lean Manufacturing system drives value, flows smoothly, maximizes production, and minimizes the waste.
A Lean Enterprise can be achieved by identifying and effectively eliminating all waste (which will result in a flowing, cost-effective system).

## Slide 157: The 5 Lean Principles
The following 5 principles of lean are taken from the book Lean Thinking (1996) by James P. Womack and Daniel T. Jones.
  Specify value desired by customers.
  Identify the value stream.
  Make the product flow continuous.
  Introduce pull systems where continuous flow is possible.
  Manage toward perfection so that the number of steps and the amount of time and information needed to serve the customer continually falls.
Notes: Identify customers and specify value – Only a small fraction of the total time and effort spent in an organization actually adds value for the end customer. With a clear definition of value (from the customer’s perspective), it is much easier to identify where the waste is.
Identify and map the value stream – The value stream is the entire set of activities across all parts of the organization involved in jointly delivering the product or service. It is the end-to-end process that delivers the value to the customer. As stated above, once you understand what determines value to the customer, it is easier to determine where the waste is.
Create flow through eliminating waste – Typically you will find that only 5% of activities add value, but the percentage can be as high as 45% in a service environment. Eliminating this waste ensures that your product or service flows better to the customer without interruption or waiting.
Customer pull – When possible, understand the customer demand on your product or service, then create a process to respond to it. In other words, only produce what the customer wants when they want it.
Pursue perfection – At first reorganizing the process steps will create flow, and as this is done, the layers of waste become exposed and exploited. Continuing the process of eliminating, reorganizing, and exploiting the waste will continue to drive down the number of steps and time needed to serve the customer.

## Slide 158: Lean & Six Sigma
Lean and Six Sigma both have the objectives of producing high value (quality) at lower costs (efficiency).
They approach these objectives in somewhat different manners but in the end, both Lean and Six Sigma drive out waste, reduce defects, improve processes, and stabilize the production environment.
Lean and Six Sigma are a perfect combination of tools for improving quality and efficiency.
Lean
Eliminate Waste
Process Flow
Six Sigma
Eliminate Defects
Process Yield
Pull Systems
Capable Systems
Easy Visual Approach
Rigorous Analytical Approach
Quality & Value for the Customer Efficiency for the Business
Notes: Both Lean and Six Sigma have similar goals: to produce high value at lower cost.
Both have similar objectives: to make companies more efficient, to drive out waste through optimization.
The two methodologies complement each other to improve quality, efficiency, and ultimately profitability and customer satisfaction.

## Slide 159: 1.4.2 History of Lean

## Slide 160: History of Lean
Polaroid
Notes: Recall this timeline we saw at the beginning of this training?
The concepts and principles of Lean have been applied since the early 1900s, but the term was introduced only in 1990.

## Slide 161: History of Lean
Lean thinking originated, as far as is known, the 1400s.
Henry Ford established the first mass production system in 1913 by combining standard parts, conveyors, and work flow.
Decades later, Kiichiro Toyoda and Taiichi Ohno at Toyota improved and implemented various new concepts and tools (e.g., value stream, takt time, kanban etc.) based on Ford’s effort.
Toyota developed what is known today as the Toyota Production System (TPS) based on lean principles.
Notes: The first person to truly apply the principles in a production process was Henry Ford.
In 1913, he brought together the concepts of consistently interchangeable parts, standard work, and moving conveyance to create what he called flow production. The problem with Ford’s system was its inability to provide variety (remember the Model T?).
Between 1948 and 1975, Taiichi Ohno, Shigeo Shingo, and Eiji Toyoda developed the Toyota Production System. It advanced the concepts of Ford’s system through a series of innovations that provided the continuity of flow and a variety of product offerings.

## Slide 162: History of Lean
Starting in the mid 1990s, Lean became extensively recognized and implemented when more and more Fortune 100 companies began to adopt Lean and Six Sigma.
The term “Lean manufacturing” was introduced by James Womack in the 1990s.
Lean and Six Sigma share similar objectives, work hand in hand, and have benefited from one another in the past 30 years.
Notes: In the 1990s, the principles of Lean became widely recognized and applied across Fortune 100 companies.
The term “Lean” was coined in the 1990s. The term came from John Krafcik, who was a graduate student at MIT, working on a research for the book The Machine That Changed the World for Lean Enterprise Institute founder, Jim Womack.

## Slide 163: 1.4.3 Seven Deadly Muda

## Slide 164: The 7 Deadly Muda
The Japanese word for waste is “muda.”
There are 7 commonly recognized forms of waste, often referred to as the “7 deadly muda.”
  Defects
  Overproduction
  Over-Processing
  Inventory
  Motion
  Transportation
  Waiting
Notes: Muda is a Japanese word meaning “futility, uselessness, idleness, superfluity, waste, wastage, wastefulness.”
The “Seven Deadly Muda,” as defined by Taiicho Ohno (the Toyota Production System), are:
  Defects
  Overproduction – producing more than what your customers are demanding
  Over-processing – unnecessary time spent (e.g., relying on inspections instead of designing a process to eliminate problems)
  Inventory – things awaiting further processing or consumption
  Motion – extra, unnecessary movement of employees
  Transportation – unnecessary movement of goods
  Waiting – for an upstream process to delivery, for a machine to finish processing, or for an interrupted worker to get back to work.

## Slide 165: The 7 Deadly Muda: Defects
Defects or defectives are an obvious waste for any working environment or production system.
Defects require rework during production and/or after the product is returned from an unhappy customer.
Some defects are difficult to solve and they create “workarounds” and hidden factories.
Eliminating defects is a sure way to improve product quality, customer satisfaction, and production costs.
Notes: Nobody likes defects. They are an obvious form of waste – wasted time, wasted materials, and wasted money.
Defects take time and resources to be fixed, and can be especially costly if they get into the hands of a customer.
Sometimes when defects are hard to fix, processes are redesigned around the issue, creating unwanted hidden factories.

## Slide 166: The 7 Deadly Muda: Overproduction
Overproduction is wasteful because your system expends energy and resources to produce more materials than the customer or next function requires.
Overproduction is one of the most detrimental of the seven deadly muda because it leads to many others:
Inventory
Transportation
Waiting etc.
Notes: What is the matter with producing more of something than what you need?
It takes valuable time, energy, and money to produce more and, once extra production is made, it must be transported and stored for some period of time.

## Slide 167: The 7 Deadly Muda: Over-processing
Over-processing occurs any time more work is done than is required by the next process step, operation, or consumer.
Over-processing also includes being over capacity (scheduling more workers than required or having more machines than necessary).
Another form of over processing can be buying tools or software that are overkill (more precise, complex, or expensive than required).
Notes:   Over-processing is the unnecessary time spent (e.g., relying on inspections instead of designing a process to eliminate problems).
  You might think of this as over-engineering a process or just doing more than is required at a specific step of the process (having more labor available than necessary, having more machines than are needed, or having tools that are not adding incremental value because they do more than the product requires).

## Slide 168: The 7 Deadly Muda: Inventory
Inventory is an often overlooked waste. Look at the picture above and imagine all the time, materials, and logistics that went into establishing such an abundance of inventory.
If this were your personal business, and inventory velocity was not matched with production, how upset would you be?
Notes: Inventory are things awaiting further process or consumption.
Everything in this picture represents investment by the company that makes or sells a product.
How would you feel about this inventory if you were the owner of this business?

## Slide 169: The 7 Deadly Muda: Motion
Motion is another form of waste often occurring as a result of poor setup, configuration, or operating procedures.
Wasted motion can be experienced by machines or humans.
Wasted motion is very common with workers who are unaware of the impact of small unnecessary movements in repetitive tasks.
Wasted motion is exaggerated by repetition or recurring tasks.
Notes: Motion is extra, unnecessary movement of employees.
It can result from an improperly planned setup, work area configuration, and operating procedure.
Small movements of an employee probably do not seem very wasteful. But when you consider repetitive motion that occurs over a long period of time, your perspective may change.

## Slide 170: The 7 Deadly Muda: Transportation
Transportation is considered wasteful because it does nothing to add value or transform the product.
Imagine for a moment driving to and from work twice before getting out of your car to go into work. . .
That is waste in the form of transportation.
The less driving you have to do, the better.
In a similar way, the less transportation a product has to endure, the better. There would be fewer opportunities for delay, destruction, loss, damage etc.
Notes: Transportation is the unnecessary movement of goods.
Can you think of a way that moving a product from point A to point B adds value for a customer?
Why is transportation wasteful? It takes energy to move something, it may take tools to move, and it introduces the risk of something getting damaged. Unless something is being transported into the hands of the customer, it probably means it is going somewhere to be stored (which is also wasteful).

## Slide 171: The 7 Deadly Muda: Waiting
Waiting is an obvious form of waste and is typically a symptom of an upstream problem.
Waiting is usually caused by inefficiency, bottlenecks, or poorly-designed work flows within the value stream.
Waiting can also be caused by inefficient administration.
Reduction in waiting time will require thoughtful applications of lean and process improvement.
Notes: Waiting is when a downstream process is being starved because there is something wrong upstream in the process (like a machine having to finish processing or a worker that has stepped away from his or her station). In other words, there is a “bottleneck” that inhibits the flow of the process.

## Slide 172: 1.4.4 Five-S (5S)

## Slide 173: What is 5S?
5S is systematic method to organize, order, clean, and standardize a workplace…and to keep it that way!
  5S is a methodology of organizing and improving the work environment.
5S is summarized in five Japanese words all starting with the letter S:
  Seiri (sorting)
  Seiton (straightening)
  Seiso (shining)
  Seiketsu (standardizing)
  Shisuke (sustaining)
5S was originally developed in Japan and is widely used to optimize the workplace to increase productivity and efficiency.
Notes: 5S is a methodology that is applied in a Lean workplace. Its intent is to bring organization and order, and keep it that way.
The five Japanese words beginning with the letter S also have English meanings that start with the letter S: Sorting, Straightening, Shining, Standardizing, and Sustaining.

## Slide 174: Five-S (5S)
Sort
Set in Order
Shine
Standardize
Sustain
Notes: Sort – to separate the needed from the unnecessary and prioritize what is needed
Set in order (or straighten) – to establish a place for everything
Shine – to clean the work area
Standardize – to ensure that work practices are done consistently and everyone knows their responsibilities
Sustain – to maintain and review the standards

## Slide 175: Goals of 5S
Reduced waste
Reduced cost
Establish a work environment that is:
  self-explaining
  self-ordering
  self-regulating
  self-improving.
  Where there is/are no more:
    Wandering and/or searching
    Waiting or delaying
    Secret hiding spots for tools
    Obstacles or detours
    Extra pieces, parts, materials etc.
    Injuries
    Waste.
Notes: Can you think of reasons why 5S might be beneficial?
Eliminates wasted time searching for tools or materials.
Reduces the time necessary to perform a job.
Reduces cost of tools and materials (lost, damaged).
Creates a safer work environment.

## Slide 176: Benefits of 5S Systems
Reduced changeovers
Reduced defects
Reduced waste
Reduced delays
Reduced injuries
Reduced breakdowns
Reduced complaints
Reduced red ink
Higher quality
Lower costs
Safer work environment
Greater associate and equipment capacity.
Notes: By meeting the goals of 5-S, the following benefits are realized.

## Slide 177: Reported Results of 5S Systems
Cut in floor space: 60%
Cut in flow distance: 80%
Cut in accidents: 70%
Cut in rack storage: 68%
Cut in number of forklifts: 45%
Cut in machine changeover time: 62%
Cut in annual physical inventory time: 50%
Cut in classroom training requirements: 55%
Cut in nonconformance in assembly: 96%
Increase in test yields: 50%
Late deliveries: 0%
Increase in throughput: 15%
Notes: Organizations that have implemented 5S systems have reported very impressive results – reduction in waste, improved safety, reduced costs, improved performance.

## Slide 178: Sorting (Seiri)
Go through all the tools, parts, equipment, supply, and material in the workplace.
Categorize them into two major groups: needed and unneeded.
Eliminate the unneeded items from the workplace. Dispose of or recycle those items.
Keep the needed items and sort them in the order of priority. When in doubt…throw it out!
Notes: How do you Sort?
As you go through the workplace, separate tools, parts, equipment, materials, and supplies into two groups – needed and unneeded.
Eliminate the unneeded items from the workplace. (If you are unsure, store them away for some period of time until you are satisfied that you clearly do not need them.)
Sort the needed items in order of priority.

## Slide 179: Straightening (Seiton)
Straightening in 5S is also called setting in order.
Label each needed item.
Store items at their best locations so that the workers can find them easily whenever they needed any item.
Reduce the motion and time required to locate and obtain any item whenever it is needed.
Promote an efficient work flow path.
Use visual aids like the tool board image on this page.
Notes: Straightening (or Set in Order)
Label each item and store it in an appropriate location.
Try to reduce Motion by storing the most frequently used items in the most convenient locations.
Promote an efficient work flow path by working to minimize movement around the workplace.
Use visual aids to remind employees where things belong so the order is sustained.

## Slide 180: Shining (Seiso)
Shining in 5S is also called sweeping.
Clean the workplace thoroughly.
Maintain the tidiness of the workplace.
Make sure every item is located at the specific location where it should be.
Create the ownership in the team to keep the work area clean and organized.
Notes: Shining means:
Clean and maintain a tidy workplace.
Ensure that all items are in their proper location.
Get the team to own and take pride in keeping the workplace clean and organized.

## Slide 181: Standardizing (Seiketsu)
Standardize the workstation and the layout of tools, equipment and parts.
Create identical workstations with a consistent way of storing the items at their specific locations so that workers can be moved around to any workstation any time and perform the same task.
Notes: Standardization – removing the variation across workstations.
Replicate the workstation setting across all workstations, so they are interchangeable and workers can move amongst them and easily perform their duties.

## Slide 182: Sustaining (Shisuke)
Sustaining in 5S is also called self-discipline.
Create the culture in the team to follow the first four S’s consistently.
Avoid falling back to the old ways of cluttered and unorganized work environment.
Keep the momentum of optimizing the workplace.
Promote innovations of workplace improvement.
Sustain the first fours S’s using:
  5S Maps
  5S Schedules
  5S Job cycle charts
  Integration of regular work duties
  5S Blitz schedules
  Daily workplace scans.
Notes: Sustaining
It takes discipline to maintain 5S. Obviously, it takes time for new habits to form, and there needs to be a culture within the team to follow this methodology. It is critical not to fall back into the old ways.
Keep the momentum by identifying improvements and optimizing. Look for better ways to set the workplace in order and reduce waste.

## Slide 183: Simplified Summary of 5S
Sort – “when in doubt, move it out.”
Set in Order – Organize all necessary tools, parts, and components of production. Use visual ordering techniques wherever possible.
Shine – Clean machines and/or work areas. Set regular cleaning schedules and responsibilities.
Standardize – Solidify previous three steps, make 5S a regular part of the work environment and everyday life.
Sustain – Audit, manage, and comply with established 5S guidelines for your business or facility.
Notes: Here is a quick summary of how to apply the 5S.

## Slide 184: Five-S (5S)
A few words about 5S and the Lean Enterprise
  As a method, 5S generates immediate improvements.
  5S is one of many effective lean methods that create observable results.
  It is tempting to implement 5S alone without considering the entire value stream.
  However, it is advisable to consider a well-planned lean manufacturing approach to the entire production system.
Notes: 5S is a quick and effective way to improve results, and it is tempting to stop at that.
Keep it going beyond 5S and consider Lean for the entire system.

## Slide 185: 2.0 Measure Phase

## Slide 186: Black Belt Training: Measure Phase
2.1 Process Definition 2.1.1 Cause and Effect Diagrams 2.1.2 Cause and Effects Matrix 2.1.3 Process Mapping 2.1.4 FMEA: Failure Modes and Effects Analysis
2.1.5 Theory of Constraints
2.2 Six Sigma Statistics 2.2.1 Basic Statistics 2.2.2 Descriptive Statistics 2.2.3 Distributions and Normality 2.2.4 Graphical Analysis
2.3 Measurement System Analysis 2.3.1 Precision and Accuracy 2.3.2 Bias, Linearity, and Stability 2.3.3 Gage R&R 2.3.4 Variable and Attribute MSA
2.4 Process Capability 2.4.1 Capability Analysis 2.4.2 Concept of Stability 2.4.3 Attribute and Discrete Capability 2.4.4 Monitoring Techniques

## Slide 187: 2.1 Process Definition

## Slide 188: Black Belt Training: Measure Phase
2.1 Process Definition 2.1.1 Cause and Effect Diagrams 2.1.2 Cause and Effects Matrix 2.1.3 Process Mapping 2.1.4 FMEA: Failure Modes and Effects Analysis
2.1.5 Theory of Constraints
2.2 Six Sigma Statistics 2.2.1 Basic Statistics 2.2.2 Descriptive Statistics 2.2.3 Distributions and Normality 2.2.4 Graphical Analysis
2.3 Measurement System Analysis 2.3.1 Precision and Accuracy 2.3.2 Bias, Linearity, and Stability 2.3.3 Gage R&R 2.3.4 Variable and Attribute MSA
2.4 Process Capability 2.4.1 Capability Analysis 2.4.2 Concept of Stability 2.4.3 Attribute and Discrete Capability 2.4.4 Monitoring Techniques

## Slide 189: 2.1.1 Cause and Effect Diagram

## Slide 190: What is a Cause and Effect Diagram?
A cause and effect diagram is also called a Fishbone Diagram or Ishikawa Diagram. It was created by Kaoru Ishikawa and is used to identify, organize, and display the potential causes of a specific effect or event in a graphical way similar to a fishbone.
It illustrates the relationship between one specified event (output) and its categorized potential causes (inputs) in a visual and systematic way.
Notes: A cause and effect diagram is a powerful brainstorming tool that is used to identify and organize possible causes of a specific effect or event.
It is sometimes referred to as a fishbone diagram or Ishikawa diagram.
It shows the relationship between the effect and potential causes or inputs.

## Slide 191: Major Categories of Potential Causes
P4ME
  People: People who are involved in the process
  Methods: How the process is completed (e.g., procedures, policies, regulations, laws)
  Machines: Equipment or tools needed to perform the process
  Materials: Raw materials or information needed to do the job
  Measurements: Data collected from the process for inspection or evaluation
  Environment: Surroundings of the process (e.g., location, time, culture).
Notes: Typically, the possible causes fall into six major categories (or branches in the diagram).
Remembering this acronym (P4ME) is a helpful way to remember these categories: People, Methods, Machines, Materials, Measurements, Environment.

## Slide 192: How to Plot a Cause and Effect Diagram
  Step 1: Identify and define the effect/event being analyzed.
  Clearly state the operational definition of the effect/event of interest.
  The event can be the positive outcome desired or negative problem targeted to solve.
  Enter the effect/event in the end box of the Fishbone diagram and draw a spine pointed to it.
Notes: Plotting a cause and effect diagram is a simple 4-step process. Step 1 is to identify and define the effect being analyzed.
The effect/event should be clearly stated and defined. It can be a positive or negative outcome.
Enter the effect/event at the head of the diagram. See next page for an illustration.

## Slide 193: How to Plot a Cause and Effect Diagram
Step 1

## Slide 194: How to Plot a Cause and Effect Diagram
  Step 2: Brainstorm the potential causes or factors of the effect/event occurring.
  Identify any factors with a potential impact on the effect/event and include them in this step.
  Put all the identified potential causes aside for use later.
Notes: Step 2 is to brainstorm the potential causes for the event or effect being analyzed.
It is brainstorming, so you should include anything with a potential impact on the event or effect analyzed.
This can be done through a whiteboard exercise, using sticky notes, or even electronically on a spreadsheet or other drawing tools.

## Slide 195: How to Plot a Cause and Effect Diagram
Step 2
Notes: This is an illustration of step 2.

## Slide 196: How to Plot a Cause and Effect Diagram
  Step 3: Identify the main categories of causes and group the potential causes accordingly.
  Besides P4ME (i.e., people, methods, machines, materials, measurements, and environment), you can group potential causes into other customized categories.
  Below each major category, you can define sub-categories and then classify them to help you visualize the potential causes.
  Enter each cause category in a box and connect the box to the spine. Link each potential cause to its corresponding cause category.
Notes: Step 3 is to identify the main categories for the causes and group the brainstormed items.
You can use P4ME, or you can use customized main categories to group the potential causes.
Under each main category, you can define sub-categories if additional levels of detail are needed.

## Slide 197: How to Plot a Cause and Effect Diagram
Step 3
Notes: This is the graphic representation of Step 3.

## Slide 198: How to Plot a Cause and Effect Diagram
Step 4: Analyze the cause and effect diagram.
  A cause and effect diagram includes all the possible factors of the effect/event being analyzed.
  Use a Pareto chart to filter causes the project team needs to focus on.
  Identify causes with high impact that the team can take action upon.
  Determine how to measure causes and effects quantitatively. Prepare for further statistical analysis.
Notes: In the fourth and final step, analyze the diagram.
Have all factors been represented?
Use any data that you have to prioritize the causes – perhaps with a Pareto chart.
Identify which high-impact items are actionable, and determine how to measure causes and effects quantitatively.

## Slide 199: Benefits to Using Cause and Effect Diagram
Helps to quickly identify and sort the potential causes of an effect.
Provides a systematic way to brainstorm potential causes effectively and efficiently.
Identifies areas requiring data collection for further quantitative analysis.
Locates “low-hanging fruit.”
Notes: The benefits to using a cause and effect diagram to analyze an effect or event are:
It is helpful in systemically brainstorming and sorting potential causes of an effect and identifying which areas will require further analysis. Often this is where some quick wins (or the so called “low-hanging fruit”) can be uncovered.

## Slide 200: Limitation of Cause and Effect Diagrams
A cause and effect diagram only provides qualitative analysis of correlation between each cause and the effect.
One cause and effect diagram can only focus on one effect or event at a time.
Further statistical analysis is required to quantify the relationship between various factors and the effect and identify the root causes.
Notes: The tool does have limitations:
Is qualitative only, so it does not leverage data to find true relationships. More analysis is needed to quantify relationships between causes and effects.
It only focuses on one effect at a time. Effects can have different causes.

## Slide 201: Cause and Effect Diagram Example
Case study:
  A real estate company is interested to find the root causes of high energy costs of its properties.
  The cause and effect diagram is used to identify, organize, and analyze the potential root causes.
Notes: Let us follow an example through the process of using a cause and effect diagram. What is the effect to be analyzed? (High energy cost)

## Slide 202: Cause and Effect Diagram Example
Step 1: Identify and define the effect/event being analyzed: high energy costs of buildings.
Notes: As you can see, in step 1 the effect is noted at the head of the diagram.

## Slide 203: Cause and Effect Diagram Example
Step 2: Brainstorm the potential causes or factors of the high energy costs.
Aged HVAC units
Poor maintenance of HVAC units
Bad energy consuming habits
Inaccurate metering
Building materials
Temperature set point is too low in summer
Temperature set point is too high in winter
Most lights are still on during non-business hours
Building air leakage
Fuel prices increasing
Notes: In step 2, you can see the multiple potential causes that can be driving the effect of high energy cost of buildings.

## Slide 204: Cause and Effect Diagram Example
Step 3: Identify the main categories of causes and group the potential causes accordingly.
Notes: In step 3, see how the possible causes were grouped into the main categories (P4ME in this example)?

## Slide 205: Cause and Effect Diagram Example
Step 4: Analyze the cause and effect (C&E) diagram.
  After completing the C&E diagram, the real estate company conducts further research on each potential root cause.
  It is discovered that:
    The utility metering is accurate
    The building materials are fine and there is not significant amount of air leakage from the building
    The fuel prices increased recently but were negligible
    Most lights are off during the non-business hours except that some lights have to be on for security purposes
    The temperature set points in the summer and winter are both adequate and reasonable
    The high energy costs are probably caused by the poor HVAC maintenance on aged units and the wasteful energy consuming habits.
  Next, the real estate company needs to collect and analyze the data to check whether root causes identified in the C&E diagram are statistically the causes of the high energy costs.
Notes: Finally, in analyzing the diagram and the potential root causes, additional information or data is uncovered to validate or invalidate the potential causes. It is determined that poor HVAC maintenance on aged units and wasteful energy consuming habits are at the root.
The real estate company needs to collect and analyze additional data to determine statistical relationships between causes and high energy costs.

## Slide 206: 2.1.2 Cause and Effects Matrix

## Slide 207: What is a Cause and Effect Matrix?
The cause and effect matrix (XY Matrix) is a tool to help subjectively quantify the relationship of several X's to several Y's.
Among the Y's under consideration, two important ones should be the primary and secondary metrics of your Six Sigma project.
The X's should be derived from your cause and effect diagram. Let us take a peek as what it looks like on the next page.
Notes: A cause and effect matrix is a powerful yet easy tool to transition from brainstorming (which you did using the cause and effect diagram) to estimating, ranking, and quantifying the relationship between those things you found during brainstorming and the Y’s that are important to the project.

## Slide 208: Cause and Effects Matrix
Notes: This is a clean cause and effect matrix where you can translate all of the potential X's brainstormed during the creation of your cause and effect diagram session.
Once you have that information entered into the matrix you can add 1 or more Y's to the top of the matrix. The Y's should be weighted relative to each other based on their importance to the project.
Once this is complete, you begin rating each X against each Y on a scale of 0, 3, 5, 7 (0 means no impact; 3 means weak impact; 5 is moderate impact; and 7 is strong impact). Try to use the whole spectrum of your scale during this process because you will need the resolution to help differentiate the X's from one another.

## Slide 209: How to Use a Cause and Effect Matrix
Across the top enter your output measures. These are the Y’s that are important to your project.
Next, give each Y a weight. Use a 1–10 scale, 1 being least important and 10 most important.
Below, in the leftmost column, enter all the variables you identified with your cause and effect diagram.
Within the matrix itself, rate the strength of the relationship between the X in the row and the corresponding Y in that column. Use a scale of 0, 3, 5, and 7.
Lastly, sort the “Score” column to order the most important X’s first.

## Slide 210: Cause and Effect Matrix Notes
Notes: When complete, sort the X's based on their scores and graph them (use a Pareto chart).
What the results will tell you should not be "taken to the bank" as this entire process from brainstorming X's to rating them against Y's is a subjective exercise. However, if you have chosen your team wisely, it is very common that someone or several SMEs on your project team know the real solutions and/or the best way to narrow down to find them.
Therefore, it is also important not to dismiss the results of your cause and effect matrix. Look at the image with comments embedded to summarize what you have just read.

## Slide 211: After You Have Completed the C&E Matrix
After you have completed your cause and effects matrix, build a strategy for validating and/or eliminating the x’s as significant variables to the Y=f(x) equation.
  Build a data collection plan
  Prepare and execute planned studies
  Perform analytics
  Review results with SMEs
  etc.
Notes: The combination of the C&E diagram and the C&E matrix is powerful. This is where some of the best ideas and theories about the Y=f(x) equation begin.
Now, it is time to start eliminating and/or validating these variables.
Put a plan together to do so. Use the resources and tools you have already learned as well as those that you are about to learn throughout this course.

## Slide 212: 2.1.3 Process Mapping

## Slide 213: What is a Process Map?
A process map is a graphical representation of a process flow.
It visualizes how the business process is accomplished step by step.
It describes how the information or materials sequentially flow from one business entity to the next.
It illustrates who is responsible for what between the process boundaries.
It depicts the input and output of each individual process step.
In the Measure phase, the project team should map the current state of the process instead of the ideal state.
Notes: Obviously, a process map is necessary to document a process. It helps us understand and drive discussion around a process.
It is a graphical representation for how a process flows, a step-by-step visual for how a process works.
It can help us understand how material or information flows.
It can help us understand who is responsible for each step in the process.
During the Measure phase of a project, the process map is used as the representation of the current state process.

## Slide 214: Process Map Basic Symbols
The following four symbols are the most commonly used symbols in a process map.
Terminator (Oval):
Shows the start/end points in the process.
Process (Rectangle):
Indicates a single process step.
Decision (Diamond):
Indicates a question with two choices (e.g., Yes/No).
Flow Line (Arrow):
Shows the direction of the process flow.
Notes: These are the basic symbols you can expect to see in most process maps (termination points, process step, decision point, and flow direction).

## Slide 215: Additional Process Symbols
Alternative Process:
Indicates a process step as the alternate of a normal process step.
Predefined Process:
Indicates a formally defined process step.
Manual Operation:
Indicates a process step conducted manually.
Preparation:
Indicates a preparation step.
Delay:
Indicates a waiting period in the process.
Notes: Here are some additional steps that are helpful to know:
An alternative process step, meaning there is a different way of performing a normal process step
A predefined process is used to hold the place of a pre-existing process, and is supported by other documentation that spells out the details of that process
A manual process – as opposed to an “automated” step
A preparation step that leads to a process step
A delay – indicating a waiting period.

## Slide 216: Additional Process Symbols
Additional file- and information-related symbols:
Data (I/O):
Shows the inputs and outputs of a process.
Document:
Indicates a process step that results in a document.
Multi-Document:
Indicates a process step that results in multiple documents.
Stored Data:
Indicates a process step that stores data.
Magnetic Disk:
Indicates a database.
Notes: These are some additional symbols that are helpful in defining how information flows in a process:
Data – as an input or output of a process step
Document – a process step with a document output
Stored data – a process step that stores data
Magnetic disk – a database that can either supply or receive data.

## Slide 217: Additional Process Symbols
Additional control of flow symbols:
Off-Page Connector:
Indicates the process flow continues onto another page.
Merge:
Indicates multiple processes merge into one.
Extract:
Indicates a process splits into multiple parallel processes.
Or:
Indicates a single data processing flow diverges to multiple branches with different criteria requirements.
Summing Junction:
Indicates multiple data processing flows converge into one.
Notes: More symbols:
The off-page connector helps the reader easily continue following the process from one page to another.
Merge and Extract – where multiple processes or pieces of information come together or where a single process splits into multiple.
  In a process map, the Merge symbol commonly indicates the storage of raw materials
  In a process map, the Extract symbol commonly indicates the storage of finished goods.
Or – for data flow it indicates how the data processing flow splits into multiple branches based on the criteria that are applied to the data. It is important to label each branch to indicate the criteria to follow the branch.
Summing junction – multiple data flows sum into a single data flow
The Or and Summing junction symbols are more commonly used in data processing flow diagrams.

## Slide 218: How to Plot a Process Map
Step 1: Define boundaries of the process you want to map.
  A process map can depict the flow of an entire process or a segment of it.
  You need to identify and define the beginning and ending points of the process before starting to plot.
  Use operational definition.
Notes: The first step in plotting a process map is deciding what the beginning and end points are for the process you are trying to depict.
You might be trying to map a whole process that begins and ends with the customer, or maybe you are trying to map out a segment of it.
An operational definition is an exact description – in other words it is useful in removing ambiguity and reduces the chances of getting disparate results from a process if performed by different people.

## Slide 219: How to Plot a Process Map
Step 2: Define and sort the process steps with the flow.
  Consult with process owners and subject matter experts or observe the process in action to understand how the process is actually performed.
  Record the process steps and sort them according to the order of their occurrence.
Notes: Step 2 is to determine what the process steps are and sort them into the proper order.
There are a few ways to do this: consult with process SMEs or observe the process to see how it is actually performed.
Usually, it is a good idea to do both; sometimes hearing what is “supposed” to happen might be different than what you observe, indicating a problem.

## Slide 220: How to Plot a Process Map
Step 3: Fill the step information into the appropriate process symbols and plot the diagram.
  In the team meeting of process mapping, place the sticky notes with different colors on a white board to flexibly adjust the under-construction process map.
  The flow lines are plotted directly on the white board. For the decision step, rotate the sticky note by 45°.
  When the map is completed on the white board, record the map using Excel, PowerPoint, or Visio.
Notes: Step 3 is to actually map the process using the appropriate symbols.
Mapping out the process with sticky notes on a white board is a good practice to do as a team because the map is easy to adjust until finished.
Use a dry-erase marker to draw the flow lines between the sticky notes.
When the team is satisfied that the process is accurate, record the map using whatever software is appropriate for your business (MS Excel, Visio, PowerPoint, Word, or any other preferred software).

## Slide 221: How to Plot a Process Map
Step 3:
  To illustrate the responsibility of different organizations involved in the process, use a Swim Lane Process Map.
Notes: This is a “swim lane” diagram or “swim lane” process map, which depicts the responsibilities for the process.
Swim-lane diagrams can be drawn vertically or horizontally.
The swim lanes can show organizations, roles, or functions within a business.

## Slide 222: How to Plot a Process Map
Step 4: Identify and record the inputs/outputs and their corresponding specifications for each process step.
  The process map helps in understanding and documenting Y=f(x) of a process where Y represents the outputs and x represents the inputs.
  The inputs of each process step can be controllable or non-controllable, standardized operational procedure, or noise. They are the source of variation in the process and need to be analyzed qualitatively and quantitatively in order to identify the vital few inputs that have significant effect on the outcome of the process.
  The outputs of each process step can be products, information, services, etc. They are the little Y’s within the process.
Notes: Step 4 is to identify and record the inputs and outputs for each process step.
Ideally, the specifications should be recorded for each step so it is understood what the inputs and outputs should look like to ensure process efficiency and quality.
Because inputs are the source of variation in a process, they need to be analyzed to understand how to monitor and control the variation.
Remember, inputs are the x’s in the transfer function. Remember y = f(x).
The outputs are the result of the process, or little Y’s.

## Slide 223: How to Plot a Process Map
Step 5: Evaluate the process map and adjust it if needed.
  If the process is too complicated to be covered in one single process map, you may create additional detailed sub-process maps for further information.
  Number the process steps in the order of their occurrence for clarity.
Notes: Step 5 is to evaluate and adjust.
There may be some components of the process where you need to describe in more detail on a “sub-process” map or in a procedure document.
It is helpful to number the process maps for reference purposes.

## Slide 224: High Level Process Map
Most high-level business process maps are also referred to as flow charts.
The key to a high-level process map is to over-simplify the process being depicted so that it can be understood in its most generic form.
As a general rule, high-level process maps should be 4–6 steps and no more.
Below is an oversimplified version of a high-level process map for cooking a 10lb prime rib for a dozen holiday guests.
Notes: A high-level process map is an oversimplification of a process, meant to display it in its basic form.
This type of map helps facilitate discussion about a process, especially with senior management that may not be as familiar with the details of the process.
It is also helpful in organizing work around a process by chunking it out.
Usually, a high-level process map should be no more than 4–6 steps.

## Slide 225: Detailed Process Map
Detailed process maps or multi-level maps take the high-level map much further.
Detailed maps can be two, three, or more levels deeper than your high-level process map.
A good guideline used to help create the second level is to take each step in the high-level map and break it down into another two to four steps each (no more).
Repeat this process (level 3, level 4 etc.) until reaching the desired level of detail.
Some detailed maps are two or three levels deep, others can be five or six levels deep. Obviously, the deeper the levels, the more complex and the more burdensome.
Notes: A detailed process map is exactly what is says it is – a much more detailed view of a process than a high-level process map.
Often process maps can be depicted at many different levels, two to four levels deeper than the high-level map. This is usually a helpful way to index a process, so when you want to understand more about a specific part of a process later on, you can find it by starting at the high level and digging down into the process step(s) you are interested in.
Each level of the process map should break the higher level steps into two to four additional steps, until the desired level of detail is attained.
Detailed process maps can go deeper than the two to four levels mentioned earlier, but they become much more complex and burdensome to create and maintain.

## Slide 226: Functional Process Map
The functional map adds dimension to the high-level or detailed map.
The dimension added is identifying which function or job performs the step or makes the decision.
Below is a generic example of a functional map. Note that functions are identified in horizontal "lanes" and each process step is placed in the appropriate lane based on which function performs the step.
Notes: The functional process map adds another dimension of information to a high-level or detailed process map.
This map conveys which function, role, job performs the step in a process or makes a decision.
The process step or decision is placed in the appropriate lane based on which function performs it.

## Slide 227: What is SIPOC?
A SIPOC (Suppliers-Input-Process-Output-Customers) is a high-level visualization tool to help identify and link the different components in a process.
It is usually applied in the Measure phase in order to better understand the current state of the process and define the scope of the project.
Notes: A SIPOC is a tool that summarizes the inputs and outputs of a process. At the outset of a process improvement effort it is very helpful to provide an overview to people who are unfamiliar or need to become reacquainted with a process.

## Slide 228: Key Components of a SIPOC
Suppliers: vendors who provide the raw material, services, and information. Customers can also be suppliers sometimes.
Input: the raw materials, information, equipment, services, people, environment involved in the process.
Process: the high-level sequence of actions and decisions that results in the services or products delivered to the customers.
Output: the services or products delivered to the customers and any other outcomes of the process.
Customers: the end users or recipients of the services or products.
Notes: Suppliers (external or internal to an organization) are those who provide raw material, services, or information for a process.
Inputs are the materials, information, equipment, services, people, and environment that are involved in the process.
The process is the sequence of activities or decisions that result in an output.
Output is a service or product that will be delivered to a customer.
Customers, of course, are the end users or recipients of the service or product, which again can be external or internal to an organization.

## Slide 229: How to Plot a SIPOC Diagram
The first method:
  Step 1: Create a template that can contain the information of the five key components in a clear way.
  Step 2: Plot a high-level process map that covers five steps at maximum.
  Step 3: Identify the outputs of the process.
  Step 4: Identify the receipt of the process.
  Step 5: Brainstorm the inputs required to run each process step.
  Step 6: Identify the suppliers who provide the inputs.
Notes: In the first method of creating a SIPOC:
Begin with the process steps (five steps at most)
Determine the outputs
Identify who the recipients of the process
Then work to the left, identifying the inputs and then the suppliers for those inputs.

## Slide 230: How to Plot a SIPOC Diagram
The second method:
  Step 1: Create a template that can contain the information of the five key components in a clear way.
  Step 2: Identify the receipt of the process.
  Step 3: Identify the outputs of the process.
  Step 4: Plot a high-level process map that covers five steps at maximum.
  Step 5: Brainstorm the inputs required to run each process step.
  Step 6: Identify the suppliers who provide the inputs.
Notes: In the second method:
Start with the customer (or the recipient of the process)
Work your way back by identifying the process outputs, then the high-level process map (five steps maximum)
Brainstorm the inputs to the process, then identify the suppliers for those inputs.

## Slide 231: Benefits of SIPOC Diagrams
A SIPOC diagram provides more detailed information than process maps and it demonstrates how each component gets involved in the process.
It helps visualize and narrow the project scope.
It serves as a great communication tool to help different process owners understand the entire process, their specific roles and responsibilities.
Notes: A SIPOC has more detail than a simple high-level process map, and it uncovers additional components about the process that are just as important as the process itself, like the inputs and outputs for each step.
It is very useful to help us visualize the process and help narrow the scope for an improvement project.
It is a great tool to help people who may not be as familiar with the process to understand it.

## Slide 232: SIPOC Diagram Example
Example of plotting a SIPOC diagram for Mom cooking scrambled eggs for two kids
Notes: This slide shows you an example of a SIPOC used to convey a very simple process of cooking scrambled eggs for two children.

## Slide 233: Creating a SIPOC
Step 1: Vertically List High-Level Process
  If you followed the general rules for a high-level process map, then you should have no more than 4–6 steps for your process.
  List those steps in a vertical manner as depicted below.
Notes: Here is a walk-through for completing a SIPOC via the first method described, starting with the process steps.
Remember, a high-level process should not have more than four to six steps; list them vertically.

## Slide 234: Creating a SIPOC
Step 2: List Process Outputs
Notes: Next, list the outputs for each step of the process.

## Slide 235: Creating a SIPOC
Step 3: List Output Customers
Notes: Then indicate the customers.

## Slide 236: Creating a SIPOC
Step 4: List Process Inputs
Notes: Next, move to the left of the process, indicating what inputs are needed for each process step.

## Slide 237: Creating a SIPOC
Step 5: List Suppliers of Inputs
Notes: Finally, enter the suppliers for the inputs.

## Slide 238: SIPOC Benefits
Visually communicate project scope
Identify key inputs and outputs of a process
Identify key suppliers and customers of a process
Verify:
  Inputs match outputs for upstream processes
  Outputs match inputs for downstream processes.
This type of mapping is effective for identifying opportunities for improvement of your process.
If you have completed your high-level process map, follow the outlined steps to create a process map of Suppliers, Inputs, Process, Outputs, and Customer.
Notes: As mentioned earlier, a SIPOC is a visual for communicating a process and the scope of a project.
It is more powerful than a simple high-level process map because it conveys the inputs and outputs of a process, as well as the suppliers and customers.
The outputs from one process step should match the inputs for the next step (and vice-versa).
This type of map is even more effective at indentifying opportunities in that the inputs and outputs could represent improvement opportunities too.

## Slide 239: What is Value Stream Mapping?
Value stream mapping is a method to visualize and analyze the path of how information and raw materials are transformed into products or services customers receive.
It is used to identify, measure, and decrease the non-value-adding steps in the current process.
Notes: Value stream mapping is just that – creating a visual for where value is added to a product or service by transforming raw materials and information.
It helps us determine where the non-value added activity takes place in a process, which we can then focus on minimizing.

## Slide 240: Non-Value-Added Activities
Non-value-adding activities are activities in a process that do not add any other value to the products or services customers demand.
Example of non-value-adding activities:
  Rework
  Overproduction
  Excess transportation
  Excess stock
  Waiting
  Unnecessary motion.
Not all non-value-adding activities are unnecessary.
Notes: A non-value added activity is an activity that occurs during the process, but from the customer’s perspective does not add any value to the product or service.
Here are some activities that can take place in a process before a product reaches a customer, but do not add value:
Rework – it should have been done right the first time, so a second time certainly does not add value
Overproduction – work that is done before it is needed, and could change, leading to rework
Excess transportation – moving the product around does not add value
Excess stock – similar to overproduction
Waiting – wasted time
Unnecessary motion – wasted energy
Sometimes, non-value added activities are required. For example, an inspection that is done for regulatory compliance purposes is necessary but does not add value to the product or service the customer receives.

## Slide 241: How to Plot a Value Stream Map
Plot the entire high-level process flow from when the customer places the order to when the customer receives the products or services in the end.
A value stream map requires more detailed information for each step than the standard process map.
  Cycle time
  Preparation time
  Actual working time
  Available time
  Scrap rate
  Rework rate
  Number of operators
Assess the value stream map of current process, identity and eliminate the waste.
Notes: To plot a value stream map, start by mapping the high-level process from when the customer places an order to when the customer receives the product or service at the end.
There are several pieces of information that can and should be provided with each step of the process to help illustrate where waste is occurring and value is added.
Finally, assess the map to identify the waste that should be eliminated.

## Slide 242: Basic Value Stream Map Prototype
Notes: In this process you can see where the customer talks to the customer service representative, who cuts the order to the master scheduler, who sets the process in motion.
There are four sub-processes, and the final delivers the product to the customer.
Notice the individual pieces of information that are conveyed for each sub-process.

## Slide 243: Additional Mapping Techniques
Spaghetti Chart
Thought Process Mapping
Notes: We are now going to talk about a few other mapping techniques that can come in very handy during a process – the spaghetti chart and the thought process map.

## Slide 244: Spaghetti Chart
A spaghetti chart is a graphical tool to map out the physical flow of materials, information, and people involved in a process. It can also reflect the distances between multiple workstations the physical flow has been through.
A process that has not been streamlined has messy and wasteful movements of materials, information, and people, resembling a bowl of cooked spaghetti.
Notes: This tool is used to map the physical flow of material, information, or people that are involved in a process.
A non-optimized process typically has a lot of wasteful transportation, information flow, and people movement. When you have mapped it out, it will look like a jumbled mess…like spaghetti.

## Slide 245: How to Plot a Spaghetti Chart
Step 1: Create a map of the work area layout.
Step 2: Observe the current work flow and draw the actual work path from the very beginning of work to the end when products exit the work area.
Step 3: Analyze the spaghetti chart and identify improvement opportunities.
Notes: Start by mapping out the work area (the floor plan).
Observe the work flow and trace the path of the work from beginning to end.
Analyze the spaghetti chart and identify the areas where the work flow can be streamlined (look for waste like transportation, motion, etc.).

## Slide 246: Spaghetti Chart Example
Workstation
1
Workstation
2
Workstation
4
Workstation
7
Workstation
3
Workstation
5
Workstation
6
Work
station
8
Notes: This is an example of a spaghetti chart of a work path.

## Slide 247: Thought Process Mapping
A thought process map is a graphical tool to help brainstorm, organize, and visualize the information, ideas, questions, or thoughts regarding reaching the project goal.
It is a popular tool generally used at the beginning of a project in order to:
  identify knowns and unknowns
  communicate assumptions and risks
  discover potential problems and solutions
  identify resources, information, and actions required to meet the goal
  present relationship of thoughts.
Notes: This is a simple yet powerful tool that creates a visual for the thought process used to solve a problem or reach a project goal. It helps a project team map to understand where they have been, where they still need to go, what questions have been answered, how were they answered, and what is yet to be answered.
It helps document what is known and unknown; communicate assumptions and risks; discover problems and solutions; determine what information, actions, or resources are needed to achieve the goal; and, of course, present the relationship of all of the thoughts.

## Slide 248: How to Plot a Thought Process Map
Step 1: Define the project goal.
Step 2: Brainstorm knowns and unknowns about the project.
Step 3: Brainstorm questions and group the unknowns and questions into five phases (Define, Measure, Analyze, Improve, and Control).
Step 4: Sequence the questions below the project goal and link the related questions.
Step 5: Identify tools or methods that would be used to answer the questions.
Step 6: Repeat steps 3 to 5 as the project continues.
Notes: Start with the goal of the project.
Through brainstorming, document the knowns and unknowns.
Group the unknowns and questions into five phases (DMAIC).
Sequence the questions under the project goal and link any related questions.
Continue to leverage steps 3, 4, and 5 throughout the project until the goal is met.

## Slide 249: Thought Process Map Example
Deliver the pizza to clients in time
Transportation
Staff
System
Process
Car Battery
Traffic
How often?
Which area?
What time?
Training
Too few?
Scheduling
Routing
Process Map
Online ordering system
Phone ordering system
Notes: This is an example of a thought process map. In this case, the goal is on-time pizza delivery.

## Slide 250: 2.1.4 FMEA

## Slide 251: What is FMEA?
The FMEA (Failure Modes and Effects Analysis) is an analysis technique to identify, evaluate, and prioritize a potential deficiency in a process so that the project team can design action plans to reduce the probability of the failure/deficiency occurring.
FMEA is completed in cross-functional brainstorming sessions in which attendees have a good understanding of the entire process or of a segment of it.
Notes: The failure mode and effects analysis is a very useful tool to identify, analyze, and prioritize any potential weaknesses in a process. The point is to prioritize the greatest deficiencies so that the project team can design action plans to reduce the probability of a failure occurring.
The activity of performing an FMEA follows the process mapping exercise. A process map is used during the FMEA to determine where potential process breakdowns can occur. At each step, the team must ask, “what can go wrong?”
A Pareto analysis may follow to quantitatively validate or invalidate the results of the FMEA.
To be effective, the FMEA should be done with a cross-functional group that has a thorough understanding of the process.

## Slide 252: Basic FMEA Terms
Process Functions
  Process steps depicted in the process map. FMEA is based on a process map and one step/function is analyzed at a time.
Failure Modes
  Potential and actual failure in the process function/step. It usually describes the way in which failure occurs. There might be more than one failure mode for one process function.
Failure Effects
  Impact of failure modes on the process or product. One failure mode might trigger multiple failure effects.
Failure Causes
  Potential defect of the design that might result in the failure modes occurring. One failure mode might have multiple potential failure causes.
Current Controls
  Procedures currently conducted to prevent failure modes from happening or to detect the failure mode occurring.
Notes: There are several basic terms that anyone participating in an FMEA should know:
Process Function – is a step in the process.
Failure Mode – is a description of how a failure can occur during a process step. There can be multiple failure modes for a single process step.
Failure Effect – is the impact that the failure has. There can be multiple effects for a failure.
Failure Cause – describes the flaw (or defect) in the process that results in a failure mode occurring.
A control is a anything established within the process to prevent or detect the failure mode occurring.
Toaster Example
Process Function: engage toaster handle to heat toaster
Failure Mode: handle sticks in engaged position
Failure Effect: toaster catches fire
Failure Cause: debris in handle mechanism
Current Control: thermostatic safety release incorporated into design

## Slide 253: Basic FMEA Terms
Severity Score
  The seriousness of the consequences of a failure mode occurring.
  Ranges from 1 to 10, with 10 indicating the most severe consequence.
Occurrence Score
  The frequency of the failure mode occurring.
  Ranges from 1 to 10, with 10 indicating the highest frequency.
Detection Score
  How easily failure modes can be detected.
  Ranges from 1 to 10, with 10 indicating the most difficult detection.
Notes: Here are some additional FMEA terms:
The Severity Score – is a quantification for how serious the effect of the failure mode is (10 is the most severe).
The Occurrence Score – is a rating for how frequently the failure mode occurs (10 is the most frequent).
The Detection Score – is a rating for how effective any controls are in the process. A score of 1 means there are excellent controls to prevent or detect a failure mode, and a 10 would mean there are very weak to no controls.

## Slide 254: Basic FMEA Terms
RPN (Risk Prioritization Number)
  The product of the severity, occurrence, and detection scores.
  Ranges from 1 to 1000.
  The higher RPN is, the more focus the particular step/function needs.
Recommended Actions
  The action plan recommended to reduce the probability of failure modes occurring.
Notes: The RPN (or Risk Prioritization Number) is a calculated value that ultimately is used to prioritize the FMEA.
It is calculated by multiplying the severity, occurrence, and detection scores. It has a minimum value of 1 and a maximum of 1000.
The higher the RPN, the more attention is needed on the process step.
The recommended action plan is built by the team to reduce the probability of a failure mode or at least enable better controls to detect it when it occurs.

## Slide 255: How to Conduct an FMEA
Step 1: List the critical functions of the process based on the process map created.
Step 2: List all potential failure modes that might occur in each function. One function may have multiple potential failures.
Step 3: List all potential failure effects that might affect the process or product.
Step 4: List all possible causes that may lead to the failure mode happening.
Step 5: List the current control procedures for each failure mode.
Notes: Conducting an FMEA is not a difficult process, but can be time consuming when done correctly, particularly the first time it is performed on a process.
Start by listing the process steps, then identify all potential failure modes for a function.
List all failure effects that can effect the process or product. This means you should not focus on effects that are inconsequential.
List possible causes for the failure mode, then identify the current control procedures for each.

## Slide 256: How to Conduct an FMEA
Step 6: Determine the severity rating for each potential failure mode.
Step 7: Determine the occurrence rating for each potential failure cause.
Step 8: Determine the detection rating for each current control procedure.
Step 9: Calculate RPN (Risk Prioritization Number).
Step 10: Rank the failures using RPN and determine the precedence of problems or critical inputs of the process. A Pareto chart might help to focus on the failure modes with high RPNs. The higher the RPN, the higher the priority the correction action plan.
Notes: Next, you want to establish a severity, occurrence, and detection rating for each failure mode, cause, and control procedure, respectively.
Calculate the RPN for each, then rank the failures using the RPN.
Those with the highest RPN are where you want to put the highest priority with a corrective action plan.

## Slide 257: How to Conduct an FMEA
Step 11: Brainstorm and create recommended action plans for each failure mode.
Step 12: Determine and assign the task owner and projected completion date to take actions.
Step 13: Determine the new severity rating if the actions are taken.
Step 14: Determine the new occurrence rating if the actions are taken.
Step 15: Determine the new detection rating if the actions are taken.
Step 16: Update the RPN based on new severity, occurrence, and detection ratings.
Notes: Make sure the corrective action plan is robust. Make sure it is clear what action is to be taken, who owns the task, and what the completion date is for the task.
Re-assess the severity, occurrence, and detection ratings if the corrective action plan is carried out, and update the RPN.

## Slide 258: FMEA Example
Case study:
Joe is trying to identify, analyze, and eliminate the failure modes he experienced in the past when preparing his work bag before heading to the office every morning. He decides to run an FMEA for his process of work bag preparation.
There are only two steps involved in the process.
  Putting the work files in the bag
  Putting a water bottle in the bag.
Notes: Here is a very straightforward example of an FMEA.
Joe is analyzing his process for preparing his workbag each morning before going to work.
There are only two steps in the process.

## Slide 259: FMEA Example
Step 1: List the critical functions of the process based on the process map created.
Step 2: List all the potential failure modes for each function.
Step 3: List potential failure effects that might affect the process.
Notes: Here you see that the process steps are listed under the “Process Function” heading.
Next you can see that Joe has identified one failure mode for each step:
  The incorrect files are put in the bag
The effects Identified are:
  Work is delayed (because he packed the wrong files)
  Files were damaged (because they got wet).

## Slide 260: FMEA Example
Step 4: List all possible causes to the failure mode.
Step 5: List any control procedures for each failure mode.
Step 6: Determine the severity rating for each failure mode.
Notes: The causes for the two failure modes are:
  His files are not well organized.
  Water bottle cap cannot be tightened completely.
His only control is a quality control “check”.
Severity Ratings:
  Work is delayed got a ranking of 9
  Files damaged got a ranking of 7.

## Slide 261: FMEA Example
Step 7: Determine the occurrence rating for each failure cause.
Step 8: Determine the detection rating for each control.
Step 9: Calculate the RPN (Risk Prioritization Number).
Notes: The occurrence probability for each was ranked low:
  Files not organized well was ranked 3
  Water bottle cap not tightened perfectly was ranked 5.
The detection rating for both controls was ranked equally (5).
By multiplying the severity, occurrence, and detection, an RPN was reached for each failure mode.
  135 for incorrect files
  175 for water leaks.

## Slide 262: FMEA Example
Step 10: Rank the failures using the RPN and determine the precedence of problems or critical inputs of process.
Step 11: Brainstorm and create recommended action plans.
Step 12: Determine and assign owners with completion dates.
Notes: The two failure modes are now sorted in order of decreasing RPN.
A recommended action is made for both failure modes:
  Organize and categorize files into folders
  Buy a new water bottle.
Each action is assigned to Joe, with a projected completion date.

## Slide 263: FMEA Example
Steps 13-15: Determine new severity, occurrence and detection ratings if actions are taken.
Step 16: Update RPN based on new ratings.
Notes: If the actions are taken on the failure mode, then reassess the ratings and calculate a new RPN value.

## Slide 264: 2.1.5 Theory of Constraints
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 265: 2.2 Six Sigma Statistics

## Slide 266: Black Belt Training: Measure Phase
2.1 Process Definition 2.1.1 Cause and Effect Diagrams 2.1.2 Cause and Effects Matrix 2.1.3 Process Mapping 2.1.4 FMEA: Failure Modes and Effects Analysis
2.1.5 Theory of Constraints
2.2 Six Sigma Statistics 2.2.1 Basic Statistics 2.2.2 Descriptive Statistics 2.2.3 Distributions and Normality 2.2.4 Graphical Analysis
2.3 Measurement System Analysis 2.3.1 Precision and Accuracy 2.3.2 Bias, Linearity, and Stability 2.3.3 Gage R&R 2.3.4 Variable and Attribute MSA
2.4 Process Capability 2.4.1 Capability Analysis 2.4.2 Concept of Stability 2.4.3 Attribute and Discrete Capability 2.4.4 Monitoring Techniques

## Slide 267: 2.2.1 Basic Statistics

## Slide 268: What is Statistics?
Statistics is the science of collection, analysis, interpretation, and presentation of data.
In Six Sigma, we apply statistical methods and principles to quantitatively measure and analyze the process performance to reach statistical conclusions and help solve business problems.
Notes: sta·tis·tics (defined on dictionary.com)
1. the science that deals with the collection, classification, analysis, and interpretation of numerical facts or data, and that, by use of mathematical theories of probability, imposes order and regularity on aggregates of more or less disparate elements.
2. the numerical facts or data themselves.
In Six Sigma we use statistics to measure performance and reach conclusions that are based on probability.

## Slide 269: Types of Statistics
Descriptive Statistics
  Describing what was going on
Inferential Statistics
  Making inferences from the data at hand to more general conditions
Notes: Descriptive statistics is exactly what it sounds like. Descriptive statistics simply describes what is happening, while inferential statistics helps you make comparisons, draw conclusions, or make judgments about data.

## Slide 270: Descriptive Statistics
Descriptive statistics is applied to describe the main characteristics of a collection of data.
Descriptive statistics summarizes the features of the data quantitatively.
Descriptive statistics is descriptive only and it does not make any generalizations beyond the data at hand.
The data used for descriptive statistics are for the purpose of representing or reporting.
Notes: Descriptive statistics tells us about the characteristics of the data. It describes the distribution of the data. It tells us things like the average, median, standard deviation, range, maximum, minimum, and more.
It does not help us make any judgments, it only represents the data.

## Slide 271: Inferential Statistics
Inferential statistics is applied to infer the characteristics or relationships of the populations from which the data are collected.
Inferential statistics draws statistical conclusions about the population by analyzing the sample data subject to random variation.
A complete data analysis includes both descriptive statistics and inferential statistics.
Notes: Inferential statistics, on the other hand, helps us to make inferences, tells us what the population is and what it is not.
We can draw statistical conclusions that are based on variation of data and probability.

## Slide 272: Statistics vs. Parameters
The word statistic refers to a numeric measurement calculated using a sample data set, for example, sample mean or sample standard deviation. Its plural is statistics (the same spelling as “statistics” which refers to the scientific discipline).
The parameter refers to a numeric metric describing the population, for example, population mean and population standard deviation. Unless you have the full data set of the population, you will not be able to know the population parameters.
Notes: We will use this terminology later, so it is important to understand the difference between a statistic and a parameter.
A statistic is a numerical representation of a sample data set. A sample is a subset of a population.
Statistics can be the plural of statistic, but can also describe the science discipline of statistics.
A parameter is a numeric metric that describes a whole “population”. Unless you have a complete set of data for the entire population, you will not know the parameters of the population.
Almost always, you will be working with statistics, but they will allow you to make inferences about the population.

## Slide 273: Continuous Variable vs. Discrete Variable
Continuous Variable
  Measured
  There is an infinite number of values possible
  Examples: temperature, height, weight, money, time
Discrete Variable
  Counted
  There is a finite number of values available
  Examples: count of people, count of countries, count of defects, count of defectives
Notes: Data can take different forms, which is important to recognize when it is time to analyze the data.
Continuous data are measured and can be divided infinitesimally (it can take any value within a range). Examples are temperature, time, or height and weight.
Discrete data are sometimes referred to as count data. There is a finite number of values available.

## Slide 274: Types of Data
Nominal
  Categorical data
  Examples: a set of colors, the social security number
Ordinal
  Rank-ordering data
  Examples: the first, second place in a race, scores of exams
Interval
  Equidistant data
  Examples: temperature with Fahrenheit or Celsius scale
Ratio
  The ratio between the magnitude of a continuous value and the unit value of the same category
  Examples: weight, length, time
Notes: Nominal
Comes from the Latin nomen, meaning “name” and nominal data are items that are differentiated by a simple naming system.
Be careful of nominal items that have numbers assigned to them and may appear ordinal but are not – these are used to simplify capture and referencing.
Nominal items are usually categorical, in that they belong to a definable category, such as “employees”.
Ordinal
Items on an ordinal scale are set into some kind of order by their position on the scale.
The order of items is often defined by assigning numbers to them to show their relative position.
Interval
Interval data (also sometimes called integer) are measured along a scale in which each position is equidistant from one another. This allows for the distance between two pairs to be equivalent in some way.
Another example: my level of happiness, rated from 1 to 10
Ratio
In a ratio scale, numbers can be compared as multiples of one another. Thus one person can be twice as tall as another person. Important also, the number zero has meaning.
Thus the difference between a person of 35 and a person 38 is the same as the difference between people who are 12 and 15. A person can also have an age of zero.
Interval and ratio data measure quantities and hence are quantitative. Because they can be measured on a scale, they are also called scale data.

## Slide 275: 2.2.2 Descriptive Statistics

## Slide 276: Basics of Descriptive Statistics
Descriptive statistics provides a quantitative summary for the data collected.
It summarizes the main features of the collection of data.
  Shape
  Location
  Spread
It is a presentation of data collected and it does not provide any inferences about a more general condition.
Notes: As said previously, descriptive statistics provide a quantitative summary for data, and do not provide any inferences beyond just describing what the data “looks like.”
It describes three dimensions of the data: what the distribution is shaped like, where it is located (e.g., mean), and the spread of the data (e.g., standard deviation).

## Slide 277: Shape of the Data
Distribution is used to describe the shape of the data.
Distribution (also called frequency distribution) summarizes the frequency of an individual value or a range of values of a variable (either continuous or discrete).
Distribution is depicted as a table or graph.
Notes: When we describe the “shape” of the data, we typically refer to the distribution of the data.
It is sometimes referred to as a “frequency distribution” because it depicts how often a particular value occurs within a data set.

## Slide 278: Shape of the Data
Simple example of distribution
  We are tossing a fair die. The possible value we obtain from each tossing is a value between 1 and 6.
  Each value between 1 and 6 has a 1/6 chance to be hit for each tossing.
  The distribution of this game describes the relationship between every possible value and the percentage of times the value is being hit (or count of times the value is being hit).
Notes: In this example, there is an equal probability for each value on the die occurring.
If you were to roll the die a high number of times, what might the distribution look like?
If you rolled it 600 times, you would likely get each value nearly 100 times.

## Slide 279: Shape of the Data
Examples of continuous distribution
  Normal Distribution
  T distribution
  Chi-square distribution
  F distribution
Examples of discrete distribution
  Binomial distribution
  Poisson distribution
Notes: There are different types of distributions that are commonly found in statistics.
It is important to recognize that there are different types of data distributions because the statistics can tell you different things about the data and different inferential statistics have to be used for different situations.

## Slide 280: Location of the Data
The location (i.e. central tendency) of the data describes the value where the data tend to cluster around.
There are multiple measurements to capture the location of the data:
  Mean
  Median
  Mode.
Notes: When we describe the location of the data, we are describing the central tendency of the data. This is where the majority of the values in the data set tend to be located or clustered around.
There are a few terms that are typically used to describe central tendency: mean, median, and mode, which we will describe further on the following pages.

## Slide 281: Mean
The mean is the arithmetic average of a data set.
n is the number of values in the data set
For example, we have a set of data: 2, 3, 5, 8, 5, and 9. The arithmetic mean of the data set is
Notes: The mean is another term for the average. It is easily calculated by dividing the sum of the data points by n (the number of data points).
In the example, there are 6 data points. The sum of the 6 data points is 32, and when dividing by the number of data points, 6, the arithmetic mean is 5.33.

## Slide 282: Median
The median is the middle value of the data set in numeric order.
It separates the finite set of data into two parts: one with values higher that the median and the other with values lower than the median.
For example, we have a set of data: 45, 32, 67, 12, 37, 54 and 28. The median is 37 since it is the middle value of the sorted list of values (i.e. 12, 28, 32, 37, 45, 54 and 67).
Notes: The median is the middle value when the numbers are listed in numerical order.
In this example using 7 values, the median (or middle value) is 37. There are 3 values lower and 3 values higher than the median.

## Slide 283: Mode
The mode is the value that occurs most often in the data set.
If no number is repeated, there is no mode for the data set.
For example, we have a data set: 55, 23, 45, 45, 68, 34, 45, 55. The mode is 45 since it occurs most frequently.
Notes: The mode is the value that occurs most often within a data set.
In this example, the numbers 23, 34, and 68 occur once, 55 occurs twice, and 45 occurs 3 times.
45 occurs the most, and therefore it is the mode of the given data set.

## Slide 284: Spread of the Data
The spread (i.e. variation) of the data describes the degree of data dispersing around the center value.
There are multiple measurements to capture the spread of the data:
  Range
  Variance
  Standard Deviation.
Notes: When we talk about spread of the data, we are talking about how widely or narrowly dispersed the data points are around the center value.
We typically measure this through range, variance, or standard deviation.

## Slide 285: Range
The range is the numeric difference between the greatest and smallest values in a data set.
Only two data values (i.e. the greatest and the smallest values) are accounted for calculating the range.
For example, we have a set of data: 34, 45, 23, 12, 32, 78 and 23. The range of the data is 78−12 = 66.
Notes: Range is very straightforward: it is simply the difference between the largest and smallest value in a data set.
In the example here, the largest value is 78, and the smallest is 12. Therefore, the range is 78−12 = 66.

## Slide 286: Variance
The variance measures how far on average the data points spread out from the mean.
It is the average squared deviation of each value from its mean.
All the data points are accounted for calculating the variance.
where
n is the number of values in the data set
Notes: You will notice that the variance and standard deviation are directly related to each other.
The variance measures the average distance of each point from the mean, but more specifically, it is the average squared deviation of each value from the mean.
Why is the term squared? First, because squared terms always give a positive value and we are only trying to measure the distance from the mean (positives and negatives will negate each other). Second, squaring emphasizes the larger terms (or differences) between the mean and each individual data point.

## Slide 287: Standard Deviation
Standard deviation describes how far the data points spread away from the mean.
It is simply the square root of the variance.
All the data points are accounted for calculating the standard deviation.
where
n is the number of values in the data set
Notes: Similar to variance, the standard deviation describes how far the data points spread away from the mean.
It is calculated by taking the square root of the variance.

## Slide 288: 2.2.3 Normal Distribution & Normality

## Slide 289: What is Normal Distribution?
The normal distribution is a probability distribution of a continuous random variable whose values spread symmetrically around the mean.
A normal distribution can be completely described by using its mean (μ) and variance (σ2).
When a variable x is normally distributed, we denote x ~ N(μ, σ2).
Notes: In our world, random variation tends to conform to a certain distribution called Gaussian distribution, otherwise known as the normal distribution.
It can be described by the mean (remember centering or middle point?) and the variance (the spread of the data).
The notation to describe a normal distribution includes the two terms that describe the distribution, the mean, and the variance.

## Slide 290: Z Distribution
The Z distribution is the simplest normal distribution with the mean equal to zero and the variance equal to one.
Any normal distribution can be transferred to a Z distribution by applying
where
Notes: The Z distribution is also known as the standard normal distribution. It is the simplest form of the normal distribution.
The parameters of the standard normal distribution are equal to zero (mean) and one (variance).
The standard normal distribution is important since the probabilities and quantiles of any normal distribution can be computed from the standard normal distribution – if the mean and standard deviation are known.

## Slide 291: Z Score
The Z Score is the measure of how many standard deviations an observation is above or below the mean.
Positive Z Scores indicate the observation is above the mean or “right of the mean”.
Negative Z Scores indicate the observation is below the mean of “left of the mean”
Calculate Z Score using the formula below:
where
x is the observation
μ is the mean of the population
σ is the standard deviation of the population
Notes: The Z distribution is also known as the standard normal distribution. It is the simplest form of the normal distribution.
The parameters of the standard normal distribution are equal to zero (mean) and one (variance).
The standard normal distribution is important since the probabilities and quantiles of any normal distribution can be computed from the standard normal distribution – if the mean and standard deviation are known.

## Slide 292: Shape of Normal Distribution
The probability density function curve of normal distribution is bell-shaped.
Probability density function of normal distribution
μ
Notes: You might remember teachers from your academic days referring to the “curve” when talking about how they will grade performance.
The bell curve refers to the shape of a normal distribution.
It is a probability density function. It just means that within the population that is described by this distribution, the highest probability is for values closest to the mean, then the probability drops as you move further from the mean (in either direction).

## Slide 293: Location of Normal Distribution
If a variable is normally distributed, the mean, the median, and the mode have the same value.
The probability density curve of normal distribution is symmetric around a center value which is the mean, the median, and the mode at the same time.
Notes: There are some special characteristics of a normal distribution.
As far as the location of the distribution is concerned, the mean, median, and mode all coincide.
That is because the distribution is symmetrical around the center value.

## Slide 294: Spread of Normal Distribution
The spread or variation of the normally-distributed data can be described using the variance or the standard deviation.
The smaller the variance or the standard deviation, the less variability in the data set.
Notes: Just as described earlier, the variation (or spread) of a normal distribution can be described by the variance or the standard deviation (which is the square root of the variance).
The smaller the variance, the less variability in the data set, and the narrower the distribution.

## Slide 295: 68-95-99.7 Rule
The 68-95-99.7 rule or the empirical rule in statistics states that for a normal distribution:
  About 68% of the data fall within one standard deviation of the mean
  About 95% of the data fall within two standard deviations of the mean
  About 99.7% of the data fall within three standard deviations of the mean.
Notes: One way to think about this rule is to consider the area under the normal distribution curve.
The 68-95-99.7 rule describes what percent of data fall within one, two, and three standard deviations from the mean, respectively.

## Slide 296: 68-95-99.7 Rule
Notes: The percentages represent the area under the normal curve. Most of the data values are grouped around the center.

## Slide 297: Normality
Not all the distributions with a bell shape are normal distributions.
To check whether a group of data points are normally distributed, we need to run a normality test.
There are different normality tests available:
  Anderson-Darling test
  Sharpiro-Wilk test
  Jarque-Bera test.
More details of normality test will be introduced in the Analyze module.
Notes: Normality – it is important to understand whether or not data being analyzed fit this distribution because there are implications for how the data are analyzed and what inferences are made from the data.
A normality test can be used to determine whether the data are normal, and there are several tests to do this: Anderson-Darling, Sharpiro-Wilk, and Jarque-Bera are some examples.

## Slide 298: Normality Testing
To check whether the population of our interest is normally distributed, we need to run normality test.
  Null Hypothesis (H0): The data points are normally distributed.
  Alternative Hypothesis (Ha): The data points are not normally distributed.
There are many normality tests available. For example, Anderson-Darling test, Sharpiro-Wilk test, Jarque-Bera test, and so on.
Notes: To determine if a data set fits a normal distribution, we must apply a normality test to the data.
The following slides will explain this in more details, but take note that:
  The null hypothesis is that the data ARE normally distribution.
  The alternative hypothesis is that the data are NOT normally distributed.

## Slide 299: Use SigmaXL to Run a Normality Test
      Case Study: we are interested to know whether the height of basketball players is normally distributed.
      Data File: “One Sample T-Test” tab in “Sample Data.xlsx”
Null Hypothesis (H0): the height of basketball players is normally distributed.
Alternative Hypothesis (Ha): the height of basketball players is not normally distributed.
Notes: We will leverage SigmaXL to determine if a dataset is normally distributed.
In this example we are wanting to know about the height of basketball players.
Null: height IS normally distributed
Alternative: height IS NOT normally distributed.

## Slide 300: Use SigmaXL to Run a Normality Test
Steps to run a normality test in SigmaXL
  Select the entire range of data
  Click SigmaXL -> Graphical Tools -> Histograms & Descriptive Statistics
  A new window named “Histograms & Descriptive” pops up with the selected range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Descriptive Statistics” appears
  Select “HtBk” as the “Numeric Data Variables (Y)”
  Click “OK”
  The normality test results appear in the newly generated tab “Hist Descript (1)”
Notes: Using your SigmaXL software, follow these instructions to run a normality test.

## Slide 301: Use SigmaXL to Run a Normality Test
Notes: This slide shows you how to do this through the SigmaXL menus.

## Slide 302: Use SigmaXL to Run a Normality Test
Null Hypothesis (H0): The data are normally distributed.
Alternative Hypothesis (Ha): The data are not normally distributed.
Since the p-value of the normality is 0.2748 greater than alpha level (0.05), we fail to reject the null and claim that the data are normally distributed.
Notes: The output from SigmaXL is shown here. We need to know the p-value to determine if we should ACCEPT or REJECT the null hypothesis that the distribution IS normal.
The P value (Prob<W) is 0.3197 is greater than alpha (or significance level). Since P>0.05, we fail to reject the null hypothesis, which was that the data is normal. Therefore, the data IS normal.

## Slide 303: 2.2.4 Graphical Analysis

## Slide 304: What is Graphical Analysis?
In statistics, graphical analysis is a method to visualize the quantitative data.
Graphical analysis is used to discover the structure and patterns in the data, explaining and presenting the statistical conclusions.
A complete statistical analysis includes both quantitative analysis and graphical analysis.
Notes: When we think of statistics, we often think of numbers. However, graphical analysis is complementary to purely quantitative statistics because it allows us to visualize structure and patterns in the data.
Often the graphical presentation of data can tell a story on its own, but the total statistical analysis is important to complete the picture. Sometimes our eyes can deceive us.

## Slide 305: Graphical Analysis Example
There are various graphical analysis tools available. Here are four most commonly used examples:
  Box Plot
  Histogram
  Scatter Plot
  Run Chart.
Notes: Over the next several pages we will look at some types of commonly used graphical analysis: box plots, histograms, scatter plots, and run charts.

## Slide 306: Box Plot
A box plot is a graphical method to summarize a data set by visualizing the minimum value, 25th percentile, median, 75th percentile, the maximum value, and potential outliers.
A percentile is the value below which a certain percentage of data fall. For example, if 75% of the observations have values lower than 685 in a data set, then 685 is the 75th percentile of the data.
Notes: The graphical technique of using the box plot summarizes a dataset by breaking it into quartiles.
At the 50th percentile, or median, 50% of the values are lower and 50% are higher than that value.

## Slide 307: Box Plot
Interquartile Range = 75th Percentile – 25th Percentile
25th Percentile (Q1)
75th Percentile
(Q3)
Median
(Q2)
Interquartile Range
(IQR)
Maximum (Minimum Value in the Data, Q1 – I.5*IQR)
Minimum (Maximum Value in the Data, Q3 + I.5*IQR)
Minimum Value in the Data
Maximum Value in the Data
Potential Outliers
Potential Outliers
Notes: The diagram above describes how to read a box plot.
The middle part of the plot, or the “interquartile range,” represents the middle quartiles (or the 75th minus the 25th percentile).
The line near the middle of the box represents the median (or middle value of the data set).
The whiskers on either side of the IQR represent the lowest and highest quartiles of the data.
The ends of the whiskers represent the maximum and minimum of the data, and the individual dots beyond the whiskers represent outliers in the data set.

## Slide 308: How to Use SigmaXL to Generate a Box Plot
Data File: “Box Plot” tab in “Sample Data.xlsx”
Steps to render a Box Plot in SigmaXL
  Select the entire range of the data
  Click SigmaXL -> Graphical Tools -> Boxplots
  A new window named “Boxplots” pops up with the selected range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window also named “Boxplots” appears
  Select “HtBk” as the “Numeric Data Variables (Y)”
  Check the check box “Show Legend”
  Click “OK>>”
  The Boxplot appears automatically in the new tab “Boxplot (1)”
Notes: The following steps instruct on how to create a box plot using SigmaXL.

## Slide 309: How to Use SigmaXL to Generate a Box Plot

## Slide 310: How to Use SigmaXL to Generate a Box Plot

## Slide 311: Histogram
A histogram is a graphical tool to present the distribution of the data.
The X axis represents the possible values of the variable and the Y axis represents the frequency of the value occurring.
A histogram consists of adjacent rectangles erected over intervals with heights equal to the frequency density of the interval.
The total area of all the rectangles in a histogram is the number of data values.
Notes: A histogram is a graphical tool to help us visualize the distribution of a data set.
The X axis represents the possible values, and the Y axis represents the frequency of occurrence of these values.
A histogram consists of a series of rectangles, one at each value, for which the height represents the number of data points at each value.

## Slide 312: Histogram
A histogram can also be normalized. In this case, the X axis still represents the possible values of the variable, but the Y axis represents the percentage of observations that fall into each interval on the X axis.
The total area of all the rectangles in a normalized histogram is 1.
With the histogram, we have a better understanding of the shape, location, and spread of the data.
Notes: Instead of the Y-axis representing the frequency of data at each value, we can also plot a percentage of observations at each value.

## Slide 313: Histogram
Histogram with frequency (count) as the Y axis
Normalized histogram with proportion (probability) as the Y axis
Notes: This is a comparison of a regular histogram, which has frequency (or count) represented on the Y axis and a normalized histogram, which has proportion (or probability) represented on the Y axis.

## Slide 314: How to Use SigmaXL to Generate a Histogram
Data File: “Histogram” tab in “Sample Data.xlsx”
Steps to render a histogram in SigmaXL
  Select the entire range of data
  Click SigmaXL -> Graphical Tools -> Histograms & Descriptive Statistics
  A new window named “Histograms & Descriptive” pops up with the selected range of data appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Descriptive Statistics” appears
  Select “HtBk” as the “Numeric Data Variables (Y)”
  Click “OK>>”
  The histogram appears in the new tab “Hist Descript (1)”
Notes: The following steps instruct on how to create a histogram using SigmaXL.

## Slide 315: How to Use SigmaXL to Generate a Histogram

## Slide 316: How to Use SigmaXL to Generate a Histogram
Histogram

## Slide 317: Scatter Plot
A scatter plot is a diagram to present the relationship between two variables of a data set.
A scatter plot consists of a set of data points.
On the scatter plot, a single observation is presented by a data point with its horizontal position equal to the value of one variable and its vertical position equal to the value of the other variable.
Notes: A scatter plot is a great way to demonstrate a relationship between two variables.
Each data point on a scatter plot represents a coordinate. There is a data point at each observation where the coordinates represent the horizontal axis and vertical axis.

## Slide 318: Scatter Plot
A scatter plot helps to understand:
  Whether the two variables are related to each other or not
  How is the strength of their relationship
  What is the shape of their relationship
  What is the direction of their relationship
  Whether outliers are present.
Notes: A scatter plot tells us about the relationship between two variables:
If a relationship exists
The strength of the relationship
The shape (i.e., linear or non-linear)
The direction (positive or negative; the values go up/down together or they relate inversely)
If there are outliers that clearly do not follow the relationship.

## Slide 319: How to Use SigmaXL to Generate a Scatter Plot
Data File: “Scatter Plot” tab in “Sample Data.xlsx”
Steps to render a histogram in SigmaXL
  Select the entire range of data (both “MPG” and “weight”)
  Click SigmaXL -> Graphical Tools -> Scatter Plots
  A new window named “Scatter Plots” pops up with the selected range of data appearing in the box under “Please select your data”
  Click “Next>>”
  A new window also named “Scatter Plots” appears
  Select “MPG” as the “Numeric Response (Y)”
  Select “weight” as the “Numeric Predictor (X1)”
  Click “OK>>”
  The scatterplot appears in the new tab “Scatterplot (1)”
Notes: Here are instructions for creating a scatter plot in SigmaXL.

## Slide 320: How to Use SigmaXL to Generate a Scatter Plot

## Slide 321: How to Use SigmaXL to Generate a Scatter Plot

## Slide 322: Run Chart
A run chart is a chart used to present the data in time order. It captures the process performance over time.
The X axis of the run chart indicates the time and the Y axis indicates the observed values.
Run chart looks similar to control charts except that a run chart does not have control limits plotted. It is easier to produce a run chart than a control chart.
It is often used to identify the anomalies in the data and discover the pattern of data changing over time.
Notes: A run chart is similar to a scatter plot in that it shows the relationship between X and Y, but is special because it shows how the Y variable changes with an X variable of time.
It is a great tool to see how a process performs over time. It helps to identify patterns in the data, or see if there are trends or anomalies.

## Slide 323: How to Plot a Run Chart in SigmaXL
Steps to plot a run chart in SigmaXL:
  Data File: “Run Chart” tab in “Sample Data.xlsx”
  Select the entire range of the data (“Measurement”, “Cycle” and “Trend”). In this first example, let’s select the data in column “Measurement’. We will use the other two columns later.
  Click SigmaXL -> Graphical Tools -> Run Chart
  A new window named “Run Chart” pops up with the selected range of data appearing in the box under “Please select your data”
  Click “Next>>”
  A new window also named “Run Chart” appears
  Select “Measurement” as the “Numeric Data Variable (Y)”
  Click “OK”
  The run chart appears automatically in the tab “Run Chart (1)”
Notes: Here are the instructions for creating a run chart in SigmaXL.

## Slide 324: How to Plot a Run Chart in SigmaXL

## Slide 325: Run Chart Example
Run chart is used to identify the trend, cycle, seasonal pattern, abnormality in the data.
  The time series in this chart appear stable.
  There are no extreme outliers, trending or seasonal patterns.
Notes: In this example, the data seems to vary randomly over time. There don’t seem to be any cyclical (or seasonal) patterns, and no extreme outliers.
Let’s see some other examples that look different.

## Slide 326: Run Chart Example
Create another run chart using the data listed in column “Cycle” in the “Run Chart” tab of “Sample Data.xlsx”.
In this example, the data clearly is exhibiting a pattern. It could be something that is “seasonal”, or could be something cyclical in a process.
Imagine that the data points are monthly, and this is showing us a process performing over the period of 2.5 years. Perhaps this represent the number of customers buying new homes. The home buying market tends to peak in the summer months and dies down in the winter.
Seasonal Pattern
Notes: In this example, the data clearly is exhibiting a pattern. It could be something that is “seasonal”, or could be something cyclical in a process.
Imagine that the data points are monthly, and this is showing us a process performing over the period of 2.5 years. Perhaps this represent the number of customers buying new homes. The home buying market tends to peak in the summer months and dies down in the winter.

## Slide 327: Run Chart Example
Create another run chart using the data listed in column “Trend” in the “Run Chart” tab of “Sample Data.xlsx”.
Trending Pattern
Notes: In this example the process starts out randomly, but after the 7th data point almost every data point has a lower value than the one before it. Clearly a downward trend.
What might this represent? A process winding down. Product sales at the end of its life cycle. Defects coming down after introducing a process improvement.

## Slide 328: 2.3 MSA (Measurement System Analysis)

## Slide 329: Black Belt Training: Measure Phase
2.1 Process Definition 2.1.1 Cause and Effect Diagrams 2.1.2 Cause and Effects Matrix 2.1.3 Process Mapping 2.1.4 FMEA: Failure Modes and Effects Analysis
2.1.5 Theory of Constraints
2.2 Six Sigma Statistics 2.2.1 Basic Statistics 2.2.2 Descriptive Statistics 2.2.3 Distributions and Normality 2.2.4 Graphical Analysis
2.3 Measurement System Analysis 2.3.1 Precision and Accuracy 2.3.2 Bias, Linearity, and Stability 2.3.3 Gage R&R 2.3.4 Variable and Attribute MSA
2.4 Process Capability 2.4.1 Capability Analysis 2.4.2 Concept of Stability 2.4.3 Attribute and Discrete Capability 2.4.4 Monitoring Techniques

## Slide 330: 2.3.1 Precision and Accuracy

## Slide 331: What is Measurement System Analysis
Measurement System Analysis (MSA) is a systematic method to identify and analyze the variation components in the measurement.
It is a mandatory step in any Six Sigma project to ensure the data are reliable before making any data-based decisions.
The MSA is the check point of data quality before we start any further analysis and draw any conclusions from the data.
Notes: When you use data to make decisions, it is important to have confidence in how the data are created. If your data is unreliable, then you may as well have no data at all.
Measurement system analysis is a method to determine how much variation is in a measurement system. MSA is a mandatory, but often looked-over step in a Six Sigma project.
It is critical to check the quality of the data before drawing any conclusions from the data.

## Slide 332: Data-Based Analysis
Here are some examples of data-based analysis where MSA is the prerequisite:
  Correlation analysis
  Regression analysis
  Hypothesis testing
  Analysis of variance
  Design of experiments
  Multivariate analysis
  Statistical process control.
Notes: These are just a few examples of analytical tools that require that an MSA be done. You will see where and how these tools are used later, but it is critical that the data represent variation in the process and not in the measurement system.

## Slide 333: Measurement System
A measurement system is a process to obtain data.
Y (output of the measurement system)
  Observed values
X’s (inputs of the measurement system)
  True values
  Measurement errors
Measurement System
Inputs (Xs)
Output (Y)
Notes: It is important for us to start with understanding what a measurement system is.
It is a process for us to obtain data about a process.
However, our data are the observed values for a process, but there are two inputs for a measurement system: the true values of whatever is being measured and the measurement errors introduced by the measurement system.

## Slide 334: Measurement Errors
Observed Value = True Value + Measurement Error
True Value
  The actual value we are interested to measure
  It reflects the true performance of the process we are measuring
Measurement Error
  The errors brought in by measurement system
Observed Value
  The observed/measured value obtained by the measurement system
Notes: To be clear, let us define the terms we introduced on the previous page.
As we said, the observed value is equal to the true value plus the measurement error.
The true value is what we are ultimately trying to determine through the measurement system. It tells us how the process is performing.
The measurement error is the variation introduced by the measurement system we are using.
Finally, the observed value is what the measurement system is telling us.

## Slide 335: Measurement Errors
Types of Observed Values:
  Continuous measurements
    Weight
    Height
    Money
  Discrete measurements
    Red/Yellow/Green
    Yes/No
    Ratings of 1–10
A variable MSA is designed for continuous measurements and an attribute MSA is for discrete measurements.
Notes: There are different types of measurement systems analyses used for different types of measurements.
There are two types of measurement: continuous and discrete.
When trying to understand errors with continuous measurements we use a variable MSA; and for discrete measurements we use an attribute MSA.

## Slide 336: Measurement Errors
Sources of measurement errors:
  Human
  Environment
  Equipment
  Sample
  Process
  Material
  Method.
Fishbone diagrams can help to brainstorm the potential factors affecting the measurement system.
Notes: When you look at all of these sources for measurement errors, it should be evident why it is important to do an MSA. There are so many ways to introduce error to a measurement system.
Human error – think of reading a ruler or a scale, or think about systems where a person has to make a qualitative judgment.
Environment – sometimes the temperature of the air or humidity can effect how a measurement system reads or the equipment itself may need to be calibrated from time to time.
Sampling can introduce variation based on how/where/when we choose to sample a process.
When doing a measurement system analysis, sometimes it helps to brainstorm possible sources of measurement system errors – a fishbone diagram is perfect for this.

## Slide 337: Measurement Errors
The more errors the measurement system brings in, the less reliable the observed values are.
A valid measurement system brings in minimum amount of measurement errors.
The goal of MSA is to qualify the measurement system by quantitatively analyzing its characteristics.
Notes: So why is important to understand measurement error?
The more errors that exist within a measurement system, the less reliable the measurements (or observed values) are. Nobody wants to make decisions based on unreliable data.
A good measurement system is one that minimizes the amount of error.
Ultimately, the goal of a measurement systems analysis is to understand how much error exists in the system by analyzing the characteristics of the system. Then one can make a decision as to whether the system needs to be changed or is reliable enough.

## Slide 338: Characteristics of a Measurement System
Any measurement systems can be characterized by two aspects:
  Accuracy (location related)
  Precision (variation related).
A valid measurement system is both accurate and precise.
  Being accurate does not guarantee the measurement system is precise.
  Being precise does not guarantee the measurement system is accurate.
Notes: You might ask, what are the characteristics of a measurement system?
There are two attributes that can describe any measurement system, accuracy and precision, but having one characteristic has no bearing on the other.
A valid measurement system has both attributes – it is accurate AND precise.

## Slide 339: Accuracy vs. Precision
Accuracy:
  The level of closeness between the average observed value and the true value
  How well the observed value reflects the true value.
Precision:
  The spread of measurement values
  How consistent the repeated measurements deliver the same values under the same circumstances.
Notes: Here we define what each attribute means:
Accuracy describes how close the average observed value is to the true value for what is being measured.
Precision describes how close or repeatable the measurement is.

## Slide 340: Accuracy vs. Precision
Accurate and precise
  high accuracy and high precision
Notes: In this visual, think of the center of the target as the “true value” and the black dots as “observed values.”
In this example, all six measurements are located at the center of the target and are grouped tightly together. This means that the measurements are both accurate AND precise.

## Slide 341: Accuracy vs. Precision
Accurate and not precise
  high accuracy and low precision
Notes: In this example, all the observations are located around the center of the target, but are spread much further apart than in the last example.
This measurement system would be described as accurate, but NOT precise.

## Slide 342: Accuracy vs. Precision
Precise and not accurate
  high precision and low accuracy
Notes: In this example, all the observations are grouped closely together, but are NOT located near the center of the target.
This system is precise, but NOT accurate.

## Slide 343: Accuracy vs. Precision
Not accurate and not precise
  low accuracy and low precision
Notes: This example shows a system that is neither accurate nor precise.
The observations are not located around the center AND they are spread far apart from each other.

## Slide 344: MSA Conclusions
If the measurement system is considered both accurate and precise, we can start the data-based analysis or decision making.
If the measurement system is either not accurate or not precise, we need to identify the factor(s) affecting it and calibrate the measurement system until it is both accurate and precise.
Notes: Upon completing an MSA, you will reach one of two possible conclusions.
One conclusion is that the measurement system is both accurate AND precise, meaning you can start analyzing the data for the purpose of making decisions.
Another possibility is that the measurement system is not reliable. Either it is not accurate/precise or is neither accurate nor precise.
If the system is not reliable, the next step is to identify the factors that are causing the problem and calibrate the system until it provides the accuracy and precision that are needed.

## Slide 345: Stratification of Accuracy and Precision
Accuracy
  Bias
  Linearity
  Stability
Precision
  Repeatability
  Reproducibility
Notes: In the next sections we will talk about different categories of accuracy and precision.

## Slide 346: 2.3.2 Bias, Linearity and Stability
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 347: 2.3.3 Gage R&R

## Slide 348: Repeatability
Repeatability evaluates whether the same appraiser can obtain the same value multiple times when measuring the same object using the same equipment under the same environment.
It refers to the level of agreement between the repeated measurements of the same appraiser under the same condition.
Repeatability measures the inherent variation of the measurement instrument.
Notes: Repeatability evaluates the ability of an appraiser to repeat the measurement and get the same value when observing the same object several times, using the same equipment.
The measure of repeatability is the level of agreement between those several observations. It measures the inherent variation of the measurement system.

## Slide 349: Reproducibility
Reproducibility evaluates whether different appraisers can obtain the same value when measuring the same object independently.
It refers to the level of agreement between different appraisers.
It is not caused by the inherent variation of the measurement instrument. It reflects the variability caused by different appraisers, locations, gauges, environments etc.
Notes: Reproducibility assesses the ability of different appraisers to obtain the same value when measuring the same object.
The measure of reproducibility is the level of agreement between two appraisers. So while repeatability is inherent to the measurement system, reproducibility is not; it can be caused by different people, in different places, using different instruments, in different environments.

## Slide 350: Gauge R&R
Gauge R&R (i.e. Gauge Repeatability & Reproducibility) is a method to analyze the variability of a measurement system by partitioning the variation of the measurements using ANOVA (Analysis of Variance).
Gauge R&R only addresses the precision of a measurement system.
Notes: Gauge R&R is a common method to analyze the precision of a measurement system.
The variation is analyzed using the Analysis of Variance (ANOVA).
Remember that gauge R&R measures only the precision of the measurement system.

## Slide 351: Gauge R&R
Data collection of a gauge R&R study:
  let k appraisers measure n random samples independently and repeat the process p times.
Different appraisers perform the measurement independently.
The order of measurement (e.g. sequence of samples and sequence of appraisers) is randomized.
Notes: A gauge R&R is a controlled study in which multiple appraisers are given multiple, random samples to measure, and they must repeat the process multiple times. You can see the number of each factor can be varied, as evidenced by the representative letters k, n, and p.
To conduct the study, each of the appraisers will measure each sample independently. The order in which they measure must be randomized.

## Slide 352: Gauge R&R
The potential sources of variance in the measurement:
  Appraisers:
  Parts:
  Appraisers × Parts:
  Repeatability:
Variance Components
Notes: As can be seen in this equation for total measurement variance, there are several components: the appraisers, the parts being measured, the interaction between the appraisers and parts, and the repeatability.

## Slide 353: Gauge R&R
A valid measurement system has low variability in both repeatability and reproducibility so that the total variability observed can reflect the true variability in the objects (parts) being measured.
Gauge R&R variance reflects the precision level of the measurement system.
where
Notes: As you can see here, we can also show the total variance of the measurement system is a function of the reproducibility, the repeatability, and the variance in parts. It ties back to the equation on the previous page when you substitute variance in the appraisers and the variance in interaction between appraisers and parts with reproducibility.
The goal is to minimize reproducibility variance and repeatability variance so you are only left with variance in parts – the variance in the parts is the “true” variance.
The precision of the measurement system is represented by the sum of the repeatability variance and reproducibility variance.

## Slide 354: Gauge R&R
Variation Components
where
Z0 is a sigma multiplier that assumes a specific confidence level in the spread of the data.
Notes: The variation of each component can be represented by the standard deviation (or sigma) for each component multiplied by Z(0), which is a sigma multiplier that assumes a specific confidence level for the spread of the data.
This is important because we will use the variation to calculate each component’s contribution to the total measurement variation of the system.

## Slide 355: Gauge R&R
The percentage of variation R&R contributes to the total variation in the measurement:
where
Measurement System | % Study Var | % Contribution | Distinct Categories
Acceptable | 10% or less | 1% or Less | 5 or Greater
Marginal | 10% - 30% | 1% - 9% | 
Unacceptable | 30% or Greater | 9% or Greater | Less than 5
Notes: The goal for this calculation is to determine how much variation is contributed by repeatability and reproducibility variation.
As you can imagine, the lower the contribution from these components the better, but there are some guidelines for how to assess the quality of the measurement system:
Less than 10% – R&R contribution is satisfactory.
10–30% – is a bit tougher and one must consider risks and tradeoffs before deciding if the measurement system is adequate.
Over 30% – is unacceptable.

## Slide 356: 2.3.4 Variable and Attribute MSA

## Slide 357: Variable Gage R&R
Whenever something is measured repeatedly or by different people or processes, the results of the measurements will vary. Variation comes from two primary sources:
  Differences between the parts being measured
  The measurement system.
We can use a gage R&R to conduct a measurement system analysis to determine what portion of the variability comes from the parts and what portion comes from the measurement system.
There are key study results that help us determine the components of variation within our measurement system.
Notes: As we have learned on the previous pages, variation in measurements comes from two main sources: from the actual objects being measured, and from the measurement system.
We can use a variable gage R&R” study to determine how much variation comes from the objects (or parts) and how much comes from the measurement system.
We will now look at the key measures from this type of study to help us understand which components are driving the variation.

## Slide 358: Key Measures of a Variable Gage R&R
%Contribution: The percent of contribution for a source is 100 times the variance component for that source divided by the total variation.
%Study Var (6*SD): The percent of study variation for a source is 100 times the study variation for that source divided by the total variation.
%Tolerance (SV/Tolerance): The percent of spec range taken up by the total width of the distribution of the data based on variation from that source.
Distinct Categories: The number of distinct categories of parts that the measurement system is able to distinguish. If a measurement system is not capable of distinguishing at least five types of parts, it is probably not adequate.
Notes: The measures described on this slide require understanding to interpret the results of a variable gage R&R study.
Contribution is the amount that each component “contributes” toward the total variation. To calculate a percentage, just divide the variance for the component by the total variance and multiply by 100.
The percent study variation is calculated by dividing the study variation for the source by the total variation and then multiply by 100.
The percent of tolerance gives us an idea how much “wiggle room” we have within spec limits. The calculation tells us what percent of the spec range is consumed by the variation from that source.
Each measurement system should be capable of distinguishing at least 5 types of parts.
This should become more clear as we walk through examples.

## Slide 359: Variable Gage R&R Guidelines (AIAG)
Percent Tolerance and Percent Study Variation
  10% or less – Acceptable
  10% to 30% – Marginal
  30% or greater – Unacceptable
Percent Contribution
  1% or less – Acceptable
  1% to 9% – Marginal
  9% or greater – Unacceptable
Distinct Categories
  Look for five or more distinct categories to indicate that your measurement system is acceptable.
Notes: The following guidelines should be used to assess a measurement system through variable gage R&R.

## Slide 360: Guidelines for Distinct Categories
Number of Categories | Conclusion
Distinct Categories = 1 | Measurement system cannot discriminate between parts
Distinct Categories = 2 | Measurement system can only distinguish between high/low or big/small
Distinct Categories = 3 or 4 | Measurement system is of little or no value
Distinct Categories = 5+ | According to AIAG, the measurement system can acceptably discriminate parts
Distinct categories is the number of categories of parts that your measurement system can distinguish. If it is below five, it is likely not able to distinguish between parts.
Notes: As we indicated earlier, a measurement system should be able to distinguish at least five different categories. The table provides a little more definition for values less than five.
A 1 means the system cannot discriminate between parts.
A 2 means the system has very coarse distinction capability; it can only tell between high/low or big/small.
A 3 or 4 still means the system does not have much value.
A 5 or better means the system has acceptable ability to discriminate between parts.

## Slide 361: Use SigmaXL to Implement a Variable MSA
Data File: “Variable MSA” tab in “Sample Data.xlsx” (an example in the AIAG MSA Reference Manual, 3rd Edition)
Step 1: Initiate the MSA study
  Click on SigmaXL -> Measurement Systems Analysis -> Create Gauge R&R (Crossed) Worksheet
  A new window named “Create Gauge R&R (Crossed) Worksheet” appears
  Enter 10 as the “Number of Parts/Samples”
  Enter 3 as the “Number of Operators/Appraisers”
  Enter 3 as the “Number of Replicates/Trials”
  Uncheck the checkboxes for both “Randomize Parts/Sample” and “Randomize Operators/Appraisers”
  Click “OK>>”
  A new tab named “Gage R&R (Crossed) WKS” is generated.
Notes: We will now use SigmaXL to analyze a measurement using variable MSA. Follow these instructions to create the data template.

## Slide 362: Use SigmaXL to Implement a Variable MSA
Notes: You can use these visuals to navigate through the proper windows in SigmaXL.

## Slide 363: Use SigmaXL to Implement a Variable MSA
Notes: You can use these visuals to navigate through the proper windows in SigmaXL.

## Slide 364: Use SigmaXL to Implement a Variable MSA
Step 2: Data collection
  In the newly generated tab “Gage R&R (Crossed) WKS”, SigmaXL has provided the template which we organize the data
  In the “Variable MSA” tab in “Sample Data.xlsx”, there are all the measurement data collected by three operators (i.e. operator A, B and C). The data are listed in the same standardized order as the tab “Gage R&R (Crossed) WKS”.

## Slide 365: Use SigmaXL to Implement a Variable MSA
Step 3: Enter the data into the tab “Gage R&R (Crossed) WKS”
  Transfer the data from the “Measurement” column in “Variable MSA” tab of “Sample Data.xlsx” to the “Measurement” column in “Gage R&R (Crossed) WKS” tab.
Notes: Now transfer the data into the measurement column of the Gage R&R (crossed) template.

## Slide 366: Use SigmaXL to Implement a Variable MSA
Step 4: Implement Gauge R&R
  Click SigmaXL -> Measurement Systems Analysis -> Analyze Gage R&R (Crossed)
  A new window named “Analyze Gage R&R (Crossed)” appears with the data range automatically selected in the box right below “Please select your data”
  Click “Next>>”
  A new window also named “Analyze Gauge R&R (Crossed)” pops up.
  Select “Part” column as “Part”
  Select “Operator” column as “Operator”
  Select “Measurement” column as “Measurement”
  Enter 5.15 as the “Standard Deviation Multiplier” and enter 95% as the “Confidence Level”.
  Click “OK”
  A new tab named “Analyze Gage R&R (1)” appears automatically.
Notes: Now you can actually run the Gauge R&R analysis. Just follow these instructions.

## Slide 367: Use SigmaXL to Implement a Variable MSA

## Slide 368: Use SigmaXL to Implement a Variable MSA
5.15 is the recommended standard deviation multiplier by the Automotive Industry Action Group (AIAG). It corresponds to 99% of data in the normal distribution. If we use 6 as the standard deviation multiplier, it corresponds to 99.73% of the data in the normal distribution.
Confidence Level | Sigma Multiplier
90% | 3.29
95% | 3.92
99% | 5.15
99.73% | 6
Notes: Take note of the confidence levels and the corresponding Sigma multiplier. We will use the 5.15, which is a recommended multiplier by the Automotive Industry Action Group.

## Slide 369: Use SigmaXL to Implement a Variable MSA
Step 4: Analyze the MSA results
The percentage of variation R&R contributes to the total variation is 27.86% and the precision level of this measurement system is not good. Actions are required to calibrate the measurement system.
Note: The tab “Analyze Gage R&R (1)” in SigmaXL covers the detailed calculation of the sources of variation and also variance components.

## Slide 370: Use SigmaXL to Implement an Attribute MSA
Data File: “Attribute MSA” tab in “Sample Data.xlsx” (an example in the AIAG MSA Reference Manual, 3rd Edition)
Steps in SigmaXL to run an attribute MSA
Notes: Now we’ll do an example with an attribute MSA. Follow these instructions.

## Slide 371: Use SigmaXL to Implement an Attribute MSA
  Step 1: Organize the original data into four columns (“Part”, “Reference”, “Appraiser” and “Assessed Result”)
  Select the entire range of the original data (“Part”, “Reference”, “Appraiser A”, “Appraiser B” and “Appraiser C” columns)
  Click SigmaXL -> Data Manipulation -> Stack Subgroups Across Rows
  A new window named “Stack Subgroups” pops with the selected data range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Stack Subgroups Across Rows” appears
  Select “Appraiser A”, “Appraiser B” and “Appraiser C” as “Numeric Data Variables”
  Select “Part” and “Reference” as the “Additional Category Columns”
  Enter “Assessed Result” as the “Stacked Data (Y) Column Heading (Optional)
  Enter “Appraiser” as the “Category (X) Column Heading (Optional)”
  Click “OK>>”
  The stacked data are created in a new worksheet.

## Slide 372: Use SigmaXL to Implement an Attribute MSA

## Slide 373: Use SigmaXL to Implement an Attribute MSA

## Slide 374: Use SigmaXL to Implement an Attribute MSA
Step 2: Run MSA using SigmaXL
  Select the entire range of the data (“Part”, “Reference”, “Appraiser” and “Assessment Result” columns)
  Click SigmaXL -> Measurement Systems Analysis -> Attribute MSA (Binary)
  A new window named “Attribute MSA (Binary)” pops with the selected data range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Attribute MSA (Binary)” appears
  Select “Part” column as “Part/Sample”
  Select “Appraiser” column as “Appraiser”
  Select “Assessed Result” column as “Assessed Result”
  Select “1” as “Good Level”
  Click “OK”
  The MSA results appear in the newly generated tab “Att_MSA_Bin”.

## Slide 375: Use SigmaXL to Implement an Attribute MSA

## Slide 376: Use SigmaXL to Implement an Attribute MSA
Within Appraiser Agreement Percent: the agreement percentage within each individual appraiser.
Each Appraiser vs. Standard Agreement Percent: the agreement percentage between each appraiser and the standard. It reflects the accuracy of the measurement system.
Notes: The rater scores represent how the raters agree with themselves. Appraiser A, for instance, agreed with himself on 84% of the measurements made.

## Slide 377: Use SigmaXL to Implement an Attribute MSA
Between Appraiser Agreement Percent: the agreement percentage between different appraisers.
All Appraisers vs. Standard Agreement Percent: overall agreement percentage of both within and between appraisers. It reflects how precise the measurement system performs.
Notes: Of the 50 total measurements performed, for 78% of those (39) the appraisers agreed with both themselves and the other appraisers.

## Slide 378: Use SigmaXL to Implement an Attribute MSA
Kappa statistic is a coefficient indicating the agreement percentage above the expected agreement by chance.
Kappa ranges from -1 (perfect disagreement) to 1 (perfect agreement).
When the observed agreement is less than the chance agreement, Kappa is negative.
When the observed agreement is greater than the chance agreement, kappa is positive.
Rule of Thumb: If Kappa is greater than 0.7, the measurement system is acceptable. If Kappa is greater than 0.9, the measurement system is excellent.
Notes: On the next slide we will look at the Kappa statistic as an output of the MSA.
The goal of the Kappa statistic is to measure how likely it is that there is agreement between and within raters purely by chance or not.
Kappa values range from -1 to 1, where negative values mean that the observed agreement is less than the chance agreement…and positive values indicates that the observed agreement is greater than the chance agreement.
Rule of thumb is that is Kappa is greater than 0.7, then the measurement system is acceptable, and greater than 0.9 is excellent

## Slide 379: Use SigmaXL to Implement an Attribute MSA
Kappa statistic of the agreement within each appraiser
Kappa statistic of the agreement between individual appraiser and the standard
Notes: In all cases the Kappa indicates that the measurement system is acceptable.

## Slide 380: Use SigmaXL to Implement an Attribute MSA
Kappa statistic of the agreement between appraisers
Kappa statistic of the overall agreement between appraisers and the standard

## Slide 381: 2.4 Process Capability

## Slide 382: Black Belt Training: Measure Phase
2.1 Process Definition 2.1.1 Cause and Effect Diagrams 2.1.2 Cause and Effects Matrix 2.1.3 Process Mapping 2.1.4 FMEA: Failure Modes and Effects Analysis
2.1.5 Theory of Constraints
2.2 Six Sigma Statistics 2.2.1 Basic Statistics 2.2.2 Descriptive Statistics 2.2.3 Distributions and Normality 2.2.4 Graphical Analysis
2.3 Measurement System Analysis 2.3.1 Precision and Accuracy 2.3.2 Bias, Linearity, and Stability 2.3.3 Gage R&R 2.3.4 Variable and Attribute MSA
2.4 Process Capability 2.4.1 Capability Analysis 2.4.2 Concept of Stability 2.4.3 Attribute and Discrete Capability 2.4.4 Monitoring Techniques

## Slide 383: 2.4.1 Capability Analysis

## Slide 384: What is Process Capability?
The process capability measures how well the process performs to meet given specified outcome.
It indicates the conformance of a process to meet given requirements or specifications.
Capability analysis helps to better understand the performance of the process with respect to meeting customer’s specifications and identify the process improvement opportunities.
Notes: Process capability is a term used to describe how well a process can operate within specific parameters, or how it meets a given specified outcome.
For example, if a product is expected to fall within certain specification limits, capability is a measure of how often it can meet those specifications.

## Slide 385: Process Capability Analysis Steps
Step 1: Determine the metric or parameter to measure and analyze.
Step 2: Collect the historical data for the parameter of interest.
Step 3: Prove the process is statistically stable (i.e., in control).
Step 4: Calculate the process capability indices.
Step 5: Monitor the process and ensure it remains in control over time. Update the process capability indices if needed.
Notes: To analyze process capability, follow these steps:
First of all, choose the process metric that is to be analyzed.
Second, collect data for the process metric.
Third, determine if the process is stable. It must be stable to get a true read on process capability.
Fourth, calculate process capability indices.
Fifth, monitor the process over time and ensure it remains in control.
The following pages describe in more detail what all these terms mean.

## Slide 386: Process Capability Indices
Process capability can be presented using various indices depending on the nature of the process and the goal of the analysis.
Popular process capability indices:
  Cp
  Pp
  Cpk
  Ppk
  Cpm
Notes: There are different indices that can be used to describe process capability.

## Slide 387: Cp
Cp stands for capability of the process.
where
USL and LSL are the upper and lower specification limits.
n is the sample size.
Notes: The Cp index is process capability. It can be calculated by dividing the difference between the upper and lower spec limits by 6 times sigma (within).
It assumes the process mean is centered between the spec limits and essentially is the ratio of the distance between the spec limits to 6 process standard deviations.
Obviously, the higher this value the better, because it means you can fit the process variation between the spec limits more easily.

## Slide 388: Cp
Cp measures the process’ potential capability to meet the two-sided specifications.
It does not take the process average into consideration.
High Cp indicates the small spread of the process with respect to the spread of the customer specifications.
Cp is recommended when the process is centered between the specification limits.
Cp works when there are both upper and lower specification limits.
Notes: Cp measures the capability of a process to meet two-sided specifications (meaning it has upper spec and lower spec limits).
It assumes the average is centered in the process, or basically it does not take the average into account.
The higher Cp the better, meaning the spread of the process is smaller relative to the spread of the specifications.
Since it does not take the average into account, it is best to use Cp when the process is actually centered between the customer’s spec limits.

## Slide 389: Pp
Pp stands for performance of the process.
where
USL and LSL are the upper and lower specification limits.
n is the sample size.
Notes: The Pp index is the performance of the process. It can be calculated by dividing the difference between the upper and lower spec limits by 6 times sigma (overall).
Like Cp, it assumes the process mean is centered between the spec limits and essentially is the ratio of the distance between the spec limits to 6 process standard deviations.
Obviously, the higher this value the better, because it means you can fit the process variation between the spec limits more easily.

## Slide 390: Pp
Similar to Cp, Pp measures the capability of the process to meet the two-sided specifications.
It only focuses on the spread and does not take the process centralization into consideration.
It is recommended when the process is centered between the specification limits.
Cp considers the within-subgroup standard deviation and Pp considers the total standard deviation from the sample data.
Pp works when there are both upper and lower specification limits.
Notes: The assumptions for Pp are similar to Cp, with the exception of the standard deviation used to calculate it.
The difference between Pp and Cp is how they take into account process decentralization.
Cp considers within subgroup standard deviation, but Pp considers the total standard deviation from the sample data.
Pp is a more conservative method for determining capability because it considers the total variation of a process instead of a subgroup of data.

## Slide 391: Cpk
Cpk stands for the capability of the process with a k factor adjustment.
where
μ is the process mean; n is the sample size.
USL and LSL are the upper and lower specification limits.
Notes: Cpk is process capability with a “k factor adjustment.”
The m is essentially the center point between the spec limits (it is calculated like an average).
When calculating k, the numerator is the absolute value of the difference between the center point between the spec limits (m) and the process mean (μ); the denominator is half the distance between the specs.
As you can guess from the calculation of k, it takes into consideration the location of the mean between the spec limits.

## Slide 392: Cpk
The formulas to calculate Cpk can also be expressed as follows:
where
USL and LSL are the upper and lower specification limits.
Notes: The formula for Cpk can also be expressed in another way.
The expression for Cpk is indicating that the limiting factor is which spec limit the mean is closer to. This is why Cpk is the minimum of the two expressions shown on this slide.

## Slide 393: Cpk
Cpk measures the process’ actual capability by taking both the variation and average of the process into consideration.
The process does not need to be centered between the specification limits to make the index meaningful.
Cpk is recommended when the process is not in the center between the specification limits.
When there is only a one-sided limit, Cpk is calculated using Cpu or Cpl.
Notes: As we saw, Cpk considers the process average (and where it is located relative to the spec limits) when determining capability.
If the process is not centered, this index is recommended.
The one-sided method of calculating Cpk is Cpu or Cpl.

## Slide 394: Cpk
Cpk for upper specification limit:
Cpk for lower specification limit:
USL and LSL are the upper and lower specification limits.
μ is the process mean.
Notes: Here you can see the formulas for calculating Cpu and Cpl.

## Slide 395: Ppk
Ppk stands for the performance of the process with a k factor adjustment.
where
USL and LSL are the upper and lower specification limits.
μ is the process mean.
Notes: Ppk is to Pp as Cpk is to Cp.
The k factor is the same used earlier to calculate Cpk.

## Slide 396: Ppk
The formulas to calculate Ppk can also be expressed as follows:
USL and LSL are the upper and lower specification limits.
μ is the process mean. n is the sample size.
Notes: Ppk can also be expressed this way, like Cpk, and the difference is the use of overall process variation instead of within subgroup variation.

## Slide 397: Ppk
Similar to Cpk, Ppk measures the process capability by taking both the variation and the average of the process into consideration.
Ppk solves the decentralization problem Pp cannot overcome.
Cpk considers the within-subgroup standard deviation, while Ppk considers the total standard deviation from the sample data.
When there is only a one-sided specification limit, Ppk is calculated using Ppu or Ppl.
Notes: Just as Pp is a more conservative alternative to Cp, Ppk is a more conservative choice when it is not clear if a rational subgroup variation can be used.

## Slide 398: Ppk
Ppk for upper specification limit:
Ppk for lower specification limit:
USL and LSL are the upper and lower specification limits.
Notes: Variations of Ppk can be calculated when there is only an upper or a lower spec limit.

## Slide 399: Cpm
Cp, Pp, Cpk, and Ppk all consider the variation of the process. Cpk and Ppk take both the variation and the average of the process into consideration when measuring the process capability.
It is possible that the process average fails to meet the target customers require while the process still remains between the specification limits. Cpm (Taguchi’s capability index) helps to capture the variation from the specified target.
Notes: We have learned that the k factor is the difference between Cpk/Ppk and Cp/Pp. They all take into account process variation, but the k factor takes into account the average of the process.
Cpm is another type of capability index to determine how far the process average varies from the specified target.
Cpm is also referred to as “Taguchi’s capability index,” and rather than only telling us if a measurement is good (between the spec limits), it helps us understand how good it is.

## Slide 400: Cpm
Formula to calculate Cpm
USL and LSL are the upper and lower specification limits.
T is the specified target.
μ is the process mean.
Note: Cpm can work only if there is a target value specified.

## Slide 401: Use SigmaXL to Run a Process Capability Analysis
Data File: “Capability Analysis” tab in “Sample Data.xlsx”
Steps in SigmaXL to run a process capability analysis:
  Select the entire range of data (i.e. the column “HtBk”)
  Click SigmaXL -> Process Capability -> Histograms & Process Capability
  A new window named “Histogram & Process Cap” pops up with the selected range of data appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Process Capability” appears
  Select “HtBk” as the “Numeric Data Variables”
  Enter 6 in LSL, 6.5 in T and 7 in USL into the boxes for “Lower Spec Limit”, “Target” and “Upper Spec Limit” respectively
  Click “OK”
  The histogram and the process capability analysis results are in the newly generated tab “Hist Cap (1)”
Notes: This example will walk through how to run a process capability analysis in SigmaXL.

## Slide 402: Use SigmaXL to Run a Process Capability Analysis
Notes: Here are the proper selections for SigmaXL.

## Slide 403: Use SigmaXL to Run a Process Capability Analysis
Process capability indices
Notes: Here in the output of the analysis, you can see where the process capability indices are provided.

## Slide 404: 2.4.2 Concept of Stability
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 405: 2.4.3 Attribute & Discrete Capability

## Slide 406: Process Capability Analysis for Binomial Data
If we are measuring the count of defectives in each sample set to assess the process performance of meeting the customer specifications, we use “%Defective” (percentage of items in the samples that are defective) as the process capability index.
where Ndefectives is the total count of defectives in the samples and Noverall is the sum of all the sample sizes.
Notes: Binomial data means that we have only two options, yes or no/true or false/defective or not defective.
When we are measuring the portion of defective units, we use “%Defective” as the process capability index.
%Defective is given by a very simple calculation: determine the number of defective units divided by the number of units overall.

## Slide 407: Process Capability Analysis for Poisson Data
If we are measuring the count of defects in each sample set to assess the process performance of meeting the customer specifications, we use Mean DPU (defects per unit of measurement) as the process capability index.
where Ndefects is the total count of defects in the samples and Noverall is the sum of all the units in the samples.
Notes: When we are measuring the number of defects per unit (vs. the number of defective units divided by total units), we can measure capability by dividing the number of defects (which can be more than one per unit) by the number of units.

## Slide 408: 2.4.4 Monitoring Techniques

## Slide 409: Capability and Monitoring
In the Measure phase of the project, process stability analysis and process capability analysis are used to baseline the performance of current process.
In the Control phase of the project, process stability analysis and process capability analysis are combined to monitor whether the improved process is maintained consistently as expected.
Notes: Capability and stability are important concepts to grasp in both the Measure and Control phases of a project.
In Measure, these concepts are used to understand the baseline performance of a process. This is our starting point, our basis for improvement.
In the Control phase, these concepts help us to ensure any improvements are sustained over time.

## Slide 410: 3.0 Analyze Phase
Notes: In the Analysis phase, we will use statistical tools to help us make inferences about data. Those tools will help us prove/disprove hypotheses that are formed during the Measure phase, where we brainstorm potential root causes for a problem.
We will discuss how we look at and analyze patterns of variation.
Also, we will discuss how to use hypothesis tests to draw conclusions from data about a process, using probability to drive our decisions instead of “gut feeling.”

## Slide 411: Black Belt Training: Analyze Phase
3.1 Patterns of Variation
  3.1.1 Multi-Vari Analysis
  3.1.2 Classes of Distributions
3.2 Inferential Statistics
  3.2.1 Understanding Inference
  3.2.2 Sampling Techniques and Uses
  3.2.3 Sample Size
  3.2.4 Central Limit Theorem
3.3 Hypothesis Testing
  3.3.1 Goals of Hypothesis Testing
  3.3.2 Statistical Significance
  3.3.3 Risk; Alpha and Beta
  3.3.4 Types of Hypothesis Tests
3.4 Hypothesis Testing: Normal Data
  3.4.1 One and Two Sample T-Tests
  3.4.2 One sample variance
  3.4.3 One Way ANOVA
3.5 Hyp Testing: Non-Normal Data
  3.5.1 Mann-Whitney
  3.5.2 Kruskal-Wallis
  3.5.3 Moods Median
  3.5.4 Friedman
  3.5.5 One Sample Sign
  3.5.6 One Sample Wilcoxon
  3.5.7 One and Two Sample Proportion
  3.5.8 Chi-Squared (Contingency Tables)
  3.5.9 Test of Equal Variances

## Slide 412: 3.1 Patterns of Variation

## Slide 413: Black Belt Training: Analyze Phase
3.1 Patterns of Variation
  3.1.1 Multi-Vari Analysis
  3.1.2 Classes of Distributions
3.2 Inferential Statistics
  3.2.1 Understanding Inference
  3.2.2 Sampling Techniques and Uses
  3.2.3 Sample Size
  3.2.4 Central Limit Theorem
3.3 Hypothesis Testing
  3.3.1 Goals of Hypothesis Testing
  3.3.2 Statistical Significance
  3.3.3 Risk; Alpha and Beta
  3.3.4 Types of Hypothesis Tests
3.4 Hypothesis Testing: Normal Data
  3.4.1 One and Two Sample T-Tests
  3.4.2 One sample variance
  3.4.3 One Way ANOVA
3.5 Hyp Testing: Non-Normal Data
  3.5.1 Mann-Whitney
  3.5.2 Kruskal-Wallis
  3.5.3 Moods Median
  3.5.4 Friedman
  3.5.5 One Sample Sign
  3.5.6 One Sample Wilcoxon
  3.5.7 One and Two Sample Proportion
  3.5.8 Chi-Squared (Contingency Tables)
  3.5.9 Test of Equal Variances

## Slide 414: 3.1.1 Multi-Vari Analysis

## Slide 415: What is Multi-Vari Analysis?
Multi-Vari analysis is a graphic-driven method to analyze the effects of categorical inputs on a continuous output.
  Y: continuous variable
  X’s: discrete categorical variables. One X may have multiple levels.
It studies how the variation in the output changes across different inputs and helps us quantitatively determine the major source of variability in the output.
Multi-Vari charts are used to visualize the source of variation. They work for both crossed and nested hierarchies.
Notes: We begin with Multi-Vari Analysis. We need to understand patterns of variation, and graphical tools are a great way to start.
Multi-Vari is a method to analyze categorical inputs on a continuous output, meaning your X (input) is a discrete category and your Y (output) is a continuous output.
This tool helps us understand visually how an output variable changes with changes in a discrete input variable.
A multi-Vari analysis works for both crossed and nested hierarchies, which we will review shortly.

## Slide 416: Hierarchy
Hierarchy is a structure of objects in which the relationship of objects can be expressed similar to an organization tree.
Each object in the hierarchy is described as above, below, or at the same level as another one.
  If object A is above object B and they are directly connected to each other in the hierarchy tree, A is B’s parent and B is A’s child.
In Multi-Vari analysis, we use the hierarchy to present the relationship between categorical factors (inputs).
Each object in the hierarchy tree indicates a specific level of a factor (input).
There are generally two types of hierarchies: crossed and nested.
Notes: When we talk about the structure of data, we will use the term hierarchy.
Hierarchy is a structure that can be expressed in a way similar to an organizational tree.
Think of hierarchy as a series of parent-child relationships.
In this type of analysis, the hierarchy helps us present the relationship between factors.

## Slide 417: Crossed Hierarchy
In the hierarchy tree, if one child item has more than one parent item at the higher level, it is a crossed relationship.
Notes: In a crossed hierarchy relationship, the child items can be linked to more than one parent.
Consider the blue dot is a school district, the yellow dots are schools, and the green dots are neighborhoods.
In many cities there are choice systems that allow children from the same neighborhood to attend different schools, so the neighborhoods cannot be perfectly nested under a school.

## Slide 418: Nested Hierarchy
In the hierarchy tree, if one child item only has one parent item at the higher level, it is a nested relationship.
Notes: In a nested hierarchy relationship, the child items can be linked to only one parent.
Consider the example of a call center (the blue dot), the yellow dots represent units in the call center, and the green dots represent associates in the unit.
Each associate can only be a part of one unit, and each unit can only be a part of the one site.

## Slide 419: Use SigmaXL to Perform Multi-Vari Analysis
Data File: “Multi-Vari’ tab in “Sample Data.xlsx”
  Case study: ABC company produces 10 kinds of units with different weights. Operators measure the weights of the units before sending them out to customers.
  Multiple factors would have impact on the weight measurement. ABC company wants to have a better understanding on the main source of the variability existing in the weight measurement.
  ABC company randomly selected 3 operators (Joe, John and Jack) each of whom measures the weights of 10 kinds of units. For each kind of unit, there are 3 items sampled.
Notes: We will now use SigmaXL to perform a multi-vari analysis.
Company ABC produces 10 different “units”
Operators measure the units before sending to customers.
The company wants to understand what is the source of variability of the weight measurement.
They select three operators, each of whom measure 3 samples of each of the 10 kinds of “units”.

## Slide 420: Use SigmaXL to Perform Multi-Vari Analysis
Multi-Vari Analysis in SigmaXL:
  Open the “Multi-Vari’ tab in “Sample Data.xlsx”
  Select the range of data that we are interested in analyzing.
  Click SigmaXL -> Graphical Tools -> Multi-Vari ChartsA window named “Multi-Vari Charts” pops up.
  Click on “Next >>” button. A new window also named “Multi-Vari Charts” pops up.
  Select “Measurement” as “Numeric Response (Y)”
  Select “Unit” as “Group Category (X1)”
  Select “Operator” as “Group Category (X2)”
  Click “OK >>”
Notes: Here are the instructions to perform the analysis in SigmaXL.

## Slide 421: Use SigmaXL to Perform Multi-Vari Analysis

## Slide 422: Use SigmaXL to Perform Multi-Vari Analysis
A new spreadsheet with three charts is created.
We call the newly generated charts “Multi-Vari Charts”.
Analyze the charts to determine major sources of the variation

## Slide 423: Interpreting SigmaXL’s Multi-Vari Analysis
    The horizontal line in the center of the chart indicates the group mean of Jack’s measurement.
    The maximum and minimum bars present the range of measurements for each unit. The center bar presents the mean measurement for each unit.
    The red line connects all the center bars together.
    Jack’s Multi-Vari Chart

## Slide 424: Interpreting SigmaXL’s Multi-Vari Analysis
Based on the Multi-Vari Chart, the measurement of units ranges from 0.39 to 1.09.
Jack’s and John’s average measurement stays between 0.79 and 0.89. Joe’s average is slightly low than both Jack’s and Johns.
John has the worst variation when measuring the same kind of unit because John has the highest difference between maximum and minimum bars for any kind of unit.
By observing the red lines of three operators, it seems like all three operators’ measurements follow the same pattern. The operator-to-operator variability is not large.
The unit-to-unit variability is large and it might be the main source of variation in measurements.
Notes: So what does the analysis tell us?
The individual unit measurements range from 0.4 to 1.1…quite a spread.
The group means for the operators are very close together, with Jack’s being slightly lower than the other two.
John has the largest ranges in his unit measurements.
The operators measurements seem to follow the same pattern.
There is great variability between units, so it seems that the unit to unit variability could be the main source of variation.

## Slide 425: Use SigmaXL to Perform Multi-Vari Analysis
To add more features to your Multi-Vari Chart
  Click SigmaXL -> Graphical Tools -> Multi-Vari Options
  A new window named “Multi-Vari Options” pops up.
  In this new widow, you may add grand mean, confidence intervals, medians etc. to the Multi-Vari Chart to further your analysis of variation.

## Slide 426: 3.1.2 Classes of Distribution

## Slide 427: What is Probability?
Probability is the likelihood of an event occurring.
The probability of event A occurring is written as P(A).
Probability is a percentage between 0% and 100%. The higher the probability, the more likely the event will happen.
When probability is equal to 0%, it indicates that the event will take place with no chance.
When probability is equal to 100%, it indicates the event will definitely take place without any uncertainty.
Example of probability: when tossing a coin, there is 50% chance that the head lands face up and 50% chance that the head lands face down.
Notes: Probability is the measure of the likelihood that an event will occur.
It is a number between 0 and 1, or 0% and 100%. 1 or 100% probability means that an event is certain to occur.
The classic example of probability is the coin flip. What is the probability of getting heads up?

## Slide 428: Probability Property
The probability of event A not occurring:
To be, or not to be: that is the question.
William Shakespeare
Notes: This is the notation for how the probability of event A not occurring is written. See the hat on the A?

## Slide 429: Probability Property
The probability of event A OR B OR both events occurring:
If event A and B are mutually exclusive:
and
Notes: The probability of A OR B, OR “A and B” occurring is written as: the probability of A plus the probability of B minus the probability of A AND B.
If the events are mutually exclusive, meaning only one can occur, the probability of A and B occurring is zero.
Consider rolling a die. What is the probability of rolling a 2 or a 4? Because you cannot role more than one value at a time, they are mutually exclusive; therefore, the probability of rolling a 2 or a 4 is written as P(2) + P(4).

## Slide 430: Probability Property
The probability of event A AND B occurring together:
If event A and B are independent of each other:
and
Notes: P(A|B) refers to the conditional probability that event A occurs, given that event B has occurred.

## Slide 431: Probability Property
The probability of event A occurring given event B taking place:
where
Notes: P(A|B) refers to the conditional probability that event A occurs, given that event B has occurred.

## Slide 432: What is Distribution?
Distribution (or probability distribution) describes the range of possible events and the possibility of each event occurring.
In statistical terms, distribution is the probability of each possible value of a random variable when the variable is discrete, or the probability of a value falling in a specific interval when the variable is continuous.
Notes: A probability distribution describes a range of possible events and the probability (or possibility) of each individual event.
Think of an event as a specific numerical value for a random variable, when the variable is discrete.
If the variable is continuous, then the distribution describes the probability of a value falling within a certain range or interval.

## Slide 433: Probability Mass Function
PMF (Probability Mass Function) is a function describing the probability of a discrete random variable equal to a particular value.
Here is the probability mass function chart for a fair die.
Notes: A probability mass function (PMF) describes the probability of a discrete random variable, such as with this example of a fair die.
There are 6 possible outcomes of the die, and with a fair die, each outcome has equal probability.

## Slide 434: Probability Density Function
PDF (Probability Density Function) is a function used to retrieve the probability of a continuous random variable falling within a particular interval.
The probability of a variable falling within a particular region is the integral of the probability density function over the region.
Here is the probability density function chart of a standard normal distribution.
Notes: A probability mass function is to discrete data as a probability density function is to continuous data.
The bars represent the probability of a value occurring within a particular interval.
In this example of a standard normal distribution, there is nearly a 20% chance that a value will fall between 94 and 108.

## Slide 435: Advantages of Distribution
Distributions capture the most basic features of data
  Shape
    Which distribution family may the data belong to?
    Is the data symmetric?
    Are the tails of the data flat?
  Center
    Where is the midpoint of the data?
  Scale
    What is the range of data?
Notes: A distribution is helpful because it gives us information about data.
The shape of the distribution tells us what type of distribution it is and how we should analyze the data.
The symmetry of the distribution tells us the probabilities are the same or different at the low and high end of the range of data values.
The center, or midpoint, tells us what is most likely to occur – average, or median, for example.
The scale refers to how much spread there is in the data – think range, or standard deviation.

## Slide 436: Measures of Skewness and Kurtosis
The shape, center (i.e. location) and scale (i.e. variability) are three basic data characteristics that probability distributions capture.
Skewness and kurtosis are the two more advanced characteristics of the probability distribution.
Notes: As discussed on the previous slide – shape, center, and scale are the three basic characteristics of a probability distribution.

## Slide 437: Skewness
  Skewness is a measure of the asymmetry degree of the probability distribution.
  The mathematical definition of the skewness is
The skewness of a normal distribution is zero.
When the distribution looks symmetric to the left side and the right side of the center point, the skewness is close to zero.
Potential causes of skewness:
  Extreme values exist in the data
  Data have a lower or higher bound.
  where µ3 is the third moment about the mean and σ is the standard deviation.
Notes: Skewness tells us about the symmetry (or lack of symmetry) of the distribution.
For a normal distribution, the skewness value is 0; so when the distribution looks nearly the same on either side of the center, the skewness is close to zero.
The skewness can be caused by extreme values or bounds on one side of the distribution, such as when no negative values are possible.

## Slide 438: Skewness
Left Skew
  Skewness < 0
  The left tail of the distribution is longer than the right tail.
Right Skew
  Skewness > 0
  The right tail of the distribution is longer than the left tail.
Notes: A negative value of skewness indicates that the distribution is left skewed, meaning the left tail is longer than the right. It could be caused by having an upper bound on the distribution.
A positive value of skewness indicates that the distribution is right skewed, meaning the right tail is longer than the left. It could be caused by a lower bound of zero.

## Slide 439: Kurtosis
  Kurtosis is a measure of the peakedness of the probability distribution.
  The mathematical definition of the excess kurtosis is
  The kurtosis of a normal distribution is zero.
  Distributions with a zero excess kurtosis are called mesokurtic.
  The distribution with a high kurtosis has a more distinct peak and fatter, longer tails.
  The distribution with a low kurtosis has a more rounded peak and thinner, shorter tails.
  where µ4 is the fourth moment about the mean and σ is the standard deviation.
Notes: Kurtosis measures the peakedness of the distribution.

## Slide 440: Kurtosis
Leptokurtic
  Excess Kurtosis > 0
  A sharper peak near the mean, declining rapidly, and fatter tails.
Platykurtic
  Excess Kurtosis < 0
  A flatter top near the mean, declining slowly, and thinner tails.
Notes: As you can see, the distribution with excess kurtosis greater than zero looks more narrow, less rounded at its peak vs. the normal distribution. This type of kurtosis is called leptokurtic.
The distribution with excess kurtosis less than zero looks more squat than the normal distribution. The type is called platykurtic.

## Slide 441: Multimodal Distribution
In statistics, a continuous probability distribution with two or more different unimodal distributions is called a multimodal distribution.
A unimodal distribution has only one local maximum which is equal to its global maximum.
A multimodal probability distribution has more than one local maximum.
  Example: a bivariate, multimodal distribution
  (picture source: http://en.wikipedia.org/wiki/Multimodal_distribution)
Notes: A normal distribution is unimodal, meaning it only has one peak (local maximum). However, there are some distributions that have multiple peaks, called multimodal.

## Slide 442: Bimodal Distribution
In statistics, a continuous probability distribution with two different unimodal distributions is called a bimodal distribution.
A bimodal probability distribution has two local maxima.
Example (picture source: http://en.wikipedia.org/wiki/Multimodal_distribution)
By mixing two unimodal distributions with different means, the mixture distribution is not necessarily a bimodal distribution.
The mixture of two normal distributions with the same standard deviation is a bimodal distribution only if the difference between their means is at least twice their common standard deviation.
Notes: In statistics, a probability distribution with two different unimodal distributions is called bimodal (having two local maxima).
When two unimodal distributions with different means come together, they may not necessarily be bimodal. To assess if the distribution is bimodal, the difference between the means of the two distributions must be at least twice their common standard deviation.

## Slide 443: Examples of Discrete Distribution
Binomial Distribution
Poisson Distribution
Notes: Here are two examples of discrete distributions that we will now discuss.

## Slide 444: Binomial Distribution
Assume there is an experiment with n independent trials, each of which only has two potential outcomes (i.e. yes/no, fail/pass). p is the probability of one outcome and (1 – p) is the probability of the other.
Binomial distribution is a discrete probability distribution describing the probability of any outcome of the experiment.
Excel formula for binomial distribution:
  BINOMDIST(number_s, trials, probability_s, cumulative)
Notes: In probability theory and statistics, the binomial distribution is the discrete probability distribution of the number of successes in a sequence of n independent yes/no experiments, each of which yields success with probability p. Such a success/failure experiment is also called a Bernoulli experiment or Bernoulli trial; when n = 1, the binomial distribution is a Bernoulli distribution.
Consider the coin flip example. There are only two possible outcomes of a trial.
The Excel formula will return the probability of a desired result, given the known probability of success. For example, if a batter’s average is 0.300, and we want to know the probability that the batter will get 7 hits out of 10 at-bats. The entry of the formula would look like this: BINOMDIST(7,10,0.3,0), where the 0 will return the probability mass function. The result is 0.009, meaning less than a 1% chance of getting 10 at-bats.

## Slide 445: Binomial Distribution
PMF of Binomial Distribution
the probability of getting k successes in n trials:
Mean of Binomial Distribution
Variance of Binomial Distribution
where
Notes: Here is the formula for calculating the probability mass function. In the example we used, n = 10, k = 7, and p = 0.3. Carrying out the calculations, you will get 0.009.
On this page, you will also calculate the mean of a binomial distribution. For a given number of trials, it is just the number of trials times the probability of success. For our example, the mean is 10 x 0.3 = 3.
For the variance, it is the mean times the difference between 1 minus the probability of success. For our example, the variance is 10 x 0.3 x 0.7 = 2.1

## Slide 446: Poisson Distribution
Poisson distribution is a discrete probability distribution describing the probability of a number of events occurring at a known average rate and in a fixed period of time. The expected number of occurrences in this fixed period of time is λ.
Excel formula for Poisson distribution
  POISSON(x, mean, cumulative)
Notes: In probability theory and statistics, the Poisson distribution is a discrete probability distribution that expresses the probability of a given number of events occurring in a fixed interval of time if these events occur with a known average rate and independently of the time since the last event.
The Greek letter lambda is used to denote the number of occurrences in a fixed interval of time.
The Excel formula is shown here, where x is the number of events for which we are trying to determine the probability, mean is the expected number of events, and the last argument is telling Excel whether to return the PMF or the cumulative Poisson probability.
An example to consider: Let us assume an office worker typically gets 25 e-mails a day, and we want to determine the probability of getting 40 emails, Excel returns the result of 0.001.

## Slide 447: Poisson Distribution
PMF of Poisson Distribution
the probability of getting k occurrences in n trials
Mean of Poisson Distribution
Variance of Poisson Distribution
Notes: Here is the formula for calculating the probability mass function, where lambda is the mean (or expected number of occurrences, 25 in our email example) and also the variance of the distribution.

## Slide 448: Examples of Continuous Distribution
Normal Distribution
Exponential Distribution
Weibull Distribution
Student’s t distribution
Chi-square distribution
F distribution
Notes: We will now talk about different types of continuous distributions.

## Slide 449: Normal Distribution
Normal distribution is a continuous probability distribution describing random variables which cluster around the mean.
Its probability density function is a bell-shaped curve. But not all the bell-shaped PDFs are from normal distributions.
It is the most extensively used distribution.
Excel formula for normal distribution
  NORMDIST(x, mean, standard_dev, cumulative)
The 68-95-99.7 rule for normal distribution:
  about 68% of the data stay within σ from the mean
  about 95% of the data stay within 2σ from the mean
  about 99.7% of the data stay within 3σ from the mean.
Notes: In probability theory, the normal (or Gaussian) distribution is a continuous probability distribution that has a bell-shaped probability density function, known as the Gaussian function or more commonly the “bell curve.” It is the most frequently used distribution.
Not all bell-shaped curves are from the normal distribution.
The Excel formula here can be used to determine the probability of a value X occurring, when the mean and standard deviation are known.
As an example, consider the height of professional basketball players. The average height is 77 inches, and the standard deviation is 4 inches. Let us determine the probability that a player is 8 feet tall (or 84 inches). The probability is 0.02.
Remember the 68-95-99.7 rule? These represent the percentage of data that fall within 1, 2, and 3 standard deviations from the mean.

## Slide 450: Normal Distribution
PDF of Normal Distribution
Mean of Normal Distribution
Variance of Normal Distribution
Notes: Here is the formula for calculating the PDF for a normal distribution. It a little easier to do with Excel, where the Greek letter mu is used for the mean, and sigma squared is the variance.

## Slide 451: Exponential Distribution
Exponential distribution is a continuous probability distribution describing the probability of events occurring at a known constant average rate between points of time.
The exponential distribution is very similar to the Poisson distribution, except that the former is built on continuous variables and the latter is built on discrete variables.
Excel formula for exponential distribution
  EXPONDIST(x, lambda, cumulative)
Notes: In probability theory and statistics, the exponential distribution (or negative exponential distribution) is a family of continuous probability distributions. It describes the time between events in a Poisson process, i.e., a process in which events occur continuously and independently at a constant average rate.
Example: Busses arrive at a bus stop at an average of 3 busses per hour. (a) What is the expected time between busses? (b) What is the probability that the next bus will arrive within 5 minutes?
Solution: Bus arrivals represent rare events, thus the time T between them is exponential, with rate 3 busses/hour i.e., 3. So the expected time between arrivals is 1/3 hours or 20 minutes. To determine the probability that the next bus will arrive in 5 minutes or 1/12 of an hour, let us plug the value of 1/12 in for X, 1/3 in for lambda. The result is 0.32.
In real-world scenarios, the constant rate assumption is rarely satisfied. For example, the rate of incoming phone calls differs according to the time of day. But if we focus on a time interval during which the rate is roughly constant, such as from 2 to 4 p.m. during work days, the exponential distribution can be used as a good approximate model for the time until the next phone call arrives. In the real world there are always caveats, but the key is that we can estimate or approximate using distribution models:
The time until a radioactive particle decays, or the time between clicks of a Geiger counter
The time it takes before your next telephone call
The time until default (on payment to company debt holders) in reduced form credit risk modeling.
Exponential variables can also be used to model situations where certain events occur with a constant probability per unit length, such as the distance between road kills on a given road.
In queuing theory, the service times of agents in a system (e.g., how long it takes for a bank teller etc. to serve a customer) are often modeled as exponentially-distributed variables.

## Slide 452: Exponential Distribution
PDF of Exponential Distribution
Mean of Exponential Distribution
Variance of Exponential Distribution
Notes: Here is the formula for the PDF of the exponential distribution, where lambda is the known rate, the mean is 1/lambda, and variance is 1/lambda-squared.

## Slide 453: Weibull Distribution
Weibull distribution is a continuous probability distribution which is widely used to model a great variety of data due to its flexibility.
K is the shape parameter and λ is the scale parameter. Both are positive numbers.
Excel formula for Weibull distribution
  WEIBULL(x, alpha, beta, cumulative)
Notes: In probability theory and statistics, the Weibull distribution is a continuous probability distribution.
It is named after Waloddi Weibull, who described it in detail in 1951, although it was first identified by Fréchet (1927) and first applied by Rosin and Rammler (1933) to describe the size distribution of particles.
It is widely used because it is flexible enough to model different kinds of data.
It is used in survival analysis, reliability/failure analysis, weather analysis, and particle size distributions to name a few.
In Excel, the function is as described on the page. X is the value at which we look to evaluate the probability, and alpha and beta are parameters of the distribution.

## Slide 454: Weibull Distribution
PDF of Weibull Distribution
Mean of Weibull Distribution
Variance of Weibull Distribution
Notes: You can see the PDF for the Weibull here, where k > 0 is the shape parameter and λ > 0 is the scale parameter of the distribution.

## Slide 455: Student’s T Distribution
Student’s t distribution is a continuous probability distribution that resembles a normal distribution.
When n random samples were drawn from a normally-distributed population with the mean μ and the standard deviation σ, then
  follows a t distribution with (n – 1) degrees of freedom.
Its probability density function is a bell-shaped curve but with heavier tails than those of the normal distribution.
Notes: In probability and statistics, Student’s t-distribution (or t-distribution) is a family of continuous probability distributions that arise when estimating the mean of a normally-distributed population in situations where the sample size is small and population standard deviation is unknown.
It plays a role in a number of widely used statistical analyses, including the Student’s t-test for assessing the statistical significance of the difference between two sample means, the construction of confidence intervals for the difference between two population means, and in linear regression analysis.
The t-distribution is symmetric and bell-shaped, like the normal distribution, but has heavier tails, meaning that it is more prone to producing values that fall far from its mean. This makes it useful for understanding the statistical behavior of certain types of ratios of random quantities, in which variation in the denominator is amplified and may produce outlying values when the denominator of the ratio falls close to zero.

## Slide 456: Student’s T Distribution
PDF of Student’s T Distribution
Mean of Student’s T Distribution
Variance of Student’s T Distribution
0 for degrees of freedom greater than 1, otherwise undefined
undefined
otherwise
Notes: The Greek letter nu is the number of degrees of freedom and gamma is the “gamma function.”

## Slide 457: Chi-Square Distribution
Chi-square distribution is a continuous probability distribution of the sum of squares of multiple independent standard normal random variables.
If Y1, Y2, …, Yk are a group of independent normal distributed variables, each with mean 0 and standard deviation 1, then
  follows a chi-square distribution with k degrees of freedom.
Notes: In probability theory and statistics, the chi-squared distribution (also chi-square or χ²-distribution) with k degrees of freedom is the distribution of a sum of the squares of k independent standard normal random variables.
It is one of the most widely used probability distributions in inferential statistics, e.g., in hypothesis testing or in construction of confidence intervals.
The chi-squared distribution is used in the common chi-squared tests for goodness of fit of an observed distribution to a theoretical one, the independence of two criteria of classification of qualitative data, and in confidence interval estimation for a population standard deviation of a normal distribution from a sample standard deviation. Many other statistical tests also use this distribution.

## Slide 458: Chi-Square Distribution
PDF of Chi-Square Distribution
Mean of Chi-Square Distribution
Variance of Chi-Square Distribution
Notes: The Greek letter gamma is the gamma function.

## Slide 459: F Distribution
F distribution is a continuous probability distribution which arises in the analysis of variance or test of equality between two variances.
If and are independent variables with chi-square distributions with and degrees of freedom,
  follows a F distribution.

## Slide 460: F Distribution
PDF of F Distribution
Mean of F Distribution
Variance of F Distribution
Notes: The PDF function for an F distribution, where nu 1 and nu 2 represent the degrees of freedom for two chi-squared distributions, and beta represents the beta function.

## Slide 461: Use SigmaXL to Fit a Distribution
Case Study: we are interested to fit the height data of basketball players into a distribution.
  Data File: “One Sample T-Test” tab in “Sample Data.xlsx”
Steps to fit a distribution in SigmaXL
  Select the entire range of the variable “HtBk”
  Click SigmaXL -> Process Capability -> Nonnormal -> Distribution Fitting
  A new window named “Distribution Fitting” pops up and the selected range appears automatically in the box under “Please select your data”.
  Click “Next>>”
  Another window also named “Distribution Fitting” appears
  Select ‘HtBk” as the “Numeric Data Variable (Y)”
  Click “OK>>”
Notes: Here we see instructions that show us how to used SigmaXL to fit a data distribution.

## Slide 462: Use SigmaXL to Fit a Distribution

## Slide 463: Use SigmaXL to Fit a Distribution
The distribution fitting report is in the newly generated tab “Distribution Fitting (1)”.
The distributions and transformations are sorted in the descending order of AD p-values.

## Slide 464: Use SigmaXL to Fit a Distribution
To fit a specific distribution, in the window “Distribution Fitting”, click on the radio button “Specify Distribution”, select the distribution of interest and click on “OK>>”.
In this example, we select “Normal” (i.e. normal distribution).

## Slide 465: Use SigmaXL to Fit a Distribution
The result of fitting the specified distribution, normal distribution in this case, is generated in the tab “Dist Fit Normal (1)”.
Since the p-value is 0.2748 higher than the alpha level, the variable HtBk is normally distributed.
Notes: By following these instructions, you can choose which distributions to overlay on your data before deciding which distribution best fits.

## Slide 466: 3.2 Inferential Statistics

## Slide 467: Black Belt Training: Analyze Phase
3.1 Patterns of Variation
  3.1.1 Multi-Vari Analysis
  3.1.2 Classes of Distributions
3.2 Inferential Statistics
  3.2.1 Understanding Inference
  3.2.2 Sampling Techniques and Uses
  3.2.3 Sample Size
  3.2.4 Central Limit Theorem
3.3 Hypothesis Testing
  3.3.1 Goals of Hypothesis Testing
  3.3.2 Statistical Significance
  3.3.3 Risk; Alpha and Beta
  3.3.4 Types of Hypothesis Tests
3.4 Hypothesis Testing: Normal Data
  3.4.1 One and Two Sample T-Tests
  3.4.2 One sample variance
  3.4.3 One Way ANOVA
3.5 Hyp Testing: Non-Normal Data
  3.5.1 Mann-Whitney
  3.5.2 Kruskal-Wallis
  3.5.3 Moods Median
  3.5.4 Friedman
  3.5.5 One Sample Sign
  3.5.6 One Sample Wilcoxon
  3.5.7 One and Two Sample Proportion
  3.5.8 Chi-Squared (Contingency Tables)
  3.5.9 Test of Equal Variances

## Slide 468: 3.2.1 Understanding Inference

## Slide 469: What is Statistical Inference?
Statistical inference is the process of making inferences regarding the characteristics of an unobservable population based on the characteristics of an observed sample.
We rely on sample data to draw conclusions about the population from which the sample is drawn.
Statistical inference is widely used since it is difficult or sometimes impossible to collect the entire population data.
Notes: We have talked about inference a number of times throughout the course.
Statistical inference is the process of making inferences or judgments regarding the characteristics of a population based on the characteristics of an observable sample.
It is rare that we ever know the characteristics of a population, so we need to take limited data and infer what the population looks like.

## Slide 470: Outcome of Statistical Inference
The outcome or conclusion of statistical inference is a statistical proposition about the population.
Examples of statistical propositions:
  Estimating a population parameter
  Identifying an interval or a region where the true population parameter would fall with some certainty
  Deciding whether to reject a hypothesis made on characteristics of the population of interest
  Making predictions
  Clustering or partitioning data into different groups.
Notes: The outcome of statistical inference is a statistical proposition about the population, such as an estimate of the population mean or standard deviation.
We will express this as a confidence interval around the parameter, because we do not know with certainty what the population parameter is.
Other examples of inference – evaluating a hypothesis about the characteristics of the population, making predictions, or partitioning the data into groups.

## Slide 471: Population and Sample
                A statistical population is an entire set of objects or observations about which statistical inferences are to be drawn based on its sample.
It is usually impractical or impossible to obtain the data for the entire population. For example, if we are interested in analyzing the population of all the trees, it is extremely difficult to collect the data for all the trees that existed in the past, exist now, and will exist in the future.
A sample is a subset of the population (like a piece of the pie above). It is necessary for samples to be representative of the population.
The process of selecting a subset of observations within a population is referred to as sampling.
Notes: When we talk about statistical inference, it is because we are trying to make inferences about a population based upon a sample size.
Consider the presidential elections. The “population” includes every single person that casts a vote. However, on election day you will see the news outlets making projections (inferences) about how people have voted, based upon sampling being done throughout the day.
Unless the population is very small, it is typically impractical or impossible to obtain measurements on an entire population.
A sample is a portion (or subset) of a population. If we choose a sample that is representative of a population, we can take measurements on the sample to make inferences about the population. This process is called sampling.

## Slide 472: Population and Sample
Population Parameters (Greek letters)
  Mean: μ
  Standard deviation: σ
  Variance: σ2
  Median: η
Sample Statistics (Roman letters)
  Sample Mean:
  Standard deviation: S
  Variance: S2
  Median:
The population parameter is the numerical summary of a population.
The sample statistic is the numerical measurement calculated based on a sample of that population. It is used to estimate the true population parameter.
Notes: There is a different nomenclature and there are different symbols that we use when referring to a population or a sample.
A population parameter is a summary statistic that is for an entire population, where a sample statistic is just that – a statistic based on a sample to represent the population.
Note the different symbols used for the different parameters: Greek letters for population, and Roman letters for sample.
Greek letters: mu = mean, sigma = standard deviation, eta = median.

## Slide 473: Descriptive Statistics vs. Statistical Inference
Descriptive Statistics
  Descriptive statistics summarize the characteristics of a collection of data.
  Descriptive statistics are descriptive only and they do not make any generalizations beyond the data at hand.
  Data used for descriptive statistics are for the purpose of representing or reporting.
Statistical Inference
  Statistical inference makes generalizations from a sample at hand of a population.
  Data used for statistical inference are for the purpose of making inferences on the entire population of interest.
A complete statistical analysis includes both descriptive statistics and statistical inference.
Notes: Descriptive statistics are used to summarize the characteristics of a set of data, e.g., the mean or median (center) or the standard deviation (spread).
They are only descriptive, meaning they are only meant to represent data you are using.
Statistical inference, on the other hand, is about making generalizations to a population.
A complete analysis should have both.

## Slide 474: Error Sources of Statistical Inference
Statistical inference uses sample data to best approximate the true features of the population.
A valid sample must be unbiased and representative of the population.
Two sources of error in statistical inference:
  Random sampling error
  Selection bias.
Notes: When we use a sample to make an inference about a population, there are two sources of error to be aware of.
The sample that is collected must be unbiased and representative, meaning that the data should not be selected in a way that only represents a certain segment of the population.
For example, what would happen if we wanted to understand income for the population of the US? In our sampling, if we only pulled data for professional athletes, or if we only pulled our sample in Beverly Hills, CA, what would happen to our data?
The two sources of error are random sampling error and selection bias, which we will now dive into.

## Slide 475: Error Sources of Statistical Inference
Random Sampling Error
  Random variation due to observations being selected randomly
  It is inherent to the sampling process and beyond one’s control.
Selection Bias
  Non-random variation due to inadequate design of sampling
  It can be improved by adjusting the sampling size and sampling strategy.
Notes: Random sampling error is expected when observations are selected randomly. This error is expected when we are not able to look at an entire population.
Selection bias is when we do not consider the profile of the population in the design of our sampling strategy, meaning the design is inadequate to represent the population.

## Slide 476: 3.2.2 Sampling Techniques

## Slide 477: What is Sampling?
Sampling is the process of selecting objects or observations from a population of interest about which we wish to make a statistical inference.
It is extensively used to collect information about a population, which can represent physical or intangible objects.
Sampling
Population
Sample
Notes: So we know that we usually cannot get data for an entire population. When we want to understand the population, we need to make sure we are getting a good sample that will allow us to make statistical inference.

## Slide 478: Advantages of Sampling
It is usually impractical or impossible to collect the data of an entire population:
  High cost
  Time consuming
  Unavailability of historical records
  Dynamic nature of the population.
Advantages of sampling a representative subset of the population:
  Lower cost
  Faster data collection
  Easier to manipulate.
Notes: Why do we sample?
Because it is not practical to measure an entire population; it can be cost prohibitive and time consuming.
In some cases we do not have historical data, which automatically means we do not have the entire population (yes, a population stretches over time too).
Sampling is cheaper, quicker, and easier.

## Slide 479: Uses of Sample
With valid samples collected, we can draw statistical conclusions about the population of our interest.
There are two major uses of samples in making statistical inference:
  Estimation: estimating the population parameters using the sample statistics.
  Hypothesis testing: testing a statement about the population characteristics using sample data.
This module covers sample size calculation for estimation purposes only. Sample size calculations for hypothesis testing purposes will be covered in the Hypothesis Testing module.
Notes: When we have good, valid samples, we are able to draw conclusions about the population.
We are able to estimate the population parameters (mean, standard variation).
We are also able to do hypothesis testing – where we are able to test the validity of a certain assumption about the population using sample data.
In this module, we will cover sample size calculations only for the purposes of estimating the population parameters.

## Slide 480: Basic Sampling Steps
Determine the population of interest
Determine the sampling frame
Determine the sampling strategy
Calculate the sample size
Conduct sampling
Notes: Over the next few pages, we will go into some detail about these basic steps to follow when doing sampling.
What population are we interested in knowing about?
What are the “guardrails” we put around the sample?
What is the sampling strategy?
What is the size of the sample needed?
Do the sampling.

## Slide 481: Population
Population in statistics is the entire set of objects or observations about which we are interested to draw conclusions or make generalizations based on some representative sample data.
A population can be either physical or intangible.
  Physical: trees, customers, monitors etc.
  Intangible: credit score, pass/fail decisions etc.
A population can be static or dynamic
  Characteristics of individuals are relatively static over time
  Items making up the population continue to change or be generated over time
The population covers all the items with characteristics we are interested to analyze.
Notes: A population is the entire set that we are interested in learning about, for instance, all residents of the state of North Carolina, the breed of Golden Retrievers, California Redwood trees.
All of the examples stated above are physical examples, but there are intangible examples as well. Consider credit scores, home values, stock prices.
Populations can change over time, meaning they are dynamic. For instance, the world population is constantly changing. On the other hand, the average stock price in 2011 is no longer changing.

## Slide 482: Sampling Frame
In the ideal situation, the scope of a population could be defined.
  Example: Mary is interested to know how the soup she is cooking tastes. The population is simply the pot of soup.
However, in some other situations, the population cannot be identified or defined precisely.
  Example: to collect the information for an opinion poll, we do not have a list of all the people in the world at hand.
A sampling frame is a list of items of the population (preferably the entire population; if not, approximate population).
  Example: The telephone directory would be a sampling frame for opinion poll data collection.
Notes: A challenge with identifying a population is “putting a fence around it” to clearly define it so that it can be easily identified.
The example here talks about a pot of soup as a very easy population to put a frame around, but when we are talking about a very large group of people it becomes more difficult.
A sampling frame is a list of items of the population, e.g., for an opinion poll the telephone directory would represent a good sample frame for a specific area.

## Slide 483: Basic Sampling Strategies
Simple Random Sampling
Matched Random Sampling
Stratified Sampling
Systematic Sampling
Proportional to Size Sampling
Cluster Sampling
Notes: The next step in the sampling process is to choose a sample strategy. So let us talk about some basic strategies.

## Slide 484: Simple Random Sampling
Simple random samples are selected in such a way that each item in the population has an equal chance of being selected.
There is no bias involved in the sample selection. Such selection minimizes the variation between the characteristics of samples and the population.
It is the basic sampling strategy.
Notes: In a simple random sampling strategy, every item in a population has an equal chance of being selected, and the variation between the characteristics of a sample and the population are minimized.

## Slide 485: Matched Random Sampling
Matched random samples are samples randomly selected in pairs, each of which has the same attribute.
Example:
  Researchers are interested in understanding the weight of twins.
  Researchers are interested in understanding the patients’ blood pressure before and after taking some medicine.
Notes: Matched random samples are basically the same as a random sampling strategy, but there is a good reason to collect two samples. See the examples provided here.

## Slide 486: Stratified Sampling
A population can be grouped or “stratified” into distinct and independent categories. An individual category can be considered as a sub-population. Stratified samples are randomly selected in each category of the population.
The categories can be gender, region, income level etc.
Stratified sampling requires advanced knowledge of the population characteristics.
Example: A fruit store wants to measure the quality of all their oranges. They decide to use stratified sampling by region to collect sample data. Since about 40% of their oranges are from California, 40% of the sample is selected from the California oranges sub-population.
Notes: A stratified sampling strategy may be used when the population is split into distinct categories (or “sub-populations”). The samples are selected randomly within each category.
Categories can be gender, race, region, age ranges to name a few.
In the example provided, the fruit store knows that they get a majority of their fruit from California; therefore, to get a representative sample of the fruit they receive they want to make sure that 40% of what is sampled comes from the California sub-population.

## Slide 487: Systematic Sampling
Systematic samples are selected at regular intervals based on an ordered list where items in the population are arranged according to a certain criterion.
Systematic sampling has a random start and then every ith item is selected going forward.
For example, we are sampling the every 5th unit produced on the production line.
Notes: System sampling is done by getting the samples at regular intervals. It is typical of a manufacturing process, where we would sample every i-th item.

## Slide 488: Cluster Sampling
Cluster sampling is a sampling method in which samples are only selected from certain clusters or groups of the population.
It reduces the cost and time spent on the sampling but bears the risk that the selected clusters are biased.
For example, selecting samples from the region where researchers are located so that the cost and time spent on travelling is reduced.
Notes: Cluster sampling is done by selecting samples from within certain groups of a population. It can certainly be quick and cost-effective, but obviously is subject to risk based on what or where the clusters are.

## Slide 489: Sampling Strategy Decision Factors
When determining the sampling strategy, we need to consider the following factors:
  Cost and time constraints
  Nature of the population of interest
  Availability of advanced knowledge of the population
  Accuracy requirement.
Notes: So how does one decide what sampling strategy to use?
Consider how much time is available to collect the data and what cost restrictions are in place.
Consider the nature of the population, and what you know about the population. Are there specific segments you are interested in? Are the samples streaming like in a manufacturing operation?
Determine how accurate you need to be – this can compete with how much you have to spend on sampling, but usually this will determine how big of a sample you should collect.

## Slide 490: Sample Size
The sample size is a critical element that can influence the results of statistical inference.
The smaller the sample size, the higher the risk that the sample statistic will not reflect the true population parameter.
The greater the sample size, the more time and money we will spend on collecting the samples.
Notes: Why is sample size important? It is vital when thinking about statistical inference.
The smaller the size of the sample, the higher the risk that the sample is not accurately depicting the population.
However, there is always a cost tradeoff. While more accuracy comes with larger sample size, so does the cost.

## Slide 491: Sample Size Factors
Is the variable of interest continuous or discrete?
How large is the population size?
How much risk do you want to take regarding missing the true population parameters?
What is the acceptable margin of error you want to detect?
How much is the variation in the population?
Notes: There are a few factors to consider when determining the right sample size:
What kind of data is being measured and analyzed? Continuous or discrete?
How large is the population that the sample is to represent?
How much risk is acceptable, and how much confidence do you need to have in terms of how close the sample statistics are to the population parameters?
How much spread is in the population? The larger the variation in the population, the larger the risk in sample variation.

## Slide 492: Sample Size Calculation for Continuous Data
Sample size equation for continuous data
where
n0 is the number of samples.
is the Z score when risk level is α/2.
  When α is 0.05, it is 1.96.
  When α is 0.10, it is 1.65.
s is the estimation of standard deviation in the population
d is the acceptable margin of error.
Notes: Here we see the formula for calculating the sample size (when using continuous data).
n is the sample size we are trying to determine
Z is a value that we look up based upon the confidence level. If we want 95% confidence, then alpha is 1 – 0.95 = 0.05 (or 5%). Therefore, we will look up the Z value for when alpha is 0.05, which is 1.96.
s is the estimated standard deviation for the population, and d is the acceptable margin of error.

## Slide 493: Sample Size Calculation for Continuous Data
When the sample size calculated using the formula
  exceeds 5% of the population size, we use a correction formula to calculate the final sample size.
where
n0 is the sample size calculated using equation
N is the population size.
Notes: When the sample size exceeds 5% of the population size, we use this formula to calculate the sample size. The small n(0) represents the sample size calculated using the formula on the previous page, and N is the size of the population.

## Slide 494: Sample Size Calculation for Discrete Data
Sample size equation for discrete data
where
n0 is the number of samples.
is the Z score when risk level is α/2.
  When α is 0.05, it is 1.96.
  When α is 0.10, it is 1.65.
s is the estimation of standard deviation in the population.
d is the acceptable margin of error.
p is the proportion of one type of event occurring (e.g., proportion of passes).
p × (1 – p) is the estimate of variance.
Notes: When using discrete data, the formula is a little different. However, the Z value (based on the alpha value) is the same, and d still represents the acceptable margin of error.
The key difference here is p, the proportion of a certain occurrence.

## Slide 495: Sample Size Calculation for Discrete Data
When the sample size calculated using the formula
  exceeds 5% of the population size, we use a correction formula to calculate the final sample size.
where
n0 is the sample size calculated using equation
N is the population size.
Notes: Similar to what we saw with continuous data, there is a correction formula to use when the sample size exceeds 5% of the population size.

## Slide 496: Sampling Errors
Random Sampling Error
  Random variation due to observations being selected randomly
  It is inherent in the sampling process and beyond one’s control.
Selection Bias
  Non-random variation due to inadequate design of sampling
  It can be improved by adjusting the sampling size and sampling strategy.
Notes: Random sampling error is expected when observations are selected randomly. This error is expected when we are not able to look at an entire population.
Selection bias – this is when we do not consider the profile of the population in the design of our sampling strategy, meaning the design is inadequate to represent the population.

## Slide 497: 3.2.3 Sample Size

## Slide 498: Sample Size
The sample size is a critical element that can influence the results of hypothesis testing.
The smaller the sample size, the higher the risk that the statistical conclusions will not reflect the population relationship.
The greater the sample size, the more time and money we will spend on collecting the samples.
Notes: In the last model we talked about sample size considerations for when we are looking to estimate parameters for a population. Now we want to use sample size considerations for hypothesis tests.
As mentioned before, the smaller the sample size, the higher the risk. In this case it is a higher risk that we draw the wrong conclusions.
Of course, the greater the sample size, the higher the cost. So we have to figure out where the right balance is.

## Slide 499: Sample Size Calculation
General sample size formula for continuous data
General sample size formula for discrete data
Notes: These two formulas are used to determine the sample size for continuous and discrete data, respectively.

## Slide 500: Sample Size Calculation
n is the number of observations in the sample.
α is the risk of committing a false positive error.
β is the risk of committing a false negative error.
s is the estimation of standard deviation in the population
d is the size of effect you want to be able to detect.
p is the proportion of one type of event occurring (e.g., proportion of passes).
Notes: These are the variables to consider in the sample size calculation:
n is the number of observations (the sample size).
alpha is the risk of committing a false positive (or Type I error). A false positive error, commonly called a false alarm, is a result that indicates a given condition has been fulfilled, when it actually has not been fulfilled. In the case of "crying wolf," the condition tested for was "is there a wolf near the herd?“ The actual result was that there had not been a wolf near the herd. The shepherd wrongly indicated there was one, by calling "Wolf, wolf!"
beta is the risk of committing a false negative (or Type II error). A false negative error is where a test result indicates that a condition failed, while it actually was successful. An example is a guilty prisoner freed from jail. The condition, "Is the prisoner guilty?" actually had a positive result (yes, he is guilty). But the test failed to realize this, and wrongly decided the prisoner was not guilty.
s is the standard deviation of the population.
d is the size of the effect you want to detect (the margin of error).
p is the proportion of one type of effect.

## Slide 501: Use SigmaXL to Calculate the Sample Size
Case Study:
  We are interested in comparing the average retail price of a product between two states.
  We will run a hypothesis test on the two sample means to determine whether there is a statistically significant difference between the retail price in the two states.
  The average retail price of the product is 23 based on our estimation and the standard deviation is 3. We want to detect at least 2 dollars difference with 90% chance when it is true and we can tolerate the alpha risk at 5%
  What should the sample size be?
Notes: To use the software to calculate the sample size, consider this example where we are trying to determine if there is a statistical difference between two sample means.

## Slide 502: Use SigmaXL to Calculate the Sample Size
Steps to calculate the sample size in SigmaXL
  Click SigmaXL -> Statistical Tools -> Power & Sample Size Calculators -> 2 Sample t-Test Calculator
  A window named “Power & Sample Size: 2 Sample t-Test Calculator” appears
  Click the radio button “Solve for Sample Size (N) for Each Group”
  Enter “0.9” as “Power (1-Beta)”
  Enter “2” as “Difference (Mean1 – Mean2)”
  Enter “3” as “Standard Deviation”
  Enter “0.05” as “Significance Level (Alpha)”
  Click “OK>>”
  The sample size calculation results appear in the new tab “PS - 2 Sample t-Test (1)”
Notes: Instructions to perform the test

## Slide 503: Use SigmaXL to Calculate the Sample Size
Notes: Software selections to perform the test…

## Slide 504: Use SigmaXL to Calculate the Sample Size
The sample size for each group is 49 based on the sample size calculator.
When the difference to detect decreases, the required sample size would increase.

## Slide 505: 3.2.4 Central Limit Theorem

## Slide 506: What is Central Limit Theorem?
The Central Limit Theorem is one of the fundamental theorems of probability theory.
It states a condition under which the mean of a large number of independent and identically-distributed random variables, each of which has a finite mean and variance, would be approximately normally distributed.
Notes: So why is the central limit theorem important?
It is the foundation for all tests of means.
It provides a set of simple rules for determining the mean, variance, and shape of a distribution of sample means.
Distributions of sample means are used in all hypothesis tests with means.

## Slide 507: What is Central Limit Theorem?
Let us assume Y1, Y2, …, Yn is a sequence of n i.i.d. random variables, each of which has finite mean μ and variance σ2, where σ2 > 0.
When n increases, the sample average of the n random variables is approximately normally distributed, with the mean equal to μ and variance equal to σ2/n, regardless of the common distribution Yi follows where i = 1, 2, …, n.
Notes: i.i.d. = independent and identically distributed
Even when data are not normally distributed, as long as sample sizes are large enough, the sample averages will be very close to normally distributed.

## Slide 508: Independent and Identically Distributed
A sequence of random variables is independent and identically distributed (i.i.d.) if each random variable is independent of others and has the same probability distribution as others.
It is one of the basic assumptions in Central Limit Theorem.
Notes: Consider the law of large numbers (LLN) – it is a theorem that describes the result of performing the same experiment a large number of times. According to the LLN, the average of the results obtained from a large number of trials should be close to the expected value, and will tend to become closer as more trials are performed. The example on the following page will explain this further.

## Slide 509: Central Limit Theorem Example
Let us assume we have 10 fair die at hand.
Each time we roll all 10 die together we record the average of the 10 die.
We repeat rolling the die 50 times until we will have 50 data points.
Upon doing so, we will discover that the probability distribution of the sample average approximates the normal distribution even though a single roll of a fair die follows a discrete uniform distribution.
Notes: Knowing that each die has 6 possible values (1, 2, 3, 4, 5, 6), when we record the average of the 10 dice over time, we would expect the number to start approximating 3.5 (the average of all possible values). The more rolls we perform, the closer the distribution would be to a normal distribution centered around a mean of 3.5.

## Slide 510: Central Limit Theorem Explained in Formulas
Let us assume Y1, Y2, …, Yn are i.i.d. random variables with
As , the distribution of becomes approximately normally distributed with
where
where
Notes: Y1, Y2, Yn are independent and identically distributed random variables.
E(Yi) = the expected value for Y is the mean for Y.
Var(Yi) = the expected variance for Y
As the n gets infinitely large, the distribution of Y means becomes approximately a normal distribution.

## Slide 511: Central Limit Theorem Application
Use the sample mean to estimate the population mean.
If the assumptions of Central Limit Theorem are met,
where
Notes: Because of the Central Limit Theorem, we are able to use a sample mean to estimate a population mean, if the assumptions are met.

## Slide 512: Central Limit Theorem Application
Use standard error of the mean to measure the standard deviation of the sample mean estimate of a population mean.
Standard deviation of the population mean
where s is the standard deviation of the sample and n is the sample size.
where σ is the standard deviation of the population and n is the sample size.
Notes: Furthermore, we are able to use the standard error of the mean to measure the standard deviation of the sample mean estimate of the population mean.

## Slide 513: Central Limit Theorem Application
Use a larger sample size, if economically feasible, to decrease the variance of the sampling distribution.
The larger the sample size, the more precise the estimation of the population parameter.
Use a confidence interval to describe the region which the population parameter would fall in.
The sample distribution approximates the normal distribution in which 95% of the data stays within two standard deviations from the center.
Population mean would fall in the interval of two standard errors of the mean away from the sample mean, 95% of the time.
Notes: Furthermore, we are able to use the standard error of the mean to measure the standard deviation of the sample mean estimate of the population mean.

## Slide 514: Confidence Interval
The confidence interval is an interval where the true population parameter would fall within a certain confidence level.
A 95% confidence interval indicates that the population parameter would fall in that region 95% of the time or we are 95% confident that the population parameter would fall in that region.
95% is the most commonly used confidence level.
Confidence interval is used to describe the reliability of a statistical estimate of a population parameter.
Notes: A 95% confidence interval means that the interval around the sample statistic would include the population parameter 95% of the time, or, conversely, only 5% of the time it will not include the population parameter.
If we wish to have more confidence around whether or not the interval contains the population parameter, what must we do? The interval must be wider. So a 99% confidence interval would be wider than the 95% confidence interval.
This is how we communicate reliability of a statistical estimate for a population parameter.

## Slide 515: Confidence Interval
The width of a confidence interval depends on:
  Confidence level
  Sample size
  Variability in the data.
The higher the confidence level, the wider the confidence interval.
The smaller the sample size, the wider the confidence interval.
The more variability, the wider the confidence interval.
Notes: The width of the interval depends on
  the confidence level
  the sample size
  the amount of variability inherent to the data.
As confidence level goes up, the interval gets wider.
As sample size goes down, the interval gets wider.
As variability increases, the interval gets wider.

## Slide 516: Confidence Interval of the Mean
Confidence interval of the population mean μY of a continuous variable Y is
is the sample mean
is the standard deviation of the population
is the sample size
  is the Z score when risk level is α/2.
    When α is 0.05, it is 1.96.
    When α is 0.10, it is 1.65.
is (1 – confidence level).
When confidence level is 95%, α is 5%. When the confidence level is 90%, α is 10%.
where
Note: Since 95% is the most commonly used confidence level, 0.05 is the most commonly used α (also called alpha level).

## Slide 517: SigmaXL: Calculate the Confidence Interval of the Mean
Data File:
  “Central Limit Theorem” tab in “Sample Data.xlsx”
Step 1:
  Select the entire range of “Cycle Time (Minutes)”
  Click SigmaXL -> Graphical Tools -> Histogram & Descriptive Statistics
  A new window named “Histogram & Descriptive” pops up with the selected range automatically appearing in the box under “Please select your data”
  Click “Next”
  Another window named “Histogram & Descriptive Statistics” pops up.
  Select “Cycle Time (Minutes)” as the “Numeric Data Variable (Y)”
  Click “OK>>”
Notes: We’ll now work through an example.

## Slide 518: SigmaXL: Calculate the Confidence Interval of the Mean

## Slide 519: SigmaXL: Calculate the Confidence Interval of the Mean
The 95% confidence interval of the mean is shown in the newly generated ta “Hist Descript (1)”

## Slide 520: SigmaXL: Calculate the Confidence Interval of the Mean
In SigmaXL, the confidence level is 95% by default.
In order to see the confidence interval of “Cycle Time (Minutes)” at other confidence levels, we need to enter the confidence level of our interest in the window “Histogram and Descriptive Statistics” and click “OK>>”
Below shows how to generate 90% confidence interval of the mean.
Notes: Here the example shows what selections to make in SigmaXL to get the confidence intervals around the mean and standard deviation. While SigmaXL defaults to 95%, you can see that other confidence levels can be selected as well.

## Slide 521: 3.3 Hypothesis Testing

## Slide 522: Black Belt Training: Analyze Phase
3.1 Patterns of Variation
  3.1.1 Multi-Vari Analysis
  3.1.2 Classes of Distributions
3.2 Inferential Statistics
  3.2.1 Understanding Inference
  3.2.2 Sampling Techniques and Uses
  3.2.3 Sample Size
  3.2.4 Central Limit Theorem
3.3 Hypothesis Testing
  3.3.1 Goals of Hypothesis Testing
  3.3.2 Statistical Significance
  3.3.3 Risk; Alpha and Beta
  3.3.4 Types of Hypothesis Tests
3.4 Hypothesis Testing: Normal Data
  3.4.1 One and Two Sample T-Tests
  3.4.2 One sample variance
  3.4.3 One Way ANOVA
3.5 Hyp Testing: Non-Normal Data
  3.5.1 Mann-Whitney
  3.5.2 Kruskal-Wallis
  3.5.3 Moods Median
  3.5.4 Friedman
  3.5.5 One Sample Sign
  3.5.6 One Sample Wilcoxon
  3.5.7 One and Two Sample Proportion
  3.5.8 Chi-Squared (Contingency Tables)
  3.5.9 Test of Equal Variances

## Slide 523: 3.3.1 Goals of Hypothesis Testing

## Slide 524: What is Hypothesis Testing?
A hypothesis test is a statistical method in which a specific hypothesis is formulated about a population, and the decision of whether to reject the hypothesis is made based on sample data.
Hypothesis tests help to determine whether a hypothesis about a population or multiple populations is true with certain confidence level based on sample data.
Notes: Hypothesis testing is a critical tool in the Six Sigma tool belt. It helps us separate fact from fiction, and special cause from noise, when we are looking to make decisions based on data.
It is a method of using statistics to confirm or reject a hypothesis formed about a population, based on sample data.
It allows us to use sample data to determine if a hypothesis about a population, or multiple populations, is true within a certain confidence level.

## Slide 525: Hypothesis Testing Examples
Hypothesis testing tries to answer whether there is a difference between different groups or there is some change occurring.
  Are the average SAT scores of graduates from high school A and B the same?
  Is the error rate of one group of operators higher than that of another group?
  Are there any non-random causes influencing the height of kids in one state?
Notes: Here are some example hypotheses. What are some examples the class can think of that are specific to the their business?

## Slide 526: What is Statistical Hypothesis?
A statistical hypothesis is an assumption about one or multiple population.
It is a statement about whether there is any difference between different groups.
It can be a conjecture about the population parameters or the nature of the population distributions.
A statistical hypothesis is formulated in pairs:
  Null Hypothesis
  Alternative Hypothesis.
Notes: A statistical hypothesis is stated as an assumption about a population or populations. Typically, we use them when we are trying to determine if there are differences between groups.
Statements like the following reflect a null hypothesis:
The data are normally distributed.
The population mean is the same as X.
Group A and Group B are the same.
And the alternative hypothesis are:
The data are NOT normally distributed
The population mean is NOT the same as X.
Group A and Group B are NOT the same.

## Slide 527: Null and Alternative Hypotheses
Null Hypothesis (H0) states that:
  there is no difference in the measurement of different groups
  no changes occurred
  sample observations result from random chance.
Alternative Hypothesis (H1 or Ha) states that:
  there is a difference in the measurement of different groups
  some changes occurred
  sample observations are affected by non-random causes.
Notes: Null hypotheses typically reflect that there are no differences between groups or that changes only occur due to random events (chance).
Alternative hypotheses state that there are differences between groups, or that changes occurred that are not just random (chance).

## Slide 528: Null and Alternative Hypotheses
A statistical hypothesis can be expressed in mathematical language by using population parameters (Greek letters) and mathematical symbols.
Population Parameters (Greek letters)
  Mean: μ
  Standard deviation: σ
  Variance: σ2
  Median: η
Mathematical Symbols
  Equal: =
  Not equal: ≠
  Greater than: >
  Smaller than: <
Notes: The symbols on this page are what you will use to write a statistical hypothesis. The population parameters you see here are the same that were discussed earlier.

## Slide 529: Null and Alternative Hypotheses
Examples of null and alternative hypotheses written in mathematical language.
H0: μ1 = μ2
H1: μ1 ≠ μ2
H0: σ1 = 0
H1: σ1 ≠ 0
H0: η1 = 10
H1: η1 > 10
H0: μ1 = 10
H1: μ1 < 10
Notes: The first pair reads: Null hypothesis where population mean 1 is equal to population mean 2. Alternative hypothesis is population mean 1 is NOT equal to population mean 2.
Or in the third pair: Null hypothesis where population mean 1 = 10. Alternative hypothesis is population mean greater than 10.

## Slide 530: Hypothesis Testing Conclusion
There are two possible conclusions of hypothesis testing:
  Reject the null
  Fail to reject the null.
When there is enough evidence based on the sample information to prove the alternative hypothesis, we reject the null.
When there is not enough evidence or the sample information is not sufficiently persuasive, we fail to reject the null.
Notes: There only two possible conclusions from hypothesis testing.
If the samples provide sufficient evidence to prove the alternative hypothesis, we reject the null.
If not enough evidence, we fail to reject the null.

## Slide 531: Decision Rules in Hypothesis Testing
Sampling distribution based on the null hypothesis
The critical value is derived from statistical tables. Different hypotheses use different statistical tables. It is the threshold value to determine whether to reject the null.
The acceptance region is the non-shaded area under the sampling distribution and not beyond the critical value. It is the opposite area of critical region.
The test statistic is calculated based on a function of sample data. Different hypotheses use different formulas to calculate test statistic. It can be any value along the x axis.
The critical region is the shaded area under the sampling distribution and beyond the critical value. The critical value defines the boundary of critical region.
α
Notes: As we get into the technicalities of hypothesis testing, it is important to understand some terms as they pertain to a distribution. Consider in this picture a normal distribution, and what we know about the distribution. Remember 68-95-99.7? The amount of data that falls within +/-1, 2, and 3 standard deviations of the mean.
The sampling distribution is based on the null hypothesis.
The critical region is the black shaded area. It represents the area beyond the critical value, which is a threshold value used to determine whether to reject the null hypothesis.
The test statistic is a function of sample data. This is used as a comparison to the critical value when determining the outcome of the hypothesis test.
The acceptance region is the rest of the sampling distribution that is NOT beyond the critical value.

## Slide 532: Decision Rules in Hypothesis Testing
The test statistic in hypothesis testing is a value calculated using a function of the sample.
Test statistics are considered the sample data’s numerical summary that can be used in hypothesis testing.
Different hypothesis tests have different formulas to calculate the test statistic.
The critical value in hypothesis testing is a threshold value to which the test statistic is compared in order to determine whether the null hypothesis is rejected.
The critical value is obtained from statistical tables.
Different hypothesis tests need different statistical tables for critical values.
Notes: Hypothesis testing is made easy with our fancy software packages, but it is important that you understand how the theory and rules work behind the software.
The test statistic is a calculated value, and it is a function of the sample data. Depending on the type of hypothesis tests, different formulas can be used to calculate the test statistic.
The critical value is what the test statistic is compared to in order to decide if the null hypothesis is rejected. It comes from statistical tables.
Different statistical tables are used for different types of hypothesis tests.

## Slide 533: Decision Rules in Hypothesis Testing
When the test statistic falls into the acceptance region, we fail to reject the null and claim that there is no statistically significant difference between the groups.
When the test statistic falls into the critical region, we reject the null and claim that there is a statistically significant difference between the groups.
Notes: How do we compare the test statistic and critical value to come to a decision?
If the test statistic falls into the acceptance region, we fail to reject the null; there is no difference.
Conversely, if the test statistic falls into the critical region, we reject the null; there is a difference.

## Slide 534: Decision Rules in Hypothesis Testing
The proportion of the area under the sampling distribution and beyond the critical value indicates α risk (also called α level). The most commonly selected α level is 5%.
The proportion of the area under the sampling distribution and beyond the test statistic is the p-value. It is the probability of getting a test statistic at least as extreme as the observed one, given the null is true.
Notes: The area beyond the critical value, which we looked at a few slides earlier, represents the alpha level. It represents the alpha risk value.
To illustrate, let us assume the test statistic is equal the critical value of 5%. In this case, there is a 5% risk that we will reject the null hypothesis when it is true. So, as the test statistic falls in the critical region, the risk of rejecting the null when it is actually true is less than 5%. Another way to state it is that we are 95% confident that we should reject the null hypothesis.
We typically refer to the area under the sampling distribution, and beyond the test statistic, as the p-value.

## Slide 535: Decision Rules in Hypothesis Testing
When the p-value is smaller than the α level, we reject the null and claim that there is a statistically significant difference between different groups.
When the p-value is higher than the α level, we fail to reject the null and claim that there is no statistically significant difference between different groups.
Notes: When the p-value is less than the alpha level, we reject the null. The implication is that there is a statistical difference between groups.
When the p-value is greater than the alpha level, we fail to reject the null. There is not a statistically significant difference between the groups.

## Slide 536: Steps in Hypothesis Testing
Step 1: State the null and alternative hypothesis.
Step 2: Determine α level.
Step 3: Collect sample data.
Step 4: Select a proper hypothesis test.
Step 5: Run the hypothesis test.
Step 6: Determine whether to reject the null.
Notes: Only six steps are necessary to do hypothesis testing.
State the null and alternative hypothesis.
Determine alpha level, 1 – confidence level. For 95% confidence, alpha is 1 – 0.95 = 0.05
Collect the sample data.
Choose the appropriate type of hypothesis test.
Run the test.
Determine whether to reject the null hypothesis.

## Slide 537: 3.3.2 Statistical Significance

## Slide 538: Statistical Significance
In statistics, an observed difference is statistically significant if it is unlikely that the difference occurred by pure chance, given a predetermined probability threshold.
Statistical significance indicates that there are some non-random factors causing the result to take place.
The statistical significance level in hypothesis testing indicates the amount of evidence which is sufficiently persuasive to prove that a difference between groups exists not due to random chance alone.
Notes: Statistical difference is the difference between noise and probability.
Statistical significance is important because we aim to make decisions based on what is probable vs. what is chance.
When we talk about determining if something is statistically significant, we will use the p-value. The p-value is the probability that the difference between two groups is driven by chance. The lower the p-value, the more likely that there is some non-random factor that is causing the difference.

## Slide 539: Practical Significance
An observed difference is practically significant when it is large enough to make a practical difference.
A difference between groups that is statistically significant might not be large enough to be practically significant.
In some business situations, statistical differences can have little to no meaning because the difference is not large enough to be practical for a business to act upon.
Notes: Sometimes we determine with statistics that there are differences. However, while those differences might be statistically significant, they may not be large enough to make a practical difference from a business standpoint. When analysis determines that a difference is statistically significant, ask yourself the question, “Why does it matter?” or “Why should we care?”

## Slide 540: Example
You started to use the premium gas recently, which was supposed to make your car run better.
After running a controlled experiment to measure the performance of the car before and after using the premium gas, you performed a statistical hypothesis test and found that the difference before and after was statistically significant.
Using premium gas did improve the performance.
However, due to the high cost of the premium gas, you decided that the difference was not large enough to make you pay extra money for it. In other words, the difference is not practically significant.
Notes: In this example, the premium gas did make a difference in performance. However, you must ask what is important. If cost is important, does the increased cost of premium gas have long term savings benefit – better gas mileage, lower maintenance, and repair cost, longer engine life?

## Slide 541: 3.3.3 Risk; Alpha & Beta

## Slide 542: Errors in Hypothesis Testing
In statistical hypothesis testing, there are two types of errors:
  Type I Error
    a null hypothesis is rejected when it is true in fact.
  Type II Error
    a null hypothesis is not rejected when it is not true in fact.
Notes: When making decisions, there is always risk. When we talk about hypothesis testing, we refer to type I and type II errors.
Type I error is when we react as though there is a change or a difference, when in fact it is only chance that is driving the difference.
Type II error is when we do not react when we should, meaning there is a difference but we act as though there is not.

## Slide 543: Type I Error
Type I error is also called false positive, false alarm, or alpha (α) error.
Type I error is associated with the risk of accepting false positives.
It occurs when we think there is a difference between groups but in fact there is none.
Example: telling a patient he is sick and in fact he is not.
Notes: Type I error is also called a false positive, false alarm, or alpha error.
Type I error leads to “tampering,” meaning we make changes or adjustments when we should not. We create a moving target and make it even more difficult to control the process.

## Slide 544: Alpha (α)
α indicates the probability of making a type I error. It ranges from 0 to 1.
α risk is the risk of making a type I error.
5% is the most commonly used α.
(100% – α) is the confidence level which is used to calculate the confidence intervals.
When making a decision on whether to reject the null, we compare the p-value against α:
  If p-value is smaller than α, we reject the null
  If p-value is greater than α, we fail to reject the null.
To reduce the α risk, we decrease the α value to which the p-value is compared.
Notes: We refer to type I error as alpha error. So what is alpha?
Alpha is the probability of making a type I error and, being a probability, it ranges between 0 and 1 (or 0 to 100%).
The most common alpha is 5%. It corresponds to the fact that most commonly we use a 95% confidence level. Confidence level = 1 – alpha.
When we make a decision about statistical significance, we compare the p-value against the alpha value. So if our confidence level is 95%, our alpha is 5%; therefore, our p-value is 0.05.
If p-value is less than alpha, then we reject the null hypothesis.
To reduce risk, or increase confidence, we lower the alpha value that the p-value is compared to. To be 99% confident, our alpha would be (1 – 0.99) = 0.01.

## Slide 545: Type II Error
Type II error is also called false negative, oversight, or beta (β) error.
Type II error is associated with the risk of accepting false negatives.
It occurs when we think there is not any difference between groups but in fact there is.
Example: telling a patient he is not sick and in fact he is.
Notes: Type II error is also called a false negative, oversight, or beta error.
Type II error describes when we are unresponsive to situations that we should respond to.

## Slide 546: Beta (β)
β indicates the probability of making a type II error. It ranges from 0 to 1.
β risk is the risk of making a type II error.
10% is the most commonly used β.
(100% – β) is called power, which denotes the probability of detecting a difference between groups when in fact the difference truly exists.
To reduce the β risk, we increase the sample size.
When holding other factors constant, β is inversely related to α.
Notes: We refer to type II error as beta error. So what is beta?
Beta is the probability of making a type II error, and, being a probability, it ranges between 0 and 1 (or 0 to 100%).
The most common beta is 10%. It corresponds to the fact that most commonly we use a 90% power. Power = 1 – beta.
Power is the probability of detecting a difference when a difference truly exists.
This type of risk comes into play with sample size analysis. We reduce risk by increasing the sample size.

## Slide 547: 3.3.4 Types of Hypothesis Tests

## Slide 548: Two Types of Hypothesis Tests
Two-tailed hypothesis test
  It is also called two-sided hypothesis test
  It is a statistical hypothesis test in which the critical region is split into two equal areas, each of which stays on one side of the sampling distribution.
One-tailed hypothesis test
  It is also called one-sided hypothesis test
  It is a statistical hypothesis test in which the critical region is only on one side of the sampling distribution.
Notes: When we talk about these two type of hypothesis tests, two-tailed and one-tailed, they are a direct reference to the tails of a data distribution.
A two-tailed hypothesis test, also called two-sided, is when we split the critical region to both sides of the sampling distribution.
A one-tailed hypothesis test, or one-sided, is when the critical region is only on one side of the sampling distribution.

## Slide 549: Two-Tailed Hypothesis Test
A two-tailed hypothesis test is used when we care about whether there is a difference between groups and we do not care about the direction of the difference.
Examples of two-tailed hypothesis tests:
The null hypothesis (H0) is rejected when:
  the test statistic falls into either half of the critical region
  the test statistic is either sufficiently small or sufficiently large
  the absolute value of the test statistic is greater than the absolute value of the critical value.
A two-tailed hypothesis test is the most commonly used hypothesis test. In the next modules we will cover more details about it.
H0: μ1 = 10
Ha: μ1 ≠ 10
Notes: When we are comparing group A and group B, and we only care to know if they are different, vs. one specific group being greater than another, we use a two-tailed test.
We reject the null hypothesis if the test statistic falls into either half of the critical region (which means the test statistic would have to be either really small or really large).
This is the most commonly used hypothesis test.

## Slide 550: Two-Tailed Hypothesis Test
α/2
α/2
Acceptance Region
Critical Region
Notes: As described on the previous page, the critical regions are on both (two) tails of the sample distribution.

## Slide 551: One-Tailed Hypothesis Test
A one-tailed hypothesis test is used when we care about one direction of the difference between groups.
Examples of one-tailed hypothesis tests:
The null hypothesis is rejected when the test statistic:
  falls into the critical region which only exits on the right side of the sampling distribution
  is sufficiently large
  is greater than the critical value.
H0: μ1 = 10
Ha: μ1 > 10
Notes: We use a one-tailed hypothesis test when we only care about one direction when comparing two groups, for instance, a null hypothesis where a population mean is equal to 10. An alternative hypothesis is where the population mean is not just unequal to 10, but greater than 10.
Of course, we look for the test statistic to fall into the critical region to reject the hypothesis. But in this situation we are only looking for the test statistic to be sufficiently large – greater than the critical value.

## Slide 552: One-Tailed Hypothesis Test
α
Acceptance Region
Critical Region
Notes: The critical region is only on one side of the distribution.

## Slide 553: One-Tailed Hypothesis Test
Examples of one-tailed hypothesis test
The null hypothesis is rejected when the test statistic:
  falls into the critical region which only exits on the left side of the sampling distribution
  is sufficiently small
  is smaller than the critical value.
H0: μ1 = 10
Ha: μ1 < 10
Notes: This is the other side of the one-tailed hypothesis test, where the alternative hypothesis is that the population mean is less than 10.
We look for the test statistic to fall into the critical region to reject the hypothesis. But in this situation we are only looking for the test statistic to be sufficiently small – less than the critical value.

## Slide 554: One-Tailed Hypothesis Test
α
Acceptance Region
Critical Region
Notes: The critical region is on the other side of the distribution.

## Slide 555: 3.4 Hypothesis Tests: Normal Data

## Slide 556: Black Belt Training: Analyze Phase
3.1 Patterns of Variation
  3.1.1 Multi-Vari Analysis
  3.1.2 Classes of Distributions
3.2 Inferential Statistics
  3.2.1 Understanding Inference
  3.2.2 Sampling Techniques and Uses
  3.2.3 Sample Size
  3.2.4 Central Limit Theorem
3.3 Hypothesis Testing
  3.3.1 Goals of Hypothesis Testing
  3.3.2 Statistical Significance
  3.3.3 Risk; Alpha and Beta
  3.3.4 Types of Hypothesis Tests
3.4 Hypothesis Testing: Normal Data
  3.4.1 One and Two Sample T-Tests
  3.4.2 One sample variance
  3.4.3 One Way ANOVA
3.5 Hyp Testing: Non-Normal Data
  3.5.1 Mann-Whitney
  3.5.2 Kruskal-Wallis
  3.5.3 Moods Median
  3.5.4 Friedman
  3.5.5 One Sample Sign
  3.5.6 One Sample Wilcoxon
  3.5.7 One and Two Sample Proportion
  3.5.8 Chi-Squared (Contingency Tables)
  3.5.9 Test of Equal Variances

## Slide 557: 3.4.1 1 & 2 Sample T-Tests

## Slide 558: What is a T-Test?
In statistics, a t-test is a hypothesis test in which the test statistic follows a Student t distribution if the null hypothesis is true.
We apply a t-test when the population variance (σ) is unknown and we use the sample standard deviation (s) instead.
Notes: The t-statistic was introduced in 1908 by William Sealy Gosset, a chemist working for the Guinness brewery in Dublin, Ireland ("Student" was his pen name). Gosset had been hired due to Claude Guinness's policy of recruiting the best graduates from Oxford and Cambridge to apply biochemistry and statistics to Guinness's industrial processes. Gosset devised the t-test as a cheap way to monitor the quality of stout. He published the test in Biometrika in 1908, but was forced to use a pen name by his employer, who regarded the fact that they were using statistics as a trade secret. In fact, Gosset's identity was known to fellow statisticians (http://en.wikipedia.org/wiki/Student's_t-test).
The t-test is a specific type of hypothesis test; usually, it is used when the data follow a normal distribution.
We use this test when the variance of the population is unknown and we use the standard deviation of the sample instead.

## Slide 559: What is One Sample T-Test?
One sample t-test is a hypothesis test to study whether there is a statistically significant difference between a population mean and a specified value.
  Null Hypothesis (H0): μ = μ0
  Alternative Hypothesis (Ha): μ ≠ μ0
  where μ is the mean of a population of our interest and μ0 is the specific value we want to compare against.
Notes: A one-sample t-test is used to study if there is a difference between a population and a specified value.

## Slide 560: Assumptions of One Sample T-Test
The sample data drawn from the population of interest are unbiased and representative.
The data of the population are continuous.
The data of the population are normally distributed.
The variance of the population of our interest is unknown.
One sample t-test is more robust than the z-test when the sample size is small (< 30).
Notes: For a t-test to be valid, these assumptions must be met:
The sample data drawn from a population are unbiased and representative of the population.
The data of the population are continuous and normally distributed.
The variance of the population is unknown.
One sample t-test is more robust than a z-test when the sample size is small.

## Slide 561: Normality Test
To check whether the population of our interest is normally distributed, we need to run normality test.
  Null Hypothesis (H0): The data are normally distributed.
  Alternative Hypothesis (Ha): The data are not normally distributed.
There are a lot of normality tests available:
  Anderson-Darling
  Sharpiro-Wilk
  Jarque-Bera etc.
Notes: Before conducting any hypothesis tests, it is important to understand if the data is normally distributed. For this, we run a normality test.
The null hypothesis in a normality test is that the data are normally distributed.

## Slide 562: Test Statistic and Critical Value of One Sample T-Test
Test Statistic
Critical Value
  tcrit is the t-value in a Student t distribution with the predetermined significance level α and degrees of freedom (n –1).
  tcrit values for a two-sided and a one-sided hypothesis test with the same significance level α and degrees of freedom (n – 1) are different.
, where
is the sample mean, n is the sample size, and s is the sample standard deviation
Notes: To understand what is happening when you run a t-test with your software, the formulas here will walk you through the key calculations and how to determine if the null hypothesis should be accepted or rejected.
To determine significance, you must calculate the t-statistic and compare it to the critical value, which is a reference value based on the alpha value and degrees of freedom (n – 1).
The t-statistic is calculated based on the sample mean, the sample standard deviation, and the sample size.

## Slide 563: Decision Rules of One Sample T-Test
Based on the sample data, we calculated the test statistic tcalc, which is compared against tcrit to make a decision of whether to reject the null.
  Null Hypothesis (H0): μ = μ0
  Alternative Hypothesis (Ha): μ ≠ μ0
If |tcalc| > tcrit, we reject the null and claim there is a statistically significant difference between the population mean μ and the specified value μ0.
If |tcalc| < tcrit, we fail to reject the null and claim there is not any statistically significant difference between the population mean μ and the specified value μ0.
Notes: To decide if we should reject the null hypothesis, we must compare the calculated t-statistic to the critical t value.
If the absolute value of the t-statistic is greater than the critical t value, then we must reject the null hypothesis.
If the absolute value of the t-statistic is less than the critical t value, then we fail to reject the null – and claim no difference between the population mean and the specified value we are comparing against.

## Slide 564: Use SigmaXL to Run a One-Sample T-Test
Case Study: we are trying to compare the average height of basketball players against 7 feet.
  Data File: “One Sample T-Test” tab in “Sample Data.xlsx”
Null Hypothesis (H0): μ = 7
Alternative Hypothesis (Ha): μ ≠ 7
Notes: In the example, we are comparing the average height of basketball players against 7 feet.
The null hypothesis is that the population mean is 7, and the alternative is that the population mean is NOT 7.

## Slide 565: Use SigmaXL to Run a One-Sample T-Test
Step 1: Test whether the data are normally distributed
  Select the entire range of “HtBk”
  Click SigmaXL -> Graphical Tools -> Histogram & Descriptive Statistics
  A new window named “Histogram & Descriptive” pops up with the selected range automatically appearing in the box under “Please select your data”
  Click “Next >>”
  Another window named “Histogram & Descriptive Statistics” pops up.
  Select “HtBk” as the “Numerical Data Variable (Y)”
  Click “OK”
Notes: Now we’ll use the software to run an example. First we must check normality of the sample data.

## Slide 566: Use SigmaXL to Run a One-Sample T-Test

## Slide 567: Use SigmaXL to Run a One-Sample T-Test
Null Hypothesis (H0): The data are normally distributed.
Alternative Hypothesis (Ha): The data are not normally distributed.
Since the p-value of the normality is 0.2748 greater than alpha level (0.05), we fail to reject the null and claim that the data are normally distributed.
If the data are not normally distributed, you need to use other hypothesis tests other than one sample t-test.
Notes: Now we can run the one-sample t-test, knowing the data is normally distributed.

## Slide 568: Use SigmaXL to Run a One-Sample T-Test
Step 2: Run the one-sample t-test
  Select the entire range of “HtBk”
  Click SigmaXL -> Statistical Tools -> 1 Sample t-Test & Confidence Intervals
  A new window named “1 Sample t-Test” pops up with the selected range pre-populated in the box under “Please select your data”
  Click “Next>>”
  Another window also named “1 Sample t-Test” appears
  Select “HtBk” as the “Numerical Data Variable (Y)”
  Enter the hypothesized value “7” into the box next to “H0: Mean =”
  Select “Not Equal To” in the box next to “Ha:”
  Click “OK>>”
  The one-sample t-test result appears automatically in the tab “1 Sample t-Test (1)”.

## Slide 569: Use SigmaXL to Run a One-Sample T-Test

## Slide 570: Use SigmaXL to Run a One-Sample T-Test
Null Hypothesis: (H0): μ = 7
Alternative Hypothesis: (Ha): μ ≠ 7
Since the p-value is smaller than alpha level (0.05), we reject the null hypothesis and claim that the average height of our basketball players is statistically different from 7 feet.
Notes: In this example, because the p-value is very low, we reject the null hypothesis and claim that the average height of basketball players is different from 7 feet.

## Slide 571: What is Two Sample T-Test?
Two sample t-test is a hypothesis test to study whether there is a statistically significant difference between the means of two populations.
  Null Hypothesis (H0): μ1 = μ2
  Alternative Hypothesis (Ha): μ1 ≠ μ2
  where μ1 is the mean of one population and μ2 is the mean of the other population of our interest.
Notes: Where a one sample t-test looks to determine if a single population mean is different from a specified value, a two sample t-test compares the means of two populations.

## Slide 572: Assumptions of Two Sample T-Tests
The sample data drawn from both populations are unbiased and representative.
The data of both populations are continuous.
The data of both populations are normally distributed.
The variances of both populations are unknown.
Two sample t-test is more robust than a z-test when the sample size is small (< 30).
Notes: Similar to the assumptions of a two sample t-test:
The samples drawn from the populations are unbiased and representative.
Data from both populations are continuous, and both are normally distributed.
The population variances are unknown.

## Slide 573: Three Types of Two Sample T-Tests
Two sample t-test when the variances of two populations are unknown but equal
  Two sample t-test (when σ1 = σ2)
Two sample t-test when the variances of the two population are unknown and unequal
  Two sample t-test (when σ1 ≠ σ2)
Paired t-test when the two populations are dependent of each other
Notes: There are a few types of two sample t-tests. The first two depend on the variances of the two populations:
Either the variances of the two populations are unknown but equal, or
The variances of the populations are unknown and unequal.
A paired t-test is used when the two populations are dependent, so each data point from one distribution corresponds to a data point in the other distribution.

## Slide 574: Test of Equal Variance
To check whether the variances of two populations of interest are statistically significant different, we use the test of equal variance.
  Null Hypothesis (H0):
  Alternative Hypothesis (H1):
An F-test is used to test the equality of variances between two normally distributed populations.
Notes: As you saw on the previous slide, the different types of two sample t-tests depend on whether or not the variances are equal.
We can do statistical tests to determine is the variances are equal.
In statistics, an F-test is sometimes used for the null hypothesis that two normal populations have the same variance.

## Slide 575: Test of Equal Variance
An F-test is a statistic hypothesis test in which the test statistic follows an F-distribution when the null hypothesis is true.
The most known F-test is the test of equal variance for two normally distributed populations.
The F-test is very sensitive to non-normality. When any one of the two populations is not normal, we use the Brown-Forsythe test for checking the equality of variances.
Notes: In statistics, an F-test is a hypothesis test in which the test statistic follows an F-distribution when the null is true.
The test of equal variance is the most known F-test for two normally distributed populations.
It is very sensitive to non-normality, so when either distribution is not normally distributed, you must use the Brown-Forsythe test to check the equality of variances.

## Slide 576: Test of Equal Variance
Test Statistic
Critical Value
  Fcrit is the F value in a F distribution with the predetermined significance level α and degrees of freedom (n1 – 1) and (n2 – 1).
  Fcrit values for a two-sided and a one-sided F-test with the same significance level α and degrees of freedom (n1 – 1) and (n2 – 1) are different.
where
s1 and s2 are the sample standard deviations.
Notes: To calculate the F statistic, you divide the squared standard deviation of one population by the other.
The critical value is a reference value that you will find in a table, using the prescribed parameters – the significance level alpha, and degrees of freedom for both samples.

## Slide 577: Test of Equal Variance
Based on the sample data, we calculated the test statistic Fcalc, which is compared against Fcrit to make a decision of whether to reject the null.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha):
If Fcalc > Fcrit, we reject the null and claim there is a statistically significant difference between the variances of the two populations.
If Fcalc < Fcrit, we fail to reject the null and claim there is not any statistically significant difference between the variances of the two populations.

## Slide 578: Test Statistic & Critical Value of a Two Sample T-Test when σ1 = σ2
Test Statistic
Critical Value
  tcrit is the t value in a Student t distribution with the predetermined significance level α and degrees of freedom (n1 + n2 – 2).
  tcrit values for a two-sided and a one-sided t-test with the same significance level α and different degrees of freedom (n1 + n2 – 2).
where
are the sample means of the two populations of our interest.
and
n1 and n2 are the sample sizes. n1 is not necessarily equal to n2.
spooled is a pooled estimate of variance. s1 and s2 are the sample standard deviations.
Notes: For a two sample t-test, the test statistic is calculated using the sample means for the two populations, the pooled standard deviation, and the sample sizes.
Pooled variance is a method for estimating variance given several different samples taken in different circumstances where the mean may vary between samples but the true variance is assumed to remain the same.
The critical t value is pulled from the Student t distribution using the desired significance level and the degrees of freedom calculated by (n1 + n2 – 2).

## Slide 579: Test Statistic & Critical Value of a Two Sample T-Test when σ1 ≠ σ2
Test Statistic
Critical Value
  tcrit is the t value in a Student t distribution with the predetermined significance level α and degrees of freedom df calculated using the formula above.
  tcrit values for a two-sided and a one-sided t-test with the same significance level α and different degrees of freedom df.
where
are the sample means of the two populations of our interest.
and
n1 and n2 are the sample sizes. n1 is not necessarily equal to n2.
s1 and s2 are the sample standard deviations.
Notes: For a two sample t-test with unknown variances or with known unequal variances, the test statistic is not calculated using the pooled standard deviation.
Pooled variance is a method for estimating variance given several different samples taken in different circumstances where the mean may vary between samples but the true variance is assumed to remain the same. When we cannot assume equal variances or if we know they are unequal we cannot make the same assertions by using pooled variances. Therefore we use the standard deviation of each sample separately in our tcalc equation.

## Slide 580: Test Statistic & Critical Value of a Paired T-Test
Test Statistic
Critical Value
  tcrit is the t value in a Student t distribution with the predetermined significance level α and degrees of freedom (n – 1).
  tcrit values for a two-sided and a one-sided t-test with the same significance level α and different degrees of freedom (n – 1).
where
is the average of d.
n is the sample size of either population of interest.
sd is standard deviation of d.
d is the difference between each pair of data.
Notes: When using a paired t-test, the test statistic is calculated using the average difference between the data pairs, the standard deviation of the differences, and the sample size of either population.
The critical t is looked up using the significance level alpha and degrees of freedom (n – 1).

## Slide 581: Decision Rules of a Two Sample T-Test
Based on the sample data, we calculated the test statistic tcalc, which is compared against tcrit to make a decision of whether to reject the null.
  Null Hypothesis (H0): μ1 = μ2
  Alternative Hypothesis (Ha): μ1 ≠ μ2
If |tcalc| > tcrit, we reject the null and claim there is a statistically significant difference between the means of the two populations.
If |tcalc| < tcrit, we fail to reject the null and claim there is not any statistically significant difference between the means of the two populations.
Notes: The decision rules leverage the calculated t-statistic and the critical t statistic, which we learned how to determine a few pages earlier.
If the absolute value of the calculated t is greater than the critical t, we reject the null hypothesis that the population means are equal, and claim there is a statistically significant difference.
If the absolute value of the calculated t is less than the critical t, we fail to reject the null hypothesis.

## Slide 582: Use SigmaXL to Run a Two-Sample T-Test
Case Study: We are trying to compare the average retail price of a product in state A and state B.
  Data File: “Two-Sample T-Test” tab in “Sample Data.xlsx”
Null Hypothesis (H0): μ1 = μ2
Alternative Hypothesis (Ha): μ1 ≠ μ2
Notes: In this example we will be comparing the average price of a product in two different states.
The null hypothesis is that the price in state “A” is equal to the price in state “B”

## Slide 583: Use SigmaXL to Run a Two-Sample T-Test
Step 1: Test the normality of the retail price for both state A and B.
  Select the entire range of data (both State and Retail Price)
  Click SigmaXL -> Graphical Tools -> Histogram & Descriptive Statistics
  A window named “Histogram & Descriptive” pops up with the selected range pre-populated in the box below “Please select your data”
  Click “Next >>”
  Another window named “Histogram & Descriptive Statistics” appears
  Select “Retail Price” as the “Numeric Data Variables”
  Select “State” as the “Group Category (X1)”
  Click “OK>>”
  The normality test results would appear in the tab “Hist Descript (1)” automatically.
Notes: First we must check normality of the data.

## Slide 584: Use SigmaXL to Run a Two-Sample T-Test

## Slide 585: Use SigmaXL to Run a Two-Sample T-Test
Null Hypothesis (H0): The data are normally distributed.
Alternative Hypothesis (Ha): The data are not normally distributed.
Both retail price data of state A and B are normally distributed since the p-values are both greater than alpha level (0.05).
If any of the data series is not normally distributed, we need to use other hypothesis testing methods other than the two sample t-test.
Notes: By following the instructions on the previous page, we first determine if the data follow a normal distribution. In this case you can see that the P-value for both is higher than 0.05, so we fail to reject the null hypothesis that the data are normally distributed.
If the data are not normally distributed, we must use a different test.

## Slide 586: Use SigmaXL to Run a Two-Sample T-Test
Step 2: Test whether the variances of the two data sets are equal.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha):
  Select the entire range of data (both “State” and “Retail Price”)
  Click SigmaXL -> Statistical Tools -> 2 Sample Comparison Tests
  A new window named “2 Sample Comp Test” pops up with the selected range pre-populated in the box under “Please select your data”.
  Click “Next>>”
  Another window named “2 Sample Comparison Test” appears
  Click the radio button “Stacked Column Format (1 Numeric Data Column & 1 Group Category Column)
  Select “Retail Price” as the “Numeric Data Variable (Y)”
  Select “State” as the “Group Category (X)”
  Click “OK>>”
  The results show up in the tab “2 Sample Comparison Test (1)”
Notes: Now that we know the data are normal, we now must determine if the variances are equal.

## Slide 587: Use SigmaXL to Run a Two-Sample T-Test

## Slide 588: Use SigmaXL to Run a Two-Sample T-Test
  Because the retail prices at state A and state B are both normally distributed, F test is used to test their variance equality.
  The p-value of F test is 0.87 greater than the alpha level (0.05), so we fail to reject the null and we claim that the variances of the two data sets are equal. We will use the two sample t-test (when σ1 = σ2) to compare the means of the two groups.
  If σ1 ≠ σ2, we will use the two sample t-test (when σ1 ≠ σ2) to compare the means of the two groups.
Notes: Now that we know the data are normal, and the variances are equal, we can run the two-sample T-test.

## Slide 589: Use SigmaXL to Run a Two-Sample T-Test
Step 3: Run two-sample t-test to compare the means of two groups.
  The two sample comparison test we ran in step 2 also automatically generates the two-sample t-test result.
  Since the p-value of t test (assuming equal variance) is 0.6651 greater than the alpha level (0.05)
  we fail to reject the null hypothesis and we claim that the means of the two data sets are equal.

## Slide 590: Use SigmaXL to Run a Two-Sample T-Test
If the variances of the two groups do not equal, we will need to use the two-sample t-test (when σ1 ≠ σ2) to compare the means of the two groups.
Since the p-value of the t test (assuming unequal variance) is 0.6656 greater than the alpha level (0.05)
we fail to reject the null hypothesis and we claim that the means of two groups are equal.

## Slide 591: Use SigmaXL to Run a Paired T-Test
Case Study: We are interested to know whether the average salaries ($1000/yr) of male and female professors at the same university are the same.
  Data File: “Paired T-Test” tab in “Sample Data.xlsx”
  The data were randomly collected from 22 universities. For each university, the salaries of a male and female professors were randomly selected.
  The differences were calculated displayed in the data file.
Null Hypothesis (H0): μmale – μfemale = 0
Alternative Hypothesis (Ha): μmale – μfemale ≠ 0

## Slide 592: Use SigmaXL to Run a Paired T-Test
Step 1: Test whether the difference is normally distributed.
  Null Hypothesis (H0): The difference between two data sets is normally distributed.
  Alternative Hypothesis (Ha): The difference between two data sets is not normally distributed.
  Select the entire range of “Difference”
  Click SigmaXL -> Graphical Tools -> Histograms & Descriptive Statistics
  A new window named “Histogram & Descriptive” pops up with the selected range pre-populated in the box under “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Descriptive Statistics” appears.
  Select “Difference” as the “Numeric Data Variables (Y)”
  Click “OK>>”

## Slide 593: Use SigmaXL to Run a Paired T-Test

## Slide 594: Use SigmaXL to Run a Paired T-Test
The p-value of the normality test is 0.2874 greater than the alpha level (0.05), so we fail to reject the null hypothesis and we claim that the difference is normally distributed.
If the difference is not normally distributed, we need other hypothesis testing methods.
Notes: In this case study we will use a paired t-test. We are looking to determine if the average salaries of male and female professors are the same.
The null hypothesis is the difference between the two groups is 0. First we must determine if the data is normally distributed.

## Slide 595: Use SigmaXL to Run a Paired T-Test
Step 2: Run the paired t-test to compare the means of two dependent data sets.
  Select the entire range of both MALES and FEMALES data
  Click SigmaXL -> Statistical Tools -> Paired t-Test
  A new window named “Paired t-Test” pops up with the selected range pre-populated in the box under “Please select your data”
  Click “Next >>”
  Another new window named “Paired t-Test” pops up
  Select “MALES” as “Numeric Data Variable 1”
  Select “FEMALES” as “Numeric Data Variable 2”
  Click “OK>>”
  The paired t-test results appears in the tab “Paired t-Test (1)”
Notes: Finally – we run the paired t-test to compare the means of the two data sets.

## Slide 596: Use SigmaXL to Run a Paired T-Test

## Slide 597: Use SigmaXL to Run a Paired T-Test
The p-value of the paired t-test is 0.2127 greater than the alpha level (0.05), so we fail to reject the null hypothesis and we claim that there is no statistically significant difference between the salaries of male and female professors’ salaries.
Notes: Because the p-value is higher than 0.05, we again fail to reject the null hypothesis, meaning that there is no statistically significant difference between the salaries of male and female professors salaries.

## Slide 598: 3.4.2 One Sample Variance

## Slide 599: What is One Sample Variance Test?
One sample variance test is a hypothesis testing method to study whether there is a statistically significant difference between a population variance and a specified value.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha):
  where σ2 is the variance of a population of our interest and is the specific value we want to compare against.
Notes: Similar to the one-sample t-test, the one-sample variance test is a study to determine if there is a difference between a population parameter and a specific value. Instead of it being a comparison for the mean, it is the variance.
The null hypothesis is that the population variance is equal to a specified value.

## Slide 600: Chi-Square Test
A chi-square test is a statistical hypothesis test in which the test statistic follows a chi-square distribution when the null hypothesis is true.
A chi-square test can be used to test the equality between the variance of a normally distributed population and a specified value.
Notes: In a chi-square test, the test statistic follows a chi-square distribution when the null hypothesis is true.
The test can be used to test the equality of a variance to a specified value. For the test to be valid, the distribution must be normally distributed.

## Slide 601: Chi-Square Test
Test Statistic
Critical Value
  is the χ2 value in a χ2 distribution with the predetermined significance level α and degrees of freedom (n – 1).
  values for a two-sided and a one-sided χ2-test with the same significance level α and different degrees of freedom (n –1).
where
s2 is the observed variance and n is the sample size.
is the specified value we compare against.
Notes: The test statistic is calculated using the observed variance of the sample from the population, as well as the sample size and the specified value for variance we are comparing against.
Like in other tests we discussed, we compare the calculated chi-square statistic against a critical value, which is a chi-square table value that can be located based on the determined significance level and (n – 1) degrees of freedom.

## Slide 602: Chi-Square Test
Based on the sample data, we calculated the test statistic , which is compared against to make a decision of whether to reject the null.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha):
If , we reject the null and claim there is a statistically significant difference between the population variance and the specified value.
If , we fail to reject the null and claim there is not any statistically significant difference between the population variance and specified value.
Notes: We compare the calculated chi-square statistic to the critical value to determine how we resolve the hypothesis.
If the absolute value of the statistic is greater that the critical value, then we reject the null and claim that the population variance is different than the specified value. Otherwise, we fail to reject the null.

## Slide 603: Use SigmaXL to Run a One Sample Variance Test
Case Study: we are interested in comparing the variance of the height of basketball players with zero.
  Data File: “One Sample T-Test” tab in “Sample Data.xlsx”
Null Hypothesis (H0): σ2 = 0
Alternative Hypothesis (Ha): σ2 ≠ 0
Notes: In this case study we will use the software to determine if the variance in the height of basketball players is zero or different from zero.

## Slide 604: Use SigmaXL to Run a One Sample Variance Test
Step 1: Test whether the data are normally distributed
  Select the entire range of “HtBk”
  Click SigmaXL -> Graphical Tools -> Histograms & Descriptive Statistics
  A new window named “Histogram & Descriptive” pops up with the selected range pre-populated in the box under “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Descriptive Statistics” appears.
  Select “Difference” as the “Numeric Data Variables (Y)”
  Click “OK>>”
  The normality test results appears in the tab “Hist Descript (1)”
Notes: Follow these steps to use the software to run the one-sample variance test. First test if the data is normally distributed.

## Slide 605: Use SigmaXL to Run a One Sample Variance Test

## Slide 606: Use SigmaXL to Run a One Sample Variance Test
Null Hypothesis (H0): The data are normally distributed.
Alternative Hypothesis (Ha): The data are not normally distributed.
Since the p-value of the normality is 0.2748 greater than alpha level (0.05), we fail to reject the null and claim that the data are normally distributed.
If the data are not normally distributed, you need to use other hypothesis tests.
Notes: Recall that the data must be normally distributed in order for a one-sample variance test to be valid. As you can see from the results, the p-value is greater than 0.05, so we fail to reject the null hypothesis that the data are normally distributed.

## Slide 607: Use SigmaXL to Run a One Sample Variance Test
Step 2: Check if the specified value is different from 0.01 [we really want to know if it’s different from zero but we need a value other than 0 for SigmaXL to calculate so we will use 0.01].
  Select the entire range of “HtBk”
  Click SigmaXL -> Statistical Tools -> Basic Statistical Templates -> 1 Sample Chi-Square Test and CI for Standard Deviation
  The one sample variance test appears in the newly generated tab “1 Sample CI StDev”
  A New Template Opens, Enter 40 in Sample Size
  Enter 0.324222 in Sample Standard Deviation
  Enter 0.01 in (hypothesized StdDev)
Notes: Since the data is normal, we can run the one-sample variance test.

## Slide 608: Use SigmaXL to Run a One Sample Variance Test
  If the square root of the specified value is between the upper and lower confidence interval boundaries then we fail to reject the null hypothesis and claim that the variance of the population is not statistically different from the specified value.
  In this case, the square root of 0.01 is outside the confidence interval of the population standard deviation and we claim that the population variance is statistically different from zero.
Notes: Since the data is normal, we can run the one-sample variance test.
To interpret the results, we can see the lower and upper 95% confidence interval for the population standard deviation.
We want to check to see if the specified value falls within the interval. To do so we must take the square root of the variance (zero) to get the standard deviation, which in this case is also zero.
Since the specified value does not fall within the confidence interval, we can claim that the population variance is different from the specified value of zero.

## Slide 609: 3.4.3 One Way ANOVA

## Slide 610: What is One-Way ANOVA?
One-way ANOVA (one-way analysis of variance) is a statistical method to compare means of two or more populations.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha): at least one μi is different, where i is any value from 1 to k.
It is a generalized form of the two sample t-test since a two sample t-test compares two population means and one-way ANOVA compares k population means where k ≥ 2.
Notes: Similar to a two-sample t-test to compare two population means, a one-way ANOVA compares two or more population means.
The null hypothesis is that all the means are the same, and the alternative hypothesis is that at least one mean is different from the rest.

## Slide 611: Assumptions of One-Way ANOVA
The sample data drawn from k populations are unbiased and representative.
The data of k populations are continuous.
The data of k populations are normally distributed.
The variances of k populations are equal.
Notes: For a valid test, the following assumptions must be true:
the samples drawn from the populations are unbiased and representatives,
the data are continuous and normally distributed, and
the variances of the populations are equal.

## Slide 612: How ANOVA Works
ANOVA compares the means of different groups by analyzing the variances between and within groups.
Let us say we are interested in comparing the means of three normally distributed populations. We randomly collected one sample for each population of our interest.
  Null Hypothesis (H0): μ1 = μ2 = μ3
  Alternative Hypothesis (Ha): one of the μ is different from the others.
Notes: ANOVA is able to compare the means of different populations by examining the variances.

## Slide 613: How ANOVA Works
Based on the sample data, the means of the three populations might look different because of two variation sources.
  Variation between groups
      There are non-random factors leading to the variation between groups.
  Variation within groups
      There are random errors resulting in the variation within each individual group.
What we care about the most is the variation between groups since we are interested in whether the groups are statistically different from each other.
Variation between groups is the signal we want to detect and variation within groups is the noise which corrupts the signal.
Notes: The means of three populations could look different because of the variation between groups and variation within groups.
We are looking to see if the means of the groups are the same or are different, so we are more interested in the variation between the groups.
You will hear the terms signal and noise again. The signal is where we want to detect variation between the groups, and the noise is the variation within a population.

## Slide 614: How ANOVA Works
Grand mean of all observations:
Individual observation:
Group means of each individual sample:
Total Variation = SS(Total) =
Between Variation = SS(Between) =
Within Variation = SS(Within) =
Notes: Using this visual, the purpose of using the ANOVA is to determine if there is a difference between the red data points (the group means of the individual samples).
The variation within the groups can make it difficult to detect the difference between the group means.

## Slide 615: How ANOVA Works
Variation Components
  Total Variation = Variation Between Groups + Variation Within Groups
    Total Variation = sums of squares of the vertical difference between the individual observation and the grand mean
    Variation Between Groups = sums of squares of the vertical difference between the group mean and the grand mean
    Variation Within Groups = sum of squares of the vertical difference between the individual observation and the group mean
=
+
Notes: On the previous slide, you saw formulas for computing the variation between groups and within groups. The total variation is the sum of the two, and can be computed as the sum of the squares of the differences between the individual observations and grand means.
Between group variation is the sum of the squares of the differences between the grand mean and the group mean.
Within group variation is the sum of the squares of the differences between the individual observations and group mean.

## Slide 616: How ANOVA Works
Degrees of Freedom (DF)
  In statistics, the degrees of freedom is the number of unrestricted values in the calculation of a statistic.
Degrees of Freedom Components
  DFtotal= DFbetween + DFwithin
  DFtotal = n – 1
  DFbetween= k – 1
  DFwithin= n – k
  where
  n is the total number of observations
  k is the number of groups.
Notes: In statistics, the number of degrees of freedom is the number of values in the final calculation of a statistic that are free to vary.
For the different components of variation, you can see the formulas to calculate the degrees of freedom within.

## Slide 617: How ANOVA Works
Signal-to-Noise Ratio (SNR)
  SNR denotes the ratio of a signal to the noise corrupting the signal.
  It measures how much a signal has been corrupted by the noise.
  When it is higher than 1, there is more signal than noise.
  The higher the SNR, the less the signal has been corrupted by the noise.
F-ratio is the SNR in ANOVA
  In ANOVA, we use the F-test to compare the means of different groups. The F-ratio calculated as above is the test statistic Fcalc.
  The critical value (Fcri) in an F-test can be derived from the F table with predetermined significance level (α) and with (k –1) degrees of freedom in the numerator and (n – k) degrees of freedom in the denominator.
Notes: Earlier, the terms signal and noise were introduced.
The signal is the variation between groups that we are trying to detect. The noise is the variation within a group that makes it difficult to see the signal.
We measure the ratio of signal to noise (SNR) to determine how much the signal is corrupted by the noise.
A ratio greater than 1 means there is more signal variation than noise variation. The higher the SNR number, the less the signal is corrupted.
In ANOVA, the SNR is the same thing as the F-ratio. ANOVA uses the F-test to compare the means of the different groups, where we compare a calculated F statistic to a critical F value derived from a table.

## Slide 618: How ANOVA Works
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha): at least one μi is different, where i is any value from 1 to k.
If |Fcalc| < Fcrit, we fail to reject the null and claim that the means of all the populations of our interest are the same.
If |Fcalc| > Fcrit, we reject the null and claim that there is at least one mean different from the others.
Notes: As mentioned earlier, the null hypothesis for ANOVA is that all of the group means are equal, and the alternative is that at least one mean is different.
Using the F-ratio, we can compare the calculated value against the critical value. If the absolute value of the calculated value is less than the critical value, then we fail to reject the null hypothesis. If the absolute value of the calculated value is greater than the critical value, then we reject the null hypothesis.

## Slide 619: Model Validation
ANOVA is a modeling procedure. To make sure the conclusions made in ANOVA are reliable, we need to perform residuals analysis.
Good residuals:
  Have a mean of zero
  Are normally distributed
  Are independent of each other
  Have equal variance.
Notes: ANOVA is a modeling procedure, which means we are using a model to try to predict results. The difference between the actual and predicted result is called a residual or unexplained variation.
To ensure that the results of ANOVA are valid, we must validate some things about the residuals to make sure there is not some other factor contributing to the variation (that we can explain), outside of randomness.
A residuals analysis must be performed to ensure that the mean of the residuals is zero, they are normally distributed, independent of each other, and have equal variance.

## Slide 620: Use SigmaXL to Run ANOVA
Case Study: We are interested in comparing the average startup costs of five kinds of business.
  Data File: “One-Way ANOVA” tab in “Sample Data.xlsx”
Null Hypothesis (H0): μ1= μ2= μ3=μ4=μ5
Alternative Hypothesis (Ha): at least one of the five means is different from others.
Notes: Now we will use the software to run an ANOVA analysis. We are interested in comparing the average startup costs of five different kinds of businesses.
Remember the null and alternative hypotheses for ANOVA…

## Slide 621: Use SigmaXL to Run ANOVA
Step 1 : Test whether the data for each level are normally distributed.
  Select the entire range of data (both “Business” and “Cost”)
  Click SigmaXL -> Graphical Tools -> Histogram & Descriptive Statistics
  A new window named “Histogram & Descriptive” pops up with the selected range pre-populated
  Click “Next>>”
  A new window named “Histogram & Descriptive” appears
  Select “Cost” as “Numeric Data Variables (Y)” and “Business” as “Group Category (X1)”
  Click “OK>>”
  The normality results appear in the new tab “Hist Descript (1)”
Notes: The first step is to check our assumption that the data for each group are normally distributed.

## Slide 622: Use SigmaXL to Run ANOVA

## Slide 623: Use SigmaXL to Run ANOVA
Business = X1:
Business = X3:
Business = X2:
Business = X4:
Business = X5:
Notes: Notice all of the p-values are greater than 0.05, therefore we fail to reject the null hypothesis that the data are normally distributed.

## Slide 624: Use SigmaXL to Run ANOVA
Null Hypothesis (H0): The data are normally distributed.
Alternative Hypothesis (Ha): The data are not normally distributed.
Since the p-values of normality tests for the five data sets are higher than alpha level (0.05), we fail to reject the null hypothesis and claim that the startup costs for any of the five businesses are normally distributed.
If any of the five data sets are not normally distributed, we need to use other hypothesis testing methods other than one way ANOVA.
Notes: In this example, all five data sets are normally distributed; however, if ANY of them were not normally distributed we would need to use another hypothesis test.

## Slide 625: Use SigmaXL to Run ANOVA
Step 2: Test whether the variance of the data for each level is equal to the variance of other levels.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha): at least one of the variances is different from others.
  Select the entire range of data (both “Business” and “Cost”)
  Click SigmaXL -> Statistical Tools -> Bartlett’s Test (Since there are more than two levels in the data and the data of each level are normally distributed, we use Barlett’s test for testing the variances between the five levels.
  A new window named “Bartlett’s Test” pops up with the selected range pre-populated
  Click “Next>>”
  A new window named “Bartlett’s Test” appears
  Select “Cost” as the “Numeric Data Variable (Y)”
  Select “Business” as the “Group Category (X)”
  Click “OK>>”
  The results shows up in the newly generated tab “Bartlett's Test (1)”
Notes: Now we must check the assumption that the variances are equal among the five groups.

## Slide 626: Use SigmaXL to Run ANOVA

## Slide 627: Use SigmaXL to Run ANOVA
The p-value of Barlett’s test is 0.7768 greater than the alpha level (0.05), so we fail to reject the null hypothesis and we claim that the variances of five groups are equal.
If the variances are not all equal, we need to use other hypothesis testing methods other than one way ANOVA.
Notes: Because there are more than 2 levels (5 in this case), and the data are normally distributed, we used Bartlett’s test for equal variances.
Since the result of the test is a p-value greater than 0.05, we fail to reject the null hypothesis that the variances of all five groups are equal.
If this test suggested that at least one variance was different, then we would need to use a different hypothesis test to evaluate the group means.

## Slide 628: Use SigmaXL to Run ANOVA
Step 3: Test whether the mean of the data for each level is equal to the means of other levels.
  Null Hypothesis (H0): μ1= μ2= μ3=μ4=μ5
  Alternative Hypothesis (Ha): at lease one of the means is different from others.
  Select the entire range of the data (both “Business” and “Cost”
  Click SigmaXL -> One-Way ANOVA & Means Matrix
  A new window named “One-Way ANOVA” pops up with selected range pre-populated
  Click “Next>>”
  A new window named “One-Way ANOVA & Means Matrix” appears
  Select “Cost” as “Numeric Data Variable (Y)”
  Select “Business” as “Group Category (X)”
  Check the checkbox “Display ANOVA Table Details”
  Click “OK>>”
  The ANOVA results appear in the newly generated tab “One-Way ANOVA (1)”
Notes: Now that we’ve checked the assumptions, we can run the ANOVA test.

## Slide 629: Use SigmaXL to Run ANOVA

## Slide 630: Use SigmaXL to Run ANOVA
Since the p-value of the F test is 0.0184 lower than alpha level (0.05). The null hypothesis is rejected and we conclude that the at least one of the means of the five groups is different from others.
Notes: Upon running the ANOVA test, we see that the P-value is less than 0.05. This means we must reject the hypothesis and claim that at least one of the means of the five groups is different from the others.

## Slide 631: 3.5 Hypothesis Testing: Non-Normal Data
Notes: The tests we have discussed up to this point all apply when we are working with data that follow normal distributions. So what do we do if that is not the case? The following pages describe tests available to us when the data do NOT follow the normal distribution.

## Slide 632: Black Belt Training: Analyze Phase
3.1 Patterns of Variation
  3.1.1 Multi-Vari Analysis
  3.1.2 Classes of Distributions
3.2 Inferential Statistics
  3.2.1 Understanding Inference
  3.2.2 Sampling Techniques and Uses
  3.2.3 Sample Size
  3.2.4 Central Limit Theorem
3.3 Hypothesis Testing
  3.3.1 Goals of Hypothesis Testing
  3.3.2 Statistical Significance
  3.3.3 Risk; Alpha and Beta
  3.3.4 Types of Hypothesis Tests
3.4 Hypothesis Testing: Normal Data
  3.4.1 One and Two Sample T-Tests
  3.4.2 One sample variance
  3.4.3 One Way ANOVA
3.5 Hyp Testing: Non-Normal Data
  3.5.1 Mann-Whitney
  3.5.2 Kruskal-Wallis
  3.5.3 Moods Median
  3.5.4 Friedman
  3.5.5 One Sample Sign
  3.5.6 One Sample Wilcoxon
  3.5.7 One and Two Sample Proportion
  3.5.8 Chi-Squared (Contingency Tables)
  3.5.9 Test of Equal Variances

## Slide 633: 3.5.1 Mann-Whitney

## Slide 634: What is the Mann-Whitney Test?
The Mann-Whitney test (also called Mann-Whitney U test or Wilcoxon rank-sum test) is a statistical hypothesis test to compare the medians of two populations that are not normally distributed.
  Null Hypothesis (H0): η1 = η2
  Alternative Hypothesis (Ha): η1 ≠ η2
  where η1 is the median of one population and η1 is the median of the other population.
Notes: The Mann-Whitney test, also called the Mann-Whitney U Test or Wilcoxon rank-sum test, compares medians of two non-normal populations. The key difference here is that it compares medians, not averages. In a non-normal distribution, the median is the better representation of the center of the distribution.
The null hypothesis and alternative hypothesis follow a similar pattern of other tests we have looked at. The null is that the medians are equal, and the alternative is that they are not equal.

## Slide 635: Mann-Whitney Test Assumptions
The sample data drawn from the populations of interest are unbiased and representative.
The data of both populations are continuous or ordinal when the spacing between adjacent values is not constant.
The two populations are independent to each other.
The Mann-Whitney test is robust for the non-normally distributed population.
The Mann-Whitney test can be used when shapes of the two populations’ distributions are different.
Notes: There are several assumptions made about populations:
Samples drawn from the two populations are unbiased and representative.
Data from the populations are continuous or ordinal when the spacing between adjacent values is not constant. (Reminder – Ordinal data: A set of data is said to be ordinal if the values can be ranked or have a rating scale attached. You can count and order, but not measure, ordinal data.)
The two populations are independent to each other, meaning the values of one do not drive the others.
It is a robust test, and can be used when the distribution shapes are different.

## Slide 636: How Mann-Whitney Test Works
Step 1: Group the two samples from two populations (sample 1 is from population 1 and sample 2 is from population 2) into a single data set and then sort the data in ascending order ranked from 1 to n, where n is the total number of observations.
Step 2: Add up the ranks for all the observations from sample 1 and call it R1. Add up the ranks for all the observations from sample 2 and call it R2.
Notes: To run the test, group the two population samples into a single data set and sort the data into ascending order and rank them from 1 to n.
Add up the ranks for all observations from sample 1, calling it R1. Do the same for sample 2, call it R2.

## Slide 637: How Mann-Whitney Test Works
Step 3: Calculate the test statistics
where
n1 and n2 are the sample sizes.
R1 and R2 are the sum of ranks for observations from sample 1 and 2 respectively.
Notes: Calculate the test statistics, denoted U, by using the sample sizes and the R values that were calculated in Step 2.

## Slide 638: How Mann-Whitney Test Works
Step 4: Make a decision on whether to reject the null hypothesis.
  Null Hypothesis (H0): η1 = η2
  Alternative Hypothesis (Ha): η1 ≠ η2
If both of the sample sizes are smaller than 10, the distribution of U under the null hypothesis is tabulated.
  The test statistic is U and, by using the Mann-Whitney table, we would find the p-value.
  If the p-value is smaller than alpha level (0.05), we reject the null hypothesis.
  If the p-value is greater than alpha level (0.05), we fail to reject the null hypothesis.
Notes: Next, we assess the hypothesis. If the sample sizes are less than 10, we use the test statistic U to look up the p-value in the Mann-Whitney table.
If p is less than the alpha value (0.05), then we reject the null hypothesis; if p is greater than the alpha, we fail to reject the null hypothesis.

## Slide 639: How Mann-Whitney Test Works
If both sample sizes are greater than 10, the distribution of U can be approximated by a normal distribution. In other words, follows a standard normal distribution.
where
When |Zcalc| is greater than Z value at α/2 level (e.g., when α = 5%, the z value we compare |Zcalc| to is 1.96), we reject the null hypothesis.
Notes: If the sample sizes are greater than 10, then the distribution of U can be approximated by a normal distribution.
The U value is then plugged into the formula seen here to calculate a Z statistic.
The calculated Z value is then compared to a critical Z value. When alpha is 5%, the critical Z-value is 1.96.
If the absolute value is greater than the critical value, then we reject the null hypothesis.

## Slide 640: Use SigmaXL to Run a Mann-Whitney Test
Case Study: We are interested in comparing the customer satisfaction between two types of customers using nonparametric (i.e. distribution-fee) hypothesis test: Mann-Whitney test.
  Data File: “Mann-Whitney” tab in “Sample Data.xlsx”
Null Hypothesis (H0): η1 = η2
Alternative Hypothesis (Ha): η1 ≠ η2
Notes: Now let’s use a case study to demonstrate how the Mann-Whitney Test works to compare the customer satisfaction results between two types of customers.

## Slide 641: Use SigmaXL to Run a Mann-Whitney Test
Steps to run a Mann-Whitney Test in SigmaXL:
  Select the entire range of data (both “Customer Type” and “Overall Satisfaction”)
  Click SigmaXL -> Statistical Tools -> Nonparametric Tests -> 2 Sample Mann-Whitney
  A new window named “2 Sample Mann Whitney” pops up with the selected range populated in the box under “Please select your data”
  Click “Next>>”
  A new window named “2 Sample Mann-Whitney” appears
  Select “Overall Satisfaction” as the “Numeric Data Variables (Y)”
  Select “Customer Type” as the “Group Category (X)”
  Select “Not Equal To” as the “Ha”
  Click “OK>>”
  The Mann-Whitney test results appear in the newly generated tab “2 Sample Mann-Whitney (1)”
Notes: To implement the test within the software package, follow these steps.

## Slide 642: Use SigmaXL to Run a Mann-Whitney Test

## Slide 643: Use SigmaXL to Run a Mann-Whitney Test
The p-value of the test is lower than alpha level (0.05) so we reject the null hypothesis and conclude that there is statistically significant difference between the overall satisfaction medians of the two customer types.
Notes: The result of the test is boxed in…the p-value is lower than the alpha value of 0.05; therefore, we must reject the null hypothesis and claim that there is a significant difference between the median customer satisfaction levels of the two groups.

## Slide 644: 3.5.2 Kruskal-Wallis
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 645: 3.5.3 Mood’s Median

## Slide 646: What is Mood’s Median Test?
Mood’s median test is a statistical test to compare the medians of two or more populations.
  Null Hypothesis (H0): η1 = … = ηk
  Alternative Hypothesis (Ha): at least one of the medians is different from the others.
  k is the number of groups of our interest and is equal to or greater than two.
Mood’s median is an alternative to Kruskal-Wallis.
It is the extension of one sample sign test.
For the data with outliers, Mood’s median test is more robust than the Kruskal-Wallis test.
Notes: The Mood’s Median test is similar to the Kruskall-Wallis in that it allows us to compare the medians of two or more populations. However, a key difference is that it is more robust when there are outliers.
Noted here is that the Mood’s Median test is an extension of the one-sample sign test. In a one-sample sign test, the null hypothesis is that the probability of a random value from the population being above the specified value is equal to the probability of a random value being below the specified value.

## Slide 647: Mood’s Median Test Assumptions
The sample data drawn from the populations of interest are unbiased and representative.
The data of k populations are continuous or ordinal when the spacing between adjacent values is not constant.
The k populations are independent to each other.
The distributions of k populations have the same shape.
Mood’s median test is robust for non-normally distributed populations.
Mood’s median test is robust for data with outliers.
Notes: Aside from the outliers, the assumptions for Mood’s Median test are the same as those for Mann Whitney or Kruskal-Wallis.

## Slide 648: How Mood’s Median Test Works
Step 1: Group the k samples from k populations (sample i is from population i) into one single data set and get the median of this combined data set.
Step 2: Separate the data in each sample into two groups. One consists of all the observations with values higher than the grand median and the other consists of all the observations with values lower than the grand median.
Notes: To conduct a Mood’s Median Test, we must first group the samples from all populations into a single data set and get the median of the combined data set.
Then for each sample, form two groups: one consisting of observations with values higher than the grand median and the other consisting of values lower than the grand median.

## Slide 649: How Mood’s Median Test Works
Step 3: Run a Pearson’s chi-square test to determine whether to reject the null hypothesis.
  Null Hypothesis (H0): η1 = … = ηk
  Alternative Hypothesis (Ha): at least one of the medians is different from the others.
If is greater than , we reject the null hypothesis and claim that at least one median is different from the others.
If is smaller than , we fail to reject the null hypothesis and claim that the medians of k populations are not statistically different.
Notes: A Pearson’s chi-square test is used to compare the actual number of observations less than and greater than the grand median to what is expected if the populations were the same.

## Slide 650: Use SigmaXL to Run a Mood’s Median Test
Case Study: We are interested in comparing the customer satisfaction among three types of customers using nonparametric (i.e. distribution-fee) hypothesis test: Mood’s median test.
  Data File: “Median Test” tab in “Sample Data.xlsx”
Null Hypothesis (H0): η1 = η2 = η3
Alternative Hypothesis (Ha): at least one of the customer type has different overall satisfaction from the others.
Notes: In a case study like we’ve looked at before, we will now use the software to run a Mood’s Median test…comparing the customer satisfaction among three types of customers.

## Slide 651: Use SigmaXL to Run a Mood’s Median Test
Steps to run a Mood’s median test in SigmaXL
  Select the entire range of data (both “Customer Type” and “Overall Satisfaction”
  Click SigmaXL -> Statistical Tools -> Nonparametric Tests -> Mood’s Median Test
  A new window named “Mood's Median” pops up with the selected range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Mood's Median Test” appears
  Select “Overall Satisfaction” as the “Numeric Data Variables (Y)”
  Select “Customer Type” as the “Group Category (X)”
  Click “OK”
  The Mood’s median test results appear in the newly generated tab “Mood's Median (1)”

## Slide 652: Use SigmaXL to Run a Mood’s Median Test

## Slide 653: Use SigmaXL to Run a Mood’s Median Test
The p-value of the test is lower than alpha level (0.05) and we reject the null hypothesis and conclude that at least the overall satisfaction median of one customer type is statistically different from the others.
Notes: Since the p-value is less than 0.05, we reject the null hypothesis and claim that at least one customer group has a different level of satisfaction.

## Slide 654: 3.5.4 Friedman
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 655: 3.5.5 One Sample Sign

## Slide 656: What is the One Sample Sign Test?
The one sample sign test is a hypothesis test to compare the median of a population with a specified value.
  Null Hypothesis (H0): η = η0
  Alternative Hypothesis (Ha): η ≠ η0
It is an alternative test of one sample t-test when the distribution of the data is non-normal. It is robust for the data with non-symmetric distribution.
Notes: A one sample sign test is similar to a one-sample t-test, where we compare the mean of a population to a specific value. However, with this test we are comparing the median of the population instead of the mean.
The one sample sign test is used instead of the one-sample t-test when the data distribution is non-normal.

## Slide 657: One Sample Sign Test Assumptions
The sample data drawn from the population of interest are unbiased and representative.
The data are continuous or ordinal when the spacing between adjacent values is not constant.
The one sample sign test is robust for the non-normally distributed population.
The one sample sign test does not have any assumptions on the distribution. It is a distribution-free test.
Notes: Assumptions for this test are very similar to those of other non-parametrics; however, a key difference is that there are no assumptions about the shape of the distribution.

## Slide 658: How the One Sample Sign Test Works
Step 1: Separate the sample set of data into two groups: one with values greater than and the other with values less than the hypothesized median η0. Count the number of observations in each group.
Step 2: Calculate the test statistic.
  If the null hypothesis is true, the number of observations in each group should not be significantly different from half of the total sample size.
  The test statistic follows a binomial distribution when the null is true. When n is large, we use the normal distribution to approximate the binomial distribution.
Notes: To perform the test, the sample data set is separated into two groups: one group with values higher than the specified value, and the other with values less than the specified value.
The null hypothesis for the test is that the number of values in each of the two groups is not different from half the total sample size.
The test statistic follows a binomial distribution when the null is true. When n is large, we use the normal distribution to approximate the binomial.

## Slide 659: How the One Sample Sign Test Works
Step 3: Make a decision on whether to reject the null hypothesis. If the |Zcalc| is smaller than Zcrit, we fail to reject the null hypothesis and claim that there is no significant difference between the population median and the hypothesized median.
Test Statistic:
where
n+ is the number of observations with values greater than the hypothesized median.
n is the total number of observations .
p is 0.5.
Notes: The test statistic Z is calculated using the n+, the number of values greater than the hypothesized median, the total number of observations (n), and p = 0.5
Make the determination about the hypothesis by comparing the absolute value of the test statistic to the critical Z value.

## Slide 660: Use SigmaXL to Run a One Sample Sign Test
Case Study: We are interested in comparing the overall satisfaction of customer type 1 against a specified benchmark satisfaction (3.5) using nonparametric (i.e. distribution-fee) hypothesis test: 1 Sample Sign test.
  Data File: “One Sample Wilcoxon” tab in “Sample Data.xlsx”
Null Hypothesis (H0): η1 = 3.5
Alternative Hypothesis (Ha): η1 ≠ 3.5
Notes: Now lets look at a case study and apply the software to run a one sample sign test.
In the example we are comparing the customer satisfaction level to a benchmark level of 3.5.

## Slide 661: Use SigmaXL to Run a One Sample Sign Test
Steps to run a one sample sign test in SigmaXL
  Select the entire range of data (both “Customer Type” and “Overall Satisfaction”
  Click SigmaXL -> Statistical Tools -> Nonparametric Tests -> 1 Sample Sign
  A new window named “1 Sample Sign” pops up with the selected range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “1 Sample Sign Test” appears
  Select “Overall Satisfaction” as the “Numeric Data Variables (Y)”
  Select “Customer Type” as the “Group Category (X)”
  Enter “3.5” in the box next to “H0: Median=“
  Click “OK”
  The one sample sign test results appear in the newly generated tab “1 Sample Sign Test (1)”

## Slide 662: Use SigmaXL to Run a One Sample Sign Test

## Slide 663: Use SigmaXL to Run a One Sample Sign Test
The p-value of the one sample sign test is 1.00 higher than the alpha level (0.05) and we fail to reject the null. There is not any statistically significant difference between the overall satisfaction of customer type 1 and the benchmark satisfaction level.
Notes: Since the p-value in this test is higher than 0.05, we fail to reject the null hypothesis and we conclude that there isn’t a statistically significant difference between the customer type 1 and the benchmark satisfaction level.

## Slide 664: 3.5.6 One Sample Wilcoxon
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 665: 3.5.7 One & Two Sample Proportion

## Slide 666: What is the One Sample Proportion Test?
One sample proportion test is a hypothesis test to compare the proportion of one certain outcome occurring in a population following the binomial distribution with a specified proportion.
  Null Hypothesis (H0): p = p0
  Alternative Hypothesis (Ha): p ≠ p0
Notes: A one-sample proportion test allows us to compare a proportion (i.e., the number of successes per the number of trials, or the number of defects per the total number of opportunities) to a specified proportion.
The population is following a binomial distribution.

## Slide 667: One Sample Proportion Test Assumptions
The sample data drawn from the population of interest are unbiased and representative.
There are only two possible outcomes in each trial: success/failure, yes/no, and defective/non-defective etc.
The underlying distribution of the population is binomial distribution.
When np ≥ 5 and np(1 – p) ≥ 5, the binomial distribution can be approximated by the normal distribution.
Notes: The sample that is pulled must be unbiased and representative of the population.
There must be only two possible outcomes for each trial (e.g., yes/no, defect or not, success/failure).
The population must follow the binomial distribution.
When n times p is greater than or equal to five AND n times p times one minus p is greater than or equal to five, the binomial distribution can be approximated by the normal distribution.

## Slide 668: How the One Sample Proportion Test Works
When np ≥ 5 and np(1 – p) ≥ 5, we use normal distribution to approximate the underlying binomial distribution of the population.
Test Statistic:
where
is the observed probability of one certain outcome occurring.
is the hypothesized probability.
is number of trials.
When |Zcalc| is smaller than Zcrit, we fail to reject the null hypothesis and claim that there is no statistically significant difference between the population proportion and the hypothesized proportion.
Notes: So why is the assumption about following the normal distribution important? Because we use the Z-test statistic.
We calculate the Z value as follows; using the sample proportion, the specified value, and the number of trials.
When the absolute value of the calculated test statistic is less than the critical value, then we fail to reject the null and claim that there is not a statistical difference between the sample and the specified value.

## Slide 669: Use SigmaXL to Run a One Sample Proportion Test
Case Study: We are interested in comparing the exam pass rate of a high school this month against a specified rate (70%) using nonparametric (i.e. distribution-fee) hypothesis test: one sample proportion test.
  Data File: “One Sample Proportion” tab in “Sample Data.xlsx”
Null Hypothesis (H0): p = 70%
Alternative Hypothesis (Ha): p ≠ 70%
Notes: In this case study we examine the pass rate of a high school exam and want to determine if it is statistically different from a specified value of 70%.

## Slide 670: Use SigmaXL to Run a One Sample Proportion Test
Steps to run a one sample proportion test in SigmaXL.
  Click SigmaXL -> Statistical Tools -> Basic Statistical Templates -> 1 Proportion Test and Confidence Interval
  A new tab named “1 Proportion Test CI” appears
  Enter “77” in the yellow box of “Number of Events in category of interest x”
  Enter ‘105” in the yellow box of “Sample Size”
  Enter 0.70 as “hypothesized proportion” test against 70%
  Keep 95% as the default confidence level
  See next page for steps as results..

## Slide 671: Use SigmaXL to Run a One Sample Proportion Test
The interpretation highlighted at bottom right, says “we are 95% confident that the true proportion lies between 0.6381 and 0.8149”
The p-value is 0.5286, therefore, we claim that there is not any statistically significant difference between the school’s exam passing rate and 70%.
Notes: In the output from the test we see the 95% confidence interval (alpha value is 0.05). It means we are 95% confident that the exam pass rate is between 0.6381 and 0.8149. The specified value of 70% falls within this interval; therefore we fail to reject the null hypothesis and claim that the exam pass rate is not different from the value of 70%

## Slide 672: What is the Two Sample Proportion Test?
The two sample proportion test is a hypothesis test to compare the proportions of one certain event occurring in two populations following the binomial distribution.
  Null Hypothesis (H0): p1 = p2
  Alternative Hypothesis (Ha): p1 ≠ p2
Notes: A two-sample proportion test allows us to compare two populations when looking for the probability of a certain event occurring in each.
The null hypothesis is that the proportions for the two populations are equal.

## Slide 673: Two Sample Proportion Test Assumptions
The sample data drawn from the populations of interest are unbiased and representative.
There are only two possible outcomes in each trial for both populations: success/failure, yes/no, and defective/non-defective etc.
The underlying distributions of both populations are binomial distribution.
When np ≥ 5 and np(1 – p) ≥ 5, the binomial distribution can be approximated by the normal distribution.
Notes: The assumptions for this test are the same as for the one sample proportion test.

## Slide 674: How the Two Sample Proportion Test Works
When np ≥ 5 and np(1 – p) ≥ 5, we use normal distribution to approximate the underlying binomial distributions of the populations.
Test Statistic:
where
and are the observed proportions of events in the two samples.
and are the number of trials in the two samples respectively.
and are the number of events in the two samples respectively.
When |Zcalc| is smaller than Zcrit, we fail to reject the null hypothesis.
Notes: Like the one sample proportion test, the assumption around the binomial distribution being approximated by the normal distribution comes into play.
The Z statistic is calculated using the observed proportions, the number of trials from the two samples, and the number of events (meeting the pass or fail characteristic, or the yes or no, etc.).

## Slide 675: Use SigmaXL to Run a Two Sample Proportion Test
Case Study: We are interested in comparing the exam pass rates of a high school in March and April using nonparametric (i.e. distribution-fee) hypothesis test: two sample proportion test.
  Data File: “Two Sample Proportion” tab in “Sample Data.xlsx”
Null Hypothesis (H0): pMarch = pApril
Alternative Hypothesis (Ha): pMarch ≠ pApril
Notes: In this case study we want to determine if the pass rates for an exam taken in March or April are statistically the same or different.

## Slide 676: Use SigmaXL to Run a Two Sample Proportion Test
Steps to run a two sample proportion test in SigmaXL
  Click SigmaXL -> Statistical Tools -> 2 Proportions Test & Confidence Interval
  A new tab named “2 Proportions Test and CI” appears automatically.
  Enter “89” in the yellow box of “Number of Events” in Sample #1 column
  Enter “112” in the yellow box of “Sample Size in Sample #1 column.
  Enter “102” in the yellow box of “Number of Events” in Sample #2 column.
  Enter “130” in the yellow box of “Sample Size” in Sample #2 column.
  Select “Fisher’s Exact” as the testing method.

## Slide 677: Use SigmaXL to Run a Two Sample Proportion Test
Fisher’s exact p-value (2-sided, Ha: P1 ≠ P2) is 0.8756 and higher than the alpha level of 0.05.
Therefore, we fail to reject the null and we claim that the exam pass rates in March and April are not statistically different.
Notes: In the output from the test we see the Fisher’s exact p-value is 0.876, higher than the alpha value of 0.05; therefore, we fail to reject the null hypothesis and claim there is not a difference between the schools exam pass rate in March and April.

## Slide 678: 3.5.8 Chi-Squared (Contingency Tables)
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 679: 3.5.9 Tests of Equal Variance

## Slide 680: What are Tests of Equal Variance?
Tests of equal variance are a family of hypothesis tests used to check whether there is a statistically significant difference between the variances of two or more populations.
  Null Hypothesis (H0):
  Alternative Hypothesis (Ha): at least the variance of one population is different from others.
  k is the number of populations of interest. k ≥ 2.
A tests of equal variance can be used alone but most of the time it is used with other statistical methods to verify or support the assumption about the variance equality.
Notes: Tests of equal variance are used to determine if there is a statistically significant difference between the variances of two or more populations.
Usually, the variance test is used as a prerequisite for other statistics tests. Often, the validity of a test rests upon whether the variance of the populations are the same; however, it also can be used alone.

## Slide 681: F-Test
The F-test is used to compare the variances between two normally distributed populations.
It is extremely sensitive to non-normality and serves as a preliminary step for two sample t-test.
Test Statistic:
, where
s1 and s2 are the sample standard deviations.
The sampling distribution of the test statistic follows F distribution when the null is true.
Notes: The F-test is applicable when we are interested in comparing the variances of only two populations.
This test serves as a precursor for the two sample t-test. It is very sensitive to non-normality, so it is crucial to validate that the data is normal before using this test.

## Slide 682: Bartlett’s Test
Bartlett’s test is used to compare the variances among two or more normally distributed populations.
It is sensitive to non-normality and it serves as a preliminary step for ANOVA.
Test Statistic:
, where
and
The sampling distribution of test statistic follows chi2 distribution when the null is true.
Notes: Bartlett’s test is used when we are comparing the variances of two or more normally distributed populations.
This test is used prior to ANOVA.

## Slide 683: Brown-Forsythe Test
The Brown-Forsythe test is used to compare the variances between two or more populations with any distributions.
It is not so sensitive to non-normality as Bartlett’s test.
The Test statistic is the model F statistic from the ANOVA on the transformed response where is the median response at ith level.
Notes: Like the Bartlett’s test, the Brown-Forsythe test is also used to compare the variances between two or more populations.
However, it is different in that is not as sensitive to non-normality in the data.
The test statistic is based on a transformation of the response variable, where the transformed response is the spread between the response and the median response of the group.

## Slide 684: Levene’s Test
Levene’s test is used to compare the variances between two or more populations with any distributions.
It is not so sensitive to non-normality as Bartlett’s test.
The test statistic is the model F statistic from the ANOVA on the transformed response where is the mean response at ith level.
Notes: The Levene’s test is similar to the Brown-Forsythe, but instead of transforming the response using the median for the group, it uses the mean.

## Slide 685: Brown-Forsythe Test vs. Levene’s Test
where
N is the total number of observations.
k is the number of groups.
Ni is the number of observations in the ith group.
Zi. is the group mean of the ith group.
Z.. is the grand mean of all the observations.
, where is the group median of the ith group.
In Brown-Forsythe Test,
, where is the group mean of the ith group.
In Levene’s Test,
Notes: The F statistic for both the Brown-Forsythe and Levene’s test are calculated the same way; however, you can see at the bottom of the slide how Z represents a different value for each.
In Brown-Forsythe, the Z calculation uses the group median.
In Levene, the Z calculation uses the group mean.

## Slide 686: Use SigmaXL to Run Tests of Equal Variance
Case Study: We are interested in comparing the variances of the retail price of a product in state A and state B.
  Data File: “Two-Sample T-Test” tab in “Sample Data.xlsx”
Null Hypothesis (H0):
Alternative Hypothesis (Ha):
Notes: We use a case study to compare the variances of a retail price of a product in state A and state B.

## Slide 687: Use SigmaXL to Run Tests of Equal Variance
Step 1: run the normality test to check whether all levels of data are normally distributed
  Select the entire range of data (both “State” and “Retail Price” columns)
  Click SigmaXL -> Graphical Tools -> Histograms & Descriptive Statistics
  A new window named “Histograms & Descriptive ” pops up with the selected range appearing in the box under “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Descriptive Statistics” appears
  Select “Retail Price” as the “Numeric Data Variables (Y)”
  Select “State” as “Group Category (X1)”
  Click “OK>>”
  The normality test results appear automatically in the new tab “Hist Descript (1)”

## Slide 688: Use SigmaXL to Run Tests of Equal Variance

## Slide 689: Use SigmaXL to Run Tests of Equal Variance
Null Hypothesis (H0): The data are normally distributed.
Alternative Hypothesis (Ha): The data are not normally distributed.
Both retail price data of state A and B are normally distributed since the p-values are both greater than alpha level (0.05).
Notes: The first step is to determine if the data follow the normal distribution.
When the p-value is greater than the alpha value, we fail to reject the null hypothesis and claim that the distributions are normal.
Both samples from state A and state B are normally distributed.

## Slide 690: Use SigmaXL to Run Tests of Equal Variance
Step 2: run tests of equal variance in SigmaXL
  If all the groups of data are normally distributed, run Bartlett’s test in SigmaXL to test the equality of the variance.
    Select the entire range of data (both “State” and “Retail Price” columns)
    Click SigmaXL -> Statistical Tools -> Equal Variance Tests -> Bartlett
    A new window named “Bartlett’s Test” pops up with the selected range appearing in the box under “Please select your data”
    Click “Next>>”
    A new window named “Bartlett’s Test” appears
    Select “Retail Price” as the “Numeric Data Variable (Y)”
    Select “State” as “Group Category (X)”
    Click “OK>>”
    The results of Bartlett’s test appear automatically in the new tab “Bartlett's Test (1)”
Notes: The next steps is to run the test for equal variance.

## Slide 691: Use SigmaXL to Run Tests of Equal Variance

## Slide 692: Use SigmaXL to Run Tests of Equal Variance
  The p-value of Bartlett’s test is greater than the alpha level of 0.05.
  Therefore, we fail to reject the null hypothesis and claim that the variances of different groups are identical.
Notes: Bartlett’s and F-test are used if the data are normally distributed. Levene’s test must be used if at least one of the groups is not normally distributed.
We had already determined that the data from both states are normal, so Bartlett’s test is appropriate.
The P-value is >0.05; therefore, we fail to reject the null hypothesis and claim that the variances between populations are the same.

## Slide 693: Use SigmaXL to Run Tests of Equal Variance
  If at least one of the groups is not normally distributed, run Levene’s test in SigmaXL to test the equality of the variance.
    Select the entire range of data (both “State” and “Retail Price” columns)
    Click SigmaXL -> Statistical Tools -> Equal Variance Tests -> Levene
    A new window named “Levene’s Test” pops up with the selected range appearing in the box under “Please select your data”
    Click “Next>>”
    A new window named “Levene’s Test” appears
    Select “Retail Price” as the “Numeric Data Variable (Y)”
    Select “State” as “Group Category (X)”
    Click “OK>>”
    The results of Levene’s test appear automatically in the new tab “Levene's Test (1)”
Notes: If at least one of the data sets were not normally distributed, we would run Levene’s test to determine the equality of the variances.

## Slide 694: Use SigmaXL to Run Tests of Equal Variance

## Slide 695: Use SigmaXL to Run Tests of Equal Variance
  The p-value of Levene’s test is greater than the alpha level of 0.05.
  Therefore, we fail to reject the null hypothesis and claim that the variances of different groups are identical.
Notes: The p-value for Levene’s test is greater than alpha of 0.05; therefore we fail to reject the null and claim that the variances are equal.

## Slide 696: Hypothesis Testing Roadmap: Putting it all together
Notes: The roadmap is a great way to quickly decide what type of hypothesis test fits a given situation by evaluating the type of data (discrete vs. continuous), the normality of the data, the number of levels, and other factors.

## Slide 697: 4.0 Improve Phase
Notes: The objective of the Improve phase is to identify a solution to the problem that the project is looking to address. It involves brainstorming potential solutions, selecting solutions to test, and evaluating the results of the implemented solutions. Often a pilot or test is used to evaluate the solution before a full-scale deployment.

## Slide 698: Black Belt Training: Improve Phase
4.1 Simple Linear Regression
4.1.1 Correlation
4.1.2 X-Y Diagram
4.1.3 Regression Equations
4.1.4 Residuals Analysis
4.2 Multiple Regression Analysis
4.2.1 Non-Linear Regression
4.2.2 Multiple Linear Regression
4.2.3 Confidence Intervals
4.2.4 Residuals Analysis
4.2.5 Data Transformation, Box Cox
4.2.6 Stepwise Regression
4.2.7 Logistic Regression
4.3 Designed Experiments
4.3.1 Experiment Objectives
4.3.2 Experimental Methods
4.3.3 DOE Design Considerations
4.4 Full Factorial Experiments
4.4.1 2k Full Factorial Designs
4.4.2 Linear and Quadratic Models
4.4.3 Balanced and Orthogonal Designs
4.4.4 Fit, Model, and Center Points
4.5 Fractional Factorial Experiments
4.5.1 Designs
4.5.2 Confounding Effects
4.5.3 Experimental Resolution

## Slide 699: 4.1 Simple Linear Regression
Notes: After identifying and validating the critical Xs during the Analyze phase, we will use some statistical tools during the Improve phase to define the settings needed to achieve the desired output. One such tool is simple linear regression.

## Slide 700: Black Belt Training: Improve Phase
4.1 Simple Linear Regression
4.1.1 Correlation
4.1.2 X-Y Diagram
4.1.3 Regression Equations
4.1.4 Residuals Analysis
4.2 Multiple Regression Analysis
4.2.1 Non-Linear Regression
4.2.2 Multiple Linear Regression
4.2.3 Confidence Intervals
4.2.4 Residuals Analysis
4.2.5 Data Transformation, Box Cox
4.2.6 Stepwise Regression
4.2.7 Logistic Regression
4.3 Designed Experiments
4.3.1 Experiment Objectives
4.3.2 Experimental Methods
4.3.3 DOE Design Considerations
4.4 Full Factorial Experiments
4.4.1 2k Full Factorial Designs
4.4.2 Linear and Quadratic Models
4.4.3 Balanced and Orthogonal Designs
4.4.4 Fit, Model, and Center Points
4.5 Fractional Factorial Experiments
4.5.1 Designs
4.5.2 Confounding Effects
4.5.3 Experimental Resolution

## Slide 701: 4.1.1 Correlation
Notes: We will start with correlation before regression, because it is a tool that helps us understand whether a relationship exists between two variables without having to know causality (which variable causes a response in the other). There are many similarities between correlation and simple linear regression.

## Slide 702: What is Correlation?
Correlation is a statistical technique that describes whether and how strongly two or more variables are related.
Correlation analysis helps to understand the direction and degree of association between variables, and it suggests whether one variable can be used to predict another.
Of the different metrics to measure correlation, Pearson’s correlation coefficient is the most popular. It measures the linear relationship between two variables.
Notes: Correlation helps us to understand whether there is a relationship between two variables, and how strong that relationship is.
It tells us the direction (increase in one variable causes an increase or decrease in the other) and the degree of the relationship between the variables.
Pearson’s correlation coefficient is the measure of the relationship between variables. It is the most popular measure of correlation.

## Slide 703: Pearson’s Correlation Coefficient
Pearson’s correlation coefficient is also called:
  Pearson’s r or coefficient of correlation
  Pearson’s product moment correlation coefficient (r)
“r” is a statistic measuring the linear relationship between two variables.
Correlation coefficients range from -1 to 1.
  If r = 0, there is no linear relationship between the variables.
  The sign of r indicates the direction of the relationship:
    If r < 0, there is a negative linear correlation.
    If r > 0, there is a positive linear correlation.
  The absolute value of r describes the strength of the relationship:
    If |r| ≤ 0.5, there is a weak linear correlation.
    If |r| > 0.5, there is a strong linear correlation.
    If |r| = 1, there is a perfect linear correlation.
Notes: Pearson’s correlation coefficient is also called Pearson’s r, correlation coefficient, or Pearson’s product moment correlation coefficient.
The r is a statistic that measures the linear relationship between the two variables, and it ranges from -1 to 1.
  Negative numbers represent a negative linear correlation, with -1 being a perfect negative correlation.
  Positive numbers represent a positive linear correlation, with 1 being a perfect positive correlation.
When the absolute value of r is greater than 0.5, there is a strong linear correlation. Less than 0.5 is a weak correlation. And zero indicates there is no relationship.

## Slide 704: Pearson’s Correlation Coefficient
When the correlation is strong, the data points on a scatter plot will be close together (tight).
  The closer “r” is to -1 or 1, the stronger the relationship.
    -1 Strong inverse relationship
    +1 Strong direct relationship
When the correlation is weak, the data points are spread apart more (loose).
  The closer the correlation is to 0 the weaker the relationship.
Notes: The visuals on the bottom of the slide demonstrate the relationships between variables as the Pearson r value ranges from 1 to 0 and to -1.
Notice that at -1 and 1 the points form a perfectly straight line. At 0 the data points are completely random.
At 0.8 and -0.8, notice how you can see a directional relationship, but there is some noise around where a line would be.
At 0.4 and -0.4, it looks like the scattering of data points is leaning to one direction or the other, but it is more difficult to see a relationship because of all the noise.

## Slide 705: Pearson’s Correlation Coefficient
Pearson’s correlation coefficient is only sensitive to the linear dependence between two variables.
It is possible that two variables have a perfect non-linear relationship when the correlation coefficient is low.
Notice the scatter plots below with correlation equal to 0. There are clearly relationships but they are not linear and therefore can not be determined with Pearson’s correlation coefficient.
Notes: The Pearson correlation coefficient is only sensitive to linear relationships. A graphical depiction of the data may show that some kind of relationship exists in the data, but if it is non-linear, the correlation coefficient will be low.
The scatter plots on this page all have Pearson r coefficients of zero, but as you can see there are clearly relationships depicted.

## Slide 706: Correlation and Causation
Correlation does not imply causation.
If variable A is highly correlated with variable B, it does not necessarily mean A causes B or vice versa. It is possible that an unknown third variable C is causing both A and B to change.
For example, if ice cream sales at the beach are highly correlated with the number of shark attacks, it does not imply that increased ice cream sales causes increased shark attacks. They are triggered by a third factor: summer.
Notes: Did you know that as ice cream sales increase, so does the number of shark attacks? This is classic fallacy that demonstrates the difference between correlation and causation. Certainly ice cream sales do not cause more shark attacks; however, this example demonstrates a common mistake that people make: assuming causation when they see correlation. In this example, it is hot weather that is a common factor. As the weather is hotter, more people consume ice cream and more people swim in the ocean, making them susceptible to shark attacks.

## Slide 707: Correlation and Dependence
If two variables are independent, the correlation coefficient is zero.
WARNING! If the correlation coefficient of two variables is zero, it does not imply they are independent.
The correlation coefficient only indicates the linear dependence between two variables. When variables are non-linearly related, they are not independent of each other but their correlation coefficient could be zero.
Notes: What does the correlation coefficient tell us if the value is zero?
If two variables are independent of each other, the correlation coefficient will be zero. However, a correlation coefficient of zero does NOT mean that they are independent.
Consider the non-linear relationships we saw earlier. There was clearly a relationship between the variables, but the Pearson r value was zero in each case.

## Slide 708: Correlation Coefficient and X-Y Diagram
The correlation coefficient indicates the direction and strength of the linear dependence between two variables but it does not cover all the existing relationship patterns.
With the same correlation coefficient, two variables might have completely different dependence patterns.
A scatter plot or X-Y diagram can help to discover and understand additional characteristics of the relationship between variables.
Correlation coefficient is not a replacement for examining the scatter plot to study the variables’ relationship.
Notes: The correlation coefficient by itself does not tell us everything about the relationship between two variables. Two relationships could have the same correlation coefficient, but completely different patterns.
To help us with this, we can use a scatter plot (also called and X-Y diagram) to see the other characteristics of the relationship between the variables.
The correlation coefficient is a complement, not a replacement, for using a scatter plot to study a relationship.

## Slide 709: Statistical Significance of the Correlation Coefficient
The correlation coefficient could be high or low by chance (randomness). It may have been calculated based on two small samples that do not provide good inference on the correlation between two populations.
In order to test whether there is a statistically significant relationship between two variables, we need to run a hypothesis test to determine whether the correlation coefficient is statistically different from zero.
  Hypothesis Test Statements
    H0: r = 0: Null Hypothesis: There is no correlation.
    H1: r ≠ 0: Alternate Hypothesis: There is a correlation.
Notes: A correlation analysis will always return a value. However, it is important to know if the relationship is real or only by chance.
If two small samples are used to calculate the coefficient, it is possible that the result it returns is purely by chance.
We can run a hypothesis test to determine if there is a statistically significant relationship between the two variables.
The null hypothesis is that r = 0, that there is no correlation. The alternative is that there is a correlation.

## Slide 710: Statistical Significance of the Correlation Coefficient
Hypothesis tests will produce p-values as a result of the statistical significance test on r.
  When the p-value for a test is low (less than 0.05), we can reject the null hypothesis and conclude that “r” is significant; there is a correlation.
  When the p-value for a test is > 0.05, then we fail to reject the null hypothesis; there is no correlation.
We can also use the t statistic to draw the same conclusions regarding our test for significance of the correlation coefficient.
Notes: The p-value will tell us whether or not the relationship is statistically significant. If the p < 0.05, then we reject the null and claim that there is a correlation.
The t statistic can also help us determine whether there is a real relationship between two variables.

## Slide 711: Statistical Significance of the Correlation Coefficient
Test Statistic:
Critical Statistic: t-value in t-table with (n – 2) degrees of freedom
If |t| ≤ tcritical, we fail to reject the null. There is no statistically significant linear relationship between X and Y.
If |t| > tcritical, we reject the null. There is a statistically significant linear relationship between X and Y.
Notes: To use the t-test to determine the statistical significance of the Pearson correlation, calculate the t statistic using the Pearson r value and the sample size, n.
The critical t value can be looked up in a t-table, using (n – 2) degrees of freedom.
If the absolute value of the calculated t value is less than or equal to the critical t value, then we fail to reject the null and claim no statistically significant linear relationship between X and Y.

## Slide 712: Using Software to Calculate the Correlation Coefficient
We are interested in understanding whether there is linear dependence between a car’s MPG and its weight and if so, how they are related.
The MPG and weight data are stored in the “Correlation Coefficient” tab in “Sample Data.xlsx.” We will discuss three ways to get the results.
Notes: In this example we will use the software to calculate the correlation coefficient.
We are looking to determine if there is a relationship between a car’s gas mileage and its weight, and how they are related.

## Slide 713: Use Excel to Calculate the Correlation Coefficient
The formula CORREL in Excel calculates the sample correlation coefficient of two data series.
The correlation coefficient between the two data series is -0.83, which indicates a strong negative linear relationship between MPG and weight.
Notes: We can use Microsoft Excel to calculate the correlation coefficient using the formula CORREL.
The result of this formula is -0.83, which indicates there is a strong negative linear relationship between gas mileage and weight.
In other words, as weight gets larger, gas mileage gets smaller.

## Slide 714: Interpreting Results
How do we interpret results and make decisions based Pearson’s correlation coefficient (r) and p-values?
  Let us look at a few examples:
    r = -0.832, p = 0.000 (previous example). The two variables are inversely related and the linear relationship is strong. Also, this conclusion is significant as supported by p-value of 0.00.
    r = -0.832, p = 0.71. Based on r, you should conclude the linear relationship between the two variables is strong and inversely related. However, with a p-value of 0.71, you should then conclude that r is not significant and that your sample size may be too small to accurately characterize the relationship.
    r = 0.5, p = 0.00. Moderately positive linear relationship, r is statistically significant.
    r = 0.92, p = 0.61. Strong positive linear relationship but r is not statistically significant. Get more data.
    r = 1.0, p = 0.00. The two variables have a perfect linear relationship and r is significant.
Notes: On this slide we will look at several example combinations of r coefficients and p-values and discuss how to interpret them.
In the first example, we see r=-0.832 and p = 0.00. This tells us that there is a strong negative linear relationship between them, and that the correlation is statistically significant.
In the second example, we see r=-0.832 and p = 0.71. With the p-value alone, you would conclude that there is a strong negative relationship between the variables; however, the p-value is greater than 0.05, so we reject the null and claim that there is not a statistically significant relationship.
The next pair indicates a moderately positive linear relationship, and the p-value does indicate statistical significance.
The next pair appears to show a strong positive relationship, but the p-value indicates that it is not statistically significant.
Finally, the last pair shows a perfect positive linear correlation and the relationship is statistically significant.

## Slide 715: Correlation Coefficient Calculation
Population Correlation Coefficient (ρ)
Sample Correlation Coefficient (r)
It is only defined when the standard deviations of both X and Y are non-zero and finite.
When covariance of X and Y is zero, the correlation coefficient is zero.
Notes: At the top is a formula to calculate the population correlation coefficient, but mostly you would use the second equation to calculate the correlation coefficient for a sample.
The formula is undefined when the standard deviation of either the X or Y variables is equal to zero.
When the covariance of both X and Y is zero, then the correlation coefficient is equal to zero.

## Slide 716: 4.1.2 X-Y Diagram
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 717: 4.1.3 Regression Equations

## Slide 718: Correlation and Regression Analysis
The correlation coefficient answers the following questions:
  Are two variables correlated?
  How strong is the relationship between two variables?
  When one variable increases, does the other variable increase or decrease?
The correlation coefficient cannot address the following questions:
  How much does one variable changes when the other variable changes by one unit?
  How can we set the value of one variable to obtain a targeted value of the other variable?
  How can we use the relationship between two variables to make predictions?
The simple linear regression analysis helps to answer these questions.
Notes: Correlation only tells us whether two variables are related, as well as the strength and direction of the relationship.
It does not allow us to model or predict behavior between the two variables, but simple linear regression does.

## Slide 719: What is Simple Linear Regression?
Simple linear regression is a statistical technique to fit a straight line through the data points.
It models the quantitative relationship between two variables.
It describes how one variable changes according to the change of another variable.
Both variables need to be continuous.
It is simple because only one predictor variable is involved.
Notes: Simple linear regression creates an algebraic model between the two variables, which we can use to describe how much one variable causes another to change.
Both variables must be continuous. There are other types of regression to model discrete data.

## Slide 720: Simple Linear Regression Equation
The simple linear regression analysis fits the data to a regression equation in the form
Y = α × X + β + e
  where:
  Y is the dependent variable (the response) and X is the single independent variable (the predictor).
  α is the slope describing the steepness of the fitting line. β is the intercept indicating the Y value when X is equal to 0.
  e stands for error (residual). It is the difference between the actual Y and the fitted Y (i.e., the vertical difference between the data point and the fitting line).
Notes: The regression equation for simple linear regression describes a line, where Y is the dependent variable, X is the independent variable, alpha is the slope of the line, and beta is the Y-intercept.
The e represents the residual error that the line cannot describe, the difference between the fitted line and the actual Y values.

## Slide 721: Ordinary Least Squares
The ordinary least square is a statistical method used in linear regression analysis to find the best fitting line for the data points.
It estimates the unknown parameters of the regression equation by minimizing the sum of squared residuals (i.e., the vertical difference between the data point and the fitting line).
In mathematical language, we look for α and β that satisfy the following criteria:
where
Notes: The method used for finding the best fitting line in regression analysis is called ordinary least squares.
The goal of the ordinary least squares is to minimize the total vertical distance between the line and the observed values.

## Slide 722: Ordinary Least Squares
The actual value of the dependent variable:
The fitted value of the dependant variable:
By using calculus, it can be shown the sum of squared error is minimal when
where i = 1, 2,…, n
where i = 1, 2,…, n

## Slide 723: ANOVA in Simple Linear Regression
X: the independent variable that we use to predict;
Y: the dependent variable that we want to predict.
Total Variation = Total Sums of Squares =
Explained Variation = Regression Sums of Squares =
Unexplained Variation = Error Sums of Squares =
Notes: The variance in simple linear regression can be expressed as a relationship between the actual value, the fitted value, and the grand mean – all in terms of Y.

## Slide 724: ANOVA in Simple Linear Regression
Linear regression is also analysis of variance (ANOVA).
  Variation Components:
    Total Variation = Explained Variation + Unexplained Variation
    i.e., Total Sums of Squares = Regression Sums of Squares + Error Sums of Squares
  Degrees of Freedom Components
    Total Degrees of Freedom = Regression Degrees of Freedom + Residual Degrees of Freedom
    i.e., n – 1 = (k – 1) + (n – k), where n is the number of data points, k is the number of predictors
Notes: Regression follows the same methodology as ANOVA and the hypothesis tests behind it use the same assumptions.

## Slide 725: ANOVA in Simple Linear Regression
Whether the overall model is statistically significant can be tested by using F-test of ANOVA.
  H0: The model is not statistically significant.
  Ha: The model is statistically significant.
Test Statistic:
Critical Statistic: F value in F table with (k – 1) degrees of freedom in the numerator and (n – k) degrees of freedom in the denominator.
If F ≤ Fcritical, we fail to reject the null. There is no statistically significant relationship between X and Y.
If F > Fcritical, we reject the null. There is a statistically significant relationship between X and Y.
Notes: The statistical significance of the regression model can be tested using the same F-test used in ANOVA.
The calculated test statistic is the mean squared regression divided by the mean squared error.
If the calculated F is less than or equal to the critical F, then we fail to reject the null and claim there is no statistically significant relationship between X and Y.

## Slide 726: Coefficient of Determination
R2 (also called coefficient of determination) measures the proportion of variability in the data that can be explained by the model.
R2 ranges from 0 to 1. The higher R2 is, the better the model can fit the actual data.
How to calculate R2:
Notes: R-squared is the proportion of the variability in the data that can be explained by the model. It tells you how well the model predicts future outcomes.

## Slide 727: Use SigmaXL to Run a Simple Linear Regression
Case Study
  We are trying to see whether the score in exam one has any statistically significant relationship with the score in final exam. If yes, how much impact does exam one have on the final exam?
  Data File: “Simple Linear Regression” tab in “Sample Data.xlsx”
Step 1: Determine the dependent and independent variables. Both should be continuous variables.
  Y (dependent variable) is the score of final exam.
  X (independent variable) is the score of exam one.
  Both variables are continuous.
Notes: In this example we want to determine if exam one has any bearing on the score of the final exam…if so, how much.
The first step is to determine which variable is the X (independent variable) and which is the Y (dependent variable).

## Slide 728: Use SigmaXL to Run a Simple Linear Regression
Step 2: Create a scatter plot to eyeball whether there seems to be a linear relationship between X and Y.
  Select the range of both independent and dependent variables in Excel.
  Click SigmaXL -> Graphical Tools -> Scatter Plots
  A new window named “Scatter Plots” pops up and the selected range appears automatically in the box below “Please select your data”.
  Click “Next >>”
  A new window also named “Scatter Plots” pops up.
  Select “FINAL” as Numeric Response (Y)” and “EXAM1” as “Numeric Predictor (X1) >>”
  Click “OK>>”
  A scatter plot is generated in a new spreadsheet “Scatterplot(1)”.
Notes: In the second step, we want to get a visual on the data to see if it looks like there is a linear relationship.

## Slide 729: Use SigmaXL to Run a Simple Linear Regression

## Slide 730: Use SigmaXL to Run a Simple Linear Regression
Based on the scatter plot, the relationship between exam one and final seems linear. The higher the score on exam one, the higher the score on the final.
Notes: It appears you could “fit” a line through this data.

## Slide 731: Use SigmaXL to Run a Simple Linear Regression
Step 3: Run the Simple Linear Regression analysis.
  Select the range of both independent and dependent variables in Excel.
  Click SigmaXL -> Statistical Tools -> Regression -> Multiple Regression
  A new window named “Multiple Regression” pops up and the selected range appears automatically in the box below “Please select your data”
  Click “Next >>”
  A new window also named “Multiple Regression” pops up
  Select “FINAL” as “Numeric Response (Y)” and “EXAM1” as “Continuous Predictor (X)”
  Click “OK>>”
  The regression analysis results appear in the newly generated spreadsheet “Multiple Regression” and the residual analysis results appear in another new spreadsheet “Mult Reg Residuals (1)”.

## Slide 732: Use SigmaXL to Run a Simple Linear Regression

## Slide 733: Use SigmaXL to Run a Simple Linear Regression
Step 4: Check whether the model is statistically significant. If not significant, we will need to re-examine the predictor or look for new predictors before continuing.
The “Analysis of Variance for Model” section provides a ANOVA table covering degrees of freedom, sum of squares and mean square information for total, model and error. The p-value of the F-test is lower than α level (0.05) indicating that the model is statistically significant.
The “Model Summary” section provides R2 which measures the percentage of variation in the data set which can be explained by the model. 89.51% of the variability in the data can be accounted for by this linear regression model.
Notes: Determine if the model is significant before looking at any of the other regression output. If the P-value is greater than alpha, then the model isn’t valid and we must look for other predictors.
The p-value is 0.0001, therefore we reject the null and claim the model is statistically significant.
The Rsquare value says that 89.5% of the variability can be explained by this model.

## Slide 734: Use SigmaXL to Run a Simple Linear Regression
Step 5: Understand regression equation
The estimates of slope and intercept are shown in the “Parameter Estimate” section.
In this example, Y = 15.622 + 1.852 * X.
A one unit increase in the score of Exam1 would increase the final score by 1.852.
Notes: The regression equation is Y = 15.6 + 1.85X, where X is the score on Exam 1 and Y is the final exam score.

## Slide 735: Interpreting the Results
Rsquare Adj = 89.0%
  89% of the variation in FINAL can be explained by EXAM1
P-value of the F-test = 0.000
  We have a statistically significant model
Prediction Equation: 15.6 + 1.85 × EXAM1
  15.6 is the Y intercept, all equations will start with 15.6
  1.85 is the EXAM1 Coefficient: multiply it by EXAM1 score
      Let us say you are the professor and you want to use this prediction equation to estimate what two of your students might get on their final exam.
Notes: Because the model is significant, and it explains 89% of the variability, we can use the model to predict final exam scores based on the results of exam 1.

## Slide 736: Interpreting the Results
Let us assume the following:
  Student “A” exam 1 results were: 79
  Student “B” exam 1 results were: 94.
Remember our prediction equation?
  15.6 + 1.85 × Exam1
  Now apply the equation to each student
    Student “A” Estimate: 15.6 + (1.85 × 79) = 161.8
    Student “B” Estimate: 15.6 + (1.85 × 94) = 189.5
          Now you can use your “magic” as the professor and allocate your time appropriately to the student(s) who you predict need the most help
          Nice Work!
Notes: By simply replacing exam 1 scores into the equation we can predict their final exam scores. But the key thing about the model is whether or not it is useful. In this case, the professor can use the results to figure out where to spend his time helping students.

## Slide 737: 4.1.4 Residuals Analysis

## Slide 738: What are Residuals?
Residuals are the vertical differences between actual values and the predicted values or the “fitted line” created by the regression model.
Vertical Distance
Actual Point
Predicted Value
Notes: Residuals are an important component of evaluating the quality of a regression model.
A residual is the vertical (y-axis) distance between an actual value and a value predicted by a regression model.

## Slide 739: Why Perform Residuals Analysis?
Regression equations are generated on the basis of certain statistical assumptions.
Residuals analysis helps to determine the validity of these assumptions.
The assumptions are:
  The residuals are normally distributed, mean equal to zero.
  The residuals are independent.
  The residuals have a constant variance.
  The underlying population relationship is linear.
If residuals performance does not meet the requirements, we will need to rebuild the model by replacing the predictor with a new one, adding new predictors, building non-linear models, and so on.
Notes: A linear regression model is not always appropriate for the data; therefore, assess the appropriateness of the model by analyzing the residuals.

## Slide 740: Use SigmaXL to Perform Residual Analysis
The residuals of the model are automatically generated in a new tab “Mult Reg Residuals (1)”

## Slide 741: Use SigmaXL to Perform Residual Analysis
Step 1: Check whether residuals are normally distributed around the mean of zero.
  Select the range of residuals in spreadsheet “Mult Reg Residuals (1)”
  Click SigmaXL -> Graphical Tool -> Histograms & Descriptive Statistics”
  A new window named “Histograms & Descriptive” pops up and the selected range of residuals automatically appears in the box below “Please select your data”.
  Click “Next >>”
  A new window also named “Histograms & Descriptive” pops up.
  Select “Residuals” as “Numeric Data Variables (Y)”
  Click “OK>>”
  The analysis results are shown automatically in the new spreadsheet “Hist Descript(1)”

## Slide 742: Use SigmaXL to Perform Residual Analysis

## Slide 743: Use SigmaXL to Perform Residual Analysis
The mean of residuals is 1.16E-12 which is approximately zero.
Anderson-Darling Test is used to test the normality. Since the p-value (0.3391) is greater than the alpha level (0.05), we fail to reject the null and the residuals are normally distributed.
  H0: The residuals are normally distributed.
  H1: The residuals are not normally distributed.
Notes: The first assumption about residuals is that they are normally distributed and have a mean equal to zero. With a p-value > 0.3391, we must reject the null and claim the data is normally distributed.

## Slide 744: Use SigmaXL to Perform Residual Analysis
Step 2: If the data are in time order, run the IR chart to check whether residuals are independent.
  Select the range of residuals in spreadsheet “Mult Reg Residuals (1)”
  Click SigmaXL -> Control Charts -> Individuals & Moving Range
  A new window named “Individuals & Moving Range” pops up and the selected range of residuals automatically appears in the box below “Please select your data”.
  A new window also named “Individuals & Moving Range” pops up.
  Select “Residuals” as “Numeric Data Variables (Y)” and check the box of “Test for special causes”
  Click “OK>>”
  The analysis results are shown automatically in the new spreadsheet “Indiv & MR Charts (1)”

## Slide 745: Use SigmaXL to Perform Residual Analysis

## Slide 746: Use SigmaXL to Perform Residual Analysis
If no data points are out of control in both the I-Chart and MR charts, the residuals are independent of each other. If the residuals are not independent, it is possible that some important predicators are not included in the model. In this example, since the IR chart is in control, residuals are independent.
Notes: An I-MR chart, showing that no data points are out of control, indicates that the data are independent.

## Slide 747: Use SigmaXL to Perform Residual Analysis
Step 3: Check if the residuals have equal variance across the predicted responses.
  We are looking for the pattern in which residuals spread out evenly around zero from the top to the bottom.
  The “Regular Residuals vs Predicted Values for: FINAL” chart is automatically generated in the right “Mult Reg Residulas (1)”.
Notes: Finally we verify that the residuals have equal variance across the predicted responses. In this example, you can see how the residual values disperse evenly around zero.
Heteroscedasticity is the condition where the assumption of equal variance is violated, and can lead us to believe a variable is a predictor when it is not.

## Slide 748: 4.2 Multiple Regression Analysis

## Slide 749: Black Belt Training: Improve Phase
4.1 Simple Linear Regression
4.1.1 Correlation
4.1.2 X-Y Diagram
4.1.3 Regression Equations
4.1.4 Residuals Analysis
4.2 Multiple Regression Analysis
4.2.1 Non-Linear Regression
4.2.2 Multiple Linear Regression
4.2.3 Confidence Intervals
4.2.4 Residuals Analysis
4.2.5 Data Transformation, Box Cox
4.2.6 Stepwise Regression
4.2.7 Logistic Regression
4.3 Designed Experiments
4.3.1 Experiment Objectives
4.3.2 Experimental Methods
4.3.3 DOE Design Considerations
4.4 Full Factorial Experiments
4.4.1 2k Full Factorial Designs
4.4.2 Linear and Quadratic Models
4.4.3 Balanced and Orthogonal Designs
4.4.4 Fit, Model, and Center Points
4.5 Fractional Factorial Experiments
4.5.1 Designs
4.5.2 Confounding Effects
4.5.3 Experimental Resolution

## Slide 750: 4.2.1 Non-Linear Regression
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 751: 4.2.2 Multiple Linear Regression

## Slide 752: What is Multiple Linear Regression?
Multiple linear regression is a statistical technique to model the relationship between one dependent variable and two or more independent variables by fitting the data set into a linear equation.
The difference between simple linear regression and multiple linear regression:
  Simple linear regression only has one predictor.
  Multiple linear regression has two or more predictors.
Notes: The multiple linear regression allows you to predict the dependent variable through two or more predictors.

## Slide 753: Multiple Linear Regression Equation
Y is the dependent variable (response).
X1, X2, … , Xp are the independent variables (predictors). There are p predictors in total.
Both dependent and independent variables are continuous.
β is the intercept indicating the Y value when all the predictors are zeros.
α1, α2, … , αp are the coefficients of predictors. They reflect the contribution of each independent variable in predicting the dependent variable.
e is the residual term indicating the difference between the actual and the fitted response value.
Notes: The terms carry the same meaning as in simple linear regression, only here there are multiple predictors, each with a coefficient.
Beta is the Y-intercept, and e is the error term for the residuals.

## Slide 754: Use SigmaXL to Run a Multiple Linear Regression
Case Study
  We are trying to see whether the scores in exam one, two and three have any statistically significant relationship with the score in final exam. If so, how are they related to final exam score? Can we use the scores in exam one, two and three to predict the score in final exam?
  Data File: “Multiple Regression Analysis” tab in “Sample Data.xlsx”
Step 1: Determine the dependent and independent variables. All should be continuous.
  Y (dependent variable) is the score of final exam.
  X1, X2 and X3 (independent variables) are the scores of exam one, two and three respectively.
  All the variables are continuous.
Notes: In this case study we are looking to see if scores on exams one, two, and three have a statistically significant relationship with the score in the final exam. The first step is to establish the dependent variable (the final exam score) and the independent variables (exams one, two, three).

## Slide 755: Use SigmaXL to Run a Multiple Linear Regression
Step 2: Start building the multiple linear regression model
  Select the range of independent and dependent variables in Excel.
  Click SigmaXL -> Statistical Tools -> Regression -> Multiple Regression
  A new window named “Multiple Regression” pops up and the selected range appears automatically in the box below “Please select your data”
  Click “Next >>”
  A new window also named “Multiple Regression” pops up
  Select “FINAL” as “Numeric Response (Y)” and “EXAM1”, “EXAM2” and “EXAM3” as “Continuous Predictor (X)”
  Click “OK>>”
  The regression analysis results appear in the newly generated spreadsheet “Multiple Regression” and the residual analysis results appear in another new spreadsheet “Mult Reg Residuals (1)”.

## Slide 756: Use SigmaXL to Run a Multiple Linear Regression

## Slide 757: Use SigmaXL to Run a Multiple Linear Regression
Step 3: Check whether the whole model is statistically significant. If not, we need to re-examine the predictors or look for new predictors before continuing.
H0: The model is not statistically significant (i.e. all the parameters of predictors are not significantly different from zeros).
H1: The model is statistically significant (i.e. at least one predictor parameter is significantly different from zero).
In this example, p-value is much smaller than alpha level (0.05), hence we reject the null and the model is statistically significant.
Notes: After running the regression using the software, the first step is to determine if the model is statistically significant. With a p-value less than 0.05, we must reject the null hypothesis and claim the model as significant.

## Slide 758: Use SigmaXL to Run a Multiple Linear Regression
Step 4: Check whether multicollinearity exists in the model.
  The VIF information is automatically generated in the “Parameter Estimate” table in the “Multiple Regression” spreadsheet.
Notes: We use the VIF (Variance Inflation Factor) to determine if multicollinearity exists.

## Slide 759: Multicollinearity
Multicollinearity is the situation when two or more independent variables in a multiple regression model are correlated with each other.
Although multicollinearity does not necessarily reduce the predictability for the model as a whole, it may mislead the calculation for individual independent variables.
To detect multicollinearity, we use VIF (Variance Inflation Factor) to quantify its severity in the model.
Notes: Multicollinearity is when two or more predictors/independent variables in a multiple regression are correlated with each other.
It does not impact the quality of the overall model, but the impact is felt with the calculations of the individual independent variables.

## Slide 760: Variance Inflation Factor (1)
VIF quantifies the degree of multicollinearity for each individual independent variable in the model.
VIF calculation:
  Assume we are building a multiple linear regression model using p predictors.
  Two steps are needed to calculate VIF for X1.
    Step 1: Build a multiple linear regression model for X1 by using X2, X3, …, Xp as predictors.
    Step 2: Use the R2 generated by the linear model in step 1 to calculate the VIF for X1.
    Apply the same methods to obtain the VIFs for other Xs. The VIF value ranges from one to positive infinity.
Notes: To calculate the VIF for a predictor, it is modeled as a dependent variable to the other predictors. The R-square value for that model is used to calculate the VIF for that variable.

## Slide 761: Variance Inflation Factor (2)
Rules of thumb to analyze variance inflation factor (VIF):
  If VIF = 1, there is no multicollinearity.
  If 1 < VIF < 5, there is small multicollinearity.
  If VIF ≥ 5, there is medium multicollinearity.
  If VIF ≥ 10, there is large multicollinearity.
Notes: These are the guidelines for interpreting the VIF.

## Slide 762: How to Deal With Multicollinearity
Increase the sample size.
Collect samples with a broader range for some predictors.
Remove the variable with high multicollinearity and high p-value.
Remove variables that are included more than once.
Combine correlated variables to create a new one.
In this section, we will focus on removing variables with high VIF and high p-value.
Notes: There are several things that can be done to deal with multicollinearity, but in this section we will focus on the technique of removing predictors that carry a high p-value.

## Slide 763: Use SigmaXL to Run a Multiple Linear Regression
Step 5: Deal with Multicollinearity
  Step 5.1: Identify a list of independent variables with VIF higher than 5. If no variable has VIF higher than 5, go to Step 6 directly.
  Step 5.2: Among variables identified in Step 5.1, remove the one with the highest p-value.
  Step 5.3: Run the model again, check the VIFs and repeat Step 5.1.
  Note: we only remove one independent variable at a time.
Notes: If there are variables in the regression with a VIF higher than 5, remove the one with the highest p-value and run the model again.
Repeat this process until there is no variable with a VIF higher than 5.

## Slide 764: Use SigmaXL to Run a Multiple Linear Regression
In this example, all three predictors have VIF higher than 5. Among them, EXAM1 has the highest p-value.
We will remove EXAM1 from the equation and run the model again.

## Slide 765: Use SigmaXL to Run a Multiple Linear Regression
Run the new multiple linear regression with only two predictors (i.e. EXAM2 and EXAM3).
Check the VIFs of EXAM2 AND EXAM3 and they are both smaller than 5. Hence, there is little multicollinearity existing in the model.

## Slide 766: Use SigmaXL to Run a Multiple Linear Regression
Step 6: Identify the statistically insignificant predictors. Remove one insignificant predictor at a time and run the model again. Repeat this step until all the predictors in the model are statistically significant.
  Insignificant predictors are ones with p-value higher than alpha level (0.05). When p>alpha level, we fail to reject the null and the predictor isn’t significant.
    H0: The predictor is not statistically significant.
    H1: The predictor is statistically significant.
  As long as the p-value is greater than 0.05, remove the insignificant variables one at a time in the order of the highest p-value.
  Once one insignificant variable is eliminated from the model, we need to rerun the model again to obtain new p-values for other predictors left in the new model.
Notes: Remove predictors with a p-value of greater than 0.05 (alpha), one at a time, starting with that with the highest p-value and re-run the model.
Repeat until all predictors are significant.

## Slide 767: Use SigmaXL to Run a Multiple Linear Regression
In this example, both predictors’ p-values are smaller than alpha level (0.05). As a result, we don’t need to eliminate any variables from the model.

## Slide 768: Use SigmaXL to Run a Multiple Linear Regression
Step 7: Display regression equation
  The multiple linear regression equation appears automatically at the top of the spreadsheet “Multiple Regression (2)”
  Parameter Estimates section provides the estimates of parameters in the linear regression equation.
Notes: Now that we have removed multicollinearity and all of the insignificant predictors, we have the parameters for the regression equation.

## Slide 769: Interpreting the Results
Rsquare Adj = 98.4%
  98% of the variation in FINAL can be explained by the predictor variables EXAM2 & EXAM3.
P-value of the F-test = 0.000
  We have a statistically significant model.
Variables p-value:
  Both are significant (less than 0.05).
VIF
  EXAM2 & EXAM3 are both below 5; we’re in good shape!
Equation: -4.34 + 0.722*EXAM2 + 1.34*EXAM3
  -4.34 is the Y intercept, all equations will start with -4.34.
  0.722 is the EXAM2 coefficient; multiply it by EXAM2 score.
  1.34 is the EXAM3 coefficient; multiply it by EXAM3 score.

## Slide 770: Interpreting the Results
      Let us say you are the professor again, and this time you want to use your prediction equation to estimate what one of your students might get on their final exam.
Assume the following:
  Exam 2 results were: 84
  Exam 3 results were: 102.
Use your equation: -4.34 + 0.722*EXAM2 + 1.34*EXAM3
Predict your student’s final exam score:
  -4.34 + (0.722*84) + (1.34*102) =-4.34 + 60.648 + 136.68 = 192.988
          Nice work again! Now you can use your “magic” as the smart and efficient professor and allocate your time to other students because this one projects to perform much better than the average score of 162.
Notes: Now that we know that exams two and three are statistically significant predictors, we can plug them into the regression equation to predict the results of the final exam for any student.

## Slide 771: 4.2.3 Confidence & Prediction Intervals

## Slide 772: Prediction
The purpose of building a regression model is not only to understand what happened in the past but more importantly to predict the future based on the past.
By plugging the values of independent variables into the regression equation, we obtain the estimation/prediction of the dependent variable.
Notes: Perhaps the most valuable attribute of a regression model is its ability to predict what will happen in the future, given certain conditions (the independent variables).

## Slide 773: Uncertainty of Prediction
We build the regression model using the sample data to describe as close as possible the true population relationship between dependent and independent variables.
Due to noise in the data, the prediction will probably differ from the true response value.
However, the true response value might fall in a range around the prediction with some certainty.
To measure the uncertainty of the prediction, we need confidence interval and prediction interval.
Notes: The model’s ability to predict is limited due to noise – other environmental factors that influence the value of the dependent variable.
We can put a confidence interval around the predicted values that will likely contain the true value.

## Slide 774: Confidence Interval
The confidence interval of the prediction is a range in which the population mean of the dependent variable would fall with some certainty, given specified values of the independent variables.
The width of confidence interval is related to:
  Sample size
  Confidence level
  Variation in the data.
We build the model based on a sample set {y1, y2,…, yn}. The confidence interval is used to estimate the value of the population mean μ of the underlying population.
The focus of the confidence interval are the unobservable population parameters.
The confidence interval accounts for the uncertainty in the estimates of regression parameters.
Notes: The confidence interval for the model depends on the sample size used to create the model, the confidence level one wants to have in the predicted results, and the amount of variation in the data.
The confidence interval is focused on the population parameters, the mean, and standard deviation.

## Slide 775: Prediction Interval
The prediction interval is a range in which future values of the dependent variable would fall with some certainty, given specified values of the independent variables.
We build the model based on a sample set {y1, y2,…, yn}. The prediction interval is used to estimate the value of future observation yn+1.
The focus of the prediction interval are the future observations.
Prediction interval is wider than confidence interval because it accounts for the uncertainty in the estimates of regression parameters and the uncertainty of the new measurement.
Notes: The prediction interval is focused on the future observations (predicted values).
It is wider than the confidence interval because of the uncertainty in the regression parameter estimates.

## Slide 776: Use SigmaXL to Obtain Prediction
On the right side of the newly generated spreadsheet “Multiple Regression (2)” is the table “Predicted Response Calculator”.
By entering the values of the independent variables into the table “Predicted Response Calculator”, the predicted response would appear automatically. In this case, if we enter 85 and 75 as the values for EXAM2 and EXAM3 respectively, the predicted response is 157.359.

## Slide 777: Use SigmaXL to Obtain Confidence Interval
On the right side of the newly generated spreadsheet “Multiple Regression (2)” is the table “Predicted Response Calculator”.
By entering the values of the independent variables into the table “Predicted Response Calculator”, the upper and lower 95% confidence levels would appear automatically. In this case, if we enter 85 and 75 as the values for EXAM2 and EXAM3 respectively, the 95% confidence interval for the response is [154.74,159.98].

## Slide 778: Use SigmaXL to Obtain Prediction Interval
On the right side of the newly generated spreadsheet “Multiple Regression (2)” is the table “Predicted Response Calculator”.
By entering the values of the independent variables into the table “Predicted Response Calculator”, the upper and lower 95% prediction levels would appear automatically. In this case, if we enter 85 and 75 as the values for EXAM2 and EXAM3 respectively, the 95% prediction interval for the response is [150.55,164.17].

## Slide 779: 4.2.4 Residuals Analysis

## Slide 780: Remember what Residuals Are?
Residuals are the vertical difference between actual values and the predicted values or the “fitted line” created by the regression model.
Vertical Distance
Actual Point
Predicted Value
Notes: Residuals are an important component of evaluating the quality of a regression model.
A residual is the vertical (y-axis) distance between an actual value and a value predicted by a regression model.

## Slide 781: Why Perform Residuals Analysis?
The regression equation generated based on the sample data can make accurate statistical inference only if certain assumptions are met. Residuals analysis can help to validate these assumptions. The following assumptions must be met to ensure the reliability of the linear regression model:
  The errors are normally distributed with mean equal to zero.
  The errors are independent.
  The errors have a constant variance.
  The underlying population relationship is linear.
If the residuals performance does not meet the requirement, we will need to rebuild the model by replacing the predictors with new ones, adding new predictors, building non-linear models, and so on.
Notes: A regression model is not always appropriate for the data; therefore, assess the appropriateness of the model by analyzing the residuals. The model is only reliable if certain assumptions are met: residuals are normally distributed with a mean of zero, errors are independent and have a constant variance, and the underlying population is linear.

## Slide 782: Use SigmaXL to Perform Residual Analysis
The residuals of the model are automatically saved in column E of the spreadsheet “Mult Reg Residuals (2)”

## Slide 783: Use SigmaXL to Perform Residual Analysis
Step 1: Check whether residuals are normally distributed around the mean of zero.
  Select the range of residuals in spreadsheet “Mult Reg Residuals (2)”
  Click SigmaXL -> Graphical Tool -> Histograms & Descriptive Statistics
  A new window named “Histograms & Descriptive” pops up and the selected range of residuals automatically appears in the box below “Please select your data”.
  Click “Next >>”
  A new window also named “Histograms & Descriptive” pops up.
  Select “Residuals” as “Numeric Data Variables (Y)”
  Click “OK>>”
  The analysis results are shown automatically in the new spreadsheet “Hist Descript(1)”

## Slide 784: Use SigmaXL to Perform Residual Analysis

## Slide 785: Use SigmaXL to Perform Residual Analysis
The mean of residuals is 7.18E-12 which is approximately zero.
Anderson-Darling Test is used to test the normality. Since the p-value (0.1957) is greater than the alpha level (0.05), we fail to reject the null and the residuals are normally distributed.
  H0: The residuals are normally distributed.
  H1: The residuals are not normally distributed.
Notes: The residuals are normally distributed and the mean is near zero.

## Slide 786: Use SigmaXL to Perform Residual Analysis
Step 2: If the data are in time order, run the IR chart to check whether residuals are independent.
  Select the range of residuals in spreadsheet “Mult Reg Residuals (2)”
  Click SigmaXL -> Control Charts -> Individuals & Moving Range
  A new window named “Individuals & Moving Range” pops up and the selected range of residuals automatically appears in the box below “Please select your data”.
  A new window also named “Individuals & Moving Range” pops up.
  Select “Residuals” as “Numeric Data Variables (Y)” and check the box of “Test for special causes”
  Click “OK>>”
  The analysis results are shown automatically in the new spreadsheet “Indiv & MR Charts (1)”

## Slide 787: Use SigmaXL to Perform Residual Analysis

## Slide 788: Use SigmaXL to Perform Residual Analysis
If no data points are out of control in both the I-Chart and MR charts, the residuals are independent of each other.
If the residuals are not independent, it is possible that some important predicators are not included in the model.
In this example, since the IR chart is in control, residuals are independent.
Notes: The residuals are independent.

## Slide 789: Use SigmaXL to Perform Residual Analysis
Step 3: Check whether residuals have equal variance across the predicted responses.
  We are looking for the patterns in which residuals spread out evenly around zero from the top to the bottom.
  The “Regular Residuals vs Predicted Values for: FINAL” chart is automatically generated on the right side of the sheet “Mult Reg Residulas (2)”.
Notes: The residuals are evenly distributed around zero. So are residuals pass the tests.

## Slide 790: 4.2.5 Data Transformation
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 791: 4.2.6 Stepwise Regression
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 792: 4.2.7 Logistic Regression
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 793: 4.3 Designed Experiments
Notes: Designed experiments are used as information gathering exercises in situations where variation is present. Sometimes the experimenter is controlling the situation, other times not. The goal is understanding how certain input factors affect an output factor.

## Slide 794: Black Belt Training: Improve Phase
4.1 Simple Linear Regression
4.1.1 Correlation
4.1.2 X-Y Diagram
4.1.3 Regression Equations
4.1.4 Residuals Analysis
4.2 Multiple Regression Analysis
4.2.1 Non-Linear Regression
4.2.2 Multiple Linear Regression
4.2.3 Confidence Intervals
4.2.4 Residuals Analysis
4.2.5 Data Transformation, Box Cox
4.2.6 Stepwise Regression
4.2.7 Logistic Regression
4.3 Designed Experiments
4.3.1 Experiment Objectives
4.3.2 Experimental Methods
4.3.3 DOE Design Considerations
4.4 Full Factorial Experiments
4.4.1 2k Full Factorial Designs
4.4.2 Linear and Quadratic Models
4.4.3 Balanced and Orthogonal Designs
4.4.4 Fit, Model, and Center Points
4.5 Fractional Factorial Experiments
4.5.1 Designs
4.5.2 Confounding Effects
4.5.3 Experimental Resolution

## Slide 795: 4.3.1 Experiment Objectives

## Slide 796: What is an Experiment?
An experiment is a scientific exercise to gather data to test a hypothesis, theory, or previous results.
Experiments are planned studies in which data are collected actively and purposefully.
A typical experiment follows this sequence:
  A problem arises.
  A hypothesis is stated.
  An experiment is designed and implemented to collect data.
  The analysis is performed to test the hypothesis.
  Conclusions are drawn based on the analysis results.
Notes: An experiment is used to gather data.
An output variable is measured at different levels of input variables, while holding other factors constant.
The data are collected with the purpose of understanding how an input variable will impact the output variable.

## Slide 797: Why Use Experiments?
Resolve Problems
  Eliminate defects or defectives.
  Shift performance means to meet customer expectations.
  Squeeze variation, making process more predictable.
Optimize Performance
  Use statistical methods to get desired process response.
  Minimize undesirable conditions, waste, or costs.
  Reduce variation to eliminate out-of-spec conditions.
Intelligent Design
  Design processes around variables that have significant impact on process outputs.
  Design processes around variables that are easier or more cost effective to manage.
Notes: Use experiments to determine which factors will help eliminate defects, shift performance to meet customer specs, or reduce variation in a process.

## Slide 798: Traditional Methods of Learning
Passive Learning
  Study or observe events while they occur.
  Study or analyze events after they occur.
OFAT Experiment (One Factor at a Time)
  An experimental style limited to controlling one factor independently while others remain either static or are allowed to vary.
Design of Experiments
  Purposefully and proactively manipulate variables so their effect on the dependent variable can be studied.
  Encourages an informative event to occur within specific planned parameters.
Notes: In passive learning we study the events either while they occur or after they occur. The factors in this type of study are not actively changed.
OFAT is exactly what it sounds like: changing only one factor and understanding the results.
Design of experiments is done with the intent of understanding the impact of multiple variables on an output variable.

## Slide 799: What is the Design of Experiment (DOE)?
                Design of experiment (DOE) is a systematic and cost effective approach to plan the exercises necessary to collect data and quantify the cause-and-effect relationship between the response and different factors.
In DOE, we observe the changes occurring in the output (i.e., response, dependent variable) of a process by changing one or multiple inputs (i.e., factors, independent variables).
Using DOE we are able to manipulate several factors with every run and determine their effect on the “Y” or output.
Notes: DOE is used to study the response to many factors, without the cost of gaining the same understanding of OFAT method.

## Slide 800: Common DOE Terminology
Response: Y, dependent variable, process output measurement
Effect: The change in the average response across two levels of a factor or between experimental conditions.
Factor: X’s, inputs, independent variables
Fixed Factor: Factor that can be controlled during the study
Random Factor: Factor that cannot be controlled during the study
Level: factor settings, usually high and low, + and -, 1 and -1
Treatment Combination: setting of all factors to obtain one response measurement (also referred to as a “run”)
Replication: Running the same treatment combination more than once (sequence of runs is typically randomized)
Repeat: Non-randomized replicate of all treatment combinations
Inference Space: Operating range of factors under study

## Slide 801: Y = f (Xs)
Process
X1
X2
Xk
Y
In Design of Experiments (DOEs)
  X1, X2, …, Xk are the inputs of the process. They can be either continuous or discrete variables.
  Y is the output of the process. Y is a continuous variable.
  A single X or a group of Xs potentially have statistically significant impact on the Y with different levels of influence.
Note: DOE for discrete Y is not covered in this module.
Notes: In DOE we are looking to understand the impact of the Xs (continuous or discrete input variables) on the Y (continuous output variable).

## Slide 802: Objectives of Experiments
Active Learning:
  Learn as much as possible with as little resources as possible. Efficiency is the name of the game.
Identify Critical X’s:
  Identify the critical factors that drive the output or dependent variable (“Y”).
Quantify Relationships:
  Generate an equation that characterizes the relationship between the X’s and the Y.
Optimize:
  Determine the required settings of all the X’s to achieve the optimal output or response.
Validate:
  Prove results through confirmation or pilot implementation before fully implementing solutions.
Notes: With experiments, we seek to learn as much as possible about process variables through minimal cost.
We look to identify the critical inputs, quantify their relationships with the output variable, and use the information to optimize the response variable.

## Slide 803: Principle of Parsimony
The ultimate goal of DOE is to use the minimum amount of data to discover the maximum amount of information.
The experiment is designed to obtain data as parsimoniously as possible to draw as much information about the relationship between the response and factors as possible.
DOE is often used when the resources to collect the data and build the model are limited.
Notes: The principle of parsimony (also known as Occam’s Razor or Ockham’s Razor) means that we should not look for complex solutions when a simple one will do. The principle applies to experimentation as well. DOE aims to maximize learnings about the relationship between factors and response while minimizing the amount of data.

## Slide 804: Tradeoffs
The objective of a specific DOE study should be determined by the team.
The more complex the objective is, the more data are required. As a result, more time and money are needed to collect the data.
By prioritizing the objectives and filtering factors which obviously do not have any effect on the response, a considerable amount of cost of running the DOE would be reduced.
Notes: The key tradeoff is between the objective and the resources needed to conduct a DOE study. The more one seeks to learn through a complex experiment, the more data are required. Therefore, it is important to prioritize objectives and not waste time/resources to study the effect of factors that obviously have no impact on a response.

## Slide 805: 4.3.2 Experimental Methods

## Slide 806: Planning a DOE
Problem Statement: Quantifiably define the problem
Objective: State the objective of the experiment
Primary Metric: Determine the response variable or “Y”
Key Process Input Variables (KPIV): Select the input variable(s) or X’s
Factor Levels: Determine level settings for all factors
Design: Select the experimental design for your DOE
Project Plan: Prepare a project plan for your experiment – human and capital resource allocation, timing, duration etc.
Gain Buy-in: Your experiment will need support and buy-in from several places, get it!
Run the experiment
Analyze, Interpret, and Share Results:

## Slide 807: DOE Problem Statement
Much like the overall problem statement discussed in the Define phase, a DOE problem statement should specific and have quantifiable elements.
Make sure your problem statement ties to a business goal or business performance indicator.
Problem statements should not include:
  Conclusions
  Solutions
  Causes.
Notes: A good problem statement for a DOE should be specific, quantifiable, and have a clear implication for the business.
It should not include conclusions, solutions, or causes – which are all possible outputs of a DOE.

## Slide 808: DOE Objectives
State the Objective
DOE Objective Examples:
  “To determine the effects of tire pressure on gas mileage”
  “To determine which factors have the most impact on gas mileage”
  “To determine the effects of a pick-up truck’s tailgate (up vs. down) on the truck’s gas mileage”
  “To determine which HVAC and Lighting factors are contributing most to Kwh consumption”
DOE objective statements should:
  Clearly define what you want to learn from the experiment
  Declare study parameters or scope.
Notes: The objective should clearly state what the expected outcome of the experiment is.

## Slide 809: DOE Primary Metric
Recall our discussion of primary metrics in the Define phase?
  We said something to this effect: “the primary metric is the most important measure of success.”
This statement still holds true when discussing the primary metric for a DOE.
The primary metric for a DOE is your experiment’s output or response under study.
It is the “Y” in your transfer function Y = f(x).
It is critical to understand the following things about your metric:
  Measurement accuracy, R&R, and/or bias
  Measurement frequency
  Measurement resolution.
Notes: The primary metric of a DOE is the response variable, or “Y”.
It is critical to understand the quality of the measurement system before starting a DOE.

## Slide 810: DOE Primary Metric
          Before embarking on a design of experiment you should have validated your measurement system.
          If you have not, now would be a wise time to back track and do so.
DOEs can be costly on a firm’s time and resources.
DOEs not planned and run properly will create waste and defective products because treatment combinations should “test” boundaries.
Do not allow your entire study to be wasted because of a poor measurement system or one that can not respond frequently enough for your test.
Measurement resolution is another key factor to consider for your DOE. Make sure your primary metric can decipher the size of the main effects and interactions you are looking for.
Notes: Why is a quality measurement system important?

## Slide 811: DOE Primary Metric
There is still even more to understand about your primary metric before jumping into a DOE.
Be sure to answer these questions before proceeding:
  Is it discrete or continuous?
  Do you want to shift its mean?
  Do you want to squeeze variation?
  What is the baseline?
  Is it in control?
  Is there seasonality, trending, or any cycle?
  How much change do you want to detect?
  Is your metric normally distributed?
Notes: Ensure there is solid understanding of the primary metric: discrete vs. continuous, is the goal to shift the mean or reduce variation, is it stable, is it seasonal or cyclical, etc.

## Slide 812: DOE Input Variables – KPIVs (key process input variables)
Factor selection is an important element in planning for a design of experiment.
Factors are the “things” or metrics that your study responds to.
Factors can be discrete or continuous.
Factors should have largely been determined through the use of tools and analytics used throughout the DMAIC roadmap.
  Failure modes and effects analysis
  Cause and effect diagram (fishbone)
  X-Y matrix
  Process mapping
  Planned studies
  Passive analytics
  etc.
Notes: Factors for a DOE should be determined throughout the DMAIC process, so the list of potential factors should have already been prioritized and narrowed prior to this point.

## Slide 813: DOE Factor Settings
Factor settings are the range of values selected for each factor.
Factor settings need to be predetermined before every experiment.
  Let us use this paper airplane as an example. Our factors under study for max distance as a response might be:
    Number of folds
    Paper weight
    Paperclip (yes or no)
    Thrust
    Launch height
    Launch angle etc.
  Factor settings are important because each setting selection should provide value to the study.
    Understanding the “margin” where that value can be found is where an experienced Black Belt will earn their keep.
    For example, what would we learn if we chose the test two levels for “number of folds” and we tested zero folds and 80 folds as our two settings for that factor? Right, nothing!
Notes: Factor settings are the values at which the factors will be set during the experiment. The settings are typically a high, low, and sometimes a medium setting. The range of settings should be wide enough to represent a typical operating range that will achieve a measureable response, but narrow enough to be practical.

## Slide 814: DOE – Design Considerations
Design selection is an aspect of properly planned design of experiments.
High-level overview of design types (you will learn more about these in later modules)
  Screening Designs:
    Fractional factorials
    Intended to narrow down the many factors to the vital few
    Screening designs enable many factors to be evaluated at a lower cost because of the nature of the design (main effects)
  Characterization Designs:
    Higher resolution fractional factorials
    Full factorials with fewer variables
    Main effect and interactions
  Optimization Designs:
    Full factorials
    Response surface designs.
Notes: There are different types of experiment designs used for different objectives.
Screening to narrow from many factors to the vital few.
Characterization designs to understand the main effects between factor and response, and any interactions between factors that drive a response.
Optimization designs to find the best settings to gain a desired response.

## Slide 815: DOE Project Plan
DOEs can require a fair amount of coordination between human and capital resources.
Preparing a DOE project plan is a wise step.
Make sure you identify critical dependencies like interfering with production or operating hours etc.
Use project management software or, at a minimum, a Gantt chart to help you identify critical path items.
Notes: Because of the amount of work and coordination necessary to conduct a DOE, a project plan can be useful.

## Slide 816: DOE – Getting Support
By running a DOE you are about to “discover” something new and better or validate an existing belief or assumption. (If you do not believe this you should not be running your DOE)
You are also about to cost your firm money or disrupt someone’ s routine…Get everyone on the same page before moving forward!
Hopefully, you have already established the framework for the following items. If not, follow these steps:
  Business Case and Justification
  Stakeholder Analysis – figure out who is with you and your project and who is not
  Communication Plan – build and execute your communication plan based on the first two items.
Notes: Ensure you have support before trying to run a DOE. Use some common tools to help with this.

## Slide 817: Run Your Experiment

## Slide 818: Analyze, Interpret, and Share Your DOE Results

## Slide 819: DOE Iterations
One single DOE might not be enough to completely answer the questions due to the following reasons:
  None of the potential factors identified are statistically significant to the response.
  More factors need to be included in the model.
  Residuals of the model are not performing well.
  The objectives of DOE changes due to business reasons.
Notes: There are some situations where a single DOE will not achieve the objective on its own.

## Slide 820: 4.3.3 Experiment Design Considerations

## Slide 821: Considerations of Experiments
Objectives of the experiments
Resource availability to run the experiments
Potential costs to implement the experiments
Stakeholders’ support for successful experiments
Accuracy and precision of the measurement system
Statistical stability of the process
Unexpected plans or changes
Sequence of running the experiments
Simplicity of the model
Inclusion of potential significant factors
Settings of factors
Well-behaved residuals
Notes: There are many factors to consider when deciding what type of experimental approach to take:
What are we trying to learn? What are the objectives?
What resources are available for experimenting, and how much are the experiments expected to cost?
How good is the measurement system?
Is the process stable, and can we expect the experiment to give us a true reading on how the process will react to changing factors?
What are the right factors to experiment with, and what are the appropriate settings to use?

## Slide 822: 4.4 Full Factorial Experiments

## Slide 823: Black Belt Training: Improve Phase
4.1 Simple Linear Regression
4.1.1 Correlation
4.1.2 X-Y Diagram
4.1.3 Regression Equations
4.1.4 Residuals Analysis
4.2 Multiple Regression Analysis
4.2.1 Non-Linear Regression
4.2.2 Multiple Linear Regression
4.2.3 Confidence Intervals
4.2.4 Residuals Analysis
4.2.5 Data Transformation, Box Cox
4.2.6 Stepwise Regression
4.2.7 Logistic Regression
4.3 Designed Experiments
4.3.1 Experiment Objectives
4.3.2 Experimental Methods
4.3.3 DOE Design Considerations
4.4 Full Factorial Experiments
4.4.1 2k Full Factorial Designs
4.4.2 Linear and Quadratic Models
4.4.3 Balanced and Orthogonal Designs
4.4.4 Fit, Model, and Center Points
4.5 Fractional Factorial Experiments
4.5.1 Designs
4.5.2 Confounding Effects
4.5.3 Experimental Resolution

## Slide 824: 4.4.1 2k Full Factorial Designs
Notes: With a 2k Full Factorial Design:
Each factor has two levels (often labeled + and -)
It is possible to get a useful design for preliminary analysis and weed out the unimportant factors
A 2k Full Factorial Design also allows initial study of interactions.

## Slide 825: DOE Key Terms
Response: Y, dependent variable, process output measurement
Effect: The change in the average response across two levels of a factor or between experimental conditions
Factor: X’s, inputs, independent variables
Fixed Factor: Factor that can be controlled during the study
Random Factor: Factor that cannot be controlled during the study
Factor Levels: Factor settings, usually high and low, + and -, 1 and -1
Treatment Combination: setting of all factors to obtain one response measurement (also referred to as a “run”)
Replication: Running the same treatment combination more than once (sequence of runs is typically randomized)
Repeat: Non-randomized replicate of all treatment combinations
Inference Space: Operating range of factors under study
Main Effect: The average change from one level setting to another for a single factor
Interaction: The combined effect of two factors independent of the main effect of each factor

## Slide 826: More About Factors
Factors in DOE are the potential causes that might have significant impact on the outcome of a process or a product.
Factors are the inputs of a process or system and the response is the output of it.
Factors can be continuous or discrete variables.
Most experiments use two or more factors. Ask subject matter experts’ opinions for main factors selection. The more factors in DOE, the more costs triggered.
Notes: Factors are the independent variables in an experiment, the controllable inputs that are changed in order to understand the impact on the response variable.
Only include the factors that might have a significant impact on the response variable: they can be continuous or discrete variables.
Most experiments include at least two or more factors to maximize learning from the experiment; however, they must be balanced with cost.

## Slide 827: More About Factors
The goal of a DOE is to measure the effects of factors and interactions of factors on the outcome.
In DOE:
  First, we create a set of different combinations of factors each at different levels.
  Second, we run the experiment and collect the response values in different scenarios.
  Third, we analyze the results and test how the response changes accordingly when factors change.
Notes: The goal is to understand the “main” effects of factors, as well as the interaction of factors, on the response variable.
In a DOE we do this through creating different combinations of factors at different levels, running the experimental combinations to measure the responses, and then analyzing the results to determine how the response variable reacts to the factors.

## Slide 828: Factor Levels
Factor levels are the selected settings of a factor we are testing in the experiment.
The more levels a factor has, the more scenarios we have to create and test. As a result, more resources are required to collect samples and the model is more complicated.
The most popular DOE is two-level design, meaning only two levels for each factor.
Notes: The more levels of a factor we wish to test, the more complicated and costly the experimental design becomes.
A two-level design is the most popular – using only two levels for each factor in the experiment.

## Slide 829: Factor Levels
Code of factor levels
  High vs. Low
  (+1) vs. (-1)
  (+) vs. (-)
Example of factor levels
  A study on how two factors affect the taste of cakes.
Notes: Examples of factors in a experimental design using two levels labeled +1 and -1 to indicate a high value and a low value.

## Slide 830: Treatment Combination
A treatment is a combination of different factors at different levels.
It is a unique scenario setting in an experiment.
Coding treatments:
  If there are two factors in an experiment, we name one factor A and the other factor B.
  A single treatment in an experiment is named for each factor:
    --, +-, -+ and ++
    l, a, b and ab
Notes: A “treatment” represents an experimental run where each factor is set at a particular level. Each treatment combination is a unique process setting in an experiment.

## Slide 831: Treatment Combination
Example of treatment
  A study on how two factors affect the taste of cakes.

## Slide 832: Response
A response is the output of a process, a system, or a product.
It is the outcome we are interested to improve by optimizing the settings of factors.
In an experiment, we observe, record, and analyze the corresponding changes occurring in the response after changing the settings of different factors.
Notes: At every “treatment combination” of factors we record the response – the measured output of the process, system, or product.

## Slide 833: Response
Example of treatment
  A study on how two factors affect the taste of cakes. We use a predefined metric to measure the cake’s tastiness.
  After running each treatment, we obtain and record the resulting response value.

## Slide 834: Main Effect
Main effect is the average change in the response resulting from the change in the levels of a factor.
It captures the effect of a factor alone on the response without taking into consideration other factors.
In the baking cake example, the main effects of temperature and time length are
Notes: The main effect is simply the effect of a single factor on the response variable.

## Slide 835: Main Effect
Interpretation of main effect in the example:
  By changing the temperature level of the oven from high to low, the response (i.e., tastiness of the cake) increases by 6 measurement units.
  By changing the time length of baking from high to low, the response (i.e., tastiness of the cake) increases by 2 measurement units.

## Slide 836: Interaction Effect
Interaction effect is the average change in the response resulting from the change in the interaction of multiple factors.
It occurs when the change in the response triggered by one factor depends on the change in other factor(s).
Notes: The interaction effect is the combined, or simultaneous, effect of two or more factors acting together on a response variable.
Consider two factors related to changing a response variable – the flavor of a cup of coffee. The factors are stirring the coffee and addition of sugar to the coffee. Adding sugar alone, or stirring alone, does not change the flavor of the coffee; however, the combination of the two has a significant impact on the taste of the coffee.

## Slide 837: Interaction Effect
Example of interaction effect
By changing the interaction from high to low, the response (i.e., tastiness of the cake) increases by 4 measurement units.
One interaction

## Slide 838: 2k Full Factorial DOE
In a full factorial experiment, all of the possible combinations of factors and levels are created and tested.
For example, for two-level design (i.e., each factor has two levels) with k factors, there are 2k possible scenarios or treatments.
  2 factors, each with 2 levels, we have 22 = 4 treatments
  3 factors, each with 2 levels, we have 23 = 8 treatments
  k factors, each with 2 levels, we have 2k treatments
Notes: In a full factorial experiment, the treatment combinations represent all possible combinations of factor levels.
In a two-level design, you can calculate the number of treatment combinations by raising the number of levels (two) to the number of factors (k).

## Slide 839: 2k Full Factorial DOE
Full factorial DOE is used to discover the cause-and-effect relationship between the response and both individual factors and the interaction of factors.
Generate an equation to describe the relationship between Y and the important Xs:
where
Y is the response and X1, X2, …, Xk are the factors.
α0 is the intercept and α1, α2, …, αp are the coefficients of the factors and interactions.
ε is the error of the model.
Notes: A full factorial design of experiment is useful for discovering both the main effects and interactions between factors. However, this is the most costly form of DOE for a given number of factors.

## Slide 840: Two-Level Two-Factor Full Factorial
Below is a design pattern of a two-level two-factor full factorial experiment:
Notes: 2 (level) raised to 2 (factors) = 4 treatment combinations.

## Slide 841: Two-Level Three-Factor Full Factorial
Below is a design pattern of a two-level three-factor full factorial experiment
Notes: 2 (levels) raised to 3 (factors) = 8 treatment combinations.

## Slide 842: Two-Level Four-Factor Full Factorial
Below is a design pattern of a two-level four-factor full factorial experiment
Notes: 2 (levels) raised to 4 (factors) = 16 treatment combinations

## Slide 843: Two-Level Five-Factor Full Factorial
At left is a design pattern of a two-level five-factor full factorial experiment
Notes: 2 (levels) raised to 5 (factors) = 32 treatment combinations

## Slide 844: Order to Run Experiments
The four design patterns shown earlier are listed in the standard order.
Standard order is used to design the combinations/treatments before experiments start.
When actually running the experiments, randomizing the standard order is recommended to minimize the noise.
Notes: When designing the test and the treatment combinations, there is a standard order of combinations to follow; however, it is important to randomize the order when actually running the experiments.

## Slide 845: Replication in Experiments
Each treatment can be tested multiple times in an experiment in order to increase the degrees of freedom and improve the capability of analysis. We call this method replication.
Replicates are the number of repetitions of running an individual treatment.
The order to run the treatments in an experiment should be randomized to minimize the noise.
Notes: A replicate is a repeat of a specific treatment combination, which increases the power of the experimental responses.
Advantages: helps to better identify the true sources of variation, helps estimate the true impacts of the factors on the response, and overall improves the reliability and validity of the experimental results.

## Slide 846: 22 Full Factorial DOE
Case study: we are running a 22 full factorial DOE to discover the cause-and-effect relationship between the cake tastiness and two factors: temperature of the oven and time length of baking.
Each factor has two levels and there are four treatments in total.
We decide to run each treatment twice so that we have enough degrees of freedom to measure the impact of two factors and the interaction between two factors. Therefore, there are eight observations in response eventually.
Notes: This case study looks to understand the impact of two factors, temperature and baking time, on cake tastiness. The objective is to understand the main effects and the interactions of these factors on the response variable.

## Slide 847: 22 Full Factorial DOE
After running the four treatments twice in a random order, we obtain the following results
Notes: There are two factors and two levels, so there would be 2^2 = 4 treatment combinations. With replicates, each treatment combination is repeated once; therefore, there are in total 8 runs in this experiment.

## Slide 848: 22 Full Factorial DOE
The experiment results are consolidated into the following table

## Slide 849: 22 Full Factorial DOE
Main effect of factor A (temperature of the oven):
Factor B
Factor A
low
high
low
high
l
b
ab
a
where
k is the number of factors,
r is the number of times individual treatments are being run.
Notes: The main effect of factor A is computed by averaging the difference between combinations where A was at its high settings and where A was at its low settings.
Using the formula provided, the main effect of increasing the temperature of the oven is to decrease tastiness of the cake by -6.25.

## Slide 850: 22 Full Factorial DOE
Main effect of factor B (time length of baking):
Factor B
Factor A
low
high
low
high
l
b
ab
a
where
k is the number of factors,
r is the number of times individual treatments are being run.
Notes: The main effect of factor B, similar to A, is computed by averaging the difference between combinations where B was at its high settings and where B was at its low settings.
Using the formula provided, the main effect of increasing the baking time is to decrease the tastiness of the cake by -1.75

## Slide 851: 22 Full Factorial DOE
Interaction (i.e., A*B) effect
Factor B
Factor A
low
high
low
high
l
b
ab
a
where
k is the number of factors,
r is the number of times individual treatments are being run.
Notes: The interaction effect is computed by averaging the difference between combinations where A and B were at opposite settings (low and high).
Using the formula provided, the interaction effect of the temperature and time variables on tastiness was -3.25.

## Slide 852: 22 Full Factorial DOE
Sum of squares of factors and interaction
where
k is the number of factors,
r is the number of times individual treatments are being run.
Notes: The sums of squares tells us the relative strength of each main effect and interaction. A has the strongest effect as indicated by the high SS value.

## Slide 853: 22 Full Factorial DOE
Degrees of freedom of factors and interaction
Four degrees of freedom are required in the model because there are three independent variables (a, b, ab interaction) in the equation and one degree of freedom is required for the error:
  Y = α0 + α1 * A + α2 * B + α3 * A * B + Error
Notes: The degrees of freedom are necessary to determine the mean squares value.
Four degrees of freedom are necessary because there are three effects we are looking to understand: factor A, factor B, and the interaction between them.

## Slide 854: 22 Full Factorial DOE
Mean squares of factors and interaction

## Slide 855: Use SigmaXL to Run a 2k Full Factorial DOE
Step 1: Initiate the experiment design
  Click SigmaXL -> Design of Experiments -> 2-Level Factorial/Screening -> 2-Level Factorial/Screening Designs
  A new window named “2-Level Factorial/Screening Design of Experiments” pops up.
Step 2: Enter the response.
  Select “1” as the Number of Response.
  Enter “Tastiness” into the “Response Name” box.
Step 3: Enter the factors and make the design
  Select “2” as the Number of Factors
  Select “4-Run, 2**2, Full-Factorial” as the design
  Select “2” as the Number of Replicates
  Enter “Temperature” as the name for factor A
  Enter “Time Length” as the name for factor B
  Click “OK>>”
  The 22 full factorial DOE template appears in the newly generated tab “2 Factor DOE”.
Notes: Create the design

## Slide 856: Use SigmaXL to Run a 2k Full Factorial DOE
Notes: Enter the response variable.

## Slide 857: Use SigmaXL to Run a 2k Full Factorial DOE

## Slide 858: Use SigmaXL to Run a 2k Full Factorial DOE
Step 4: Run the experiment and record the response in the table created by SigmaXL
Notes: Run the experiment and record the response for each treatment combination.

## Slide 859: Use SigmaXL to Run a 2k Full Factorial DOE
Step 5: Analyze the experiment results
  Click SigmaXL -> Design of Experiments -> 2-Level Factorial/Screening -> Analyze 2-Level Factorial/Screening Design
  A new window named “Analyze 2-Level Factorial/Screening Design” appears in which “Tastiness” is automatically selected as the response variable and three factors including the interaction term are automatically selected as the independent variables.
  Click “OK>>”
  The DOE analysis results appear in the newly generated tab “Analyze – 2 Factor DOE”.
Notes: Analyze the results

## Slide 860: Use SigmaXL to Run a 2k Full Factorial DOE

## Slide 861: Use SigmaXL to Run a 2k Full Factorial DOE
P value smaller than alpha level (0.05) indicates that the model is statistically significant (i.e. at least one of the independent variables in the model has coefficient statistically different from zero).
High R2 value shows around 98% of the variation in the response can be explained by the model.
Notes: 98% of the variation in the response variable can be explained by the model (very good results)
P-value is less than 0.05, indicating the model is significant and at least one of the factors is statistically significant.

## Slide 862: Use SigmaXL to Run a 2k Full Factorial DOE
Since p values of all the independent variables in the mode are smaller than alpha level (0.05), both factors and their interaction have statistically significant impact on the response.
Notes: The output provides intercept values and coefficients for a regression model equation.

## Slide 863: Use SigmaXL to Run a 2k Full Factorial DOE
Enter the actual settings of the independent variables into the yellow cells on the “Analyze – 2 Factor DOE” tab. The predicted response will be calculated automatically.
Notes: Using the model that the software created, now the response variable can be predicted given a setting for each factor.

## Slide 864: 4.4.2 Linear & Quadratic Models
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 865: 4.4.3 Balanced & Orthogonal Designs

## Slide 866: Balanced Design
In DOE, an experiment design is balanced if individual treatments have the same number of observations.
In other words, if an experiment is balanced, each level of each factor is run the same number of times.
The following design is balanced since the two factors are both run twice at each level.
Notes: An experiment where every treatment combination is run then same number of times is a balanced design.

## Slide 867: Orthogonal Design
In DOE, an experiment design is orthogonal if the main effect of one factor can be evaluated independently of other factors.
In other words, for each level (high setting or low setting) of a factor, the number of high setting and low setting in any other factors must be the same.
Notes: In an orthogonal design, for a given level of any factor, the number of high and low settings for any other factors must be the same.

## Slide 868: Orthogonal Design
In the following design, for the higher level (+1) of factor A, the number of “+1” in factor B is 2 but the number of “-1” in factor B is 0. Therefore, this is not an orthogonal design.
Notes: At the high level of factor A, there are two high-level settings for factor B and no low-level settings; therefore, the design is not orthogonal.

## Slide 869: Orthogonal Design
In the following design, for the higher level (+1) of factor A, the number of “+1” in factor B is 1 and the number of “-1” in factor B is 1 as well. Therefore, this is an orthogonal design.
Notes: In this design there is an equal number of high and low factor settings on factor B for each factor level of A. It is an orthogonal design.

## Slide 870: Checking for an Orthogonal Design
We can check to see if our design is orthogonal with some very simple math.
In an orthogonal design, the sum of products for each run should equal zero.
Let us check the earlier design that we said was orthogonal:
  Run 1: -1 * -1 = 1
  Run 2: +1 * -1 = -1
  Run 3: -1 * +1 = -1
  Run 4: +1 * +1 = 1
  Sum = 0
  Design is orthogonal

## Slide 871: Checking for an Orthogonal Design
Now let us check the earlier design that we said was not orthogonal:
  Run 1: -1 * -1 = 1
  Run 2: -1 * -1 = 1
  Run 3: +1 * +1 = 1
  Run 4: +1 * +1 = 1
  Sum = 4
  Design is not orthogonal

## Slide 872: 4.4.4 Fit, Diagnosis and Center Points
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 873: 4.5 Fractional Factorial Experiments

## Slide 874: Black Belt Training: Improve Phase
4.1 Simple Linear Regression
4.1.1 Correlation
4.1.2 X-Y Diagram
4.1.3 Regression Equations
4.1.4 Residuals Analysis
4.2 Multiple Regression Analysis
4.2.1 Non-Linear Regression
4.2.2 Multiple Linear Regression
4.2.3 Confidence Intervals
4.2.4 Residuals Analysis
4.2.5 Data Transformation, Box Cox
4.2.6 Stepwise Regression
4.2.7 Logistic Regression
4.3 Designed Experiments
4.3.1 Experiment Objectives
4.3.2 Experimental Methods
4.3.3 DOE Design Considerations
4.4 Full Factorial Experiments
4.4.1 2k Full Factorial Designs
4.4.2 Linear and Quadratic Models
4.4.3 Balanced and Orthogonal Designs
4.4.4 Fit, Model, and Center Points
4.5 Fractional Factorial Experiments
4.5.1 Designs
4.5.2 Confounding Effects
4.5.3 Experimental Resolution

## Slide 875: 4.5.1 Fractional Designs

## Slide 876: What Are Fractional Factorial Experiments?
              In simple terms, a fractional factorial experiment is a subset of a full factorial experiment.
              Fractional factorials use fewer treatment combinations and runs.
Fractional factorials are less able to determine effects because of fewer degrees of freedom available to evaluate higher order interactions.
Fractional factorials can be used to screen a larger number of factors.
Fractional factorials can also be used for optimization.
Notes: Fractional factorial experiments are smaller than their full factorial counterparts (i.e., they are a subset of full factorial experiments).
They allow the experimenter to learn about effects through fewer treatment combinations.
They are useful for screening a large number of factors, and can also be used for factor optimization.

## Slide 877: Why Fractional Factorial Experiments?
To run a full factorial experiment for k factors, we need 2k unique treatments. In other words, we need resources that can afford at least 2k runs.
With k increasing, the number of runs required in full factorial experiments rises dramatically even without any replications, and the percentage of degrees of freedom spent on the main effects decreases.
The main effects and two-way interaction are the key effects we need to evaluate. The higher order the interaction is, the more we can ignore it.
Notes: As the number of factors increases, the number of treatment runs necessary for a full factorial experiment increases greatly. The money and resources might not be available.
As the number of runs increases with the number of factors, the percentage of degrees of freedom spent on understanding the main effects decreases. However, the higher order interactions (3 or 4 factor interactions) can typically be ignored, which allows us to run fewer trials to understand the main effects and two-way interactions.

## Slide 878: Why Fractional Factorial Experiments?
Notes: Notice the number of treatments increases dramatically as factors are added.

## Slide 879: How Does a Fractional Factorial Work?
We are trying to find the cause-and-effect relationship between a response (Y) and three factors (factor A, B, and C) and their interactions (AB, BC, AC, and ABC).
  As follows is the 23 full factorial design (2 level 3 factor).
  There are eight treatment combinations (2 * 2 * 2).
Notes: A full factorial experiment with three factors and two levels has 2^K (2^3) runs (2*2*2 = 8 runs).

## Slide 880: How Does a Fractional Factorial Work?
To perform a 23 full factorial experiment, we need to run at least eight unique treatments (2 * 2 * 2).
What if we only have enough resources to run four treatments?
As a result, we need to carefully select a subset from the eight treatments so that all of our main effects can be evaluated and the design can be kept balanced and orthogonal.
Notes: Eight runs are needed for a full factorial, but we only have resources to run four. Therefore, we need to decide which four treatment combinations will allow us to evaluate the main effects, while keeping the design balanced and orthogonal.

## Slide 881: How Does a Fractional Factorial Work?
Example of an invalid design
Remember orthogonality?
This design is invalid because only the low setting of factor C is tested.
We cannot evaluate the main effect of factor C using this design.
Notes: In this design, we are not able to evaluate factor C.

## Slide 882: How Does a Fractional Factorial Work?
Example of an invalid design
Checking orthogonality: the sum of AC interaction signs should equal zero (0).
  Run 1 (-)
  Run 2 (-)
  Run 3 (-)
  Run 4 (+)
  Sum (-1)
This design is also invalid because it is neither balanced nor orthogonal.
Notes: This design has a low and high setting for each factor, but is not orthogonal.

## Slide 883: How Does Fractional Factorial Work?
To select the four treatments run in the 23-1 fractional factorial experiment, we start from the 22 full factorial design of experiment.
If we replace the two-way interaction (AB) column with the factor C column, the design will be valid.
Notes: Imagine a two-factor full factorial with factors A and B. We also learn about the interaction of A and B. In a fractional factorial, we sacrifice learning about the two-way interaction between A and B, and substitute factor C.

## Slide 884: How Does a Fractional Factorial Work?
23-1 Fractional Factorial Design Pattern
  Three factors and four treatments
Note: We also call this kind of design a half-factorial design since we only have half of the treatments that we would have in a full factorial design.
In 23-1 fractional factorial design of experiment, the effect of three-way interaction (ABC) is not measurable since it only has “+1”.
Notes: In four runs, we are able to run high and low settings for each of the three factors. The three-way interaction ABC is only at the high setting.

## Slide 885: How Does a Fractional Factorial Work?
In the 23-1 fractional factorial design, we notice that the column of each main effect has identical “+1” and “-1” values with one two-way interaction column.
  A and BC
  B and AC
  C and AB
In this situation, we say that A is aliased with BC or A is the alias of BC.
Notes: The factor and two-way interaction columns that have the same pattern of high/low settings are aliased with each other.

## Slide 886: How Does a Fractional Factorial Work?
By multiplying any column with itself, we obtain the identity (I).
  A * A = I
  The product of any column and the identity is the column itself.
  A * I = A
Column ABC is called the generator.
  By multiplying any column with the generator, we obtain its alias.
  A * ABC = (A*A) * BC = I * BC = BC
Notes: This is how to identify the alias of a factor by using the identity and the generator.

## Slide 887: Use SigmaXL to Run a Fractional Factorial Experiment
Step 1: Initiate the experiment design
  Click SigmaXL -> Designs of Experiments -> 2-Level Factorial/Screening -> 2-Level Factorial/Screening Designs
  A window named “2-Level Factorial/Screening Designs of Experiments” pops up.
Step 2: Enter the response and factors information in the window “2-Level Factorial/Screening Design of Experiments”
  One response: Y
  Three factors: A, B and C
  Two-level design: each factor has two settings
Step 3: Select a design from the pre-populated design list.
  In this case, we select “4-Run, 2**(3-1), ½ Fraction, Res III”.
Notes: How to use the software to run a fractional factorial experiment.

## Slide 888: Use SigmaXL to Run a Fractional Factorial Experiment
Step 4: Select the number of replications and make design
  In this case, we assume the sufficient resources allow each treatment to be run twice.
  Enter “2” into the box of “Number of Replicates”
  Click “OK>>”
  The DOE template appears in the newly generated tab “3 Factor DOE”.

## Slide 889: Use SigmaXL to Run a Fractional Factorial Experiment
Step 5: Implement the experiment and record the results in yellow cells in the DOE table being sure to enter the data by Std. Order.

## Slide 890: Use SigmaXL to Run a Fractional Factorial Experiment
Step 6: Fit the model using the experiment results
  Click SigmaXL -> Design of Experiments -> 2-Level Factorial/Screening -> Analyze 2-Level Factorial/Screening Design
  A new window named “Analyze 2-Level Factorial/Screening Design” appears with the response and factors pre-populated.
  Check the checkbox “Show Residual Plots”
  Click “OK>>”

## Slide 891: Use SigmaXL to Run a Fractional Factorial Experiment
Step 7: Analyze the model results
  Check whether the model is statistically significant.
  Check which factors are insignificant.
  If any independent variables are not significant, remove them one at a time and rerun the model until all the independent variables in the model are significant.

## Slide 892: Use SigmaXL to Run a Fractional Factorial Experiment
The p-value of factor B is greater than the alpha level (0.05), so it is not statistically significant.
Next we need to remove factor B and re-run the model.
Notes: Since factor B isn’t significant, we need to remove it and rerun the model.

## Slide 893: Use SigmaXL to Run a Fractional Factorial Experiment
The p-values of all the independent variables are smaller than 0.05. There is no need to remove any independent variables from the model.

## Slide 894: Use SigmaXL to Run a Fractional Factorial Experiment
Step 8: Conduct residual analysis to ensure that the residuals of the model satisfy the following criteria.
  Mean is equal to zero.
  Normally distributed
  Independent
  Equal variance across the fitted response values

## Slide 895: Use SigmaXL to Run a Fractional Factorial Experiment
Step 8.1: Save residuals generated by the model
  When running the “Analyze 2-Level Factorial/Screening Design”, make sure to check the checkbox “Show Residual Plots” before clicking “OK>>”
  The residual plots and the residuals appear at the bottom of the tab “Analyze – 3 Factor DOE (1)”.

## Slide 896: Use SigmaXL to Run a Fractional Factorial Experiment
Step 8.2: Check whether residuals are normally distributed with mean equal to zero.
  Select the entire range of the residuals in the residual report
  Click SigmaXL -> Graphical Tools -> Histograms & Descriptive Statistics
  A new window named “Histograms & Descriptive” appears and the selected range is automatically populated into the box below “Please select your data”
  Click “Next>>”
  A new window named “Histograms & Descriptive Statistics” pops up.
  Select “Residuals” as the “Numeric Data Variables (Y)”
  Click “OK>>”
  The histogram and the normality test of the residuals appear in the newly generated tab “Hist Descript (1)”.
  If the p-value of the normality test is greater than the alpha level (0.05), the residuals are normally distributed.

## Slide 897: Use SigmaXL to Run a Fractional Factorial Experiment

## Slide 898: Use SigmaXL to Run a Fractional Factorial Experiment
The p-value of the normality test is larger than alpha level (0.05). The residuals are normally distributed.

## Slide 899: Use SigmaXL to Run a Fractional Factorial Experiment
Step 8.3: Check whether the residuals are independent.
  Select the entire range of the residuals in the residual report.
  Click SigmaXL -> Control Charts -> Individuals & Moving Range
  A new window named “Individuals and Moving Range” appears with the selected range automatically populated into the box below “Please select your data”.
  Click “Next>>”
  A new window named “Individuals and Moving Range Chart” pops up.
  Select the “Residuals” as the “Numeric Data Variables (Y)”
  Click “OK>>”
  The control charts appear in the newly generated tab “Indiv & MR Charts (1)”.
  If no data points on the control charts fail any tests, the residuals are in control and independent of each other.
  Note: The prerequisite of plotting IR chart for residuals is that the residuals are in the time order.

## Slide 900: Use SigmaXL to Run a Fractional Factorial Experiment

## Slide 901: Use SigmaXL to Run a Fractional Factorial Experiment

## Slide 902: Use SigmaXL to Run a Fractional Factorial Experiment
Step 8.4: Check whether the residuals have equal variance across the predicted response values.
  Close to the bottom of the tab “Analyze – 3 Factor DOE (1)” is the residual by predicted plot.
  We look for patterns in which the residuals tend to have even variation across the entire range of the fitted response values.

## Slide 903: 4.5.2 Confounding Effects

## Slide 904: Confounding Effects
In full factorial experiments the effects of every factor and their interactions can be calculated because there is a degree of freedom for every treatment combination as well as the error term.
Fractional factorial experiments, however, are designed with fewer runs or treatment combinations but will have the same number of input factors.
As a result, the experimenter must understand the impact of these consequences.
Confounding (or aliased factors) is that consequence.
Resolution is a quantification or degree of confounding.
Notes: Confounding can be considered alternatively as “confusing”. If you think of it this way, confounding is when two factors or factor interactions “confuse” our ability to know which factor has the effect on ‘Y’.
Resolution is a way in which we quantify confounding.

## Slide 905: Confounding Effects
        When two input factors are aliases of each other, the effects they each have on the response cannot be separated.
        In the 23-1 fractional factorial design, A and BC are aliases.
        The main effect that A has on the response would be exactly the same as the interaction effect of BC. We cannot tell which one is truly significant.
The effects of aliased factors are what is referred to as confounded.
Due to the confounding nature of aliased factors, the effect we observe is the mixed effect of aliased factors.
  A + BC
  B + AC
  C + AB
Notes: When factors are confounded they are considered aliased factors. Factor A may be aliased with factor BC, for example. This simply means that both factor A and BC simultaneously have the same measureable impact on Y and we cannot determine which is the true driver of the change in Y.

## Slide 906: Resolution
Resolution is the measure or degree of confounding.
Higher resolution means less confounding or merely confounding main effects with higher order interactions.
The resolution of a fractional factorial experiment will always be one number higher than the order of interactions that are confounded with main effects.
Resolution III: Main effects are confounded with two-way interactions. If you are only interested in main effects, then resolution III is acceptable. Otherwise, resolution III is typically undesirable.
Resolution IV: Main effect are confounded with three-way interactions.
Resolution V: Main effects are confounded with four-way interactions.
Notes: Resolution is the measure or quantification of confounding.
Resolution III is when main effects are confounded with two-way interactions.
Resolution IV is when main effects are confounded with three-way interactions.
Resolution V is when main effects are confounded with four-way interactions.

## Slide 907: Consequences of Fractional Factorials
Benefits:
  The primary benefits of properly designed fractional factorial experiments are achieved because of fewer runs.
  You may have limited time, resources, or capital and cannot run a full factorial.
Disadvantages:
  Confounding (a.k.a. aliasing)
Mitigation Option
  Replications: by adding replicates you can introduce more study runs and increase the resolution of your experiment.
  Replications, however, will also increase the number of trials or runs sometimes, defeating the purpose of running a fractional factorial experiment.
Notes: The best way to resolve issues around confounding is to add more DOE results by using replications. However, this offsets the benefit of fractional factorial designs because it adds runs to the DOE.

## Slide 908: 4.5.3 Experimental Resolution

## Slide 909: Alias in 23-1 Fractional Factorial Experiment
In the 23-1 fractional factorial design of experiment, the main factor is aliased or confounded with two-way interactions.
  A is the alias of BC.
  B is the alias of AC.
  C is the alias of AB.
Notes: A 23-1 is a resolution III design. The main effects are confounded with two-way interactions.

## Slide 910: Alias in 24-1 Fractional Factorial Experiment
In the 24-1 fractional factorial design of experiment, the main factor is aliased with three-way interaction and two-way interaction is aliased with two-way interaction.
  A is the alias of BCD.
  B is the alias of ACD.
  C is the alias of ABD.
  D is the alias of ABC.
  AB is the alias of CD.
  AC is the alias of BD.
  AD is the alias of BC.
Notes: A 24-1 is a resolution IV design. The main effects are confounded with three-way interactions and two-way interactions are confounded with other two-way interactions.

## Slide 911: Design Resolution
Design resolution (i.e., experimental resolution) refers to the confounding patterns indicating how the effects are confounded with others.
If two factors are aliases, they have confounded effect on the response. There is no need to consider both factors in the model due to the redundancy. Only one factor needs to be included in the model for simplicity.
Most popular resolutions are resolution III, IV, and V.
  Resolution III: Main effects are aliased with two-way interactions.
  Resolution IV: Main effects are aliased with three-way interactions. Two-way interactions are aliased with other two-way interactions.
  Resolution V: Main effects are aliased with four-way interactions. Two-way interactions are aliased with three-way interactions.
Notes: A 25-1 is a resolution IV design. The main effects are confounded with four-way interactions and two-way interactions are confounded with three-way interactions.

## Slide 912: Determine Aliases
To find the alias of a particular factor, we only need to multiply the factor of interest with the identity (I) of the design.
  In 23-1 fractional factorial design, ABC is the identity. To find the alias of factor A, we use A * ABC = BC.
  In 24-1 fractional factorial design, ABCD is the identity. To find the alias of factor A, we use A * ABCD = BCD.
  In 25-1 fractional factorial design, ABCDE is the identity. To find the alias of factor A, we use A * ABCDE = BCDE.
Notes: The identity of a design is the same number of letters in the alphabet starting from A out to the same number factors in the design. For example, a three-factor design has an identity of ABC, a four-factor design has an identity of ABCD.
To find the alias of a factor, multiply the factor by the identity of the design. A multiplied by ABC leaves BC. Therefore, in a resolution III design, factor A is aliased with BC.

## Slide 913: 5.0 Control Phase
Notes: The goal of the Control phase is to ensure that any improvements implemented throughout the project are sustained over the long term.

## Slide 914: Black Belt Training: Control Phase
5.1 Lean Controls
5.1.1 Control Methods for 5S
5.1.2 Kanban
5.1.3 Poka-Yoke (Mistake Proofing)
5.2 Statistical Process Control (SPC)
5.2.1 Data Collection for SPC
5.2.2 I-MR Chart
5.2.3 Xbar-R Chart
5.2.4 U Chart
5.2.5 P Chart
5.2.6 NP Chart
5.2.7 X-S chart
5.2.8 CumSum Chart
5.2.9 EWMA Chart
5.2.10 Control Methods
5.2.11 Control Chart Anatomy
5.2.12 Subgroups, Variation, Sampling
5.3 Six Sigma Control Plans
5.3.1 Cost Benefit Analysis
5.3.2 Elements of the Control Plan
5.3.3 Elements of the Response Plan

## Slide 915: 5.1 Lean Controls

## Slide 916: Black Belt Training: Control Phase
5.1 Lean Controls
5.1.1 Control Methods for 5S
5.1.2 Kanban
5.1.3 Poka-Yoke (Mistake Proofing)
5.2 Statistical Process Control (SPC)
5.2.1 Data Collection for SPC
5.2.2 I-MR Chart
5.2.3 Xbar-R Chart
5.2.4 U Chart
5.2.5 P Chart
5.2.6 NP Chart
5.2.7 X-S chart
5.2.8 CumSum Chart
5.2.9 EWMA Chart
5.2.10 Control Methods
5.2.11 Control Chart Anatomy
5.2.12 Subgroups, Variation, Sampling
5.3 Six Sigma Control Plans
5.3.1 Cost Benefit Analysis
5.3.2 Elements of the Control Plan
5.3.3 Elements of the Response Plan

## Slide 917: 5.1.1 Control Methods for 5S
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 918: 5.1.2 Kanban

## Slide 919: What is Kanban?
The Japanese word “Kanban” means “signboard.”
Kanban system is a “pull” production scheduling system to determine when to produce, what to produce, and how much to produce based on the demand.
It was originally developed by Taiichi Ohno in order to reduce the waste in inventory and increase the speed of responding to the immediate demand.
Notes: Kanban is a “visual” production system developed by Taiichi Ohno. It is based on a pull system where production scheduling is based on demand. The pull determines what to produce, when to produce, and how much to produce.

## Slide 920: Kanban System
Kanban system is a demand-driven system.
The customer demand is the signal to trigger or pull the production.
Products are made only to meet the immediate demand. When there is no demand, there is no production.
It is designed to minimize the in-process inventory and to have the right material with the right amount at the right location at the right time.
Notes: Being a “demand-driven system” means that production only occurs when there are orders for a product. The goal is to minimize waste in the form of extra inventory.

## Slide 921: Kanban System
Principles of the Kanban System:
  Only produce products with exactly the same amount that customers consume.
  Only produce products when customers consume.
The production is driven by the actual demand from the customer side instead of the forecasted demand planned by the staff.
Notes: The goal is to match production to demand.

## Slide 922: Kanban Card
The Kanban card is the ticket or signal to authorize the production or movement of materials. It is the message of asking for more.
It is sent from the end customer up to the chain of production.
Upon receiving of a Kanban card, the production station would start to produce goods.
The Kanban card can be a physical card or an electronic signal.
Notes: The Kanban card is a visual management tool. It is the signal for the need to produce more of a particular product.

## Slide 923: Kanban System Example
The simplest example of a Kanban system is the supermarket operation.
Customers visit the supermarkets and buy what they need.
The checkout scanners send electronic Kanban cards to the local warehouse asking for more when the items are sold to customers.
When the warehouse receives the Kanban cards, it starts to replenish the exact goods being sold.
It the warehouse prepares more than what Kanban cards require, the goods would become obsolete. If it prepares less, the supermarket would not have the goods available when customers need them.
Notes: Purchasing goods at a grocery store is a good example of a Kanban system. When a product is scanned/sold, a signal is sent to the warehouse and suppliers identifying a need for more of that product.

## Slide 924: Kanban System Benefits
Minimize in-process inventory
Free up space occupied by unnecessary inventory
Prevent overproduction
Improve responsiveness to dynamic demand
Avoid the risk of inaccurate demand forecast
Streamline the production flow
Visualize the work flow.
Notes: Kanban systems are designed to minimize inventory and inefficiencies rooted in an inaccurate demand forecast.

## Slide 925: 5.1.3 Poka-Yoke

## Slide 926: What is Poka-Yoke?
The Japanese term “poka-yoke” means “mistake-proofing.”
It is a mechanism to eliminate defects as early as possible in the process.
It was originally developed by Shigeo Shingo and was initially called “baka-yoke” (fool-proofing).
Notes: The term “poka-yoke” means mistake proofing. It is an extremely effective control method because it means to prevent, correct, or draw attention to a mistake as it occurs.

## Slide 927: Two Types of Poka-Yoke
Prevention
  Preventing defects from occurring
  Removing the possibility that an error could occur
  Making the occurrence of an error impossible.
Detection
  Detecting defects once they occur
  Highlighting defects to draw workers’ attention immediately
  Correcting defects so that they would not reach the next stage.
Notes: The best way to drive quality is to prevent defects before they occur. The next best solution is to detect defects as they occur so they can be corrected. Poka-yoke solutions can aim to either prevent or detect defects.

## Slide 928: Three Methods of Poka-Yoke
Contact Method
  Use of shape, color, size, or any other physical attributes of the items.
Constant Number Method
  Use of a fixed number to make sure a certain number of motions are completed.
Sequence Method
  Use of a checklist to make sure all the prescribed process steps are followed in the right order.
Notes: Shigeo Shingo identified three methods of poka-yoke for detecting and preventing errors in a mass production system.

## Slide 929: Poka-Yoke Devices
We are surrounded by poka-yoke devices daily.
  Prevention Devices
    Example: the dishwasher does not start to run when the door is open.
  Detection Devices
    Example: the car starts to beep when the passengers do not buckle their seatbelts.
Poka-yoke devices can be in any format that can quickly and effectively prevent or detect mistakes.
  Visual, electrical, mechanical, procedural, human etc.
Notes: Other examples:
Tether on a car’s gas cap to keep driver from leaving it behind.
Inability to remove the key from car ignition until transmission is in park.
Safety bar on lawn mower must be engaged to start engine.
Hole near the top of a bathroom sink to keep it from overflowing.
Clothes dryer stops when the door is opened.

## Slide 930: Steps to Apply Poka-Yoke
Step 1: Identify the process steps in need of mistake proofing.
Step 2: Use the 5-why’s method to analyze the possible mistakes or failures for the process step.
Step 3: Determine the type of poka-yoke: prevention or detection.
Step 4: Determine the method of poka-yoke: contact, constant number, or sequence.
Step 5: Pilot the poka-yoke approach and make any adjustments if needed.
Step 6: Implement poka-yoke in the operating process and maintain the performance.

## Slide 931: 5.2 Statistical Process Control

## Slide 932: Black Belt Training: Control Phase
5.1 Lean Controls
5.1.1 Control Methods for 5S
5.1.2 Kanban
5.1.3 Poka-Yoke (Mistake Proofing)
5.2 Statistical Process Control (SPC)
5.2.1 Data Collection for SPC
5.2.2 I-MR Chart
5.2.3 Xbar-R Chart
5.2.4 U Chart
5.2.5 P Chart
5.2.6 NP Chart
5.2.7 X-S chart
5.2.8 CumSum Chart
5.2.9 EWMA Chart
5.2.10 Control Methods
5.2.11 Control Chart Anatomy
5.2.12 Subgroups, Variation, Sampling
5.3 Six Sigma Control Plans
5.3.1 Cost Benefit Analysis
5.3.2 Elements of the Control Plan
5.3.3 Elements of the Response Plan

## Slide 933: 5.2.1 Data Collection for SPC

## Slide 934: What is SPC?
Statistical process control (SPC) is a statistical method to monitor the performance of a process using control charts in order to keep the process in statistical control.
Statistical process control can be used to distinguish between special cause variation and common cause variation in the process.
It presents the voice of the process.
Notes: Statistical process control (SPC) is a method of quality control applied to monitor and control a process. Monitoring and controlling ensures that the process maximizes quality output.
Control charts are a key tool used in SPC.

## Slide 935: Common Cause Variation
Common cause variation (also called chance variation) is the inherent natural variation in any processes.
It is the random background noise, which cannot be controlled or eliminated from the process.
Its presence in the process is expected and acceptable due to its relatively small influence on the process.
Notes: The goal of of SPC is to distinguish between common cause variation and special cause variation to minimize tampering or inaction to real process changes.
Common cause variation is the inherent natural variation in a process.

## Slide 936: Special Cause Variation
Special cause variation (also called assignable cause variation) is the unnatural variation in the process.
It is the cause of process instability and leads to defects of the products or services.
It is the signal of unanticipated change (either positive or negative) in the process.
It is possible to eliminate the special cause variation from the process.
Notes: Special cause variation is unnatural variation that has an assignable cause. It is the driver of process instability and is a signal of unanticipated (not necessarily unwanted) change in the process.
In some cases, special cause variation is unwanted, but in other cases it can represent something desirable to replicate.

## Slide 937: Process Stability
A process is stable when:
  There is not any special cause variation involved in the process
  The process is in statistical control
  The future performance of the process is predictable within certain limits
  The changes happening in the process are all due to random inherent variation
  There are not any trends, unnatural patterns, and outliers in the control chart of the process.
Notes: When a process performs predictably within certain limits, we say it is “in control.”
A process that is “in control” is stable.

## Slide 938: SPC Benefits
Statistical process control can be used in different phases of Six Sigma projects to:
  Understand the stability of a process
  Detect the special cause variation in the process
  Identify the statistical difference between two phases
  Eliminate or apply the unnatural change in the process
  Improve the quality and productivity.
Notes: SPC has many benefits: monitoring process stability, detecting special cause variation, and helping process managers determine when to react to variation or not.

## Slide 939: Control Charts
Control charts are graphical tools to present and analyze the process performance in statistical process control.
Control charts are used to detect special cause variation and determine whether the process is in statistical control (stable).
Variation solutions:
  Minimize the common cause variation
  Eliminate the special cause variation when it leads to unanticipated negative changes in the outcome
  Implement the special cause variation when it leads to unanticipated positive changes in the outcome.
Notes: Control charts are used to monitor the variation of a process over time. They can differentiate assignable (special) sources of variation from common sources.

## Slide 940: Control Charts Elements
Center Line: the process mean
Lower Line: lower control limit (LCL)
Upper Line: upper control limit (UCL)
Data Points: individual observations or their calculation results
Horizontal axis: Time
Vertical Axis: Measurement Values
Notes: At its basic level, the control chart is a visual tool to illustrate when a process is stable or not.
While there are other rules that will tell us whether or not a process is in control, the basic rule is to observe if the data points fall between the upper and lower control limits.

## Slide 941: Control Charts Elements
Control charts can work for both continuous data and discrete or count data.
Control limits are approximately three sigma away from the process mean.
A process is in statistical control when all the data points on the control charts fall within the control limits and have random patterns only.
Otherwise, the process is out of control and we need to investigate the special cause variation in the process.
Notes: There are many types of control charts for different situations, including whether the data are continuous or discrete.

## Slide 942: Possible Errors in SPC
There are two types of possible errors in interpreting controls charts.
Notes: Two types of errors can be made when interpreting and acting (or not acting) on a control chart.
Type I (False Positive) – Tampering, acting to correct variation when you should not, because it is common cause variation.
Type II (False Negative) – Not acting to correct variation when you should, because it is special cause variation.

## Slide 943: Possible Errors in SPC
It is similar to the way of defining the type I and type II errors in hypothesis testing.
Control charts can be interpreted as a way of testing the hypothesis about the process stability.
  Null Hypothesis (H0): The process is stable (i.e., in statistical control).
  Alternative Hypothesis (HA): The process is unstable (i.e., out of statistical control).
Notes: A control chart is a form of a hypothesis test where the null hypothesis is that the process is stable, and the alternative is that the process is unstable.

## Slide 944: Possible Errors in SPC
Type I Error
  False positive
  False alarm
  Considering true common cause variation as special cause variation
  Type I errors waste resources spent on investigation.
Type II Error
  False negative
  Miss
  Considering true special cause variation as common cause variation
  Type II errors neglect the need to investigate critical changes in the process.
Notes: Type I error is commonly known as a “false alarm,” where resources are wasted reacting to something that should not be reacted to.
Type II error is a “miss,” where special cause variation is neglected when it should be acted upon.

## Slide 945: Data Collection Considerations
To collect data for plotting control charts, we need to consider:
  What is the measurement of interest?
  Are the data discrete or continuous?
  How many samples do we need?
  How often do we sample?
  Where do we sample?
  What is the sampling strategy?
  Do we use the raw data collected or transfer them to percentages, proportions, rates, etc.?
Notes: To effectively use control charts, it is important to plan carefully how the data will be collected.

## Slide 946: Subgroups and Rational Subgrouping
When sampling, we randomly select a group of items (i.e. a subgroup) from the population of interest.
The subgroup size is the count of samples in a subgroup. It can be constant or variable.
Depending on the subgroup sizes, we select different control charts accordingly.
Rational subgrouping is the basic sampling scheme in SPC.
The goal of rational subgrouping is to maximize the likelihood of detecting special cause variation. In other words, the control limits should only reflect the variation between subgroups.
The number of subgroups, subgroup size, and frequency of sampling have great impact on the quality of control charts.
Notes: Sampling is randomly selecting a group of items from a population in which all items are produced under the conditions where only random effects are responsible for the observed variation. This maximizes the likelihood of detecting a special cause when it occurs.

## Slide 947: Impact of Variation
The rational subgrouping strategy is designed to minimize the opportunity of having special cause variation within subgroups.
If there is only random variation (background noise) within subgroups, all the special cause variation would be reflected between subgroups. It is easier to detect an out-of-control situation.
Random variation is inherent and indelible in the process. We are more interested in identifying and taking actions on special cause variation.
Notes: Again, the point of rational subgrouping is to minimize the opportunity of having special cause within subgroups, which makes it easier to identify special cause variation when it occurs.

## Slide 948: Frequency of Sampling
The frequency of sampling in SPC depends on whether we have sufficient data to signal the changes in a process with reasonable time and costs.
The more frequently we sample, the higher costs it may trigger.
We need the subject matter experts’ knowledge on the nature and characteristics of the process to make good decisions on sampling frequency.
Notes: The objective of sampling is to minimize the cost of data collection while still being able to accurately monitor performance.
The balance is between cost and the ability to identify special cause variation when it occurs.

## Slide 949: 5.2.2 I-MR Chart

## Slide 950: I-MR Chart
The I-MR chart (also called individual-moving range chart or IR chart) is a popular control chart for continuous data with subgroup size equal to one.
The I chart plots an individual observation as a data point.
The MR chart plots the absolute value of the difference between two consecutive observations in individual charts as a data point.
If there are n data points in the I chart, there are n –1 data points in the MR chart.
The I chart is valid only if the MR chart is in control.
The underlying distribution of the I-MR chart is normal distribution.
Notes: Individuals – moving range chart, or I-MR, are control charts of individual data points over time. The MR portion is the absolute value of the change from point to point.
The underlying distribution for the I-MR chart is the normal distribution.

## Slide 951: I Chart Equations
I Chart (Individuals Chart)
  Data Point:
  Center Line:
  Control Limits:
where n is the number of observations

## Slide 952: MR-Chart Equations
MR Chart (Moving Range Chart)
  Data Point:
  Center Line:
  Upper Control Limit:
  Lower Control Limit: 0
where n is the number of observations

## Slide 953: Use SigmaXL to Plot I-MR Charts
Data File: “IR” tab in “Sample Data.xlsx”
Steps in SigmaXL to plot IR charts
  Select the entire range of data
  Click SigmaXL -> Control Charts -> Individuals & Moving Range
  A new window named “Individuals and Moving Range” appears with the selected range automatically populated into the box below “Please select your data”.
  Click “Next>>”
  A new window named “Individuals and Moving Range Chart” pops up.
  Select “Measurement” as the “Numeric Data Variable (Y)”
  Check the checkbox of “Test for special causes”
  Click “OK>>”
  The IR charts appear in the newly generated tab “Indiv & MR Charts (1)”.

## Slide 954: Use SigmaXL to Plot I-MR Charts

## Slide 955: Use SigmaXL to Plot I-MR Charts

## Slide 956: I-MR Charts Diagnosis
MR Chart (Moving Range Chart):
Two data points fall beyond the upper control limit. It indicates the MR chart is out of control (i.e. the variations between every two contiguous individual samples are not stable over time). We need to further investigate the process, identify the root causes which trigger the outliers, and correct or apply the root causes to bring the process back to control.
I Chart (Individuals Chart):
Since the MR Chart is out of control, the I chart is invalid.

## Slide 957: 5.2.3 Xbar-R Chart

## Slide 958: Xbar-R Chart
The Xbar-R chart is a control chart for continuous data with a constant subgroup size between two and ten.
The Xbar chart plots the average of a subgroup as a data point.
The R chart plots the difference between the highest and lowest values within a subgroup as a data point.
The Xbar chart monitors the process mean and the R chart monitors the variation within subgroups.
The Xbar is valid only if the R chart is in control.
The underlying distribution of the Xbar-R chart is normal distribution.
Notes: Xbar-R control charts are applicable when using continuous data, and small subgroups (between two and ten) represent each data point.
The range (R) is the difference between the high and low data points within a subgroup.
Similar to I-MR, the Xbar chart is not valid unless the R chart is in control.
Like the I-MR, the underlying distribution is the normal.

## Slide 959: Xbar Chart Equations
Xbar chart
  Data Point:
  Center Line:
  Control Limits:
where m is the subgroup size and k is the number of subgroups. A2 is a constant depending on the subgroup size.

## Slide 960: R Chart Equations
R chart (Rage Chart)
  Data Point:
  Center Line:
  Upper Control Limit:
  Lower Control Limit:
where m is the subgroup size and k is the number of subgroups. D3 and D4 are constants depending on the subgroup size.

## Slide 961: Use SigmaXL to Plot Xbar-R Charts
Data File: “Xbar-R” tab in “Sample Data.xlsx”
Steps in SigmaXL to plot Xbar-R charts
  Select the entire range of the data
  Click SigmaXL -> Control Charts -> X-Bar & R
  A new window named “X-Bar & R” appears with the selected range automatically populated into the box below “Please select your data”.
  Click “Next>>”
  A new window named “X-Bar and Range Chart” pops up.
  Select the “Measurement” as the “Numeric Data Variables (Y)”
  Select the “Subgroup ID” as the “Subgroup Column or Size”
  Check the checkbox of “Tests for Special Causes”
  Click “OK>>”
  The Xbar-R charts appear in the newly generated tab “Indiv & MR Charts (1)”.

## Slide 962: Use SigmaXL to Plot Xbar-R Charts

## Slide 963: Xbar-R Charts Diagnosis
Xbar-R Charts:
Since the R Chart is in control, the Xbar chart is valid. In both charts, there aren’t any data points failing any tests for special causes (i.e. all the data points fall between the control limits and spread around the center line with a random pattern). We conclude that the process is in control.

## Slide 964: 5.2.4 U Chart
Notes: The U chart is a type of control chart used to monitor discrete (count) data where the sample size is greater than one, typically the average number of defects per unit.

## Slide 965: Defect vs. Defective
A defect of a unit is the unit’s characteristic that does not meet the customers’ requirements.
A defective is a unit that is not acceptable to the customers.
One defective might have multiple defects.
One unit might have multiple defects but be still usable to the customers.
Notes: Remember the difference between defect and defective? A defect is a specific non-conformity of a unit. Defective means the unit is not acceptable to a customer.
A unit may have defects but still be acceptable to a customer, meaning it is not defective.

## Slide 966: U Chart
The U chart is a control chart monitoring the average defects per unit.
The U chart plots the count of defects per unit of a subgroup as a data point.
It considers the situation when the subgroup size of inspected units for which the defects would be counted is not constant.
The underlying distribution of the U chart is Poisson distribution.
Notes: Each data point on the U chart represents the average number of defects per unit, where each data point represents a subgroup of units.
This type of chart accounts for the situation where the size of the subgroups is not constant.
The underlying distribution of the U chart is Poisson.

## Slide 967: U Chart Equations
U chart
  Data Point:
  Center Line:
  Control Limits:
where ni is the subgroup size for the ith subgroup;
k is the number of subgroups;
xi is the number of defects in the ith subgroup.

## Slide 968: Use SigmaXL to Plot a U Chart
Data File: “U” tab in “Sample Data.xlsx”
Steps in SigmaXL to plot a U chart
  Select the entire range of the data
  Click SigmaXL -> Control Charts -> Attribute Charts -> U
  A new window named “U-Chart” appears with the selected range of the data automatically populated into the box below “Please select your data”.
  Click “Next>>”
  A new window named “U-Chart” pops up.
  Select “Count of Defects” as the “Numeric Data Variable (Y)”
  Select “Count of Units Inspected” as the “Subgroup Column or Size”
  Check the checkbox “Test for Special Causes”
  Click “OK>>”
  A new window named “Tests for Special Causes” pops up. Click “OK” to proceed.
  The U chart appears in the newly generated tab “U-Chart (1)”.

## Slide 969: Use SigmaXL to Plot a U Chart

## Slide 970: U Chart Diagnosis
U Chart:
Since the sample sizes are not constant over time, the control limits are adjusted to different values accordingly. The highlighted data point falls beyond the upper control limit. We conclude that the process is out of control. Further investigation is needed to determine the special causes which triggered the unnatural pattern of the process.

## Slide 971: 5.2.5 P Chart

## Slide 972: P Chart
The P chart is a control chart monitoring the percentages of defectives.
The P chart plots the percentage of defectives in one subgroup as a data point.
It considers the situation when the subgroup size of inspected units is not constant.
The underlying distribution of the P chart is binomial distribution.
Notes: The P chart is similar to the U chart in that it evaluates the amount of defectives within a subgroup. However, the P chart follows a binomial distribution because it monitors the percentage of defective units within a subgroup.
Similar to the U chart, the subgroup size is not constant.

## Slide 973: P Chart Equations
P chart
  Data Point:
  Center Line:
  Control Limits:
where ni is the subgroup size for the ith subgroup;
k is the number of subgroups;
xi is the number of defectives in the ith subgroup.

## Slide 974: Use SigmaXL to Plot a P Chart
Data File: “P” tab in “Sample Data.xlsx”
Steps in SigmaXL to plot a P chart
  Select the entire range of the data
  Click SigmaXL -> Control Chart -> Attribute Charts -> P
  A new window named “P-Chart” appears with the selected range automatically populated into the box below “Please select your data”.
  Click “Next>>”
  A new window also named “P-Chart” pops up.
  Select “Fail” as the “Numeric Data Variables (Y)”
  Select “N” as the “Subgroup Column or Size”
  Check the checkbox of “Test for Special Causes”
  Click “OK>>”
  A new window named “Tests for Special Causes” pops up. Click “OK” to proceed.
  The P chart appears in the newly generated tab “P-Chart (1)”.

## Slide 975: Use SigmaXL to Plot a P Chart

## Slide 976: P Chart Diagnosis
P Chart:
Since the sample sizes are not constant over time, the control limits are adjusted to different values accordingly. All the data points fall within the control limits and spread randomly around the mean. We conclude that the process is in control.

## Slide 977: 5.2.6 NP Chart
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 978: 5.2.7 X-S Chart
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 979: 5.2.8 CumSum Chart
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 980: 5.2.9 EWMA Chart
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 981: 5.2.10 Control Methods
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 982: 5.2.11 Control Chart Anatomy

## Slide 983: Control Chart Calculations Summary
Notes: This is a helpful reference page to understand how the parameters of various control charts are calculated.

## Slide 984: Control Chart Constants
Notes: This is another helpful reference page.
Many control charts use some of these constants in the calculation of parameters. They vary depending on the subgroup size.

## Slide 985: Unnatural Patterns
If there are unnatural patterns in the control chart of a process, we consider the process out of statistical control.
Typical unnatural patterns in control charts:
  Outliers
  Trending
  Cycling
  Auto-correlative
  Mixture.
A process is in control if all the data points on the control chart are randomly spread out within the control limits.
Notes: Control charts are designed to help us decipher special cause variation from common cause variation.
The most common way to identify special cause variation on control charts is by outliers, data points that fall outside of the upper or lower control limits. But there are other unnatural patterns that indicate that the process is “out of control.” The non-random patterns help us determine when something unusual is happening.

## Slide 986: Western Electric Rules
Western Electric Rules are the most popular decision rules to detect unnatural patterns in the control charts. They are a group of tests for special causes in a process.
The area between the upper and lower control limits is separated into six subzones.
  Zone A: between two and three standard deviations from the center line
  Zone B: between one and two standard deviations from the center line
  Zone C: within one standard deviation from the center line.
Notes: The Western Electric Rules were developed by the manufacturing division of the Western Electric Company in 1956.
They are a series of tests to help identify the unnatural patterns that indicate a process is out of control.
The area between the upper and lower control limits is separated into zones defined by the number of standard deviations from the center line. The zones help define the tests.

## Slide 987: Western Electric Rules
Zone A: three sigma zone
Zone B: two sigma zone
Zone C: one sigma zone
If a data point falls onto the dividing line of two consecutive zones, the point belongs to the outer zone.
C
B
A
A
B
C
Upper control limit
Lower control limit
Center line
Observation
Notes: Zone A, B, and C are the three, two, and one sigma zones, respectively.

## Slide 988: Western Electric Rules
Test 1: 1 point more than 3 standard deviations from the center line (i.e., 1 point beyond zone A)
Notes: Such a point is typically known as an outlier.

## Slide 989: Western Electric Rules
Test 2: 9 points in a row on the same side of the center line
Notes: Test 2 identifies situations where the process mean has temporarily shifts in the process.

## Slide 990: Western Electric Rules
Test 3: 6 points in a row steadily increasing or steadily decreasing
Notes: Test 3 identifies significant trends in performance.

## Slide 991: Western Electric Rules
Test 4: 14 points in a row alternating up and down
Notes: Test 4 indicates a cycle.

## Slide 992: Western Electric Rules
Test 5: 2 out of 3 points in a row at least 2 standard deviations from the center line (in zone A or beyond) on the same side of the center line
Notes: Test 5 is similar to test 2, but represents a more acute shift in the process mean.

## Slide 993: Western Electric Rules
Test 6: 4 out of 5 points in a row at least 1 standard deviation from the center line (in zone B or beyond) on the same side of the center line
Notes: Test 6 is similar to test 2, but represents a more acute shift in the process mean.

## Slide 994: Western Electric Rules
Test 7: 15 points in a row within 1 standard deviation from the center line (in zone C) on either side of the center line
Notes: Test 7 indicates a change in the level of variation around the process mean.

## Slide 995: Western Electric Rules
Test 8: 8 points in a row beyond 1 standard deviation from the center line (beyond zone C) on either side of the center line
Notes: While test 7 indicates a narrowing of variation, test 8 indicates an increase in variation.

## Slide 996: Next Steps
If no data points fail any tests for special causes, the process is in statistical control.
If any data point fails any tests for special causes, the process is unstable and we will need to investigate the observation thoroughly to discover and take actions on the special causes leading to the changes.
Process stability is the prerequisite of process capability analysis.
Notes: If the data pass all of the Western Electric rules, the process is considered to be in control.
If any point fails any of the tests, the process is out of control and the observation must be investigated to determine what caused the variation.
Special cause variation must be addressed and the process must be stable before process capability analysis can be done.

## Slide 997: 5.2.12 Subgroups & Sampling
This unit is a part of the full curriculum and may have related test questions. However, due to time constraints, this unit will not be covered as a part of today’s session. Please be sure to review this module online

## Slide 998: 5.3 Six Sigma Control Plans

## Slide 999: Black Belt Training: Control Phase
5.1 Lean Controls
5.1.1 Control Methods for 5S
5.1.2 Kanban
5.1.3 Poka-Yoke (Mistake Proofing)
5.2 Statistical Process Control (SPC)
5.2.1 Data Collection for SPC
5.2.2 I-MR Chart
5.2.3 Xbar-R Chart
5.2.4 U Chart
5.2.5 P Chart
5.2.6 NP Chart
5.2.7 X-S chart
5.2.8 CumSum Chart
5.2.9 EWMA Chart
5.2.10 Control Methods
5.2.11 Control Chart Anatomy
5.2.12 Subgroups, Variation, Sampling
5.3 Six Sigma Control Plans
5.3.1 Cost Benefit Analysis
5.3.2 Elements of the Control Plan
5.3.3 Elements of the Response Plan

## Slide 1000: 5.3.1 Cost Benefit Analysis

## Slide 1001: What is Cost-Benefit Analysis?
The cost-benefit analysis is a systematic method to assess and compare the financial costs and benefits of multiple scenarios in order to make sound economic decisions.
A cost-benefit analysis is recommended to be done at the beginning of the project based on estimations of the experts from the finance team in order to determine whether the project is financially feasible.
It is recommended to update the cost-benefit analysis at each DMAIC phase of the project.
Notes: For a project to be feasible, the benefits must outweigh the costs.
When carrying out a project, it is important to have finance experts conduct analysis to ensure a project is financially feasible at each phase during the DMAIC process.

## Slide 1002: Why Cost-Benefit Analysis?
In the Define phase of the project, the cost-benefit analysis helps us understand the financial feasibility of the project.
In the middle phases of the project, updating and reviewing the cost-benefit analysis helps us compare potential solutions and make robust data-driven decisions.
In the Control phase of the project, the cost-benefit analysis helps us track the project’s profitability.
Notes: The initial cost-benefit analysis is done during the Define phase to determine if it is sensible to launch the project.
In the middle phases, the cost-benefit analysis should be updated, reviewed, and leveraged to weigh potential solutions.
The final update in the Control phase is done as the final assessment of the project’s profitability.

## Slide 1003: Return on Investment
Return on investment (also called ROI, rate of return, or ROR) is the ratio of the net financial benefits (either gain or loss) of a project or investment to the financial costs.
where
Notes: A common financial measure of a project’s impact to profitability is ROI or return on investment.
It is the ratio of net benefits to total costs, expressed as a percentage.

## Slide 1004: Return on Investment (ROI)
The return on investment is used to evaluate the financial feasibility and profitability of a project or investment.
  If ROI < 0, the investment is not financially viable.
  If ROI = 0, the investment has neither gain nor loss.
  If ROI > 0, the investment has financial gains.
The higher the ROI, the more profitable the project.
Notes: Any value over 100 percent means the project has a return greater than the cost, and the higher the ROI, the more profitable the project.

## Slide 1005: Net Present Value (NPV)
The net present value (also called NPV, net present worth, or NPW) is the total present value of the cash flows calculated using a discount rate.
Where
NetCashFlowt is the net cash flow happening at time t;
r is the discount rate;
t is the time of the cash flow.
Notes: Often projects do not have immediate returns and it takes time to recover the costs incurred during the project.
The net present value is the total net, discounted value of all future cash flows, both inward and outward.
The NPV accounts for the time value of money.

## Slide 1006: Cost Estimation
Examples of costs triggered by the project:
  Administration
  Asset
  Equipment
  Material
  Delivery
  Real estate
  Labor
  Training
  Consulting.
Notes: There are many types of costs that can be incurred during a project. Some are one-time investments, such as equipment, consulting, or other assets, while others are incremental costs to be incurred going forward.

## Slide 1007: Benefits Estimation
Examples of benefits generated by the project:
  Direct revenue increase
  Waste reduction
  Operation cost reduction
  Quality and productivity improvement
  Market share increase
  Cost avoidance
  Customer satisfaction improvement
  Associate satisfaction improvement.
Notes: Benefits can take many forms: additional revenue, reduced wasted, operational resource costs, productivity improvements, or market share increases.
Other types of benefits that are harder to qualify include customer satisfaction and associate satisfaction.

## Slide 1008: Challenges in Cost and Benefit Estimation
Different analysts might come up with different cost and benefit estimations due to their subjectivity in determining:
  The discount rate
  The time length of the project and its impact
  Potential costs of the project
  The tangible/intangible benefits of the project
  The specific contribution of the project to the relevant financial gains/loss.
Notes: There are some factors that can change the cost-benefit analysis depending on things like accounting methods or judgment and subjectivity about tangible or intangible benefits.

## Slide 1009: 5.3.2 Elements of Control Plans

## Slide 1010: Control Plans
The control plans ensure that the changes introduced by a Six Sigma project are sustained over time.
Benefits of the Control phase:
  Methodical roll-out of changes including standardization of processes and work procedures
  Ensure compliance with changes through methods like auditing and corrective actions
  Transfer solutions and learning across the enterprise
  Plan and communicate standardized work procedures
  Coordinate ongoing team and individual involvement
  Standardize data collection and procedures
  Measure process performance, stability, and capability
  Plan actions that mitigate possible out-of-control conditions
  Sustain changes over time.
Notes: A key component of a solid DMAIC project is the control plan, the plan to ensure that the changes and benefits introduced by the project are sustained over time.
The Control phase ensures new processes and procedures are standardized and compliance is assured.
Other benefits of the control phase include: solutions are replicated in other areas where applicable, data collection and monitoring is standardized, and there are action plans to be triggered when out-of-control conditions are created.

## Slide 1011: What is a Control Plan?
A control plan is a management planning tool to identify, describe, and monitor the process performance metrics in order to meet the customer specifications steadily.
It proposes the plan of monitoring the stability and capability of inputs and outputs of critical process steps in the Control phase of a project.
It covers the data collection plan of gathering the process performance measurements.
Control plans are the most overlooked element of most projects. It is critical that a good solution be solidified with a great control plan!
Notes: A control plan is critical to describe data to be collected, measures to be monitored, and other controls to prevent or detect defects or undesirable conditions.

## Slide 1012: Control Plan Elements
Control Plan
  The clear and concise summary document that details key process steps, CTQs metrics, measurements, and corrective actions.
Standard Operating Procedures (SOPs)
  Supporting documentation showing the “who does what, when, and how” in completing the tasks.
Communication Plan
  Document outlining messages to be delivered and the target audience.
Training Plan
  Document outlining the necessary training for employees to successfully perform new processes and procedures.
Audit Checklists
  Document that provides auditors with the audit questions they need to ask.
Corrective Actions
  Activities that need to be conducted when an audit fails.
Notes: There are many possible elements within a control plan. All of these need to be agreed to and owned by the process owner – the person who is responsible for the process performance.

## Slide 1013: Control Plan
The control plan identifies critical process steps that have significant impact on the products or services and the appropriate controls mechanisms.
The control plan includes measurement systems that monitor and help manage key process step performance.
Specified limits and targets of the performance metrics are clearly defined and communicated.
Sampling plans to collect the measurements are declared:
  How many samples are needed?
  How often do we need to sample?
  Where should we sample?
Notes: Some additional components of the control plan include identification of critical process steps, measurement systems, limits and targets for those measures, and sampling plans for collecting data.

## Slide 1014: Control Plan
Key processes and process steps are identified
d
Critical information regarding key measurements is documented and clarified

## Slide 1015: Control Plan
Measurements are clearly defined with equations
Customer specifications are declared
Other key measurement information is documented: sample size, measurement frequency, people responsible for the measurement, etc.

## Slide 1016: Control Plan
Where will this measurement or report be found? Good control plans provide linking information or other report reference information.
Control plans identify the mitigating action or corrective actions required in the event the measurement falls out of spec or control. Responsible parties are also declared.
Notes: Not only does a control plan spell out what is measured and what the limits are around the measurement, but it also details actions that must be taken when out-of-control or out-of-spec conditions occur.

## Slide 1017: Control Plan Example

## Slide 1018: Standard Operating Procedures (SOPs)
Standard Operating Procedures (SOPs) are documents that focus on process steps, activities, and specific tasks required to complete an operation.
SOPs should not be much more than two to four pages.
SOPs should be written to the user’s level of required detail and information.
    The level of detail is dependent on the position’s required skills and training
Good SOPs are auditable, easy to follow, and not difficult to find.
    Auditable characteristics are: observable actions and countable frequencies. Results should be evident to a third party (compliance to the SOP must be measurable).
Notes: Standard operating procedures are an important element in a control plan when a specific process is being prescribed to achieve quality output.
SOPs should be accessible, easy to read and follow, and auditable.

## Slide 1019: SOP Elements
SOPs are intended to impart high value information in concise and well-documented manner.
SOP Title and Version Number:
    Provide a title and unique identification number with version information.
Date:
    List the original creation date; add all revision dates.
Purpose:
    State the reason for the SOP and what it intends to accomplish.
Scope:
    Identify all functions, jobs, positions, and/or processes governed or affected by the SOP.

## Slide 1020: SOP Elements
Responsibilities:
  Identify job functions and positions (not people) responsible for carrying out activities listed in the SOP.
Materials:
  List all material inputs: parts, files, data, information, instruments, etc.
Process Map:
  Show high level or level two to three process maps or other graphical representations of operating steps.
Process Metrics:
  Declare all process metrics and targets or specifications.
Procedures:
  List actual steps required to perform the function.
References:
  List any documents that support the SOP.

## Slide 1021: SOP Template

## Slide 1022: Communication Plans
Communication plans are documents that focus on planning and preparing for the dissemination of information.
Communication plans organize messages and ensure that the proper audiences receive the correct message at the right time.
A good communication plan identifies:
    Audience
    Key points/message
    Medium (how the message is to be delivered)
    Delivery schedule
    Messenger
    Dependencies and escalation points
    Follow-up messages and delivery mediums.
Communication plans help develop and execute strategies for delivering changes to an organization.

## Slide 1023: Communication Plan Template

## Slide 1024: Training Plans
Training plans are used to manage the delivery of training for new processes and procedures.
Most GB or BB projects will require changes to processes and/or procedures that must be executed or followed by various employees.
Training plans should incorporate all SOPs related to performing new or modified tasks.
Training plans use and support existing SOPs and do not supersede them.
Training plans should include logistics:
  One-on-one or classroom
  Instruction time
  Location of training materials
  Master training reference materials
  Instructors and intended audience
  Trainee names.

## Slide 1025: Training Plan Template

## Slide 1026: Audits
What is an audit?
  ISO 9000 defines an Audit as “a systematic and independent examination to determine whether quality activities and related results comply with planned arrangements and whether these arrangements are implemented effectively and are suitable to achieve objectives.”
Audits are used to ensure actions, processes, procedures, and other tasks are performed as expected.

## Slide 1027: Audit Guidelines
Audits should be directed by managers, supervisors, and other accountable positions.
An audit’s purpose must be well-defined and executed by independent unbiased personnel.
Auditors must:
  Be qualified to perform their tasks
  Attend and successfully complete an internal auditing training session
  Be able to identify whether or not activities are being followed according to the defined SOP
  Base conclusions on facts and objective evidence
  Use a well documented audit checklist.
Audits should confirm compliance or declare non-compliance.

## Slide 1028: Audit Checklists
Auditors should review the SOPs before preparing checklists or ensure that existing checklists properly reference SOPs.
Audit checklists:
  Serve as guides for identifying items to be examined
  Are used in conjunction with understanding of the procedure
  Ensure a well-defined audit scope
  Identify needed facts during audits
  Provide places to record gathered facts.
Checklists should include:
  A review of training records
  A review of maintenance records
  Questions or observations that focus on expected behaviors
  Questions should be open-ended where possible
  Definitive observations yes/no, true/false, present/absent, etc.

## Slide 1029: Audit Checklist Template

## Slide 1030: 5.3.3 Response Plan Elements

## Slide 1031: What is a Response Plan?
A response plan should be a component of as many control plan elements as possible.
Response plans are a management planning tool to describe corrective actions necessary in the event of out-of-control situations.
There is never any guarantee that processes will always perform as designed. Therefore, it is wise to prepare for occasions when special causes are present.
Response plans help us mitigate risks and, as already mentioned, should be part of several control plan elements.

## Slide 1032: Response Plan Elements
Action triggers
  When do we need to take actions to correct a problem or issue?
Action recommendation
  What activities are required in order to solve the problem in the process? The action recommended can be short-term (quick fix) or long-term (true process improvement).
Action respondent
  Who is responsible for taking actions?
Action date
  When did the actions happen?
Action results
  What actions have been taken?
  When were actions taken?
  What are the outcomes of the actions taken?

## Slide 1033: Response Plan Elements
Note the response plan element in this control plan template

## Slide 1034: Response Plan Elements
Note the response plan element in this communication plan template

## Slide 1035: Response Plan Elements
Note the response plan element in this audit checklist

## Slide 1036
Lean Six Sigma Black Belt Training
Featuring Examples from SigmaXL v.8